## Slide 1: A Sticky Situation: Types of Adhesives with Applications to Acoustic Guitars
The STEM Guitar Grant
Debbie French, PhD
Wilkes University

## Slide 2: Introduction:
What types of glues have you used before?
How have you used them?
List and describe three ways glues are used in the construction of an acoustic guitar.

## Slide 3: Purpose:
Throughout this unit, we are going to learn about the different types of adhesives that are used in the construction of an acoustic guitar.
We are also going to experiment with different types of glue to determine some of their properties such as viscosity and strength.

## Slide 4
Four Types of Glues
Polyvinyl Acetate (PVA)
Animal-based
Cyanoacrylate (CA)
Two-part (Catalyst)

## Slide 5: Polyvinyl Acetate (PVA)
About
The most common variety of PVA glue is white school glue.
Wood glue is another type of PVA glue and is yellow in appearance.
  It has slightly different properties than school glue.
  Wood glue dries harder and is not as affected by moisture.
General Uses
PVA glues are widely used in a variety of arts and crafts applications.

## Slide 6: Polyvinyl Acetate
Pros
Easily accessible
Water-based
Non-toxic
Cons
Sensitive to moisture/humidity
Works by being absorbed by the two surfaces. These surfaces become bonded as water in the glue evaporates. Works only on porous materials such as paper, cardboard, and wood.

## Slide 7: Polyvinyl Acetate: Guitar Uses
While the traditional white school glue is not used in the construction of the acoustic guitar, wood glue is used in several applications:
  Gluing the neck onto the body
  Gluing the bracing onto the top/bottom of guitar body
  Gluing the kerfing around the rim of the top/bottom of guitar
  Gluing the bridge to the top of the guitar
Dry Time |  | 
Instantly | Hours (gets tacky within 30 mins) | 1 day + (wood glues require 24 hours to set)

## Slide 8: Animal-based Glues (Hide Glue)
About:
Animal-based glues come in several types:
  Casein glues are made from milk
  Fish glue is made from fish bones and scales and dries clear
  Hide glues are made from animal hide, collagen, bone, and connective tissues
  Some glues have been made from eggs
General Uses:
Have been used to bind pigments together to form paint
Fish glues are used on the back of adhesive stamps (plant-based glues have also been used on stamps)

## Slide 9: Animal-based Glues (Hide Glue)
Pros
Strong
Reversible—when heated the glue joint releases. This is useful for making repairs.
Glue will not move when under tension (called “creep”).
Does not hinder sound transmission
Cons
Is usable within a narrow temperature range (~50◦C, or 120 ◦F)
Brittle (may be an advantage to break off a component to repair)
Glue joints are sensitive to extreme temperature changes and humidity changes—may affect transportation and use of instrument

## Slide 10: Animal-based Glues (Hide Glues): Guitar Uses
Hide glues were the primary glues used by luthiers and other instrument makers for centuries
Used to attach the neck onto the body (this may be removed for repairs)
Fish glues are transparent and are used on instruments where glue joints may be visible
Dry Time |  | 
Instantly | Hours | 1 day +

## Slide 11: Cyanoacrylate Glue (CA) (“Super Glue”)
About:
CA was discovered in 1942 for applications for WWII. It was “rediscovered” by Eastman Kodak in 1951.
Thinner applications bond better than thicker applications
General Uses:

## Slide 12: Cyanoacrylate (CA) Glue
Pros
Quick dry time (though some CA glues are designed to dry longer)
Dries clear
Cons
Brittle
Glue joint can come apart under tension
Skin and eye irritant
May bond instantly to skin

## Slide 13: Cyanoacrylate Glue: Guitar Uses
Low-viscosity superglues can fill gaps (can mix with saw dust so the blemish cannot be seen)
CA glue can be used to hold frets in the fret slot, if the fret will not “seat” properly
Dry Time |  | 
Instantly | Hours | 1 day +

## Slide 14: Two-part (Catalyst) Glues—Epoxy
About:
Epoxies are made by combining two compounds: epoxide resin and a polyamine compound, which hardens the material.
Uses:
Epoxy glue is used where a strong bond is required. Epoxy is used in construction and the automotive and aircraft industry.

## Slide 15: Two-part (Catalyst) Glues—Epoxys
Pros:
Glues in the epoxy family produce a strong hold.
Epoxy-based finishes are UV-cured and take only minutes to cure. They produce a hard, high-gloss finish.
Cons:
The two chemicals required to make epoxy must be mixed prior to using. Any unused epoxy cannot be stored and reused at a later time.
Epoxy-based finishes may be used on guitars.

## Slide 16: Epoxy Glues: Guitar Uses
Epoxies are not widely used in the construction of acoustic guitars.
However, they may be used to glue decorative in-lays in the wood.
Some epoxies may be used as a guitar finish.
Dry Time |  | 
Instantly (Some epoxies cure within minutes using UV light) | Hours | 1 day + Some epoxies take up to 72 hours to dry

## Slide 17: How glues work:
There are three primary mechanisms for how glues bond materials together
Mechanical Joints
Diffusion Theory
Chemical bonds (Interfacial Secondary Bonds)

## Slide 18: How glues work: Mechanical Joints
Some glues act like “Velcro™.” Velcro™ features one piece of material with “hooks” that attaches to another piece of material with loops.
Some glues may behave in a similar way by physically joining the two surfaces.
The rougher the surface, the more surface area is exposed, and therefore, the stronger the bond.

## Slide 19: How glues work: Diffusion Theory
Some glues work by chemically reacting to the two surfaces (in this case, usually plastic), by dissolving, or breaking down the bonds between those surfaces.
These surfaces mix together, and when the volatile solvent evaporates, the glue “dries,” which bonds the two surfaces together.
Model glue for plastic models is an example of this.

## Slide 20: How glues work: Interfacial Secondary Bonds
The third way in which glues work features chemical bonding between two materials.
Such chemical bonds include Hydrogen bonding or through van der Waals forces.
  Hydrogen bonding produces a weak hold
  van der Waals bonding can produce quite a strong hold.
van der Waals forces occur in glues such as starch glues, PVA (school glue) and epoxies and is used to bond materials such as glass, wood, paper, metal, and leather.

## Slide 21: References
Epp, D. N., & Dianne, E. (1998). Experimental Design: The Chemistry of Adhesives. Terrific Science Press.
French, R. M. (2012). The Technology of the Guitar. New York: Springer.