## Slide 1
UNIT CELLS AND CRYSTAL STRUCTURES Background Information

## Slide 2: MOLECULAR STRUCTURES
Crystals
Polymers
Proteins
Cells

## Slide 3: THE UNIT CELLS
The unit cell is the simplest repeating unit in a crystal.
In a single crystal, all unit cells are identical and oriented the same way (fixed distance and fixed orientation).
The opposite faces of a unit cell are parallel (see graphic of unit cell).
The edge of the unit cell connects equivalent points. The resulting structure is a lattice.
Unit cell configuration for a crystal structure

## Slide 4: ALL UNIT CELLS ARE NOT ALIKE
The Simple Cubic Structure is a unit cell consisting of one atom. Confused? You probably see eight atoms, correct?
Remember that unit cells form a lattice and the edge of the unit cell connects to equivalent points.
Therefore, each of the atoms you see in the simple cubic structure contributes ONLY 1/8 of itself to the unit cell. As the crystal structure forms, seven more unit cells bond with each of the eight atoms.
There are several different configurations for unit cells.

## Slide 5: Miller Indices define direction or planes within a crystal lattice structure Miller Indicies

## Slide 6: CRYSTAL ORIENTATION – SI PLANES
The left most image is a Si crystal.
The middle images show two different planes of the Si crystal. Think of looking at the same crystal from two different directions.
The images on the right are looking at the faces of two plane.
Same crystal, same distance between unit cells, and same orientation of unit cells. However, looking at different planes, presents a different picture.

## Slide 7: Etching
Chemical Reactions are Dependent upon surface area – which at the unit cell level is the atomic density
Different unit cell planes will have different atomic densities
This will result in different etching (chemical interaction) rates

## Slide 8
The diamond crystal is a covalently bonded network of carbon atoms. Each carbon
atom is covalently bonded to four neighbors forming a regular three dimensional
pattern of atoms which constitutes the diamond crystal.

## Slide 9: CRYSTAL STRUCTURES

## Slide 10: Crystal formations