## Slide 1: Remote Sensing Analysis Made Easy! Introduce Remote Sensing Concepts and Landsat Imagery Using a Web Browser and Esri’s Web Applications: Unlocking Earth’s Secrets and Landsat Explorer
Remote Sensing Concepts Based on iGETT‘s Concept Modules
and GeoTech Center Model Courses

## Slide 2: Remote Sensing Imagery and Analysis
Remote sensing imagery is a valuable data source for many
geospatial projects
Traditional use of remote sensing imagery is a complex, time
intensive and costly process requiring:
  Access to high end computers and software,
  Ability to find, access and manage large datasets,
  Knowledge of remote sensing imagery and concepts, and
  Ability to carry out complex analysis techniques h
For new users, this can be an overwhelming process and take many days!

## Slide 3: This Presentation will:
Introduce important remote sensing concepts with links to additional concept module videos on YouTube
Show how to use a web browser and two Esri ArcWeb Apps to access Landsat data and remote sensing analysis tools
Demonstrate the use of the two applications:
    Unlocking Earth’s Secrets
    Exploring Landsat
Link to hands on exercise to create a Poster for an area of interest to you!

## Slide 4
  U.S. Geological Survey Definition
  Acquiring information about a natural feature or phenomenon, such as the Earth’s surface, without actually being in contact with it.
How is remote sensing imagery used?
Change Detection: Land Use Change – Las Vegas
Natural Disaster – Wildfires
Agriculture
Climate & Weather

## Slide 5: Two Types of “Sensors” used for Remote Sensing
Active – Energy source is “provided” by method
  LIDAR – Light Detection and Ranging using pulsed laser beam (of varying wavelengths)
  SAR – Synthetic Aperture Radar – pulses of radio wavesof radio wavelengths
Passive – Sun as the “energy source”
  Landsat
  MODIS
  Aster
  Other imagery sources
Sensors can be on satellites, manned and unmanned (UAS) aircraft, and even on vehicles on the ground.

## Slide 6
The human eye is a passive sensor using reflected energy from the Sun.
Our brain processes the
data and we see the feature!

## Slide 7
Electromagnetic Spectrum
Our eyes use only a small region (400 to 700 nm) of the Electromagnetic Spectrum.
http://missionscience.nasa.gov/ems/emsVideo_01intro.html

## Slide 8
Top of Atmosphere
Transmitted
Reflected and
Re-emitted
Scattered
Absorbed
Sensors on Landsat satellites collect data from multiple regions of the Electromagnetic Spectrum
including regions our eyes can’t “see”

## Slide 9
For Landsat, data is stored and transmitted to ground station where it is processed and made accessible on the web!
Transmitted
Reflected or
Re-emitted
Scattered
Absorbed
Top of Atmosphere

## Slide 10: Gray shading indicates regions of the Electromagnetic Spectrum (EM) where “atmospheric windows” permit reflected energy to reach the satellite’s sensors!
Landsat 8 band numbers
Landsat 7 band numbers
Our eyes see this region
Each sensor on a satellite collects data in specific wavelength regions! These regions are numbered and called bands or channels.

## Slide 11: What does raw band “data” look like? Each pixel for each band is displayed in “gray scale” values of relative brightness based on its Digital Number (DN) value
Note: for more information on bands and brightness of pixels, see iGETT YouTube Channel at
https://www.youtube.com/watch?v=Gm32ZIakLIA
Downloaded original data (tar) and unzipped once (tar.gz) and unzipped twice (bands and metadata)
Gray scale raster layer for one band
Landsat imagery is LARGE – Up to 1 GB!

## Slide 12: Landsat 8 Band 4 Brightness and its Digital Numbers (DN)
15555 | 25000 | 25500 | 25500 | 25500 | 25500
25000 | 25000 | 25100 | 15555 | 15550 | 25500
36500 | 36250 | 40000 | 50500 | 49000 | 40010
35590 | 36600 | 50501 | 50500 | 53000 | 53500
Landsat 8, Band 4 scene
Band 4 Brightness of Buildings
Digital Number of Pixel
Pixels – 30 x 30 m
Notes: Digital Numbers correspond to “brightness” of each pixel detected by a sensor for a given wavelength or band
Brightness of a pixel is created when solar radiance or energy from the sun on an object is reflected and detected by the sensor
Solar radiance varies
  Distance from Sun
  Angle of Incoming energy

## Slide 13
Creating Composite Images
Brightness values (DN) from three Bands are combined and assigned a to either the red, green, or blue color gun on a computer monitor creating a Composite Image
Esri.com help

## Slide 14: Landsat 7 - Composites ` Natural or True Color Bands 3, 2, 1 False Color Band 4, 3, 2 Pseudo Color Bands 7, 5, 3
Note: for more information on Composite images and electromagnetic radiation see YouTube Channel from iGETT at https://www.youtube.com/watch?v=Gm32ZIakLIA
Note: A maximum of 3 bands can be combined and visualized on a computer monitor

## Slide 15: Remote Sensing Imagery “Resolutions”
Spatial – size of area on the ground of one pixel and size of image footprint
Temporal – how often data (imagery) is acquired for the same location
Radiometric – the sensitivity of sensor to collect very slight differences in emitted or reflected energy (its bit depth)
Spectral – specific wavelengths of spectrum collected by sensors
See an iGETT Remote Sensing YouTube video on Resolutions at
https://www.youtube.com/watch?v=AdXBewR-u2A

## Slide 16: Spatial Resolution Comparison
High spatial resolution:
  Meter to sub meter pixels
  Small objects can be identified
  Small area for each image footprint
Moderate spatial resolution
  Generally 30 meter pixels (Landsat)
  Object identification generally greater than 30 meters
  Moderate area image footprint
Low spatial resolution
  Km or larger pixels (MODIS)
  Objects smaller than 1 KM not observable
  Very large footprint
http://biodiversityinformatics.amnh.org/tool.php?content_id=144
Ground Footprints

## Slide 17: Radiometric Resolution
The “sensitivity” of the sensors
  Sensors with low radiometric resolution detect only large differences
  Sensors with high radiometric resolution can detect smaller differences
Radiometric Resolution was increased for Landsat 8! Pixel size is the same, but increased radiometric resolution can aid analysis
  Landsat 7 has 256 possible values (28) and is 8-bit
  Landsat 8 has possible values of 65536 and is 16-bit or (216)

## Slide 18: Why Focus on Landsat Data?
Cost – Free
Access – Download imagery from websites
Continuity - Archive of data over decades – 1972 to present
Ease of use – can be used by various software packages
Is accessible using free Esri ArcWeb Server applications
  Unlock Earth’s Secrets, and
  Landsat Explorer
http://esriurl.com/LandsatOnAWS
Landsat Missions and dates of collection
Landsat 8

## Slide 19
Note: Different Landsat Missions Use Different Band Numbers and Wavelengths to Visualize Imagery
Note: Band numbers for composite images are different for Landsat 5 and 7 than those for Landsat 8

## Slide 20: Spectral Signature graphs can help identify type of feature seen in an image
A Spectral Signature Graph uses Digital Number values
for one pixel using all bands in an image
Useful in Image Classification of features
This graph compares Spectral Signatures for different types of features (soil, vegetation, water, urban, etc.)
This graph compares Spectral Signatures for health versus Stressed Sugar Beets

## Slide 21: Determining Land Use Types – Image Classification - Unsupervised Classification – software clusters like-valued pixels and user defines what the feature is and colors it appropriately - Supervised Classification – user creates a sample file of identified land use types and pixel values and software clusters pixels using the sample file values
Natural Color Composite of San Fernando Valley, CA
Unsupervised Classification –
Data is clustered by software and colored to match Land Use types.
blue = water,
green = vegetation,
Soil = brown,
Beige = urban built up (road, building, etc.)

## Slide 22: Visualization of Patterns
Using “band algebra” equations for visualizing patterns
One common band algebra equation is Normalized Difference Vegetation Index (NDVI)
used to visualize greenness of vegetation
  The NDVI algorithm uses two bands: Near Infra Red (NIR) and Red
NDVI equation using NIR and Red Band Digital Numbers
NDVI = (NIR + Red)/(NIR – Red)
ArcGIS Pro NDVI where green indicates vegetation

## Slide 23: Normal Workflow For Remote Sensing Analysis Using Landsat Imagery
Identify a problem you want to investigate
  Find study area location and determine its Landsat path and row
  Determine how many scenes and what dates are needed
Go to website for imagery data and determine if dates are available
  if not available, reevaluate needed data that can “work” for project analysis
Download imagery data – up to 1 GB per Landsat scene
Unzip data twice and store all bands in folders
Create a Project and add imagery data
Mosaic and Clip imagery bands to study area
Create composites of each scene (natural, false, pseudo)
Create signature graphs to identify features (urban, soil, vegetation, etc.)
Start analysis (NDVI, Classification, . . . .)
This process can take days!

## Slide 24: Instead – how about spending an hour or two to quickly review data for your study area? No need for software or data downloading and it is free to use! http://www.esriurl.com/LandsatOnAWS

## Slide 25: Esri’s Unlock Earth’s Secrets AWS App
This is the “default” opening location – Redlands, California using “Agriculture”
Note: Find a place is not filled in.

## Slide 26: Esri’s Unlock Earth’s Secrets AWS App
This is the Agriculture button

## Slide 27: Esri’s Unlock Earth’s Secrets

## Slide 28: Esri’s Unlock Earth’s Secrets

## Slide 29: Esri’s Unlock Earth’s Secrets

## Slide 30: Esri’s Unlock Earth’s Secrets

## Slide 31: Key For Buttons: Landsat 8 Bands
Agriculture: Highlights agriculture in bright green. Bands 6,5,2
Natural Color: Sharpened with 15m panchromatic band. Bands 4,3,2+8
Color Infrared (False Color): Healthy vegetation is bright red. Bands 5,4,3
SWIR (Short Wave Infrared): Highlights rock formations. Bands 7,6,4
Geology: Highlights geologic features. Bands 7,4,2
Bathymetric: Highlights underwater features. Bands 4,3,1
Panchromatic: Panchromatic image at 15m. Band 8
Vegetation Index: Normalized Difference Vegetation Index (NDVI). (Band5-Band4)/(Band5+Band4)
Moisture Index: Normalized Difference Moisture Index (NDMI). (Band5-Band6)/(Band5+Band6)

## Slide 32
Using a web browser go to http://esriurl.com/landsatonaws and click on “Try It Live”
Search on Washington, D. C.
Use + to zoom as far as you can
  (you will see the Capital and the National Mall
Click on the time button
Slide the date to November 16
Click on all the other buttons.
How does the scene change?
Look at “about” to see what each band uses.
Change the date to June or July and look again at all buttons.
  Does the scene change?
Click on the identify button and different features in the image – what does the graph tell you?

## Slide 33: By scrolling down on browser you will see “Launch Landsat Explorer” it has more advance tools to use with Landsat data

## Slide 34: Landsat Explorer – data from most Landsat missions
New Buttons and capabilities
Setting your own render
Picking two dates and change
detection
Swipe tool between two dates
Create Spectral Signature graphs
Add data from ArcGIS Online
Export top layer to AGO
And much more!

## Slide 35: Landsat Explorer
Method to use it:
Hover over buttons to learn more about its use.
Click on Tutorial and follow its steps and continue through tutorial.
Use “Find a place” and enter a location that interests you.
4) Use tools to review your place
5) See Poster and create images
for your own Poster

## Slide 36: This Poster was created using imagery from Apps!

## Slide 37: You can use the Exercise Guide and Publisher Template from iGETT website to create a Poster

## Slide 38
23 Remote sensing Concept Modules can be found on YouTube by Searching on:
iGETT Remote Sensing Education Channel
See the iGETT website at http://igettremotesensing.org for links to Exercise and Poster Template – Plus many other instructional resources including additional exercises and videos.