## Slide 1: Module 3
UAS Mapping Fundamentals

## Slide 2: Objectives
Advantages and limitations of small UAS
Understand flight planning for UAS mapping
What is ground control and when do we need it?
Introduce SfM photogrammetry software
Summarize UAS-SfM data processing workflow
Identify key geospatial data products produced

## Slide 3: UAS adaptive tools for aerial surveying

## Slide 4
imagery is processed using structure-from-motion (SfM) photogrammetry
Dense, textured 3D point cloud, Little St. George Island, FL
> 1000 pts/m2
UAS aerial mapping

## Slide 5: Advantages of sUAS for Mapping
Limitations: Payload weight, endurance, spatial coverage, regulations
Rapid deployment
High temporal repeatability
Flexibile acquisition
Can be less costly and safer (no pilot onboard)
Hyperspatial imagery resolution (meters to mm)

## Slide 6
Image Source: WestCoastPlacer
4 cm
60 cm

## Slide 7
From Greenwood 2014
flight direction
Mission Planning
Define Overlap

## Slide 8
image source: Pix4D

## Slide 9: How much overlap?
Amount of overlap depends on objectives and terrain.
Increase overlap, increase flight time
From Pix4D
  75% frontal and 60% side overlap in general cases.
  85% frontal and 70% side overlap for forests, dense vegetation and fields.
  85% frontal overlap for single track corridor mapping. Use 60% side overlap if the corridor is acquired using two flight lines.

## Slide 10
Image’s Ground Sample Distance: Depends on flying height above ground, focal length of camera, and pixel pitch (size of pixel in camera)
Mission Planning
Define Resolution
From Greenwood 2014

## Slide 11
From Greenwood 2014
GSD = (pixel pitch * H’)/f
From Greenwood 2014

## Slide 12: Example Problem
S110 NIR camera on eBee
  Sensor size 7.44 x 5.58 mm
  1.86 um pixel pitch
  4000 x 3000 pixel array
What is the pixel pitch?
What is GSD at 100 m AGL for 5.2 mm f ?
GSD = (pixel pitch * H’)/f
GSD = (0.0018 mm * 100 m) / 5.2mm ~= 3.53 cm
7.44 mm / 4038 ~= 0.0018 mm 5.58 mm/3038 ~= 0.0018 mm

## Slide 13
Mission Planning
Create area to be mapped
Set flying height
Define overlap / flight direction
Command-and control
Real-time tracking
GPS location
Aeronautical information
*many work off smart phone or tablet; open source one called Mission Planner
Mission Control Software
Example eMotion

## Slide 14
What is ground control?
  Physical points on ground whose coordinate positions are known (x,y) and/or elevations (z)
Measurements of photos are tied to “real-world” coordinates on ground through ground control (GC)
Photogrammetric measurements only as reliable as the GC they are based on
Control points must be easily identifiable
  Identifiable features in scene or ground control targets
Ground Control Points (GCPs)
Notes: If you are interested in this topic, then read chapter 6 in Jensen –
Up until the early 1970s, photogrammetry represented the key method used for the analysis of aerial photographs in order to generate maps – e.g., it was the foundation for cartography
TWO Types of photogrammetry – analog and digital _ WOB from next page

## Slide 15: GCP Network
distribute as evenly as possible
boundary should be enclosed
# depends on size of area
5 to10 unless steep terrain or large area
Good to include extras for check points
Rules of thumb:
  < 1000 ft separation
  Do not place the GCPs exactly at the edges of the area

## Slide 16: GCP Accuracy

## Slide 17: Example: Ground Control Targets

## Slide 18: Use Objects in Image Post-Flight
RTK GPS used to manually survey coordinates on these identifiable features

## Slide 19: Alternative to GCP RTK GPS
Use base station or broadcast correction to differentially correct GPS on drone
Improves geotagging accuracy of imagery (e.g 15 ft down to < 1 ft)
Onboard RTK GPS receiver cost coming down
eBee RTK

## Slide 20: Remember
Absolute accuracy of UAS data products depends on accuracy of your control and/or geotagging
Even if you do have onboard RTK GPS for high accuracy geotagging, you should always acquire check points to validate accuracy

## Slide 21: SfM Software for UAS Mapping

## Slide 22
Pix4D and Agisoft PhotoScan are well known commercial SfM photogrammetry software for UAS (drone) image processing. User-friendly, powerful, flexible, and offer good documentation and customer support. But can be relatively expensive.
OpenDroneMap project is a suite of open source tools for UAS-SfM processing.
Open source software removes expense, but the user should be prepared to have less software support and less control over the processing.
Many other commercial software are available beyond these mentioned here.

## Slide 23
Dense 3D matching
Structure from Motion (SfM) Workflow
Feature detection
Feature correspondence
Sparse 3D point cloud
3D camera pose
reconstruction
Dense “textured”
3D point cloud
Dense 3D point cloud Digital Surface Model Orthorectified Image Mosaic
Notes: Bundle adjustment means the simultaneous least squares adjustment of all bundles from all exposure stations, which implicitly includes the simultaneous recovery of the exterior orientation elements of all photographs and the positions of the object points.

## Slide 24: Remember
Different software vary in how the SfM processing workflow is implemented.
SfM software offer many parameters for tuning results but can be “black box” in many aspects.
Therefore, understanding the main stages and fundamentals of SfM photogrammetry is important

## Slide 25: Geospatial Data Products

## Slide 26: 3D Point Cloud
Surveyed Coordinates (colored by height)
Image from Mitasova, NSCU

## Slide 27: Topographic Products
From Greenwood 2014

## Slide 28: Example from AgriLife: Beeville, TX

## Slide 29: What is an orthophoto?
Image that is corrected (through the process of orthorectification) from the effect of terrain relief or sensor tilt to convert it to a unified scale map.

## Slide 30: Resulting Image (orthophoto)
It is now a “Photo-Map”
Image is aligned with ground coordinates (e.g. north-south streets will be aligned)
Each pixel will have nominal ground coordinates
Scale variation, relief, tilt removed
Can accurately measure distances, areas…
Can be used for “heads-up” digitizing in a GIS

## Slide 31: Orthomosaic
Merging together a block of single ortho-photos to create a large seamless, orthorectified image

## Slide 32: Example North Padre Island, TX

## Slide 33
Example of UAS-SfM Ag. Processing Workflow