## Slide 1: Module 2
Structure from Motion (SfM) (8)

## Slide 2: Objectives
Define Structure from Motion photogrammetry
Differences to traditional photogrammetry
Understand basic methodology
Learn stages in SfM processing
How to implement it

## Slide 3: SfM versus Traditional Photogrammetry
Traditional Photogrammetry
  2 overlapping images + metric camera + camera position / orientation + bundle adjustment = matched points in 3D.
Structure from Motion (SfM)
  many overlapping images + non-metric camera + feature detection + correspondence + adjustment = matched points in 3D
  Non-metric cameras include things like typical consumer-grade hand held digital cameras
Both methods rely on calibrated cameras for accurate measurements but SfM software can calibrate the camera using automated self-calibration methods.

## Slide 4: SfM description from UNAVCO
UNAVCO is a non-profit university-governed consortium, facilitates geoscience research and education using geodesy.
Be sure to read the accompanying reading for this lecture!

## Slide 5: Structure-from-motion?
Use the locations of the camera (motion) to interpret the geometry or 3D model (structure) of a scene
Figure Kate Shervais
Notes: Structure-from-Motion photogrammetry is an emerging technique used to create three-dimensional point clouds with associated color—basically a three-dimensional model of the area of interest. The key things to notice here are that the camera needs to continually be moving (no two photos taken from the same location) and the photographs need to include the same features, so that features are in multiple photographs. You can see here that many of the gray dots on the 3D model are captured by multiple images, not just one. Scientists use this for many applications, which you will learn about today. The next slide will show what Structure-from-Motion actually produces.

## Slide 6: What do you create?
~500 points/m2 colored point cloud along a ~1 km section of the 2010 El Mayor-Cucapah earthquake rupture generated from ~500 photographs captured in 2 hours from a helium blimp
Figure Ed Nissen
Notes: The model above is a three-dimensional point cloud with associated color. This model is of a fault scarp; the red arrows point toward the location of the scarp. You will see a different view of this figure later in the presentation. Most researchers who use SfM use it to make point clouds like these: 3D models of a field area they can revisit and actually measure in the lab instead of the field. Can you think of anything to model using SfM? [Make a list on the board.] Why would SfM be a good method to use for these applications? [add to list on the board.]

## Slide 7: What can we compare sfm to?
Figure Johnson 2014
Notes: Structure-from-Motion is not the only way to create a georeferenced point cloud like the one on the previous slide. The other option is using something called LiDAR. LiDAR laser scans an area of interest to create a 3D point cloud. Two example platforms for LiDAR are shown. You can fly a plane over an area at an altitude of roughly 1 km to get a point cloud or have a scanner on a tripod as shown in B. LiDAR can be used with many other platforms not seen here. Typically, LiDAR is how scientists are able to collect 3D point clouds for research. We will see some direct comparisons between LiDAR and SfM in later slides. (Kendra Johnson, Geosphere 2014)
Note: GSA Publications allow the reproduction of a single figure or table under without permissions. http://www.geosociety.org/pubs/copyrt.htm

## Slide 8: Matching features
Step 1
Match corresponding features and measure distances between them on the camera image plane d, d’
The Scale-Invariant Feature Transform is key to matching corresponding features despite varying distances
d
d'
Figure Ed Nissen
Notes: The first step in actually creating the product we saw on the previous slide is to find the same feature in multiple photographs. You can see [spacebar] the red and purple lines tracing the line of sight from the two camera locations to two different features on the ground. This is done using an algorithm called SIFT: Scale-Invariant Feature Transform.

## Slide 9: Scale-invariant feature transform (SIFT)
Figure Ed Nissen
Notes: Each red box shows the same feature in multiple photographs. The SIFT algorithm recognizes these as the same feature.

## Slide 10: Scale-invariant feature transform (sift)
Finds matching features in multiple photographs
Scale, perspective, and illumination of the feature in the photograph do not affect algorithm
Used as the input for calculating camera locations
Figure Ed Nissen
Notes: [Read the slide.]
A primary pioneer for the SfM method is: Lowe, D.G., 1999. Object Recognition from Local Scale-invariant Features. International
Conference on Computer Vision, Corfu, Greece, pp. 1150–1157.

## Slide 11: Find camera locations
d
d'
f’
f
Step 2
When we have the matching locations of multiple points on two or more photos, there is usually just one mathematical solution for where the photos were taken.
Therefore, we can calculate individual camera positions (x, y, z), (x’, y’, z’), orientations i, i’, focal lengths f, f’, and relative positions of corresponding features b, h, in a single step known as “bundle adjustment.”
(x, y, z)
(x’, y’, z’)
i
i’
h
b
Figure Ed Nissen
analytical self-calibration of camera
Notes: When we have the matching locations of multiple points on two or more photos, there is usually just one mathematical solution for where the photos were taken. [spacebar] This step, bundle adjustment, results in the locations of the cameras and a sparse point cloud—like the one we saw on the earlier slide, but with significantly fewer points.

## Slide 12: Multi-view stereo / Densification
d
d'
f’
f
Step 3
Next, a dense point cloud and 3D surface are determined using the known camera parameters and the sparse point cloud as input.
All pixels in all images are used so the dense model is similar in resolution to the raw photographs (typically 100s–1000s point/m2). This step is called “multi-view stereo matching” (MVS) or densification.
Different algorithms including semi-global matching
(x, y, z)
(x’, y’, z’)
i
i’
h
b
Figure Ed Nissen
Notes: Multi-view stereo is a process that results in the creation of a dense point cloud, like the example on the earlier slide. The MVS algorithm takes the sparse point cloud and camera locations to populate the model with more points. The resultant point cloud may have millions of points.

## Slide 13: georectification
d
d'
f’
f
(x, y, z)
(x’, y’, z’)
i
i’
h
b
Step 4
Georectification means converting the point cloud from an internal, arbitrary coordinate system into a geographical coordinate system. This can be achieved in one of two ways:
Figure Ed Nissen
Notes: Georectification means converting the point cloud from an internal, arbitrary coordinate system into a geographical coordinate system. This step is essential; we want to be able to link the model to where it actually is in space. This results in the ability to measure features in the model, because it will be correctly scaled. [spacebar]

## Slide 14: georectification
d
d'
f’
f
(x, y, z)
(x’, y’, z’)
i
i’
h
b
Step 4
Georectification means converting the point cloud from an internal, arbitrary coordinate system into a geographical coordinate system. This can be achieved in one of two ways:
• directly, with knowledge of the camera positions and focal lengths
• indirectly, by incorporating a few ground control points (GCPs) with known coordinates. Typically these would be surveyed using differential GPS.
GCPs surveyed
with roving receiver
GPS base station
Figure Ed Nissen
Notes: The process of georectification can be achieved in two ways: directly or indirectly. Generally, the indirect process is what scientists use. This way, the model is not only correctly scaled but also correctly located geographically. The number of ground control points varies project to project; however, a minimum of three is needed. It is recommended to use more than 10 per project. Find points that are clearly recognizable or use targets (usually the recommended option).

## Slide 15: products
d
d'
f’
f
(x, y, z)
(x’, y’, z’)
i
i’
h
b
GCPs surveyed
with roving receiver
GPS base station
Optional Step 5
Generate derivative products:
Digital Surface Model
Orthomosaic for texture mapping
Figure Ed Nissen
Notes: The last step in the production of an SfM model is to create the final products. Generally, people use the topography (digital surface model) or the imagery (orthomosaic). The next slides show some examples.

## Slide 16: Photo density map
Figure Ed Nissen
Notes: This photo density map shows the amount of overlap between the photos in a dataset. Each dot is a camera location. You can see the photos are the most dense around areas with lots of camera locations like the center, but that in this model every spot was seen by at least two photographs.

## Slide 17: orthomosaic
Figure Ed Nissen
Notes: The orthomosaic is a high-resolution photograph of the area created by associating color with each point in the model. This can be used to view the features on the surface.

## Slide 18: Shaded digital elevation model
Figure Ed Nissen
Notes: DEM – Digital elevation model. This one has hillshade, so it seems like the sun is shining and it is partially in shadow to show off the features. You can see that different features stand out in the DEM in comparison to the orthomosaic, so they can be used for different research applications. You can use this to measure features.

## Slide 19: platforms
Figure Kate Shervais
Notes: Many platforms exist to assist in capturing SfM data. The figure above shows a range of platforms, from UAS on the far left, handheld mid-left to pole photography on the mid-right and a balloon on the far right. The squares with a black pattern are targets, places to survey in, so the model can be linked to geographic coordinates. A handheld platform is best for doing detail work and some outcrop scale work, but has limited applications and is not ideal for areas larger than 100–200 square meters. The slides following will go into the details of the other platforms.

## Slide 20: Platforms – pole
Figure Kate Shervais
Notes: One form of ground-based SfM is pole photography. In the photo shown, the pole is used to take photographs of the horizontal outcrop. For scale, the man holding the pole is 1.85 m tall. Poles are useful because they are inexpensive, good for photographing outcrops, easy to use, and lightweight. They can be quite high—although poles higher than around 20 feet generally need a tripod for stability. However, poles are inefficient in comparison to using an aerial system and require a mount for the camera, as most poles are intended for other applications.

## Slide 21: Platforms – kite
Figure Neal Spencer
Notes: Kites are used frequently as a platform. This example is from Amara West, an archaeological site. Kites are inexpensive, but reliant on wind. Kites also require a picavet (shown in the left photo). Kites allow photographs from a useful height for photographing topography, require no helium (unlike balloons), and have no legal complications (unlike UASs) because they use a tether.

## Slide 22: Platforms - balloon
Figure Kate Shervais
Notes: This is just an example of one type of balloon. This one is called a heli kite because it has a kite-like tail but is filled with helium. The heli kite carries small cameras only (other balloons may carry larger cameras). Balloons and kites having similar advantages/disadvantages, as well as similar applications. The main difference is balloons have no weather requirements, but do need helium (~$180 per canister). Figure Kate Shervais, photographs taken by UNAVCO

## Slide 23: Platforms – uas
Figure Mike Bunds
Notes: UASs are the final category of SfM platform. The cost is highly variable depending on type—one can spend thousands of dollars. The UAS shown in this photograph was around 1000 dollars. The height, camera position, and flightlines are easily controlled using an UAS. However, they require a skilled operator, batteries may limit the survey time (to ten minutes or less), and may require a lighter camera than a balloon. The legal landscape is also quite complex and frequently changing, so consult legal counsel before using.

## Slide 24: Remember
Accurate measurements from photogrammetry always requires calibrated cameras
  calibrated as precisely as possible for that given camera model
SfM software can calibrate the camera using automated self-calibration methods as part of the processing workflow
Image source: NASA Jet Propulsion Lab