## Slide 1: Module 1
Elements of Photogrammetry (7)

## Slide 2: Objectives
Define photogrammetry
Understand types of aerial photographs
Identify geometry of a vertical aerial photo
Measuring scale in aerial photos
Relief displacement and elevation in aerial phots

## Slide 3: 3D Reconstruction
By taking photographs from at least two different locations, so-called "lines of sight" can be developed from each camera to points on the object. These lines of sight (rays) are mathematically intersected to produce 3D coordinates

## Slide 4: Ultimately we want to do this from aircraft…
http://www.photogrammetrynews.com/2011/06/introduction-of-aerial-traingulation-in.html
http://www.sharpgis.net/page/True-Orthophoto-Generation

## Slide 5
Source: http://www.engineersjournal.ie/wp-content/uploads/2014/11/Aerial-mapping-Ireland.jpg

## Slide 6: What is photogrammetry?
Metric photogrammetry – obtaining measurements from photos from which ground positions, elevations, distances, areas, and volumes can be computed and topographic or planimetric maps can be made.
  Can be done from ground or air
Photo interpretation – evaluation of existing features in a qualitative manner.
https://www.youtube.com/watch?v=HB67qTbBr78

## Slide 7
Slide from https://www.slideshare.net/Engineeramir393/photogrammetry-amir

## Slide 8: We are concerned with aerial photos

## Slide 9: Categories of Aerial Photographs
Vertical Photograph
  Camera optical axis < 3° off vertical (minimal tilt)
Low-Oblique
  Camera optical axis > 3° off vertical
  Horizon not in image
High Oblique
  Camera optical axis > 3° off vertical
  Horizon in image

## Slide 10
Low-Oblique Aerial Photograph
Over Flat Terrain
Notes: Note in many cases, it is easier to interpret oblique photographs because they contain façade information, e.g., information based on viewing the sides of objects
 more naturally related to human vision

## Slide 11
High-Oblique Aerial Photograph
Over Flat Terrain
Notes: Here we have an example of a high oblique image
Can geometrically correct oblique imagery, however it is much more complicated than the methods used in vertical imagery

## Slide 12
Figure 10
Vertical Aerial Photograph Over Level Terrain
Notes: This is the typical view of horizontal aerial photograph
Critical components of the aerial photograph – Write this stuff on the board
1. Field of view – angular dimension covered by the photograph
Two parts – cross track and along track
2. Altitude image was collected
FOV and Altitude determine  ground coverage of the photograph
3. Principal point = center of the photograph, the point in the image below the position of the camera

## Slide 13
Stereoscopic overlap area > 50% is often necessary
Image source: Jensen, 2000

## Slide 14: Block of traditional aerial photos
Endlap “longitudinal”
Sidelap “latitudinal”

## Slide 15: Geometry of vertical aerial photo
O = principal point
What is it? intersection of optical axis and film plane
PP = ground principal point; point where optical axis intersects the terrain
Image source: Jensen, 2000

## Slide 17: Photo Scale (S)
Image source: UCSB library web link

## Slide 18: Example
from Lillesand, et al, 2007

## Slide 19: Scale Relation to Focal Length and Flying Height
H’ = flying height above datum (H) – terrain height (h)
*Most important thing to observe is that photo scale is a function of terrain elevation h. Hence, only photographs over flat level terrain have uniform scale; else varying elevations cause continuous variations in a photo’s scale

## Slide 20: Example
Solution?
from Lillesand, et al, 2007

## Slide 21
Impacts of decreasing scale (higher flying height)

## Slide 22
Relationship between aircraft altitude
and ground coverage – two ways to change FOV
a) Changing the focal length of the camera lens will alter the angular coverage of the system
increase focal lengthdecrease angular coverage
b) As the angular cover increases (focal length decreases), the FOV increases
Notes: Two ways you can increase the ground coverage of the aerial photograph
Increase the angular field of view, or lens angle of view
Increase the altitude

## Slide 23
Relationship between aircraft altitude
and ground coverage – two ways to change FOV
Changing the aircraft altitude will alter the ground coverage of the system
Notes: Two ways you can increase the ground coverage of the aerial photograph
Increase the angular field of view, or lens angle of view
Increase the altitude

## Slide 24
f =152.4 mm
H’ = 18,300m
S=1:210000
Image source: Jensen, 2000

## Slide 25
f =152.4 mm
H’ = 915 m
S=1:10500
Image source: Jensen, 2000

## Slide 26: Measurements from non-corrected Aerial Photo
Due to scale variations from terrain height and tilt of aircraft, area measurements can be inaccurate
However, simple scales over low varying relief terrain can be used to measure area
Points on a GIS map are projected to their true relative planimetric (horizontal) positions
  Orthographic projection
Points on a photo taken over varying terrain are displaced from their true “map positions”
  Perspective projection

## Slide 27: Orthographic vs. Perspective Projection
  What effect does this have on objects in photo?

## Slide 28: Relief Displacement
vertical features lean away from center of photo
Columbia, SC
Original scale = 1:6,000
Focal length = 6” (152.82 mm)
March 30, 1993
Image source: Jensen, 2000

## Slide 29
Minimal displacement of towers because they are located close to photo’s principal point
Lots of displacement of towers due to radial nature of relief displacement; it increases with increase in radial distance from principal point of a photo

## Slide 30: Correcting for Relief Displacement
Terrain (not just objects) also shows relief displacement due to height variation
Quantification of relief displacement can be used to correct image positions of terrain points in a photo
Through photogrammetric process, photos cane be “orthorectified” such that features are shown at their true planimetric position.
  More about this later!

## Slide 31: What is Parallax?
apparent change in relative positions of stationary objects caused by a change in viewing position
When viewed from "Viewpoint A", the object appears to be in front of the blue square. From "Viewpoint B", the object appears to have moved in front of the red square.

## Slide 32: Importance of parallax in photogrammetry?
Parallax at any point is directly related to elevation of that point.
Parallax is greater for higher points than low points
Stereoscopic parallax is caused by taking photographs of the same object but from different points of observation.
Graphic from http://www.ccrs.nrcan.gc.ca/ccrs/learn/tutorials/stereosc/chap4/

## Slide 33: Stereo-photogrammetry
Most photogrammetric operations use stereo-pairs or many pairs of overlapping photos (multi-view stereo-photogrammetry)
Principles of parallax and relief displacement are exploited to measure distances and elevations on ground from pairs of photos
Similar to how our eyes work!

## Slide 35
Source: http://www.remoteaerialsurveys.co.uk/photogrammetry