## Slide 1: Map Projections 3 Dimensions to 2 Dimensions A Globe to a Flat Map
Body of Knowledge
Knowledge Area 1: Conceptual Foundations
KA 105: Knowledge of georeferencing systems,
including coordinate systems, spatial
projections and horizontal and vertical datums
Empowering Colleges:
Growing the Workforce
Based upon work supported by the National Science Foundation under Grant DUE ATE 1304591, 1644409 and 1700496. Any opinions, findings, and conclusions or recommendations expressed in this material are those of the author(s) and do not necessarily reflect the views of the National Science Foundation.

## Slide 2: Map Projection Concept Module Overview
Why maps need to be flat and include a Datum
Understanding of problems going from a globe (sphere) to a planar surface
Distortions for different types of map projections
Cylinders, Cones and Planar surface projections
Rule of Thumb for picking a projection
Other types of map projections

## Slide 3: Why Map Projections?
Globes are inconvenient
Going from 3D to 2D
Geographic Coordinate System uses
Latitude, Longitude and Decimal
Degrees for locations and distances
  No real world units (ft/m)
Need to “project” features on to flat surface using a map projection and datum that can have real distance units
But distortions will occur!
https://thebigblogtheory.files.wordpress.com/2010/03/globe-triangle.jpg
Copyright 2014, Aaron Keller, adapted by permission

## Slide 4: Datums
Map projections are based on a Geographic Coordinate System that specifies what Datums (models of the Earth) were used
  Datums provide locational references and size of the Earth
  Projections based on different Datums will be offset from one another
    Amount of offset depends on region
    Offset typically ranges from 0 – 300 meters
Many desktop software options can “project” data on the fly but Datum transformation may still need to be done
  It is still advisable to re-projected data into the same projection and include any Datum transformations prior to carrying out your spatial analysis
  See Datum Concept Module on YouTube for more details
UTM Zone 13 NAD 1983 ≠ UTM Zone 13 NAD 1927!
http://vdatum.noaa.gov/docs/userguide.html
http://upload.wikimedia.org/wikipedia/commons/4/41/Datum_Shift_Between_NAD27_and_NAD83.png

## Slide 5: A closer look at the 3D to 2D problem…
Projection Plane
This much earth’s surface
2. has to fit onto this much map surface...
http://webhelp.esri.com/arcgisexplorer/900/en/map_projections.htm
...therefore, much of the earth's surface has to be represented as smaller than the nominal (real) scale and features are distorted

## Slide 6: Distortion
Anytime we go from 3D to 2D we introduce distortion
  Think “flattened globe”
  All map projections introduce distortion
4 properties (S-A-D-D)
  Shape
  Area
  Distance
  Direction
Distortion property and degree of distortion can be controlled
  Choose map projection to preserve important property for the specific needs of the application
http://thepioneerwoman.com/homeschooling/2010/11/choosing-a-globe-for-your-home-school/

## Slide 7
Types of Distortions
Area
Distance
Direction
An Album of Map Projections, USGS 1989

## Slide 8: Projections
Features are projected onto one of three “developable” surfaces.
https://en.wikipedia.org/wiki/Map_projection
Conic: a map projection where the earth’s surface is projected onto a tangent or secant cone, which is then cut from apex to base and laid flat
Cylindrical: a map projection where the earth’s surface is projected onto a tangent or secant cylinder, which is then cut lengthwise and laid flat
Planar: a map projection resulting from the conceptual projection of the earth onto a tangent or secant plane
8

## Slide 9: Planar Projection
The map projection can be onto a flat surface or plane touching one point or cutting the surface.
If the globe, after scaling, cuts the surface, the projection is called secant. Lines where the cuts take place or where the surface touches the globe have no projection distortion.
From: http://nationalatlas.gov/articles/mapping/a_projections.html
Secant is a term in mathematics derived from the Latin secare ("to cut").
The tangent line to a plane curve at a given point is the straight line that "just touches" the curve at that point.

## Slide 10: Conformal Projection
Cylindrical projection
Parallels and meridians at right angles
“Conformable” in that angles and shapes of small objects preserved (at every point, east–west scale same as north–south scale).
The size/shape/area of large objects distorted.
Seldom used for world maps.
  Example: Mercator projection (1569)
  used for nautical purposes (constant courses are straight lines).
10

## Slide 11: Conic Projections
Conceptualized as the result of wrapping a cone of paper around the Earth.
  Standard Parallels occur where the cone intersects the Earth.
  The Lambert Conformal Conic projection is commonly used to map North America.
  On this projection lines of latitude appear as arcs of circles, and lines of longitude are straight lines radiating from the North Pole.

## Slide 12: Equivalent Projection
Conic projection
“Equivalent” or equal area projection as it preserves accurate area
Scale and shape are not preserved
  Example: Albers Equal Area
  standard projection for US Geological Survey, US Census Bureau
12

## Slide 13: Cylindrical Projections
Conceptualized as the result of wrapping a cylinder of paper around the Earth.
The Mercator projection is the best-known cylindrical projection.
  The projection is conformal.
    At any point scale is the same in both directions.
    Shape of small features is preserved.
    Features in high latitudes are significantly enlarged.

## Slide 14: The Universal Transverse Mercator (UTM) Projection
A type of cylindrical projection.
Implemented as an internationally standard coordinate system.
  Initially devised as a military standard.
Uses a system of 60 zones.
  Maximum distortion is 0.04%.
Transverse Mercator because the cylinder is wrapped around the Poles, not the Equator.

## Slide 15: Universal Transverse Mercator Uses Meters
In the N Hemisphere define the Equator as 0 m N
The central meridian of the zone is given a false easting of 500,000 m E
Easting and Northing are both in meters allowing easy estimation of distance on the projection.
A UTM georeference consists of a zone number, a hemisphere, a six-digit easting and a seven-digit northing.
  For example: 14N 468324E, 5362789N

## Slide 17: UTM zones in the lower 48

## Slide 18: Choosing A Project - Rules of Thumb
Projection | Preserves | Use for:
Cylindrical | Direction, shape | N – S areas
Conic | Distance, area | E – W areas
Planar | Distance, area | Polar, satellite imagery

## Slide 19: When the Correct Projection is Important
Small-scale maps
  Comparing shapes, areas, distances, or directions of map features.
  Natural appearance desired.
New York
New York
Los Angeles
Los Angeles
Projection: Mercator Distance: 3,124.67 miles
Projection: Albers Equal Area Distance: 2,455.03 miles
Actual distance: 2,451 miles
Los Angeles
19

## Slide 20: When Projection is not Important
Many business, policy, and management applications.
On large-scale maps.
  Error is negligible
  when a small region is
  being mapped such
  as a neighborhood
20

## Slide 21: Other Coordinate Systems
State Plane System - Defined in the US by each state
  Some states use multiple zones
  Several different types of projections are used by the system
Provides less distortion than UTM
  Preferred for applications needing very high accuracy, such as surveying
Public Land Survey System - Township and Range with baselines and meridians
  http://dnr.wi.gov/topic/forestmanagement/documents/plsstutorial.pdf

## Slide 22: State Plane Coordinate System
http://geology.isu.edu/geostac/Field_Exercise/topomaps/state_plane.htm

## Slide 23: Web Mapping
Web Mercator is used by many online mapping applications (Google, Bing, etc.)
  Web Mercator is NOT truly conformable
  Distortion increases as the map location moves north or south of the equator
  Polar regions are not included
  Some users (Department of Defense) to not allow these projections to be used in their organization
  Esri suggests that data be re-projected using updated datums when used with other Web Mercator data as area and distance calculations may not be accurate

## Slide 24: References
National Imagery and Mapping Agency. 1997. World Geodetic System 1984 (WGS 84) - Its Definition and Relationships with Local Geodetic Systems, 3rd Edition. Washington, DC: National Imagery and Mapping Agency.
Snyder, John P. 1987. Map Projections, A Working Manual. Washington, DC: US Govt. Printing Office.
http://www.ngs.noaa.gov/datums/vertical/VerticalDatums.shtml
http://images.slideplayer.com/34/8316896/slides/slide_26.jpg

## Slide 25: Links to More Help
Concept Modules on Datums
  YouTube GeoTech Center Concept Module Channel
Model Course – GST 101 and GST 103 Geotechcenter.org

## Slide 26: See GeoTech Center website (geotechcenter.org) for additional Concept Modules and to take a Quiz on this Concept Module topic to earn a Micro Certificate Badge. If you need more detailed help, you will find other resources on the GeoTech Center website including Model Courses on topics needed by the geospatial technology workforce. This Module Is Licensed Under Creative Commons By: GeoTech Center geotechcenter.org Note: some content is a derivative of other CC authors
Ann Johnson
GeoTech Center
Co-PI, Associate Director
ann@baremt.com
2-27-2018 V2