## Slide 1: Increasing Efficiency and Quality
Process Operations
Professional III

## Slide 2: Objective 2
Students will identify and resolve issues related to equipment and/or procedures within their Process Operations Professional II capstone project or other selected case studies.
Complete Obj. 3 – Problems in Group Settings
Focus now on - More Technical Side (process/project)

## Slide 3: Focus on:
Lean Manufacturing
Six Sigma

## Slide 4: Lean Manufacturing
“Lean manufacturing, also known as lean production, uses techniques that systematically identify and eliminate waste, implement the concepts of continuous flow, and customer pull” (Wortman, 2014, p.II-23).

## Slide 5: Lean Manufacturing – The Beginning
1908 - Henry Ford was the first person to successfully integrate an entire production process in his business
  Reduced average station time from 8 hrs 34 min to 1 min 11 seconds by:
    Standardized work and parts
    Interchangeable parts and workers
    Created an assembly line with a moving conveyor
    Use of go/no-go switches for quality
    Better organization/layout of facility with process sequences
    Downside: worker turnover and no adaptability

## Slide 6: Lean Manufacturing-Benefits
Lean Manufacturing
  Maximizes customer value
  Minimizes waste
  Accelerates the velocity of any process (increases the efficiency)
  Driven by added value areas of lower costs, higher profit, higher quality products and services, better and faster delivery, safer production and better morale
Encompasses whole company from supply chain to final distribution

## Slide 7: Lean Manufacturing Methodologies
“Muda” Waste – 7 Types
Visual Management
5S
Standardized work
Spaghetti Mapping
Process Mapping
Value Stream Mapping
Kanban
Etc.

## Slide 8: What are value added versus non-value added steps?
Value added for who?

## Slide 9: Value Added Steps
Value added steps in a process are those in which you add something to a product or service for which the customer would be willing to pay.
These activities are where you gain the most from expending your resources when providing a product or service.
i.e. painting, welding, building, etc.

## Slide 10: Non-Added Value but Necessary Steps
Just because a process step is not value-added does not mean it is a bad thing.
Processes all include steps that do not add value, but are necessary to make the product or service happen.
i.e. completing an application,

## Slide 11: Non-Value Added
In these steps resources are expended, delays occur, and no value is added to the product or service.
Customers are absolutely not willing to pay for these activities.
These steps should be eliminated from the process.
There are 7 types of “Muda” -waste

## Slide 13: Doctor Office Example

## Slide 14: Visual Management
See what’s happening
Everyone understands –
  if it’s wrong, fix it
Immediate Feedback
Progress or Lack of Progress

## Slide 15: Kamishibai

## Slide 16: Kamishibai
Are practical, visual, control tools that assist with the allocation, sequencing, execution, and follow up of keyword routines and tasks.

## Slide 17: Kamishibai

## Slide 18: Visual Controls
What are some ways we are visually controlled?

## Slide 19: Visual Controls

## Slide 20: The Power of Color
What are some ways we use color to relay messages?

## Slide 21: The Power of Color

## Slide 22: Visual Indicators
What are some visual indicators you might see as a process operator?

## Slide 23: Visual Indicators

## Slide 24: Visual Indicators

## Slide 25: 5S
This is used to eliminate waste and organize a work area.
  Seiri (Sort) – Remove what is not needed
  Seiton (Set in Order) - Organize remaining items)
  Seiso (Shine) – Clean
  Seiketsu (Standardize) – Create standards for like items
  Shitsuke (Sustain) – Apply the standards

## Slide 26: How could you apply 5S to your car?
Take 10 minutes and write down how you could apply 5S to your car

## Slide 27: 5S
This is used to eliminate waste and organize a work area.
  Seiri (Sort) – Remove what is not needed
  Seiton (Set in Order) - Organize remaining items)
  Seiso (Shine) – Clean
  Seiketsu (Standardize) – Create standards for like items
  Shitsuke (Sustain) – Apply the standards

## Slide 28: Applying 5S

## Slide 29: Applying 5S

## Slide 30: 5S Examples: Machining Department
before the 5S event

## Slide 31: 5S – Machining Department
Seiri (Sort) – Remove garbage/junk/broken tools/etc.
Seiton (Set in Order) – Organize remaining items into categories
Seiso (Shine) – Clean the work bench and painting of the machining area
Seiketsu (Standardize) – Labeled draws, installed electric plug its, eliminated many extension cords
Shitsuke (Sustain) – Keep it clean and tidy

## Slide 32: 5S – Machining Department
Benefits:
Easier to find tools
Work table improvements will save
considerable time doing set-ups
Found 10% more space in the machining area

## Slide 33: 5S Tool Room - Before

## Slide 34: 5S Tool Room - Before

## Slide 35: 5S Tool Room - Before

## Slide 36: 5S Tool Room - Before

## Slide 37: 5S – Tool Room
Sort
  Removed everything from storage cabinets
  Removed all unnecessary items and red-tagged
  Removed all unnecessary items from work benches
  Removed all unnecessary items from mill cabinet
  Removed all unnecessary items from Metal Lax cabinet
  Removed all scrap metal from metal rack

## Slide 38: 5S Tool Room
Set in Order
  Organized storage cabinets and Utilized storage bin system in cabinets
  Moved Bridgeport Mill
  Moved die repair work benches in die repair area to allow for more room
  Made needed repairs to Bead Blast unit and area
  Moved personal work benches on south wall to allow for more room
  Moved saw closer to metal rack for easier and safer use
  Moved bulletin boards to allow for easier use
  Made a fixture rack for porosity machining fixtures on Summit lathe
  Replaced curtains to entry of tool room for better vision and improved safety

## Slide 39: 5S Tool Room
Shine
  Cleaned walls
  Scraped and Cleaned floor
  Cleaned and Painted equipment, tables and cabinets
  Cleaned fan next to die repair area and exhaust fan to tool room

## Slide 40: 5S Tool Room
Standardize
  Painted traffic lines on floor
  Labeled all cabinets and bins
  Revised Tool Ticket files to match the files in Quality Assurance
  Updated and laminated information and charts for tooling on bulletin boards

## Slide 41: 5S Tool Room
Sustain
  Incorporated changes made during 5S event into weekly 5S tour

## Slide 42: 5S Tool Room - After

## Slide 43: 5S Tool Room - After

## Slide 44: 5S Tool Room - After

## Slide 45: 5S Tool Room - After

## Slide 46: 5S Tool Room - After

## Slide 47: 5S Tool Room – Benefits of 5S
More storage space in the cabinets.
Labeling makes it easier to find items.
Creating more work space in the die repair area allows for more than one person to work in the area and also makes it safer.
Cleaning and painting helps make the department orderly and brighter.
Partition at bead blast prevents dust from settling into Die Cast Dept. storage areas.

## Slide 48: Kaizen (Continuous Improvement)
A strategy where the whole company works together to achieve regular, incremental improvements by continually eliminating waste in the manufacturing process.

## Slide 49: Just-In-Time (JIT)
A lean method that reduces inventory levels and improves cash flow and space requirements.
Instead of pushing parts through the process based on projected demand, customer demand pulls the parts through the production line.

## Slide 50: Kanban (Pull System)
inventory and overproduction waste are eliminated by regulating the flow of products through the manufacturing process to meet customer and supplier needs.
It uses cards to show how much is needed to meet demand for a specific order.

## Slide 51: Standardized Work
Uses an easy to change document that captures the best practices of a procedure.
This creates a reference point for future improvement projects and by applying the best practices consistently, it eliminates waste.

## Slide 52: Draw a Picture
It’s amazing what you can see by observing. By drawing a picture.
Jointly drawing a picture forces us to agree on how it’s done.
Others: “Really? We do it that way?”
Picture vocabulary lesson: we all see it the same way, but we think it differently.
Pictures are powerfully simple

## Slide 53: Draw a Picture Cont.
A visual display of the major steps of a process, which uses common symbols and formats.
  Helps team members to “see” and better understand the process and the scope of the problem
Useful to communicate
Useful to see from more than 1 person
Keep an open mind and Listen
Sharpen your perception – Soft Skill

## Slide 54: Process Mapping
Shows the current state of the process and where the material goes from one machine to the next
Shows an overview of the whole process from start (suppliers) to finish (distributors)
Go out and draw the process. Follow it from start to finish to get an accurate representation.

## Slide 56: Value Stream Mapping
The kay is to capture material and information flow
Maps the current and future state of production processes and is used to highlight improvement opportunities by exposing current waste.
This maps the value and non-value added steps of the process.

## Slide 58: Spaghetti Mapping
Trace the physical movement of a person or part as it goes through the process to find wasteful movement

## Slide 59: Spaghetti Mapping

## Slide 61: Continuous Flow
Multiple forms of waste are eliminated by moving products smoothly through production with minimal wait time between manufacturing steps.

## Slide 62: Gemba
Means “the real place’ which is a philosophy that reminds us to spend time on the manufacturing floor to physically see the production in action.
This promotes understanding of the process and the problems that occur by observation and talking to others

## Slide 63: The 5 Step Thought Process for Implementing Lean Techniques.
Specify the value desired by the end customer by product
Identify the value stream for each product providing that value and eliminate waste (steps that do not create value) whenever possible
Make the product in the remaining value-added steps flow continuously by placing them in a tight sequence
Where continuous flow is possible, introduce pull between all steps from the next upstream activity
To reach perfection by repeating the process repetitively so that the number of steps and the amount of time and information needed to serve the customer continually falls

## Slide 64: The 5 Step Thought Process for Implementing Lean Techniques.

## Slide 65: Lean Manufacturing - Challenges
Resistance to change
Money spent upfront
Upkeep, updates, and regular maintenance will be needed once improvement changes are made
Continuously looking for improvements – Never ending process

## Slide 66: Who is Lean for?
Lean thinking is for businesses and customers because the benefits for both are endless. Businesses, both service-oriented and manufacturers, can implement lean thinking and techniques because every system contains waste.
Lean techniques are applicable in any industry or system where people want to analyze the system, identify and reduce waste, and focus on the customer.
Customers will also benefit and appreciate lean oriented companies because the products or services will have higher quality and variety (with fewer defects) as well as lower prices and faster receiving/delivery times.

## Slide 67: Applying Lean
How can you apply Lean Techniques to your project?

## Slide 68: Questions?

## Slide 69: Helpful YouTube Videos
7 Wastes
  https://www.youtube.com/watch?v=PpNmsQm_YSw
Lean
  https://www.youtube.com/watch?v=PpNmsQm_YSw