## Slide 1: Failure Modes and Effects Analysis
Process Operations - Prof. III
Development of a 21st Century Industrial Process Operations Program is supported by the National Science Foundation under Grant No. 1700558. Any opinions, findings, and conclusions or recommendations expressed on this site are those of the authors and do not necessarily reflect the views of the National Science Foundation.

## Slide 2: Failure Modes and Effects Analysis
AKA
  Potential Failure Modes and Effects Analysis: PFMEA
  Failure Modes, Effects, and Criticality Analysis: FMECA

## Slide 3: FMEA: What is it?
Definition: A step by step approach for identifying all possible failures in a design, a manufacturing or assembly process, or a product/service.

## Slide 4: FMEA: What is it?
Failure Modes:
  The ways, or modes, in which something might fail.
  Failures are errors or defects (esp. if they affect the customer) and can be potential or actual.
  Failure mechanisms are the individual or multiple reasons that cause the failure to occur (e.g., corrosion, contamination, etc. might cause failure modes)
  And
Effects Analysis
  Studying the effects of the failures

## Slide 5: Failures:
Failures are prioritized according to:
  How serious the consequences are
  2. How frequently they occur
  3. How easily they can be detected

## Slide 6: Why use FMEA?
To take action to eliminate or reduce failures (starting with the highest priority)
Documents current knowledge and actions about the risks and failures, for use in Continuous Improvement
Used in design to prevent failures
Used for control, before and during ongoing process operation

## Slide 7: FMEA: Lifecycle
Begins: during the earliest conceptual stages of design
Ends: never
  Continues throughout the life of the product/service

## Slide 8: FMEA Start
Started in the 1940s by the US military
  Further developed by the aerospace and automotive industries
There are several industries that maintain formal FMEA standards

## Slide 9: When to use FMEA
When a process, product, or service is being designed or redesigned, after quality function deployment
When an existing process, product, or service is being applied in a new way
Before developing control plans for a new or modified process
When improvement goals are planned for an existing process, product or service
When analyzing failure of an existing process, product, or service
Periodically throughout the life of the process product or service

## Slide 10: Types of FMEAs
Design FMEAs
Process FMEAs
System FMEAs
Functional FMEAs

## Slide 11: Design FMEAs
Performed on a product or service (system) at a design level.
Purpose: to analyze how failure modes affect the system and to minimize failure effects upon the system.
Used before products are released to the manufacturing operation.
All anticipated design deficiencies should be detected or corrected by the end of this process.

## Slide 12: Process FMEAs
Performed: on the manufacturing processes.
Conducted through quality panning phase as an aid during production.
The possible failure modes in the manufacturing process, limitations in equipment, tooling, gauges, operator training, or potential sources of error are highlighted, and corrective action is taken.

## Slide 13: System FMEAs
Comprised of part level FMEAs.
All part level FMEAs will tie together to form the system.
As a FMEA goes lower into the system, into more detail, more failure modes will be considered.
A system FMEA needs only to go down to the appropriate level of detail.

## Slide 14: Functional FMEAs
AKA Black Box FMEAs
Focuses on the performance of the intended part or device, rather than on the specific characteristics of the individual part.
I.E. If a project is in the early design stages, a black box analysis would focus on the function of a device rather than on the exact specifications (color must be blue-gray, knob is 2.15 mm to the left, etc.)

## Slide 15: FMEA
It is a detailed analysis of a system down to the component level.
  All items are classified into:
    1. Failure mode
    2. Effect of the failure
    3. probability of the failure will occur
  They are given a RPN (Risk Priority Number) to rate their severity
  Most common to work from the highest RPN value down

## Slide 16: FMEA Steps
Assemble a cross functional team
Identify the scope of the FMEA (concept, system, design, process, or service? How detailed should it be? Etc.)
Fill in the relevant information in the FMEA form.
  Helps you identify:
    1. Potential failures and effects
    2. Severity
    3. Gauge likelihood of occurrence
    4. Failure detection
    5. assign risk propriety number (RPN)

## Slide 20: Risk Assessment and RPN
P = Probability this failure will occur
  Values are usually from 1-10 (1=no chance, 10=near certainty)
S = Severity of the effect of the failure on the rest of the system if it were to occur
  Values are usually from 1-10 (1=user will likely not notice, 10=user is not safe)
D=Detection =Measure of the effectiveness of the current controls to identify the potential weaknesses or failure prior to release to production.
  Values are usually from 1-10 (1=certainly be caught, 10=indicates design weaknesses will make it to final production without detection

## Slide 21: Risk Assessment and RPN
RPN = P*S*D
  RPN = Risk Priority Number
  P = Probability of failure mode occurrence
  S = Severity of the effect of the failure
  D = Detection of the effectiveness of the current controls identifying weaknesses
  The higher the RPN the more urgent the failure on the list

## Slide 22: Examples to Determine Severity
Rating | Meaning
1 | No effect, no danger
2 | Very minor – usually noticed only by discriminating or very observant users
3 | Minor – only minor part of the system affected; noticed by the average user
4-6 | Moderate – most users are inconvenienced and/or annoyed
7-8 | High – loss of primary function; users are dissatisfied
9-10 | Very high – hazardous. Product becomes inoperative, customers angered. Failure constitutes a safety hazard and can cause injury or death.

## Slide 23: Example to determine the occurrence:
Rating | Meaning
1 | No documented failures on similar products/processes
2-3 | Low – relatively few failures
4-6 | Moderate – some occasional failures
7-8 | High – repeated failures
9-10 | Very High – Failure is almost certain
9-10 | Very High – Hazardous. Product becomes inoperative, customers angered. Failure constitutes a safety hazard and can cause injury or death.

## Slide 24: Example to determine detection:
Rating | Meaning
1 | Fault is certain to be caught by testing
2 | Fault almost certain to be caught by testing
3 | High probability that tests will catch fault
4-6 | Moderate probability that tests will catch fault
7-8 | Low probability that tests will catch fault
9-10 | Fault will be passed undetected to user/customer