## Slide 1: Process Logic Diagraming
Development of a 21st Century Industrial Process Operations Program is supported by the National Science Foundation under Grant No. 1700558. Any opinions, findings, and conclusions or recommendations expressed on this site are those of the authors and do not necessarily reflect the views of the National Science Foundation.

## Slide 2: Process Logic
The primary use of process logic is SAFETY
  Personnel, Environmental, Process, Equipment
Logic statements can be used for/in the process control strategies

## Slide 3: Process Logic
Logic has two primary operator functions:
  Interlock(s)
    Insure personnel and environmental safe guards are in place & correct.
    Insure process variables & equipment are in the proper “mode” prior to operator action.
  Safety shutdown
    Return the process to a known safe condition should specific process variables exceed specific values.

## Slide 4: Interlock(s) Also called permissive(s)
e.g., Burner Management System (BMS) (FSSS)
  Prevents ignition source from entering furnace without purging the furnace.
Rotating equipment interlocks
  Prevents starting up or shutting down equipment until all critical variables/inputs are confirmed in a safe state.
    e.g., Lubricating oil pressure OK, Liquid level OK, Valves Open

## Slide 5: Shutdown Properly called Safety Instrumented System (SIS)
If a specific variable (or group of variables) exceed defined safe limits the SIS will take over control and return the process to a known safe condition.
Initiation of SIS override/control typically has a series of steps

## Slide 6: SIS Initiation Process Steps
Three Step
Normal Operating
H or L Alarm
  Operator action required
HH or LL Alarm
  SIS Override initiated
Four Step
Normal Operating
H or L Alarm
  Operator action required
HH or LL Alarm
  Operator & MGT action required (Timed)
Trip
  SIS Override initiated

## Slide 7: Basic Logic
Process logic can only have one of two possible answers:
  Either a logic statement is TRUE or it is FALSE
    e.g., permitted/not permitted, safe/not safe, etc.
Any answer other that theses:
  > you are in big trouble

## Slide 8: Logic Symbology (Most common)
There are three primary operators:
  AND
  OR
  NOT (INVERSE)
One “value” operator:
MISC

## Slide 9: AND
AND
All inputs must be True for output to be True

## Slide 10: OR
OR
One or more inputs must be True for the output to be True

## Slide 11: NOT (Inverse)
The output is the opposite of the input
  Input False output True
  Input True output False

## Slide 12: MISC
A generic operator to add specific quality or value to the logic statement.
  e.g. timer, specific measurement value, etc.

## Slide 13: Examples:

## Slide 14: SIS Input Voting
SIS system inputs are CRITICAL!
Single input.
Duplex input.
  Which one is correct?
Two out of three voting.
  If two of the three input values are the same » they are assumed correct.