## Slide 1: Process II
Process Control Strategies
Development of a 21st Century Industrial Process Operations Program is supported by the National Science Foundation under Grant No. 1700558. Any opinions, findings, and conclusions or recommendations expressed on this site are those of the authors and do not necessarily reflect the views of the National Science Foundation

## Slide 2: Course Objectives
Fundamentals of Process Control
  Manual Control
  Discrete Control
  Feed Back Control
  Cascade Control
  Feed Forward Control
Processes
  Process Types
  Process Dynamics
  Simple Process Controls
    Level, Flow, Temp, Pressure
  Process Simulator

## Slide 3: Fundamentals of Process Control
Otherwise known as:
Introduction to the Dark Arts

## Slide 4: Dark Arts?
Process Control one of the least understood engineering disciplines but:
But here’s the thing:
  Everyone uses
  Few realize it or understand it.
The question:
  How many times have you used it today?

## Slide 5: A Brief History
3rd Century BC Greece
  Ktesibios develops level control
~1770
  Watt develops the “Flyball” governor
~1880
  Fisher Pump Governor
Early 1930’s
  Pneumatic Controls
  First PID Controllers
1960’s
  Analog Electronic Controls
  First DDC Systems
1980’s
  First DCS
Today
  3rd / 4th Generation of DCS
  Smart Controls

## Slide 6: Key Points to Think About/Remember
What are you attempting to do?
You can’t get something for nothing
If you can’t measure it or model it>>>
  you can’t control it!
You must KNOW the process!!!!!

## Slide 7: Why Process Control?

## Slide 8: What is a process?
A system of equipment designed to manufacture a product with a specific set of desired qualities.
  Process Area: Single unit power plant
    Final Product: Electricity
  Process Unit: The Boiler
    Intermediate Product: Steam
  Process Systems & Equipment:
    Air Handling: Flow & Temp Control of Combustion Air
      Fans, Air Preheater(s), Control Elements,
    FW system: Quality, Level, Flow & Temp of Boiler FeedWater
      FW Storage, DEA, FW heater(s), Economizer, FWP,
  Process Sub Systems
    FW Chemical Treatment, RO system, Soot Blowing, Slag Mgt.

## Slide 9: What is a Process
Continuous or Batch?
  Continuous: Process that continuously receives raw material and continuously processes them into a intermediate or final product.
  Batch: Processes that receive materials and processes them into an intermediate or final product using a series of steps.
For this class we will focused on continuous control

## Slide 10: Process Concepts: Variables
  Controlled Variable (Measured Variable)
  Manipulated Variables
  Disturbances

## Slide 11: Discussion
Take 3 common processes from daily life and define the:
  Controlled Variable (Measured Variable)
  Manipulated Variables
  Disturbances

## Slide 12: Manual Control

## Slide 13: Manual Control
Example: Watering the lawn
Measured Variable?
  Flow?
  Coverage area?
Manipulated Variable?
  Flow?
Disturbances?
  ΔH2O Pressure
  Wind

## Slide 14: Discrete Control
Often Called
  Differential Gap
  Bang-Bang
  On/Off
Control of a process around a given setpoint with a given deadband
Control of a process between two limits.
Examples?

## Slide 15: Automatic Discrete Control

## Slide 16: Automatic Discrete Control
Level
Pressure

## Slide 17: Automatic Discrete Control
Discussion:
  Advantages/Disadvantages

## Slide 18: Feedback Control
The most basic of the continuous control strategies and the basis for industrial control.
Requires a Setpoint
  The desired process variable “value”
Feedback control corrects for Error
  Setpoint – Measured Variable = Error

## Slide 19: Automatic Control

## Slide 20: Process Controller
A device or program routine that compares the controlled variable to the setpoint and adjusts it’s output to change the manipulated variable.

## Slide 21: Basic Feedback Flow Control

## Slide 22: Block Diagram Flow Control
S
√
∑

## Slide 23: Basic Feedback Pressure Control

## Slide 24: Automatic Feedback Control
Discussion:
  Advantages/Disadvantages

## Slide 25: Cascade Control
Cascade control is the second most utilized control strategy.
Cascade control places one feedback loop inside another feedback loop
Very useful when the primary (outer) control loop is a slow loop but the disturbances are significantly faster.

## Slide 26: Cascade Control
The secondary (inner) control loop should be applied to the process variable that will the greatest impact to reducing the process Lag.

## Slide 27: Cascade Control
Heat Exchanger
Level

## Slide 28: Feedforward Control
If you can measure ALL the disturbances to a process and adjust the manipulated variables or prevent the disturbances from reaching the process there would be no need for feedback control.
The measured variable would be always at setpoint.
No feedback error

## Slide 29: Graphically:

## Slide 30: Feed Forward Control
Discussion:
  Advantages/Disadvantages

## Slide 31: Net Result
Feedforward rarely used without Feedback Control
Feedforward Control underutilized in Industry

## Slide 32: Feed Forward with Feedback Control
Heat Exchanger

## Slide 33: Feed Forward with Feedback Control
Discussion:
  Advantages/Disadvantages