## Slide 1: Precision Agriculture
Lesson 3, Part A

## Slide 2: Traditional Farming vs. Precision Agriculture
Compare/Contrast
  How data is gathered
  Detail of the data
  Decision making and implementation based on data

## Slide 3: Gathering Data
Traditional Farming Practices
One piece of data gathered per location at one time.
Extra time required for physical observations.
Number of sites observed limited due to time constraints.
Accuracy dependent upon viewpoint of observer.
Precision Agriculture
Several pieces of data may be collected at each location.
Data recorded instantaneously.
Significantly higher number of sites observed and recorded.
Data is accurate to level of equip- ment calibration.

## Slide 4
The green pin indicates how often data is taken for this field using physical observation.
Using Precision Ag, data can be gathered up to 200 times per second, and combine that with a GPS receiver, the data can be mapped at each location recorded. Giving us a coverage map looking like this.

## Slide 5: Detail of the Data
Traditional Farming Practices
Detail is subject to amount of time observer has to record what is observed. Very subjective
Fewer observations are made per field making data less applicable as distance from point of obser- vation becomes greater.
Precision Agriculture
Detail is exact as observations are taken and recorded to same level of accuracy. Very objective.
Because observations are taken constantly, data is completely applicable to the entire opera- tion.

## Slide 6: Decision Making and Implementation
Traditional Farming Practices
Decisions are applied to large, broad areas of the operation such as an entire field or section of field.
All adjustments must be made manually.
Management implemented is applied to large areas based on very limited data.
Precision Agriculture
Decisions applied to much smaller areas because observations are being taken all the time.
Many adjustments are made automatically based upon parameters set in equipment because of sensors.
Management implemented is applied precisely to an area based upon its data.

## Slide 7: Where Does the Data Come From?
Websites
Remote Sensing
Digitized Historical Maps
Physical Sampling
Equipment with Sensors Installed

## Slide 8: Websites
Atmospheric Data
  Temperature
  Rainfall
  Etc.
    https://www.usclimatedata.com/
    https://www.wunderground.com/
    https://www.climate.gov/
    https://www.ncdc.noaa.gov/
    https://www.agweb.com/weather/temperature-band/
    https://weatherspark.com/

## Slide 9: Websites (continued)
Historical weather data analyzed for Growing Degree Days or Heat Units.
  Growing Degree Days (GDD) or Growing Degree Units (GDU)
    Organisms such as plants, insects, etc. require a certain number of heat units to reach different stages of maturity.
    (Max Temp + Min Temp)/2 - Base Temp
    Example for corn: (83 + 61)/2 -50 = 22 GDD for that day
    NOTE: The max temp used cannot exceed 85 and the min temp used cannot be less than 50.
http://www.nutrien-ekonomics.com/tools-to-calculate-fertilizer-needs/calculators/gdd/
http://www.greencastonline.com/growing-degree-days/home

## Slide 10: Remote Sensing
Analyzed satellite or drone images
  https://farmlogs.com/
  geovantage.com/
  Can supply crop health images on a given date.
    Helpful to identify issues before noticeable to the eye.
  A field boundary is drawn around a field on a web tool.
    http://www.gmapgis.com/
    Field boundary is used to identify AOI on which to gather data.

## Slide 11
Example of image from FarmLogs
Example of imagery from geovantage.com

## Slide 12: Digitized Historical Maps
Soil Maps
Topographical Maps
This type of data experiences very minimal change over the years.
Maps from 5, 10 or even 50 years ago are still valid and valuable today!

## Slide 13: Physical Sampling
Example - Soil Sampling
  Identifies:
  Soil pH
  Soil’s ability to hold water
  Soil’s ability to release water
  Fertility available
  Fertility needs

## Slide 14: Soil Sampling
Drive to the field to be sampled
Use a soil probe to remove a sample of soil from the ground.
  May be taken from different zones.
  Several samples may be taken within a zone.
    All soil samples within the zone are mixed to get an average.
Soil samples are sent to a lab for analysis.

## Slide 15
Using a soil probe to collect a soil sample.
Preparing soil for shipment to the lab for analysis.

## Slide 16
Grid Sampling - a soil sample is taken within each square across the field map. Very time consuming and expensive.
Zone Sampling - fewer soil samples are taken and less costly for lab testing. Lose some of the detail.

## Slide 17: Sensors
Passive Data Collection
Examples:
  Soil temperature
  Soil moisture
  pH
  Organic matter
Active Data Collection
Examples:
  Planting population
  Seed depth
  Seed spacing
Need to be known on a higher level of granularity so sensors provide more precise rather than general information.

## Slide 18
Sensors in the SmartFirmer can capture multiple points of data such as seed spacing, soil moisture, organic matter, etc.
Sensors can also be found on weather stations to gather wind direction, speed, rainfall, etc.

## Slide 19: Saving and Transferring Collected Data
When data is collected it is stored in a temporary memory module within the equipment.
Stored data is transferred by a variety of methods.
  Download to a portable memory module.
    USB Drive, SD Card, etc.
  Transfer directly to iPad or tablet with a cable.
  WiFi or cellular transmitter sending it to the cloud to access directly.