## Slide 1
Prof. Vladimir V. Vantsevich
Jesse Paldan, Research Assistant
Lloyd Balfour, Graduate Research Assistant
Vehicle and Robotics Engineering Laboratory
University of Alabama at Birmingham
Week 1. Lecture 1
Experimental Testing of Vehicles
Safety and Role of Experiments

## Slide 2
General Automotive Laboratory Safety:
  Purpose of Safety
  Vehicle Safety
  Electrical Safety
  Personal Protective Equipment
  Outline

## Slide 3
Emergency Information
Emergency number: call 911
UAB Campus Police Emergency Number:
205-934-3535
UAB Occupational Health & Safety :
Main Office Address
933 19th St. S Suite 445 Birmingham, AL 35205-3703
Main Office Phone: 205-934-2487

## Slide 4
In emergency, contact UAB Police:
  From a campus phone - 911
  From a non-campus phone - 205-934-3535
UAB Occupational Health & Safety can be contacted at:
  During office hours - 205-934-2487
  After office hours and during holidays - contact OH&S Director on call through UAB police
Emergency Information

## Slide 5
Disregard of safety procedure can and will put not only the student’s Health in jeopardy but everyone in the Lab
Disregard of safety procedures can and will lead to costly damages of Lab equipment
Disregard of Safety Procedure can and will lead to serious injuries and possible death.
Why Is Safety Important?
Notes: you need to find a textbook on safety engineering in the library on Internet.
You can also check vehicle testing facilities. Example: Truck Research Center in Ohio, etc. They should have something on safety.
You can check companies that manufacture test rigs: MTS, Mustang Dynamometer, etc.
You can check proving grounds and research labs of Ford, GM, AVL Powertrain, etc.

## Slide 6
To find the answer to this question, it is beneficial to take a look at what happens in various labs and work spaces that did not use appropriate safety measures.
A handout of General Laboratory Safety will be provided
A handout on examples of disregarding safety in the lab will be provided
The Purpose Of Safety?

## Slide 7
Injury caused by a high voltage capacitor:
What happened?
A campus employee working in an electronics shop was repairing a power supply unit. The cooling fan had not been working properly, causing the unit to overheat. The employee replaced the defective cooling fan and then reached into the open top of the power supply unit to check the air flow from the replacement fan. The employee either made contact with a charged capacitor or was close enough (within 1/4") to allow electricity to arc to his hand causing an electric shock that entered his left hand and exited through his right hand [1].
The Purpose Of Safety?

## Slide 8
Figure 1:
Power supply left at the incident [1]
Figure 2 :
Capacitors that Discharged [1]
The Purpose Of Safety ?
Injury caused by a high voltage capacitor:

## Slide 9
What Caused this incident?
The power supply unit receives electricity from a 208 volt (V) wall outlet and converts that voltage to 5 kilo volts (kV). The 5 kilo volts are stored in the capacitor. This caused the capacitor to be able to discharge 200 milliamps (mA) of current. Physical contact or close proximity to the open power supply caused a discharge from the capacitor that resulted in an electric shock. Capacitors are able to hold their charge for awhile after a power source has been turned off resulting the discharging of current. [1].
The Purpose Of Safety ?
Injury caused by a high voltage capacitor:

## Slide 10
The Purpose Of Safety ?
Injury caused by a high voltage capacitor:
How could this incident had been prevented?
Avoid any attempts to fix and or dismantle any energized electrical equipment without proper qualifications:
Only qualified personnel are permitted to repair electrical equipment in the lab and work space.
If working on energized equipment is absolutely necessary, only do so with the permission of a knowledgeable supervisor.

## Slide 11
How could this incident had been prevented?
In the capacitor incident , the fan could have been tested without placing a hand inside the equipment from the outside.
It is important to ensure that capacitors are discharged prior to working on or near them.
The Purpose Of Safety ?
Injury caused by a high voltage capacitor:

## Slide 12
The engine must be turned off when the vehicle is not in use
Never leave the vehicle on when leaving the lab
Never have the vehicle emitting in a closed space
If a rotational part of the vehicle is not covered, inform the instructor immediately
Automotive Safety
General Automotive Safety Guidelines:

## Slide 13
Never touch any equipment that is rotating.
Never operate any equipment alone in the lab: always work within eyesight of another person
All rotational parts have to be covered
Never work on a vehicle with its key in the ignition
General Automotive Safety Guidelines:
Automotive Safety

## Slide 14
Figure 3: Shock table [3]
Electrical Safety

## Slide 15
Never Work Alone on any electrical equipment
If a student is working with energized circuits or equipment over 50 volts peak, make sure that at least one other person can see you and hear you in case urgent assistance is needed [2].
Rules of electrical equipment use
If a student is intending to work on a project using power sources of over 50 volts, the student must first receive permission from the Faculty or Staff Instructor and take an Electrical Safety test.
Electrical Safety

## Slide 16
What is Personnel Protective Equipment?
Personal protective equipment (commonly referred to as PPE) is equipment designed to protect personnel from injuries and illnesses resulting from contact with chemical, radiological, physical, electrical, mechanical and other hazards in the Lab [4].
PPE categories
There are 5 categories of PPE: eye, ear, clothing, gloves, and respiratory.
Personal Protective Equipment

## Slide 17
PPE general rules:
  Personnel in the lab must use protective equipment properly.
  Personnel in the Lab must know when PPE is necessary
  Personnel in the lab must know the limitation of PPE in order to avoid injuries
  All Personnel in the lab Must wear all required PPE at all times while in the lab, even if the person is not operating any equipment
Personal Protective Equipment

## Slide 18
Eye PPE
Eye PPE are any form of protective equipment that not only protects the eyes, but can also protect the face from injuries.
Examples include but are not limited to : safety goggles, spectacles, hard hats, surgical masks, welding masks, etc…
Figure 4: Eye PPE examples [5]
Personal Protective Equipment

## Slide 19
Ear PPE
Ear PPE are any form of equipment that helps reduce the exposure to hazardous noise.
Examples typically include earphones and earplugs
Figure 5: Ear phones [6]
Figure 6: Ear plugs [6]
Personal Protective Equipment

## Slide 20
The level of the sound, measured in decibels [5]
The length of time exposed to the sound [5]
The number and length of the “recovery time”: Recovery time is periods between exposures to hazardous noise [5]
Person’s tolerance to sound [5]
Intensity variables
Four variables affect the intensity of noise:
Personal Protective Equipment

## Slide 21
Clothing PPE
Clothing PPE are any form of equipment that protects the body from external hazards. Examples of external hazards are: chemical burns, lacerations, cuts, absorption of chemicals through the skin, thermal burns and abrasion to the skin [4].
General Rules on Clothing
  No shorts are allowed in the lab
  Do not wear any jewelry that can get caught in any lab equipment
  Loose clothing (e.g. baggy shirts and pants) are not allowed in the lab
  Wear only closed toes shoes in the lab; flip flops are prohibited.
Personal Protective Equipment

## Slide 22
Gloves PPE
Gloves PPE are any form of equipment that protects the hands from external hazards.
Figure 7: Hand PPE examples [5]
Left: rubber insulated glove
Right: leather welding glove
General Rules on Hand Protection
  Do not wear gloves around any rotating equipment, doing so may get the gloves ensnared in the equipment.
Personal Protective Equipment

## Slide 23
Respiratory PPE
Respiratory PPE are any form of equipment that protects the personnel from breathing in air contaminates.
All respiratory equipment in the lab must be NIOSH (National Institute for Occupational Safety and Health) approved.
Examples of air contaminants
Examples are harmful dust, hazardous gasses and fumes, vapors, smokes and sprays.
Personal Protective Equipment

## Slide 24
3 Categories of Respiratory PPE
There are 3 basic types of respiratory PPE, a filtering devices, Half mask, and a Full-face mask.
Filtering devices
These devices are typically made entirely of a fiber material.
They usually have to be disposed after being used [7].
Figure 8: Filtering device [7]
Personal Protective Equipment

## Slide 25
Half mask devices
These devices are typically reusable face pieces that only cover the mouth of the person.
Full mask devices
These devices are reusable face pieces that not only cover the mouth but provide full face protection.
Figure 9: Half mask device [7]
Figure 10: Full mask device [7]
Personal Protective Equipment

## Slide 26
Not adhering to the rules of the lab will result in a warning the first time
Repeated offenses will result in the person being discharged from the lab
Notes: Lloyd,
You did not include the role of experiments in the outline of this lecture

## Slide 27
Experiments are done to allow a person to practice what they learn in the classroom in a “real world” setting.
Experiments allow a person to test hypotheses and theories and make a conclusions based on knowledge of those theories.
It is important to remember that not all experiments have to be pin point accurate. In fact many experiments end in failures. The important lesson on experimental failure is to learn what caused the failure and to learn from it.
Why are Experiments Done?

## Slide 28
Vehicle Laboratory Tests
Figure 11: Vehicle in a laboratory on a dynamometer test cell, which functions similar to a treadmill. [8]
Figure 12: The amount of energy required to move the dynamometer’s rollers can be adjusted to simulate different conditions such as wind resistance [8]
Vehicle tests can be performed in a laboratory or outdoor proving ground. Laboratory tests include dynamometer and fuel economy tests.

## Slide 29
Vehicle Laboratory Tests
Figure 13: A hose connected to the tailpipe collects engine exhaust (carbon and other air pollutants released) [8]
Figure 14: Carbon in the exhaust is measured to calculate the amount of fuel burned more accurately than using a fuel gauge. [8]

## Slide 30
Purpose of Proving Ground Testing:
Test for different driving and weather conditions, such as ice.
Test different road environments, such as inclines and banked curves.
Test both on and off-road conditions.
Perform Certification and Homologation services (Homologation = process of certifying or approving a product to indicate that it meets regulatory standards and specifications, such as safety and technical requirements)
Proving Ground Tests

## Slide 31
Performance Circuits for sustained high-speed tests.
Test on varieties of road surfaces.
Graded hills for testing brakes, clutch, driveline loading, shocks.
Noise testing for exterior/interior noise levels.
Proving Ground Tests (On-road)
Figure 15: On-road Proving Ground Surfaces [9]

## Slide 32
High and low friction surfaces.
Left/Right Gradient slope (rollover testing).
Loose and firm surfaces of varying density.
Curb climbing (chassis/suspension and vehicle clearance).
Traction in water-covered or muddy surfaces.
Proving Ground Tests (Off-road)
Figure 16: Off-road Proving Ground Surfaces [9]

## Slide 33
[1] “Lessons Learned at UC Berkeley”. Berkeley EH&S Office of Environment, Health & Safety. 2017 [online]. Retrieved from: http://ehs.berkeley.edu/lessons-learned-uc-berkeley
[2] A. Agarwal , J. Lang. Department of Electrical Engineering & Computer Science. Electrical Safety for Staff and Students in EECS Instructional Laboratories. Massachusetts Institute of Technology, 2012. Retrieved from: http://www.eecs.mit.edu/docs/resources/safety_handout-fall2014.pdf
[3] Occupational Safety and Health Administration. Electrical Safety in the Workplace. US Government, 2008. Retrieved from: https://www.osha.gov/dte/grant_materials/fy09/sh-18794-09/electrical_safety_manual.pdf
[4] Occupational Safety and Health Administration. “OSHA Fact Sheet”. Personal Protective Equipment. US Government, 2006. Retrieved from: https://www.osha.gov/OshDoc/data_General_Facts/ppe-factsheet.pdf
References

## Slide 34
[5] K. Enns, M. Womochil, et all. “Career & Technical Education”. Laboratory Safety Manual Colorado. Colorado State University, 2010. Retrieved from: http://www.sd27j.org/cms/lib8/CO01900701/Centricity/Domain/1739/Colorado_Lab_Safety_Manual.pdf
[6] "Shipyard Employment eTool General Requirements: PPE Selection Hearing Protection", Osha.gov, 2017. Retrieved from: https://www.osha.gov/SLTC/etools/shipyard/standard/ppe/general_ppe/hearing_protection.html
[7] K. Majchrzycka and P. Pietrowski, "Respiratory protection equipment requirements and selection OSHWiki“. Oshwiki.eu, 2017. Retrieved from: https://oshwiki.eu/wiki/Respiratory_protection_equipment_%E2%80%93_requirements_and_selection
References

## Slide 35
[8] Unites States Environmental Protection Agency, "Testing at the National Vehicle and Fuel Emissions Laboratory", 2017.
<https://www.epa.gov/greenvehicles/testing-national-vehicle-and-fuel-emissions-laboratory>
[9] Michigan Technical Resource Park, "Vehicle Testing Courses", 2017.
<http://www.mitrp.com/vehicle-testing-courses.php>
[10] HORIBA MIRA, "Proving Ground", 2017, <https://www.horiba-mira.com/our-services/vehicle-proving-ground>
References