## Slide 1
Prof. Vladimir V. Vantsevich
Jesse Paldan, Research Assistant
Vehicle and Robotics Engineering Laboratory
University of Alabama at Birmingham
Week 6. Lecture 2
Experimental Testing of Vehicles
Overview of SAE Standards

## Slide 2
  Overview of SAE Standards and Topics
  SAE Vehicle Axis System
  SAE Classification of Stability Features
  Critical Speed Measurement
  Fuel Economy Testing
Outline

## Slide 3: SAE Standards
Standards Categories:
Aerospace Standards
Aerospace Material Specifications
Ground Vehicle Standards
Commercial Vehicle Standards
Largest automotive and aerospace standards setting body for safety, quality, and effectiveness
Database of 35,000+ standards
(10,000 active and 25,000 historical standards.)
Created through consensus standards development by SAE Technical Committees with subcommittees and task groups.

## Slide 4: SAE Standards (Topics)
Bodies and Structures
Chassis
Design Engineering and Styling
Electrical, Electronics, and Avionics
Environment
Fuels and Energy Sources
Human Factors and Ergonomics
Interiors, Cabins, and Cockpits
Maintenance and Aftermarket
Management and Organization
Manufacturing
Materials
Noise, Vibration, and Harshness
Parts and Components
Power and Propulsion
Quality, Reliability, and Durability
Safety
Tests and Testing
Transportation Systems
Vehicles and Performance

## Slide 5: SAE Standards on Vehicle Testing
J2926_201108 Rollover Testing Methods: information on techniques for rollover testing and evaluation of rollover protection systems
J2564_200406 Automotive Stability Enhancement Systems: describes automotive active stability enhancement systems, as well as common names to refer to systems and features
J2969_201701 Use of the Critical Speed Formula: guidelines for procedures used to analyze the results of the critical speed method for use at accident sites using manual or electronic measurements
J2481_201310 Dynamic Simulation Sled Testing: sled tests conducted on automotive vehicle bodies or other structures to represent various automotive collision conditions
J2264_201401 Chassis Dynamometer Simulation of Road Load Using Coastdown Techniques: procedure for adjusting an electric chassis roll dynamometer to simulate the resistance which must be overcome by the vehicle powertrain to maintain steady speed on a flat road

## Slide 6: SAE Standards on Vehicle Testing
J1082_200802 Fuel Economy Measurement Road Test Procedure: information on driving cycles used to determine fuel economy
J1711_201006 Recommended Practice for Measuring the Exhaust Emissions and Fuel Economy of Hybrid-Electric Vehicles, Including Plug-in Hybrid Vehicles: establishes uniform chassis dynamometer test procedures for hybrid-electric vehicles designed to be driven on public roads
J1321_201202 Fuel Consumption Test Procedure - Type II: fuel-consumption test procedure and statistical analysis for trucks and buses
J1634_201210 Battery Electric Vehicle Energy Consumption and Range Test Procedure: establishes uniform procedures for energy consumption and range testing of battery electric vehicles
J2084_201604 Aerodynamic Testing of Road Vehicles - Testing Methods and Procedures: aerodynamic requirements of a wind-tunnel for automotive testing, facility equipment needed, and test methods

## Slide 7: SAE Vehicle Axis System
Yaw, Pitch and Roll:
Figure 1: SAE Vehicle Axis System [1]

## Slide 8: Steering Input and Side Slip
Figure 2: Three degree-of-freedom full-vehicle model [2]
= Yaw Angle
δ = Steering Input (from driver)
α = Side Slip Angle
= Longitudinal Forces
= Lateral Reaction Forces
= f(α)

## Slide 9: Traction Control System
Traction Control Systems: monitor the wheel speeds and apply brake torques and/or control engine torque to control wheel spin during acceleration.
Figure 3: With and Without Traction Control [3]

## Slide 10: Traction Control System
Requirements:
Is computer controlled
Has a means to determine if a drive wheel is spinning
Has the capability of applying brake force individually to the drive wheels to limit wheel spin (if brake traction control or engine and brake traction control)
Has the capability of controlling engine torque to reduce the brake torque needed to limit wheel spin (if engine only traction control or engine and brake traction control)

## Slide 11: Electronic Stability Control Systems (ESC)
Requirements:
Computer controlled and contains closed-loop algorithm to limit understeer and oversteer
Has a means to determine yaw velocity ,side slip, and monitor driver steering input
Means of adjusting vehicle brakes to correct yaw torques
Operational over the full vehicle speed range
Figure 4: Categories of ESC [4]

## Slide 12: Antilock Brake Systems
ABS systems monitor vehicle wheel speeds and regulate brake forces to control the slip between tire and road surface.
By controlling wheel slip, vehicle stability is improved and the driver retains the ability to steer the vehicle
Requirements:
Is computer controlled
Has a means to determine if any wheel is about to lock
Has the capability of regulating brake torque at the wheels to limit wheel lock
Controls the brake torque to each of the front wheels independently and the rear wheels either independently or as a pair

## Slide 13: Antilock Brake Systems
Method:
Monitor speed of each wheel to detect locking (skidding with no rotation)
When suddenly braking, release braking pressure for a moment, then provide optimum braking pressure to each wheel
Repeat the process over a short period of time
Figure 5: Concept of ABS [5]

## Slide 14: Other Stability Enhancement Features
Drivetrain Controls: adjusts engine torque applied to the drive wheels to influence longitudinal and lateral forces of the tire
Integrated Vehicle Systems: combine vehicle stability features such as ABS, Traction Control, Electronic Stability Control, Suspension Controls, and/or Steering Controls on one vehicle
Figure 6: Signal Flows in a Vehicle Control System [6]

## Slide 15: Other Stability Enhancement Features
Controlled Suspensions: ability to manage vertical wheel loads and thus influence longitudinal and lateral force capability of each tire
Figure 7: Passive, Active, and Semi-active Suspensions [7]

## Slide 16: Other Stability Enhancement Features
Controlled Steering: ability to actively adjust the steered angle or the camber angle of one or more wheels to influence the longitudinal and lateral forces of the tire
Example of steering action at high speed:
Angle of the front wheels is increased when the driver begins to turn the steering wheel
The vehicle's direction is changed quickly
The rear wheels are steered in the same direction as the front wheels
The vehicle quickly moves laterally
Body sideslip is reduced
Figure 8: Steering Action at High Speed [8]

## Slide 17: Critical Speed Formula
Critical Speed: Max speed at which a vehicle can traverse a path with a specific radius of curvature without loss of directional control
Speed of a vehicle undergoing a turn maneuver at which the tires leave visible sideslip marks
Vehicle center of mass traces out a near circular arc with the center of the arc located on a horizontal plane at distance r inside of the turn
Assumes vehicle is traveling along a surface that is possibly banked (superelevation) and uphill or downhill (road grade)

## Slide 18: Critical Speed Formula
Critical Speed Formula:
A formula that calculates the speed of a vehicle from the radius of curvature of its tires critical speed scuff marks, taking into account roadway grade, superelevation and frictional drag coefficient.
Tire mark shows diagonal striations that turn to parallel striations when the tire begins to skid
Figure 9: Tire mark striations [9]

## Slide 19: Critical Speed Formula
g = acceleration due to gravity
r = radius
e = superelevation of the road (in percent)
μeq = equivalent road friction
On level surface: simplifies to
μeqe < 1
μeq+e > 0
Figure 10: Free body diagram of a car traveling on a banked, curved road with superelevation [9]

## Slide 20: Radius Measurement Methods
Method 1: Use a 15-m chord with three equally spaced ordinates. Middle ordinate should be the one used for the radius determination and the 3/4 ordinate will be larger than the 1/4 ordinate when the vehicle is decreasing in speed as it performed the critical speed maneuver.
Method 2: Use two 10-m chords with middle ordinates. The radius is calculated with both measurements and should decrease if the vehicle is slowing as the vehicle progresses through the maneuver.
Figure 11: Tire Mark Radius Measurement Methods [9]

## Slide 21: Fuel Economy Tests
Purpose: uniform testing procedures for measuring fuel economy of light-duty vehicles (primarily for transportation of persons or property and rated at 4500 kg) on suitable roads.
Average fuel economy is the total distance driven divided by the total volume of fuel consumed in a series of replicate tests. When distance driven in each test is identical, average fuel economy is determined by taking the harmonic average of the individual economies:
n = number of tests

## Slide 22: Fuel Economy Tests: Instrumentation and Conditions
Calibrated Instrumentation is needed to measure:
Absolute Barometric Pressure
Wind Speed
Distance
Vehicle Weight
Dynamometer Inertia Weight
Fuel used
Speed
Acceleration
Time
Temperature
Ambient temperatures between 30 F and 90 F
Average wind speed not exceeding 15 mph and gusts not exceeding 20 mph (for Urban Cycle; limits reduced to 10 mph Average and 15 mph gusts for Suburban and Interstate Cycles
Roads dry, clean, smooth, and not exceeding 1.0% grade.
On a closed track, start and stop points elevation difference is 10 ft or less
Testing Conditions:

## Slide 23: Characteristics of Driving Cycles
Urban: Driving pattern similar to driving conditions in the central business district of a large city
Suburban: Similar to conditions in large city suburban areas
Interstate: Similar to driving conditions on expressways
Cycle | Average Speed (km/h) | Average Speed (mph) | Nominal Test Time (s) | Test Distance (km) | Test Distance (mile) | Idle Time (s) | Stops
Urban | 25.1 | 15.6 | 463 | 3.22 | 2 | 60 | 8
Suburban | 66.1 | 41.1 | 455 | 8.37 | 5.2 | 14 | 2
55 mile/h Interstate | 88.5 | 55 | 308 | 7.56 | 4.7 | 0 | 0
70 mile/h Interstate | 112.6 | 70 | 242 | 7.56 | 4.7 | 0 | 0
Table 1: Driving Cycle Characteristics [10]

## Slide 24: Other Test Considerations
Vehicle should have accumulated a minimum of 2000 miles of operation prior to test
Engine oil has a minimum of 2000 miles use prior to testing
Tires must have operated on a road or track at least 100 miles prior to test.
Tires have at least 75% of the tread remaining and tread in good condition
Fuel measuring device and other instrumentation installed in a manner not to hinder vehicle operation or operating characteristics
Cold tire pressure minimum recommended by the manufacturer for the vehicle test weight and set immediately prior to the vehicle warm-up at the beginning of the test

## Slide 25: References
[1] Chandrasekaran, A., Rizzoni, G., Soliman, A., Josephson, J. et al., "Design Optimization of Heavy Vehicles by Dynamic Simulations," SAE Technical Paper 2002-01-3061, 2002.
https://www.researchgate.net/publication/267941285_02TB-82_Design_Optimization_of_Heavy_Vehicles_by_Dynamic_Simulations
[2] Turnip, A., and Fakhrurroja, H., "Estimation of the Wheel-Ground Contacttire Forces using Extended Kalman Filter", International Journal of Instrumentation Science, 2013. http://article.sapub.org/10.5923.j.instrument.20130202.03.html
[3] The Clemson University Vehicular Electronics Laboratory, "CVEL Automotive Electronic Systems Page”, Accessed 2017.
http://www.cvel.clemson.edu/auto/systems/traction_control.html

## Slide 26: References
[4] SAE International, "Surface Vehicle Information Report: Automotive Stability Enhancement Systems", SAE-J2564, 2014.
[5] Toyota, "Anti-lock Brake System (ABS)", Accessed 2017.
http://www.toyota-global.com/innovation/safety_technology/safety_technology/technology_file/active/
[6] Autoelex, "Signal Flows in a Vehicle Controls System", 2013.
http://autoelexblog.blogspot.com/2013/11/ecu-development-measurement-and.html

## Slide 27: References
[7] Chen, Y., Wang, Z., Qiu, J., and Huang, H., "Hybrid Fuzzy Skyhook Surface Control Using Multi-Objective Microgenetic Algorithm for Semi-Active Vehicle Suspension System Ride Comfort Stability Analysis", J. Dyn. Sys., Meas., Control 134(4), 2012.
http://dynamicsystems.asmedigitalcollection.asme.org/article.aspx?articleid=1415349
[8] Nissan Motor Corporation, "4 Wheel Active Steer", Accessed 2017. http://www.nissan-global.com/EN/TECHNOLOGY/OVERVIEW/4was.html
[9] SAE International, "Surface Vehicle Recommended Practice: Use of the Critical Speed Formula", SAE-J2969, 2017.
[10] SAE International, "Surface Vehicle Recommended Practice: Fuel Economy Measurement Road Test
Procedure", SAE-J1082, 2008.