## Slide 1
Prof. Vladimir V. Vantsevich
Jesse Paldan, Research Assistant
Lloyd Balfour, Graduate Research Assistant
Vehicle and Robotics Engineering Laboratory
University of Alabama at Birmingham
Week 3. Lecture 2
Experimental Testing of Vehicles
Signals: Static and Dynamic Characteristics

## Slide 2
  Input/Outputs
  Signal analysis
  Types of Experimental Errors
  Sources of Errors
  Bias and Precession Errors
  Statistical Analysis
  Required Number of Experiments
  Outline

## Slide 3
Input
(air flow )
Output
(pressure)
Measurement Device
A measurement system takes an input quantity and transforms it into an output quantity [1].
The two most Important aspects of physical measurement are:
Selecting a proper measurement device that is most suitable to measure the input[1].
Being able to interpret the output from the measurement device [1].
  Input/Outputs

## Slide 4
Example
Figure 1: Ranges of pressure in tires [1]
  Input/Outputs
You are given the task to measure the pressure of two different tires; one belongs to a truck while the other belongs to a bicycle.
You have a chart with the typical input ranges of pressure, Figure 1 [1].

## Slide 5
You have at your disposal two pressure gauges with different ranges of pressure values. Which gauge should you use for each tire?
Gauge A can measure pressure up to
Gauge B can measure pressure up to .
  Input/Outputs
Example
Figure 1: Ranges of pressure in tires [1]

## Slide 6
Example
Figure 1: Ranges of pressure in tires [1]
  Input/Outputs
Since the bicycle wheel has a higher limit to its pressure reading, gauge A will be the ideal measurement system. Gauge B will not be able to read the pressure in the bicycle wheel if it is greater than its limit of .

## Slide 7
Example
Figure 1: Ranges of pressure in tires [1]
  Input/Outputs
Gauge B will be best to used on the truck tire due to the gauge having a lower range of pressure values.

## Slide 8
Signal
Signals are time-varying quantities that convey some type of information [2].
When a measurement system produces a signal, that signal can be characterized as either an analog, discrete time, or digital signal [1].
Analog
An analog signal is a signal that is both smooth and continuous with time. Its magnitude is equivalent to the physical variable being measured [1].
  Signal Analysis

## Slide 9
Amplitude of the fluctuating ( AC component)
Average value (DC offset)
Analog Signal:
Figure 2: Plot of an Analog signal [1]
The average value (mean value) of the signal from Figure 2 is sometimes referred to as the DC component or DC offset [1].
The mean value of an analog signal provides a static value
  Signal Analysis

## Slide 10
Average value equation [1]
average value of the analog signal
the time
Power Equation [1]
: is the power dissipated
: the current
: the resistance value
Total Energy Dissipated equation [1]
: total energy dissipated over the time domain of to
: Is time varying current
I made the corrections to the equations. If I have time, do you want me to create and or find a handout that explains the operation of an integral? If not I will leave the equation as it currently is.
  Signal Analysis

## Slide 11
Signal Root Mean-Square Value (RMS)
Consider finding a magnitude of a constant effective current named that produces the same total energy dissipation as the time varying current over a specific time period [1].
Assuming that the resistance stays constant, the following equation is developed for constant effective current [1].
  Signal Analysis

## Slide 12
Signal Root Mean-Square Value
Based on the reasoning used to calculate the effective current, the RMS value of any continuous analog variable over the time period to can be expressed the following equation [1].
  Signal Analysis

## Slide 13
Discrete Time and Digital Signals
Figure 3: Digital signal plot
Figure 4: Discrete signal plot [3]
  Signal Analysis

## Slide 14
A time dependent analog signal can be represented by a discrete set of values over a time period of to [1].
:is a discrete number in the data set [1]
: analog time- dependent signal [1]
: delayed unit impulse function [1]
: sample time increment [1]
  Signal Analysis
Discrete Time and Digital Signals

## Slide 15
For either a discrete signal or a digital signal, the mean value equation and the root mean square equation is given below [1]
: is a discrete number in the data set [1]
: number of values [1]
: the root means square of discrete time or digital signal [1]
  Signal Analysis
Discrete Time and Digital Signals

## Slide 16
Experimental Error:
Factors that affect the experiment that are always vague and carry some form of uncertainty [2].
Errors will always in some way show up in an experiment no matter how meticulous and careful one is.
The purpose for all this discussion and emphasis on errors is to develop the ability to determine how uncertain a value may be and create a way to specify the uncertainty in an analytical form and use this knowledge to mitigate any errors.
  Experimental Errors
Notes: Pg 60-79 experiment methods
A reasonable definition of experimental
uncertainty may be taken as the possible value the error may have
The reason for this : determine how uncertain a value may be and create a way to soecify the uncertainty in an analytical form.

## Slide 17
For more information on uncertainty and how example on calculating the uncertainties, refer to the handout
  Experimental Errors

## Slide 18
The 3 types of experimental errors are as follows:
1. Fixed Errors
Errors that are caused by repeated readings [2]. Sometimes referred to as systematic errors
(aka bias errors) [2].
2. Random Error
Errors that are the results of random fluctuations, whether electrical or personal [2].
3. Blunders
Error resulting from an outright mistake [4].
  Experimental Errors

## Slide 19
For more information and examples on the types of experimental errors, refer to the handout
  Experimental Errors

## Slide 20
Identify error sources:
In order to identify error sources, think of the measurement process as being divided into three stages: calibration, data acquisition, and data reduction.
Within each of these error groups, list the types of errors that where encountered, these errors are known as elemental errors [1].
An example of the group is shown later on in Tables 1,2 &3.
  Sources Errors
Notes: Calibration errors, Data acquisition errors, Data reduction errors , systematic error and random error [1] pg 168
Page 168 of mechanical measurement

## Slide 21
Do not become engrossed in the grouping or the errors, this group is only intended to be used as a guide.
Placing an error in an incorrect group will not result in the uncertainty changing.
  Sources Errors
Identify error sources:

## Slide 22
Element | Calibration Error Source
1 | Standard or reference value errors
2 | Instrument or system errors
3 | Calibration process errors
4 | Calibration curve fit errors
 | Other misc. calibration errors
The source of calibration errors comes from the measurement system during its calibration.
Table 1: Calibration error source grouping [1]
  Calibration Error
Notes: For example, the laboratory standard used for
calibration contains some inherent uncertainty, and this is passed along with the input value on
which the calibration is based. Measuring system errors, such as linearity, repeatability, hysteresis,
and so forth, contribute uncertainty.

## Slide 23
Element | Data Acquisition Error Source
1 | Measurement system operating conditions
2 | Sensor transducer stage (instrument error)
3 | Signal conditioning stage (instrument error)
4 | Output stage (instrument error)
5 | Process operating conditions
6 | Sensor installation effects
7 | Environmental effects
8 | Spatial variation error
9 | Temporal variation error
 | Other misc. data acquisition errors
Table 2: Data Acquisition error source grouping [1]
The source of data acquisition happens during the act of measurement [1].
  Data Acquisition Error
Notes: For example, these errors include sensor and instrument errors unaccounted for by calibration; uncontrolled
variables, such as changes or unknowns in measurement system operating conditions; and
sensor installation effects on the measured variable.

## Slide 24
Element | Data Reduction Error Source
1 | Curve fit error
2 | Truncation error
3 | Modeling error
 | Etc.
Table 3: Data reduction error source grouping [1]
The source of Data reduction errors comes from the curve fits and the correlations with their unknown values [1].
  Data Reduction Error
Notes: Curve fits and correlations with their associated unknowns (Section 4.6) introduce data-reduction
errors into test results. Also, truncation errors, interpolation errors, and errors from assumed models
or functional relationships affect the quality of a result.

## Slide 25
Precision
Precision is the amount of deviation expected with repeated measurements[1]. Precision is also how closely individual measured values agree with each other [5].
Imprecision
Imprecision is the magnitude of the deviation, It is also called uncertainty [5].
  Precision and Bias Errors

## Slide 26
Bias Error
Bias is an error in the execution or design of a test in which results are consistently distorted in a direction due to nonrandom factors [6]. I.e. it is a systematic deviation from the true value [5].
Bias is also commonly referred to as inaccuracy [5].
  Precision and Bias Errors

## Slide 27
The black dots on each of the targets can be thought of as measured values
The bulls eye represents the true value.
Figure 3: Accuracy and precision [5]
  Precision and Bias Errors

## Slide 28
Inaccurate and imprecise
Accurate and imprecise
Inaccurate and precise
Accurate and precise
  Precision and Bias Errors
Figure 3: Accuracy and precision [5]

## Slide 29
Statistical analysis is a mathematical tool for quantitative analysis of data that serves as the means for extracting useful information from data [7].
Statistical analysis can be used to summarize multiple measurements of the same thing (i.e. replicated measurements) by estimating the average [7].
  Statistical Analysis
Notes: Page 74 of the experimental methods section 3.6 [2]
Also [7]

## Slide 30
Sample average (Arithmetic mean Equation) [2,7]
: is the sample average
: is the number of values
: represents the ith individual value
The sample average equation is the average of a group of arbitrary values.
  Statistical Analysis

## Slide 31
Root mean square deviation equation
(I.e. Standard deviation) [2]
Sample standard deviation equation [2]
: sample standard deviation
: is the standard deviation
: is the sample average
: is the number of values
: represents the ith individual value
  Statistical Analysis

## Slide 32
Standard deviation:
Standard deviation is sometimes referred to as population or biased standard deviation because the standard deviation only deals with large number of samples [2].
Sample standard deviation:
There may be a time when one will not be able to collect all the data points.
In this case the sample standard deviation should be used to calculate the standard deviation
Golden Rule: if number of data is less than 20, it is more accurate to use the sample standard deviation [2].
  Statistical Analysis

## Slide 33
Example:
You are tasked with organizing the data of a recent acceleration test of a new prototype vehicle called Omega123. Ten runs were done (Omega123 had some technical issues) and the values that were tabulated are given to you. Your boss wants the average and standard deviation of the time.
Run | Time (seconds)
1 | 7.3
2 | 7.1
3 | 6.9
4 | 7.1
5 | 6.0
6 | 5.9
7 | 9.4
8 | 7.3
9 | 7.2
10 | 6.4
Table 4: 0-60 times
  Statistical Analysis

## Slide 34
Example:
Run | Time (seconds)
1 | 7.3
2 | 7.1
3 | 6.9
4 | 7.1
5 | 6.0
6 | 5.9
7 | 9.4
8 | 7.3
9 | 7.2
10 | 6.4
Table 4: 0-60 times
  Statistical Analysis
7.3+7.1+6.9+7.1+6.0+5.9+9.4+7.3+7.2+6.4)

## Slide 35
Example:
Run | Time (seconds)
1 | 7.3
2 | 7.1
3 | 6.9
4 | 7.1
5 | 6.0
6 | 5.9
7 | 9.4
8 | 7.3
9 | 7.2
10 | 6.4
Table 4: 0-60 times
  Statistical Analysis

## Slide 36
Example:
Run | Time (seconds)
1 | 7.3
2 | 7.1
3 | 6.9
4 | 7.1
5 | 6.0
6 | 5.9
7 | 9.4
8 | 7.3
9 | 7.2
10 | 6.4
Table 4: 0-60 times
  Statistical Analysis

## Slide 37
Golden Rule: The least number of times that an experiment should be run is three times.
However, there is a method that calculates the minimum number of times an experiment should be done.
This method is related to the number of independent variables in the experiment [8].
  Required Number of Experiments
Notes: Golden rule is Usually a number of at least 3 times for experiment, online is a source that calculates the number of experiments needed, I have to go find it.

## Slide 38
The first step is to choose two levels for each independent variable. Levels are typically referred to as the extremes of the variable range
(e.g. on/off, red/green, 1000rpm/10rpm, 40/0) [2].
For example, consider an experiment where the dependent variable is a function of three independent variables ( A,B,C) and each of them have two possible levels [2].
  Required Number of Experiments

## Slide 39
Independent Variable Names | Possible levels | 
A | High | Low
B | High | Low
C | High | Low
If all the combination were to be tested, the number of experiments () will be raised to the power of the number of independent variables () [2].
The result of this will give the minimum number of experiments that is required to maintain accuracy.
Table 5: Independent variables [2]
  Required Number of Experiments

## Slide 40
In this example, 8 experiment runs are needed to meet accuracy requirement
  Required Number of Experiments
Independent Variable Names | Possible levels | 
A | High | Low
B | High | Low
C | High | Low
Table 5: Independent variables [2]

## Slide 41
[1] R. Figliola and D. Besley. Theory and design for mechanical measurements, 5th edition. New Jersey: J. Wiley & Sons, Ic., 2011. Retrieved from: http://www.hljp.edu.cn/attachment/20120831082417983.pdf
[2] J. Holman. Experimental Methods for Engineers 8th edition. New York: McGraw-Hill inc. 2012.
[3] MathWorks. Stem. Retrieved from : https://www.mathworks.com/help/matlab/ref/stem.html?requestedDomain=www.mathworks.com
[4] New Mexico State University Physics Department. Types of Experimental Errors. Retrieved from: http://www.physics.nmsu.edu/research/lab110g/html/ERRORS.html
  References

## Slide 42
[5] S. Chapra and R. Canale. Numerical Methods for Engineers, 7th edition. New York: McGraw-Hill Education, 2015.
[6] U. Sharma. Biases and errors in Epidemiology. Department of Community Medicine. Retrieved from: https://www.slideshare.net/jamesmacroony/bias-and-errors
[7] C. A. Peters. Statistic for Analysis of Experimental Data. Department of Civil and Environmental Engineering Princeton University. 2001. Retrieved from: https://www.princeton.edu/~cap/AEESP_Statchap_Peters.pdf
[8] Fogler & Gurmen. Collection and Analysis of Rate Data. “Professional Reference Shelf”. University of Michigan. 2008. Retrieved from: http://umich.edu/~elements/05chap/html/05prof2.htm
  References