## Slide 1
Prof. Vladimir V. Vantsevich
Jesse Paldan, Research Assistant
Lloyd Balfour, Graduate Research Assistant
Vehicle and Robotics Engineering Laboratory
University of Alabama at Birmingham
Week 2. Lecture 2
Experimental Testing of Vehicles
Instruments

## Slide 2
  Safety
  Electrometer
  Digital Multi-Meter
  Source-Measure Unit
  SourceMeter
  Micro-ohmmeter
  Outline

## Slide 3
Safety
The Following Safety information should be noted before operation of the electrometer!
If the Electrometer is used in a manner that overrides the safety information, it will impair the electrometer from being able to provide protection to the operator!
More information can be found in the Safety handout
  Electrometer

## Slide 4
Safety
ANSI (American National Standards Institute) states that a shock hazard exists when voltage levels are greater than
(RMS is root mean square ) [1].
The peak voltage of 30V RMS is .
A shock Hazard is also present when a (voltage of a direct current) level exists [1].
Good safety practice is to assume that hazardous voltage is present in any unknown circuit before any measurements are made.
  Electrometer

## Slide 5
Safety
Before operating any of the devices, make sure all line cords are connected properly to a grounded source [1].
Inspect all cables, test leads ( discussed later in the slides) and jumpers for possible wear and tear before each use before operating the electrometer [1].
If any cables fail the safety check, immediately notify your Responsible body (individual or group responsible for the maintenance of the equipment) and or instructor [1].
  Electrometer

## Slide 6
Safety
Do not touch the instruments or any other cables while power is applied to the test circuit [1].
Always remove power from the entire test system and discharge any capacitors before
  connecting or disconnecting cables [1].
  Installing or removing any internal circuits components [1].
  Electrometer

## Slide 7
An Electrometer is a highly sensitive device that is used for the measurements of voltages, electric charges ,currents and resistance [2].
Figure 1: Electrometer model LB1840-001 [2]
Figure 2: Electrometer model 6517B [3]
  Electrometer

## Slide 8
Description
The primary function of an electrometer is to measure the electric potential (i.e. voltage) or the charge (i.e. Coulombs) [4].
The Resistor value (ohms) is set to vary in different type of voltage ranges
The electrometer measures the change in the accumulated charge over time (i.e. current which is in amperes) [4]
  Electrometer

## Slide 9
Description
The voltages ranges for an electrometer are to as high as (volts) [2,3].
The current ranges for an electrometer are to as low as (attoamps i.e. ) [2,3].
The charge ranges for an electrometer are to as low as (femtocolumb i.e.
The resistance range are to as high as (ohms) [3]
  Electrometer

## Slide 10
Parameters
Voltage
Voltage is the electric potential (also referred to as the electric difference).
Measured in volts
Charge
Charge is the value that an electron carries
Measured in coulombs
  Electrometer

## Slide 11
Parameters
Current
Current is the rate of flow of electron charge.
Measured in amperes
Resistance
Resistance is the value of a resistor.
A resistor is a device that impedes the flow of the current.
Measured in ohms .
  Electrometer

## Slide 12
Operation Procedure
Example:
Insulation Resistance of a Single Battery Module Test
Figure 3: Test setup for measuring insulation resistance of the battery module [5].
  Electrometer

## Slide 13
  Electrometer
Operation Procedure
Example:
Insulation Resistance of a Single Battery Module Test
The insulation resistance test is conducted in order to determine if there are any imperfections or fractures due to dirt and or moisture [5].
The test setup is shown in Figure 3. The electrometer is connected between the short-circuited terminals and the cooling fins of the battery [5].
Notes: Use http://www.freeasestudyguides.com/index.html
To try and create automotive procedure

## Slide 14
Operation Procedure
Example:
Insulation Resistance of a Single Battery Module Test
A minimum of two test voltages is recommended when measuring the resistance value of the battery module [5].
Full details on the operation of the electrometer is described in the handout page 2-18 to 2-45 .
  Electrometer

## Slide 15
A Digital Multi-Meter is a device similar to the Electrometer in that it has the ability to measure voltage, current and resistance but not the charge [6].
Figure 4: Various types of digital multi-meters [6,7]
  Digital Multi-Meter

## Slide 16
Description
The difference between the digital multi-meter and the electrometer is that the digital multi-meter is not as sensitive as the electrometer.
This results in the digital multi-meter having a limited capacity to measure only smaller ranges of voltage, current and resistance [8].
  Digital Multi-Meter

## Slide 17
Parameters
Voltage
The electric potential (also referred to as the electric difference).
Measured in volts
Resistance
The value of a resistor.
A resistor is a device that impedes the flow of the current.
Measured in ohms .
Current
The rate of flow of charge.
Measured in amperes
  Digital Multi-Meter

## Slide 18
Operation Procedure
Example: Brake Switch Testing
Figure 5: Digital multimeter connected to a brake pedal [9]
  Digital Multi-Meter
Notes: Use http://www.freeasestudyguides.com/index.html
To try and create automotive procedure

## Slide 19
  Digital Multi-Meter
Operation Procedure
Example: Brake Switch Testing
Brake light switches are normally open. This means that when the pedal is depressed, the contact closes causing a complete circuit to form resulting in brake illumination [9]
First check if the brake switch is adjusted properly before attempting to measure the voltage [9]. After checking the brake switch , apply a voltage to the circuit.
Connect the DMM similar to Figure 5

## Slide 20
  Digital Multi-Meter
Operation Procedure
Example: Brake Switch Testing
When the pedal is released there should be a voltage entering the switch and no voltage out of the switch [9].
When the brake pedal is released, the output from the DMM should be zero [9].
When the brake pedal is depressed, the output from the DMM should be a nonzero voltage value [9].
For a more in-depth explanation, look at the handout that will be provided

## Slide 21
A Source measure unit (SMU) is a device that can both measure voltages and current while also having the sourcing capability [8].
Figures 6 and 7: SMU Graphical (left) and SMU 2400 Series (right) [10]
  Source Measure Unit

## Slide 22
Sourcing
When a load is connected to a device so that the device supplies energy (voltage or current in this example) [10].
Figure 8: Current Sourcing [11]
The device in Figure 8 can be any type of device (in this case it will be the Source measure unit)
The load is in Figure 8 is shown as a 1k ( 1000ohms) resistor.
  Source Measure Unit

## Slide 23
Description
The source measure unit has both measuring and sourcing abilities [8].
Adding current and voltage sourcing capabilities enables an extra degree of versatility in measurement applications [8].
For example, very high resistance values can be measured by applying a voltage source across an arbitrary device while measuring the resulting current [8].
  Source Measure Unit

## Slide 24
The SMU provides four functions
Measure Voltage
Measure Current
Source Voltage
Source Current
The SMU also allows for the following combinations [8].
Simultaneously sourcing voltage and measuring current
Simultaneously sourcing current and measuring voltage
The SMU has the ability to “sweep” [8]. This allows for either the voltage or the current to swept across a range of increments in order allow measurement at each step [8].
  Source Measure Unit

## Slide 25
Low level measurements
SMUs are more suitable for low level measurements
(ranges shown in Figure 9)
Figure 9: Limits of Voltage measurements [8]
  Source Measure Unit

## Slide 26
Parameters
Voltage
Voltage is the electric potential (also referred to as the electric difference).
Measured in volts
Current
Current is the rate of flow of electron charge.
Measured in amperes
  Source Measure Unit

## Slide 27
Operation Procedure
Example: Battery test of a Vehicle
Battery testing can be simplified by using a SMU. This is due to the SMU being able to charge than battery and then record the current.
Figure 10: Four wire battery connected to the SMU instrument [12]
  Source Measure Unit
Notes: Use http://www.freeasestudyguides.com/index.html
To try and create automotive procedure

## Slide 28
The SMU will be connected to the battery as shown in Figure 10. Once this is done, an input voltage is set on the SMU to prepare the sourcing of the battery.
When the battery has been fully charged by the SMU, the current that the SMU is supplying to the battery will decrease until it the current reaches zero.
When the battery is fully charged the SMU will operate as a sink (it dissipates the power from the battery instead of sourcing it) [12].
  Source Measure Unit
Operation Procedure
Example: Battery test of a Vehicle

## Slide 29
The output of the current value from the SMU will be negative due to the SMU sinking the battery [12].
The current discharge should stay constant until the battery has reached the input value of the SMU [12].
For a more in-depth explanation of the procedure, look at the handout that is provided.
  Source Measure Unit
Operation Procedure
Example: Battery test of a Vehicle

## Slide 30
The SourceMeter is a device that is almost identical to the SMU in that it can both measure voltages and current while also having the sourcing capability [8].
Figure 11: SourceMeter model 2401 [13]
  SourceMeter

## Slide 31
Description
The main differences
The SourceMeter can display measurements results directly in resistance (ohms) [8].
The SourceMeter does not have as high of an input impedance as a SMU [8].
Input Impedance
Measured value of the shunt resistor and capacitance [8].
Shunt resistor
Shunt resistor are low resistance precession resistors that are used to measure AC or DC circuits
  SourceMeter

## Slide 32
Parameters
Voltage
The electric potential (also referred to as the electric difference).
Measured in volts
Resistance
The value of a resistor.
A resistor is a device that impedes the flow of the current.
Measured in ohms .
Current
The rate of flow of charge.
Measured in amperes
  SourceMeter

## Slide 33
Operation Procedure
Example: Return to the Battery test of a Vehicle
Instead of wanting to determine the current from a battery in a vehicle, one wants to determine the internal resistance of the battery.
The SourceMeter will be set up identical to the SMU from the previous example including charging and discharging the battery.
  SourceMeter

## Slide 34
  SourceMeter
Operation Procedure
Example: Return to the Battery test of a Vehicle
The only difference will be that instead of current being outputted, resistance will be outputted from the SourceMeter.
For more information on operating a SourceMeter, look at the handout section 4 that was provided.

## Slide 35
A Micro-Ohmmeter is a special type of ohmmeter designed specifically for low level resistance measurements [8].
Figure 13: 6250 Micro-ohmmeter [14]
Figure 12: LOM 510A Micro-ohmmeter [15]
  Micro-Ohmmeter

## Slide 36
Description
The purpose of an Ohmmeter is to measure the resistance of an object [8].
The Micro-ohmmeter is able to measure resistances as low as
(micro ohms i.e ) [8].
In order to reduce errors caused by connections and test leads, the micro-ohmmeter implements measurements using the four wire techniques, also known as the Kelvin method [5,15].
  Micro-Ohmmeter

## Slide 37
Test leads are physical devices that connect to test equipment and include a probe, a cable and a terminating connector [16].
Test Leads
Figure 15: White colored test lead [17]
Figure 14: Black and red colored test lead [16]
  Micro-Ohmmeter

## Slide 38
Parameters
Voltage
The electric potential (also referred to as the electric difference).
Measured in volts
Resistance
The value of a resistor.
A resistor is a device that impedes the flow of the current.
Measured in ohms .
Current
The rate of flow of charge.
Measured in amperes
  Micro-Ohmmeter

## Slide 39
The same test of the brake light switch can be implemented by using a Micro-ohmmeter.
Note, Never use an ohmmeter on a powered circuit [9]. Using an ohmmeter on a powered circuit can damage the device.
Connect the tester lead of the micro-ohmmeter similar to way it was connected in the DMM test.
  Micro-Ohmmeter
Operation Procedure
Example: Return to the Brake Switch Testing

## Slide 40
Bring the vehicle that is being tested to an idle of about 2000 rpms [9]. After that, turn on the other electric accessories like the headlights, A/C etc…[9].
If the brake switch is working properly, a resistance value should show up on the display of the Micro-ohmmeter.
For a more detailed explanation of procedure, check pages 15 to 23 of the handout
  Micro-Ohmmeter
Operation Procedure
Example: Return to the Brake Switch Testing

## Slide 41
[1] Keithley. Model 6517A Electrometer User’s Manual. Retrieved From: http://www3.imperial.ac.uk/pls/portallive/docs/1/7293199.PDF
[2] Industrial Equipment & Control. Instruction Sheet Electrometer. Retrieved from: http://www.iecpl.com.au/z_pdfs/lb1840-101.pdf
[3] Keithely, A Tektronix Company. Electrometer/High Resistance Meter. 2016. Retrieved from: http://www.adler-instrumentos.es/imagenes_web/productos/1-6517B.pdf
[4] P. Frame. Quadrant Electrometers. Oak Ridge Associated Universities. 1999. Retrieved from: https://www.orau.org/ptp/collection/electrometers/quadrantelectrometer.htm
  References

## Slide 42
[5] M. Memari & V. Nakanwagi. Electrical Insulation in a 400 V Battery Module for Hybrid Vehicles. Chalmers Univeristy of Technology. 2014. Retrieved from: http://publications.lib.chalmers.se/records/fulltext/208860/208860.pdf
[6] Fluke Corporation. What is a digital multimeter? Retrieved from: http://en-us.fluke.com/training/training-library/measurements/electricity/what-is-a-digital-multimeter.html
[7] How to use a multimeter. Science Buddies. 2017. Retrieved from: http://www.sciencebuddies.org/science-fair-projects/how-to-use-a-multimeter.shtml
  References

## Slide 43
[8] Keithely, Low Level Measurements Handbook Precession DC Current, Voltage, and Resistance Measurements 6th edition. Cleveland, Ohio. 2004. Retrieved from: http://www.if.tugraz.at/bibliothek/handleitung/HANDBOOK-Low-Level.pdf
[9] ASE. ASE Certification Practice Tests. Brake Switch Testing. Retrieved from: http://www.freeasestudyguides.com/index.html
[10] Tektronix. Keithley Source Measure Units. 2017. Retrieved from : http://www.tek.com/keithley-source-measure-units
[11] Starting Electronics. Current Sourcing and Sinking. 2013. Retrieved from: https://startingelectronics.org/articles/current-sourcing-sinking/
  References

## Slide 44
[12] Keithley. Rechargeable Battery Charge/Discharge (Galvanic) Cycling Using the Keithley Model 2450 or Model 2460 SourceMeter SMU instrument. 2014. Retrieved from: http://www.tek.com/sites/tek.com/files/media/document/resources/2450%202460%20Recharge%20Battery%20AppNote.pdf
[13] Keithley. Low Voltage SourceMeter Instrument. Retrieved from: http://www.adler-instrumentos.es/imagenes_web/productos/5-2401DataSht.pdf
[14] Chauvin Arnoux. 6250 Micro-Ohmmeters. 2016. Retrieved from: http://www.aemc.com/products/html/moreinfo.asp?id=902&dbname=products
  References

## Slide 45
[15] IET Labs inc. Lom-510A Micro-Ohmmeter. Retrieved from: http://www.ietlabs.com/micro-ohmmeter/lom-510.html?gclid=CIzd_sWn5tICFVMdgQod62oMgA
[16] Wikipedia. Test Probe. 2017. Retrieved from: https://en.wikipedia.org/wiki/Test_probe
[17] Techni-Tool inc. Test Leads, Probes and Plugs. 2017. Retrieved from: http://www.techni-tool.com/Test-Leads-Probes-Plugs?gclid=CKHx_vCv5tICFZcbgQodxC4Djg&s_kwcid=AL!2966!3!178301127997!b!!g!!_cat%3Atechni-tool.com&ef_id=WHlAogAAAYIXNy4g:20170321004747:s#!Test-Leads-Probes-Plugs?gclid=CKHx_vCv5tICFZcbgQodxC4Djg&s_kwcid=AL!2966!3!178301127997!b!!g!!_cat%3Atechni-tool.com&ef_id=WHlAogAAAYIXNy4g:20170321004747:s
  References