## Slide 1
Prof. Vladimir V. Vantsevich
Jesse Paldan, Research Assistant
Lloyd Balfour, Graduate Research Assistant
Vehicle and Robotics Engineering Laboratory
University of Alabama at Birmingham
Week 6. Lecture 1
Experimental Testing of Vehicles
Overview of FMVSS & NHTSA

## Slide 2
  Overview of NHTSA
  Electronic Stability Control
  Test Maneuvers
  Rollover Testing
  Federal Motor Vehicle Standards
  FMVSS Organization
  FMVSS: Crash Avoidance
  FMVSS: Crashworthiness
  FMVSS: Post-crash
  FMVSS: Other Regulations
Outline

## Slide 3: Overview of NHTSA
NHTSA = National Highway Traffic Safety Administration
https://www.nhtsa.gov/
Responsible for enforcing vehicle performance standards
Evaluating and creating vehicle maneuver tests to evaluate performance, safety
Creation of Federal Motor Vehicle Safety Standards (FMVSS)
Administers grant programs for highway safety research
Creation of reports to congress on vehicle safety topics
Figure 2: NHTSA Logo [1]
Figure 1: US DOT Logo [1]

## Slide 4: Electronic Stability Control (ESC)
ESC systems, also called ESP (Electronic Stability Programs), use automatic computer-controlled braking of individual wheels to assist the driver in maintaining control in critical driving situations
NHTSA Safety Standard No. 126 requires ESC systems on passenger cars, multipurpose passenger vehicles, trucks, and buses with a gross vehicle weight rating of 4,536
Uses: Rollover Mitigation (Prevention of rollover), reduce oversteer and understeer
Type of ESC used on a specific vehicle is the decision of the vehicle manufacturer and is integrated with other technologies such as ABS and traction control

## Slide 5: Electronic Stability Control (ESC)
Avoid Understeer or Oversteer through ESC Intervention
By monitoring yaw rate and sideslip, ESC can intervene early with appropriate brake forces before the driver would attempt an over-correction
Figure 3: Oversteer [2]
Figure 4: Understeer [2]

## Slide 6: Electronic Stability Control (ESC)
Comparison of vehicle with and without ESC:
Evaluation of performance requires suitable test maneuvers
Figure 5: ESC Interventions [3]

## Slide 7: Evaluation of Test Maneuvers
Objectivity and Repeatability:
By a human driver or steering machine
Performability:
How simple a test is to perform, required instrumentation, adaptability to different vehicles
Discriminatory Capability:
Test measures a criteria of interest such as wheel lift
Appearance of Reality:
How closely test matches a real driving scenario

## Slide 8: Steering Robots
Motorized steering wheel input and angle measurement
Used for tests requiring a higher reproducibility of the steering input than a driver can provide.
Some tests such as the NHTSA fishhook test are designed for use with steering machines. The ISO and Consumer’s Union Double Lane Change Tests use a human driver
Figure 6: Steering Robot [4]

## Slide 9: Steering Robots
Figure 7: Lane Change Test, Human Driver vs. Steering Robot [4]

## Slide 10: Types of Test Maneuvers
Slowly Increasing Steer:
Continuous increase in the steer rate at a constant speed
J-Turn:
Rollover test in which a ramped motion is applied to the steering wheel, emulates turning on entrance/exit ramps
Double Lane Change:
Driver-performed handling test which emulates emergency crash avoidance maneuvers (obstacle avoidance)
Fishhook:
Tests rollover and roll rate, emulates road edge recovery

## Slide 11: Slowly Increasing Steer
Used in part of NHTSA’s dynamic rollover test procedure and in handling tests
Performed at a constant speed with a steering angle increasing at a constant rate.
Figure 8: Slowly Increasing Steer Test [5]

## Slide 12: J-Turn Test
Used to measure minimum speed capable of producing
two-wheel lift (Front and rear wheel lift > 2”)
Path of the vehicle follows a shape similar to the letter J
Variant of the test includes pulse braking
Figure 9: J-Turn Typical Vehicle Paths [2]
Figure 10: Pulse Braking J-Turn Steer
Angle, Brake Pedal Force [6]

## Slide 13: Double Lane Change Tests
Driver attempts to navigate course without striking cones (orange blocks in figures)
Figure 11: Consumers Union Short Course [7]
Figure 12: ISO 3888 Part 2 [7]

## Slide 14: Fishhook Maneuver Test
Figure 13: NHTSA Fishhook Test [2]

## Slide 15: Fishhook Maneuver Test
Used in rollover safety tests
Test measures roll rate, speed at which 2-wheel lift occurs
Follows a pre-defined path with given steering inputs, resulting in the “fishhook”-like path
A Fixed Timing Fishhook assigns times it which the handwheel position is changed
Figure 14: Fixed Timing Fishhook [7]

## Slide 16: Roll Rate Feedback Fishhook
Dwell time is varied so as to maximize the severity of the maneuver (±1.5 deg/sec roll velocity)
Steering magnitude and the steering reversal timing used for the Roll Rate Feedback Fishhook are adapted for the characteristics of the vehicle being tested.
Figure 15: Roll Rate
Fishhook [7]

## Slide 17: Measuring Roll Angle in a Rollover Test
Quartz accelerometers positioned near vehicle center of gravity
Ultrasonic distance sensors installed near longitudinal CG on both sides of the vehicle
Sensor data is resolved during post processing to produce chassis roll angle
Figure 16: Accelerometers [8]
Figure 17: Ultrasonic Sensors [8]

## Slide 18: Measuring Wheel Lift in a Rollover Test
Two laser sensors mounted parallel to the wheel and aligned vertically with the axle
Zero defined as the tire just touching ground at 0° camber angle
Figure 18: Distance Measurements [8]
Figure 19: Laser Distance Sensor [8]

## Slide 19: Measuring Wheel Lift in a Rollover Test
Dist 1 = distance between first laser sensor and inside corner of tread
Dist 2 = distance between laser sensors
1: Use laser wheel height sensor data to calculate camber angle.
2: Using known camber angle, correct wheel lift height.
Error
from
camber
Figure 18: Distance Measurements [8]
Figure 20: Wheel Lift Calculation [8]

## Slide 20: FMVSS Overview
FMVSS = Federal Motor Vehicle Standards
Issued by NHTSA (National Highway Traffic Safety Administration )
Set of standards which manufacturers of motor vehicles and equipment must conform to starting from 1967
Specify minimum safety performance requirements for risk of crashes resulting from design, construction, and performance of vehicles and protecting against unreasonable risk of death or injury due to crashes
Different standards specified for Passenger cars, trucks, and buses and for vehicles of different gross vehicle weight ratings (GVWR)

## Slide 21: FMVSS Organization
Standards are grouped into sections by topic:
CRASH AVOIDANCE: Standards No. 101 - 135
Covers vehicle systems for avoiding crashes such as brakes acceleration control, and ESC, as well as driver visibility (lights, controls, windshield)
CRASHWORTHINESS: Standards No. 201 - 224
Occupant crash protection, restraints, and performance requirements for impact protection
POST CRASH STANDARDS: Standards No. 301 - 500
Standards which reduce risks that occur after a crash
OTHER REGULATIONS: Standards No. 531 - 595
Other standards not covered by the above sections

## Slide 22: FMVSS: Crash Avoidance
Examples of crash avoidance standards
101: Controls and Displays
Identification of essential controls which must be located within reach of the driver
103, 104: Windshield Defrosting, Defogging, Wiping and Washing Systems
105: Braking effectiveness stopping distance
109, 110: Tire resistance, strength, endurance, and load rating requirements
110: Mirror location and visibility
124: Accelerator must return to idle when driver removes foot from control or disconnection in the accelerator control system

## Slide 23: FMVSS: Crashworthiness
Examples of crashworthiness standards
201: Head impact protection standards for vehicles of different Gross Vehicle Weight Rating
203, 204: Minimize risk of injury due to impact with steering system and column
207: Minimize failures of the seating system in an impact from forces acting on the seat
208, 209, 210: Requirements for occupant restraints (seat belts), their assemblies and anchors, performance requirements for crash test dummies
214: Side impact protection
216: Roof crush resistance
223, 224: Rear impact guards and protection

## Slide 24: FMVSS: Post-crash
Examples of post-crash standards
301: integrity of the fuel systems to reduce fires from fuel spillage after crashes
302: Flammability, burn resistance requirements for materials used in the occupant compartments
303, 304: Integrity of fuel system and fuel containers for vehicles using compressed natural gas (CNG) as a motor fuel to reduce fuel leakage during
500: Requirements for low-speed vehicles (a 4-wheeled motor vehicle, other than a truck, whose attainable speed is more than 20 mph and not more than 25 mph)

## Slide 25: FMVSS: Other Regulations
Examples of other regulations:
531, 532: Average fuel economy standards for passenger automobiles and light trucks
575: Specifies information manufacturers must provide to first purchases of vehicles
565 - 570: Standards for identification of manufacturer, certification, inspection, and VIN numbers
577, 579: Standards for notification and responsibility for defects
572 - Standards for crash test dummies for compliance testing of motor vehicles and motor vehicle equipment with motor vehicle safety standards

## Slide 26: References
[1] NHTSA, “Laws and Regulations". https://www.nhtsa.gov/laws-regulations/fmvss
[2] Paine, M., “Electronic Stability Control - Review of Research and Regulations”, Vehicle Design and Research Pty Limited for ROADS AND TRAFFIC AUTHORITY OF NSW, 2005.
[3] NHTSA, "PROPOSED FMVSS No. 126 Electronic Stability Control Systems", 2006.
https://www.nhtsa.gov/sites/nhtsa.dot.gov/files/fmvss/ESC_PRIA.pdf
[4] Weimart, K., "Fishhook Test", Corrsys - Datron Sensorsysteme GmbH. [PowerPoint slides]

## Slide 27: References
[5] Svenson, A.L., and Hac, A., "Influence of Chassis Control Systems on Vehicle Handling And Rollover Stability", NHTSA Paper Number 05-0324.
http://www-nrd.nhtsa.dot.gov/pdf/ESV/esv19/05-0324-O.pdf
[6] NHTSA, “Consumer Information Regulations; Federal Motor Vehicle Safety Standards; Rollover Resistance”, Docket No. NHTSA-2001- 9663; Notice 2, 2001.
[7] Forkenbrock, G.J., and Garrott, W.R, "Phase IV and NHTSA's Light Vehicle Dynamic Rollover Propensity Research", NHTSA SAE Government / Industry Meeting, 2003. [PowerPoint slides]

## Slide 28: References
[8] Forkenbrock, G.J., "Public Workshop on Dynamic Rollover and Handling Test Techniques", NHTSA Vehicle Research and Test Center, 2002. [PowerPoint slides]
[9] NHTSA Office of Vehicle Safety Compliance, "Federal Motor Vehicle Safety Standards and Regulations". https://one.nhtsa.gov/cars/rules/import/FMVSS/index.html