## Slide 1
Prof. Vladimir V. Vantsevich
Lloyd Balfour, Graduate Research Assistant
Jesse Paldan, Research Assistant
Vehicle and Robotics Engineering Laboratory
University of Alabama at Birmingham
Week 4. Lecture 1
Experimental Testing of Vehicles
DAQ for Measuring Electrical Signals and
Recording Experimental Data in a Computer

## Slide 2
  DAQ Concepts
  DAQ Structures
  DAQ Components
  Input/Output
  Real-Time DAQ
Outline

## Slide 3
DAQ (Data-Acquisition):
Data Acquisition is the process of measuring an electrical or physical quantity (e.g. temperature, pressure, voltage, force, etc…) with a computer [1].
DAQ system:
It is the section of a measurement system that quantifies and stores data [2].
Computer biased DAQ systems are hybrid systems that combines a DAQ instrument with the microprocessor and the interface of capability of a PC (personal computer) [2].
  DAQ Concepts
Notes: DAQ Concepts page 283- [1]

## Slide 4
A dedicated microprocessor system can perform programming instruction to: measure, store data, interpret data, and provide process control without the need for interventions [2].
These microprocessors have I/O (input/ output) ports that interface with other devices to measure and output instructions [2].
  DAQ Concepts

## Slide 5
The interface between an external instrument (measurement device or more DAQ devices) and the PC is done either through the use of the following [2]:
I/O board
External serial communication port
Parallel communications port
External serial bus
Wireless port
  DAQ Concepts

## Slide 6
Figure 1: Typical signal and measurement scheme [2]
Figure 1 shows a schematic (elements represented as abstract-graphic symbols) of how a DAQ device would be implemented into a measurement scheme.
  DAQ Structures

## Slide 7
Figure 2: Signal flow scheme for an automated DAQ [2]
Figure 2 shows the schematic of a measurement scheme for multiple input signals routed into a single microprocessor or DAQ device [2].
  DAQ Structures

## Slide 8
Figure 3: Basic DAQ system [1]
A DAQ structure typically consists of at least 3 components, a sensor (sometimes refereed to as a transducer), DAQ device and a computer [1].
  DAQ Components
Notes: Components
Signal Conditioning ( filters and amplification)
Components for acquiring data

## Slide 9
Sensor
Sensor:
A sensor converts a physical identity into a measurable electric signal [1].
Depending on the type of sensor, its output can vary (e.g. voltage, current, pressure, stress etc…)
Figure 4: Computer representation of a sensor [1]
Figure 5: Throttle position sensor [3]
  DAQ Components

## Slide 10
DAQ Device:
The DAQ devices behaves as the interface between the computer and the signals from the external source (i.e input from the sensor) [1].
Figure 6: Medium-Channel-Count DAQ system [4]
Figure 7: High Channel-Count DAQ system [4]
  DAQ Components

## Slide 11
Figure 8: Picture of a desktop computer
  DAQ Components
Computer
The computer’s role is to control the operation of the DAQ device while processing, visualizing and storing the measurement data [1].

## Slide 12
Analog signals require some form of signal conditioning to accurately be interfaced with a digital system [2].
Conditioning a signal is manipulating the signal in order to prepare the signal for the next stage in processing (i.e. removing noise) [5].
This causes a need for more components to be added that can mitigate noise .
The most common components that are used for this process are Filters and Amplifiers [2].
  DAQ Components

## Slide 13
Analog Filters:
Analog Filters are used to control the frequency content of the signal that is being sampled [2].
Anti-alias Analog filters are a specific type of analog filters that remove any information above the Nyquist frequency before sampling [2].
Nyquist Frequency:
One half of the sample rate or sample frequency [2].
  DAQ Components
Notes: Nyquist frequency: One-half of the sample rate or
sampling frequency.

## Slide 14
Digital Filters:
Digital Filters are used to control the frequency content of the signal that is being sampled, however digital filters have better performance than analog filters.
  DAQ Components

## Slide 15
  DAQ Components
Amplifiers:
An amplifier is a electronic device that boost the power of an incoming signal.
This is carried out by changing the amount of gain present in the amplifier.
Gain
The gain is the factor by which an incoming signal is multiplied by in an amplifier [6].
Notes: Page 231 mechanical measurement . I don’t know why but the mechanical measurement book has a separate section of discus amplifiers ????!!!!!!! Why not have it under one section instead of splitting it into 3s

## Slide 16
Current Source
Interface to DAS
Figure 9: Basic shunt resistor circuit [2]
  DAQ Components
Shunt Resistor:
It is an electric circuit that convert current signals into voltage signals by using a shunt resistor [2].

## Slide 17
Figure 10: Picture of a circuit applying a null offset voltage [2]
  DAQ Components
Offset Nulling Circuit:
This type of circuit is used to subtract a small voltage from a signal as to zero out the transducer output signal [2].
This is accomplished by using a trim potentiometer () coupled to a bridge circuit [2].

## Slide 18
Figure 11: Picture of a four-channel Multiplexer [2]
A/D (Analog/Digital) converters will be discussed later on in the slides
  DAQ Components
Multiplexer:
A Multiplexer is a device that switches between connections one at a time of multiple signals connected to a single A/D converter [2].

## Slide 19
A/D Converter
Converts an analog signal to a digital signal [2].
D/A Converter
Converts a digital signal to an analog signal [2].
Figure 12: Block diagram of an A/D Converter [7]
Figure 13: Block diagram of a D/A Converter [7]
  DAQ Components

## Slide 20
Digital Input/Output Lines:
Digital Input/Output (I/O) Lines are used to communicate between instruments, control relays (to power the equipment on or off), or to indicate the status of a device [2].
  DAQ Components

## Slide 21
  DAQ Components
Closed-Loop Controller:
A Closed-Loop Controller is a controller that is used to compare the states of a process (as determined through the value of a measured variable) with the value of a set condition and being able to take appropriate action to reduce the difference in the value of the two [2].

## Slide 22
Input/output:
Defined as the communication between an information processing system (e.g. computer or human) and an external source (e.g. another computer, sensor, mouse, keyboard, etc…) [8].
I/O Devices:
The pieces of hardware or devices that are used as a means of communicating information to and from a processing system [8].
  Input/Output
Notes: Page 288 section 7.8( Analog I/O communication) to 7.9( Digital I/O communication). is 1 section that is two paragraphs on this Mechanical measurement
Picture form exp methods page 613 pdf

## Slide 23
Input devices vs Output devices:
The main differences between an input device from an output devices are:
Input devices send data to another device while not being able to receive data from another device [9].
Keyboards
Gas pedals
Brakes
Mouse
Examples:
Ignition
Buttons
Touch screen
Shift lever
  Input/Output

## Slide 24
Input devices vs Output devices:
Output devices receive data from another device but cannot send data to another device [9].
Monitor
Speakers
HUD (heads up display)
LED/ Headlights
Examples:
Speedometer
Haptic feedback
Vibrations
Artificial speech
  Input/Output

## Slide 25
Real time DAQ:
Real-Time DAQ is the melding of data acquisition and real-time computing.
In order to understand real-time DAQ, an understanding of real-time computing is needed.
Real-time computing:
Real-Time Computing is when hardware and software systems and or devices are subjected to a real-time constraints, (commonly referred to as deadlines) [10].
  Real-Time DAQ
Notes: In order to understand real-time DAQ, it seems that one must know real-time computing first, so I should describe real time computing and then say that real-time DAQ is just the melding of a DAQ system with a real-time computing system.
I found a handout that explains a little bit about real time DAQ system by using it with a kinetic inductance senor, I can use it as a handout to help explain.
Page I-4 data acquisition book
I can try this video from national instrument http://www.ni.com/webcast/1246/en/

## Slide 26
Real-time computing:
There are three major components that characterize real-time systems: time, reliability, and the environment [11].
Real Time
Time
Reliability
Environment
  Real-Time DAQ

## Slide 27
Time:
Time is not only the most important aspect of a real-time system, but also the most precious resource to manage.
The reason time is so important is that the accuracy of the measurement depends not only on the accuracy of the measurement but when it was measured.
The measured value must be taken and outputted into in a certain amount of time (commonly referred to as deadline) in order to be considered a real-time system
  Real-Time DAQ

## Slide 28
Reliability:
Reliability of the system is crucial due to error developing in the measured data that can cause false values.
Failure of a real-time system can have detrimental effects, for example: incorrect part selected for a device, economical loss, possible loss of humans lives, etc.… [11]
  Real-Time DAQ

## Slide 29
Environment:
The environment that the computer operates is an important component for any real-time system [11].
For example, consider a drive by wire throttle system:
The drive by wire system coupled with a computer is a real-time system, however if the real-time system is not implemented in a automobile then the real-time system is useless [11].
  Real-Time DAQ

## Slide 30
[1] National Instruments. What is Data Acquisition. 2017. Retrieved from: http://www.ni.com/data-acquisition/what-is/
[2] R. Figliola and D. Beasley. Theory and design for mechanical measurements, 5th edition. New Jersey: J. Wiley & Sons, Ic., 2011. Retrieved from: http://www.hljp.edu.cn/attachment/20120831082417983.pdf
[3] M. Davidson. Automotive Sensors. “Mark’s Corner-Auto Repair Help”. 2002. Retrieved from: http://www.auto-repair-help.com/automotive_maintenance/automotive_sensors.php
[4] National Instrument. Data Acquisition. Retrieved from: http://www.ni.com/data-acquisition/?cid=Paid_Search-70131000001RoxrAAC-United_States-Google_DC1_DAQ_Broad&gclid=CLvssPrVs9MCFVQ2gQodxe0PmA
  References

## Slide 31
[5] National Instruments. What is a Signal Conditioning. 2017. Retrieved from: http://sine.ni.com/np/app/main/p/ap/daq/lang/en/pg/1/sn/n17:daq,n21:11/fmid/2998/
[6] Keithley. Data Acquisition and Control Handbook. “ A Guide to Hardware and Software for Computer-Based Measurement and Control”, 1st edition. Cleveland, Ohio. Keithley Instruments Inc. 2001
[7] All About Circuits. Introduction to Digital-Analog Conversion. “Chapter 13- Digital-Analog Conversion”. 2003. Retrieved from: https://www.allaboutcircuits.com/textbook/digital/chpt-13/digital-analog-conversion/#
[8] Wikipedia. Input/output. 2017. Retrieved from: https://en.wikipedia.org/wiki/Input/output
  References

## Slide 32
[9] Computer Hope. What is the difference between an input and output device?. 2017. Retrieved from: http://www.computerhope.com/issues/ch001355.htm
[10] Wikipedia. Real-time Computing. 2014. Retrieved from: https://en.wikipedia.org/wiki/Real-time_computing#History
[11] K.G.Shin & P. Ramanathan. Real-Time Computing: A New Discipline of Computer Science and Engineering. IEEE. 1994. Retrieved from: https://kabru.eecs.umich.edu/papers/publications/1994/ramanathan-shin-ieee-proceedings.pdf
  References