## Slide 1
Prof. Vladimir V. Vantsevich
Jesse Paldan, Research Assistant
Lloyd Balfour, Graduate Research Assistant
Vehicle and Robotics Engineering Laboratory
University of Alabama at Birmingham
Week 2. Lecture 1
Experimental Testing of Vehicles
Calibration

## Slide 2
  Static and Dynamic Calibration
  Static Sensitivity
  Range
  Accuracy
  Precision and Bias Errors
  Outline

## Slide 3
What is Calibration?
It is the process of applying a known input value into the measurement system in order to observe the output value of the system [1].
I.e. it is the process of establishing a relationship between the input and the output values [1].
The known value that is used for the calibration is called the “standard” [1].
The types of Calibration
There are two type of Calibrations, Static and Dynamic.
Calibration

## Slide 4
Static Calibration
It is the calibration procedure where the values of the variable involved remain constant ( the values do not vary with time or space) [1].
In this procedure the known value is inputted into the system under calibration and the output is recorded after the input value has reached a steady state.
Static and Dynamic Calibration
Notes: Waiting until the test system stops varying its measured output. After there is not variation and the system achieves static equilibrium, then is the measured output variables recorded from the test. take the output variables from the test

## Slide 5
Measured Values
Curve fit,
One important note about static calibration: only the magnitudes of the known inputs and the measured output are important [1]. From only these two values the calibration can be implemented.
Figure 1: Static calibration plot [1]
The purpose of doing a static calibrations is to determine the static sensitivity
(also known as the proportional coefficient).
Static and Dynamic Calibration

## Slide 6
Static Calibration Procedure
Apply a known input value. Then wait until the test system stops varying its measured output. After there is no variation and the system achieves static equilibrium, then the measured output variables are recorded from the test. Repeat and continue for all other known input values
1. Apply a known input
2. Wait until the test system stops varying its measured output
3. Record the steady state value
4. Repeat and continue for other input values
Static and Dynamic Calibration

## Slide 7
Figure 2: Torsion test of a shaft
Example
A shaft is being tested in a torsion experiment as shown in Figure 2. When a load is applied to the shaft, it will experience a strain. The strain reading comes from the strain gauge
The reading from the strain gauge oscillates between a range of values when the load is first applied .
Static and Dynamic Calibration

## Slide 8
Figure 2: Torsion test of a shaft
Example Cont.
In order to do a Static calibration, wait until the strain values stop changing and until the system achieves static equilibrium.
When that happens, the system has been statically calibrated.
Static and Dynamic Calibration
Figure 2: Torsion test of a shaft

## Slide 9
Dynamic Calibration
It is the calibration procedure that determines the relationship between a known dynamic input value (a dynamic value is a value that is time and or space dependent) and the measured output [1].
Usually , this type of calibration involves applying a sinusoidal signal or step changes
Static and Dynamic Calibration

## Slide 10
Static Sensitivity
It is the ratio of the change in output to the change in input under static or steady state conditions [2]. It is also the slope of a static calibration curve.
Static Sensitivity Equation [1,2]
: the change in the input value
: the change in the output value
Static Sensitivity
Notes: A measurement system is a tool used for quantifying the measured
variable

## Slide 11
Range
It is the difference between the highest and lowest values.
There are two types of range, one range for the input values and another for the output values.
: range of the input values
: range of the out values
: the max input value
: the minimum input value
: the max output value
: the minimum output value
Range

## Slide 12
Error
Error (absolute error, sometimes referred to as true error) is the difference between the true value (output value with no error) and the measured value
Percent Error
Percent error (sometimes referred to as the true percent error) is the difference between the true value and the measured as a percentage of the true value.
Relative Error
It is the absolute error divided by the measured value. It gives an indication on how good of a measurement is relative to the size of the object being measured.
Accuracy and Error

## Slide 13
Error Equation
Relative Error Equation
Percent error equation
Relative Percent error equation
Accuracy and Error

## Slide 14
Example
Suppose that you were tasked with measuring the length of a shaft and a bolt and you came up with 49 inches and 15 inches respectively.
If the true values or the shaft and the bolt are 50 inches and 16 inches respectively, find the true error and the true percent error. Also calculate the relative error and relative percent error.
Accuracy and Error

## Slide 15
Solution
The true error for the shaft is :
The true error of the bolt is:
The true percent error of the shaft is:
The true percent error of the bolt is:
Accuracy and Error

## Slide 16
Solution cont.
The relative error for the shaft is :
The relative error of the bolt is:
The relative percent error of the shaft is:
The relative percent error of the bolt is:
Accuracy and Error

## Slide 17
Accuracy
Accuracy in general is how close the measurement value is to the true value( the exact value) I.e. it is the measurement of the lack of error.
The purpose of error being implemented is to represent both the inaccuracy and the imprecision( this term is discussed later on) of measured values [3].
Accuracy and Error

## Slide 18
Precision
Precision is the amount of deviation expected with repeated measurements [1]. Precision is also how closely individual measured values agree with each other [3].
Imprecision
Imprecision is the magnitude of the deviation, it is also called uncertainty [3].
Precision and Bias Errors

## Slide 19
Bias Error
Bias is an error in the execution or design of a test in which results are consistently distorted in a direction due to nonrandom factors [4]. I.e. it is a systematic deviation from the true value [3].
Bias is also commonly referred to as inaccuracy [3].
Precision and Bias Errors

## Slide 20
The black dots on each of the targets can be thought of as measured values
The bulls eye represents the true value.
Figure 3: Accuracy and precision [3]
Accuracy and Precision

## Slide 21
Inaccurate and imprecise
Accurate and imprecise
Inaccurate and precise
Accurate and precise
Accuracy and Precision
Figure 3: Accuracy and precision [3]

## Slide 22
is the static sensitivity
is the change in the output value
is the range of the input values
is the range of the out values
is the max input value
is the minimum input value
is the max output value
is the minimum output value
is the absolute error
is the relative error
is percent error
is the relative percent error
Nomenclature

## Slide 23
[1] R. Figliola and D. Beasley. Theory and design for mechanical measurements, 5th edition. New Jersey: J. Wiley & Sons, Ic., 2011. Retrieved from: http://www.hljp.edu.cn/attachment/20120831082417983.pdf
[2] J. Zhang. Information for Process Automation. Department of Chemical and Process Engineering University of New Castle. Retrieved from: https://www.staff.ncl.ac.uk/jie.zhang/ipa.pdf
[3] S. Chapra and R. Canale. Numerical Methods for Engineers, 7th edition. New York: McGraw-Hill Education, 2015.
[4] U. Sharma. Biases and erros in Epidemiology. Department of Community Medicine. Retrieved from: https://www.slideshare.net/jamesmacroony/bias-and-errors
References