## Slide 1
Prof. Vladimir V. Vantsevich
Jesse Paldan, Research Assistant
Lloyd Balfour, Graduate Research Assistant
Vehicle and Robotics Engineering Laboratory
University of Alabama at Birmingham
Week 1. Lecture 2
Experimental Testing of Vehicles
Measurement Systems: General Test Characteristics

## Slide 2
General Experimental Test Characteristics:
  Variables
  Parameters
  Noise and Interference
  Random Tests
  Replication and Repetition
  Outline

## Slide 3
Variables
What is a Variable?
A variable is an entity that influences a test [1].
There are two categories of a variable:
independent and dependent.
Independent Variable
If a change in variable X does not affect the value of another variable Y, then the two variables are considered independent of each other [1].
Dependent Variable
If a variable D is affected by the changes in one or more other variables, than variable D is considered a dependent variable [1].

## Slide 4
Example of Dependent and Independent Variables:
Axis of Rotation
Figure 1: FBD of a vehicle making a left turn
Centrifugal Force Equation
Outer wheel Friction Force equation
Inner wheel Friction Force equation
Variables

## Slide 5
Nomenclature:
m is the mass of the vehicle
is the speed of the vehicle
is the distance to the axis of rotation
is the friction force coefficient
is the centrifugal force
is the friction force of the outer wheel
is the friction force of the inner wheel
is the normal force of the outer wheel
is the normal force of the inner wheel
Variables

## Slide 6
Vehicle making a Left turn
For example, if a vehicle is making a left turn and the friction force of the wheels is greater than or equal to the centrifugal force, the vehicle will make the turn.
From the above equation, normal force will be affected by any change in the mass of the vehicle. This causes the Normal force to be a dependent variable.
From the above equation, the friction coefficient is independent of all the other variables. No changes in the other variables will affect the friction coefficient
Variables

## Slide 7
What is a controlled variable
A control variable is a variable that can be held at a specific constant value or at an initial condition value [1].
Controlling Variables
Completely control of a variable is typically not possible. The reason being is that in some case it is not possible to hold an exact initial value [1] .
Example of a controlled variable
One example is the steering angle of the front wheels of a vehicle during a fishhook maneuver. During a fishhook maneuver the steering angle of the wheels is specified at a certain profile while all the other variables vary (e.g. the distance to the center of rotation, the normal force of the wheel changes).
Variables

## Slide 8
Figure 2: Diagram of a fishhook maneuver [2]
Variables

## Slide 9
Video of a fishhook maneuver [3]
Variables

## Slide 10
Discrete Variable
A variable is discrete if its value can be enumerated [1]. This means that the values for a discrete variable are one to one. This allows the variable to contain no deviation.
Variables

## Slide 11
The outcome of a dice roll is a good example of a discrete value. If one where to roll two dice and get number 20 and 12, than those values would be considered a discrete number.
Figure 3: Two 20 sided dice
Example of a Discrete Variable
Variables

## Slide 12
Continuous Variables
Is any variable that values are able to change in a continuous manner [1].
Examples of Continuous Variables
One example of a continuous variable is stress of a part under a changing load [1]. Another example is the pressure in a tire of a vehicle. As the vehicle drives and the tires spins and generates heat, the pressure in the tire changes.
Variables

## Slide 13
Non-controlled Variables
Extraneous Variable
Extraneous variable are variables that cannot be controlled during the measurement (or experiment), but that also haves an affect on the variable being measured [1].
The Power of the Extraneous Variable
The extraneous variable can influence the results of any measurement if left unchecked. This variable can also affect the trend of the variable being measured resulting in false behaviors.
Variables

## Slide 14
Example on the Effect of Extraneous Variables
Figure 4: Boiling point of water [1]
The graph shown in Figure 3 shows 3 experiments done with the same process. However there are 3 different trend lines
Variables

## Slide 15
Figure 4. Boiling point of water [1]
What can caused the variation?
One variable that could have caused deviation in results is pressure.
Each test run had a different value for the atmospheric pressure which would affect the boiling temperature of water.
Variables
In this instance, the acting extraneous variable was the atmospheric pressure value which caused the variation in temperature.

## Slide 16
Example on the Effect of Extraneous Variables
Axis of Rotation
Figure 1: FBD of a vehicle making a left turn
Consider again a vehicle making a left turn.
Variables

## Slide 17
What can caused the variation in the test results ?
One variable could have caused any deviation in the test results will be the driver. When the vehicle is turning, the drive will not always maintain the same angle of turn. This will result in a change of vehicle’s trajectory path resulting in a deviation of the test results.
Example on the Effect of Extraneous Variables
Variables

## Slide 18
What is a Parameter?
It is a value that is a part of a function which establishes a relationship between variables.
Examples of some parameters:
Force equation as a function of acceleration:
Where the density () of the fluid and dynamic viscosity
() of the fluid are the parameters.
Velocity () and characteristic length (d) are the variables
Where the mass () of the function is the parameter and acceleration () is a variable
Parameters
Reynolds Number as a function
of velocity and length of fluid:

## Slide 19
How the extraneous variables affect measured data can be described as noise and interference.
What is Noise
Noise is the random variation of the measured value as an effect of the variation of the extraneous variable [1].
What does Noise do to the results
Noise causes an increase in the scatter of the data [1].
Figure 5: Signal with noise [1]
Noise and Interference

## Slide 20
Figure 5: Signal with noise [1]
Figure 6: Signal with no extraneous variables [1]
Noise and Interference

## Slide 21
What is Interference
Interference is any uncontrolled influence that causes the signal (or test outcome) to behave differently from its true behavior [1].
What does Interference do to the results
Interference imposes a different trend that can deviate from the test [1].
Figure 7: Signal with interference [1]
Noise and Interference

## Slide 22
Figure 7: Signal with interference [1]
Figure 6: Signal with no extraneous variables [1]
Noise and Interference

## Slide 23
What is a Random Test ?
It Is a measurement matrix that sets a random order to the change in the value of the independent variable [1].
Consider the example of a dependent variable as a function of several independent variables of
If the variable was also influenced by a group of extraneous variables where [1].
The function that is developed is
Random Test

## Slide 24
In order to find the dependence of on the independent variables, the independent variables values are varied in a controlled manner [1].
Doing this however does not eliminate the influence of the extraneous variables, . However by introducing different test strategy, false trends on the variable can be minimized .One of these strategy is called Randomization [1].
Random Test

## Slide 25
Randomization
It is the effect that the random order has on the results of the test [1].
How to use Randomization
To use Randomization, one has to randomize a test matrix to minimize the discrete influences [1]. Examples of discrete influences are : different test operators, different operating conditions, different testing equipment etc… .
This is done through the use of random blocks [1].
Block
A block is a data set of measured variables( a variable that has an assigned value) where the controlled variable is varied while the extraneous variable is fixed [1].
Random Test

## Slide 26
Example of Randomization
The below example is taken from reference [1].
For example, the manufacture of a particular composite material requires mixing a percentage by weight of an arbitrary binder with an arbitrary resin to produce a gel.
The gel is used to impregnate a fiber to produce the composite material in a manual process called the lay-up.
The strength, s, of the finished material depends on the percent binder in the gel.
However, the strength may also be lay-up operator dependent.
Formulate a test matrix by which the strength to percent binder–resin ratio under production conditions can be established.
Random Test

## Slide 27
What is known
The binder and operator are a function of the strength. This leads to the equation: [1]. Where σ is the dependent variable, the binder is the independent variable, and the operator is the extraneous variable.
The Assumption
The strength is only affected by the binder and operator [1].
Random Test

## Slide 28
The Solution
σ, the dependent variable, has to be tested against binder resin ratio, the independent variable. For the test, compare the relationship between three binder gel ( ) and the measured strength [1]. Next three operators ( are chosen to produce separate test samples for each of the 3 binder gel [1]. This gives the block test matrix below.
Figure 8: Block test pattern [1].
Random Test

## Slide 29
Conclusion
The result of each block includes each of the operator’s influence on the dependent variable σ ( strength) [1]. The test matrix that was made will randomize the influence of any one operator on the strength test result [1]. This is done by introducing the influence of several operators [1].
Random Test

## Slide 30
What is Replication
It is an independent duplication of a set of measurements using similar conditions [1].
What does Replication do
Replication allows the ability to control the operating conditions [1]. I.e. it allows for the ability to reset the conditions of desired values[1]. This allows for the ability to estimate how well one can duplicate a set of conditions [1].
Replication and Repetition

## Slide 31
What is Repetition
It is repeated measurements made during any single test run [1].
What does Repetition do
Repetition allows for the ability to quantify the variations in a measured variable as it occurs between different test, with each test having the same nominal operating conditions [1]. I.e. it represents how well control can be maintained during the test [1].
Note, however, that repetition will not assess how precise the operating conditions can be set [1]. Repetition only shows the variations in a measured variable.
Replication and Repetition

## Slide 32
The below example is taken from reference [1].
What if someone where to set the temperature of a room containing a furnace at a arbitrary value and periodically measure the value of the temperature for a set amount of time?
Someone would have come to a value for the average temperature and the variation of the temperature at the specific arbitrary temperature that the room was set at.
This test was conducted using repetition.
Replication and Repetition

## Slide 33
The below example is taken from reference [1].
Suppose the room temperature was changed to another value that was different from the value that was set previously.
After some time has pass, the room temperature was returned to the first original value. Resulting in the duplication of the measurements.
In this case the two sets of test data are replications of each other.
Replication and Repetition

## Slide 34
[1] R. Figliola and D. Beasley. Theory and design for mechanical measurements, 5th ed. New Jersey: J. Wiley & Sons, Ic., 2011. Retrieved from: http://www.hljp.edu.cn/attachment/20120831082417983.pdf
[2] E. Bob. “The Counterintuitive Truth About Roof Crush Standards”. 2006. Retrieved from: http://www.thetruthaboutcars.com/2006/06/the-counterintuitive-truth-about-roof-crush-standards/
[3] Sumesh Patil. Active Roll Control-Fishhook Test 70mph. 2013. Retrieved from: https://www.youtube.com/watch?v=VHcBPXa7y68
References