## Slide 1
ACADs (08-006) Covered
Keywords
Description
Supporting Material
Accident Analysis
2.1.1.1 | 2.1.1.2 | 2.1.1.3 | 2.1.1.4 | 2.1.1.5 | 2.1.1.6 | 2.1.1.7 | 2.1.1.8
2.1.1.9 |  |  |  |  |  |  | 

## Slide 2: Emergency Classification
Level of risk to the public.
4 emergency classifications:
    Notification of Unusual Event
    Alert
    Site Area Emergency
    General Emergency
Notes: Emergency Classification
Emergency Classification is a set of plant conditions which indicate a level of risk to the public. Nuclear power plants use the four emergency classifications listed below in order of increasing severity.
Notification of Unusual Event - Under this category, events are in process or have occurred which indicate potential degradation in the level of safety of the plant. No release of radioactive material requiring offsite response or monitoring is expected unless further degradation occurs.
Alert - If an alert is declared, events are in process or have occurred that involve an actual or potential substantial degradation in the level of safety of the plant. Any releases of radioactive material from the plant are expected to be limited to a small fraction of the Environmental Protection Agency (EPA) protective action guides (PAGs). Additional information regarding PAGs can be found on the EPA Web site at:http://www.epa.gov/radiation/rert/pags.html .Site Area Emergency - A site area emergency involves events in process or which have occurred that result in actual or likely major failures of plant functions needed for protection of the public. Any releases of radioactive material are not expected to exceed the EPA PAGs except near the site boundary.
General Emergency -A general emergency involves actual or imminent substantial core damage or melting of reactor fuel with the potential for loss of containment integrity. Radioactive releases during a general emergency can reasonably be expected to exceed the EPA PAGs for more than the immediate site area.*
Retrieved from: http://www.nrc.gov/reading-rm/doc-collections/fact-sheets/emerg-plan-prep-nuc-power-bg.html March 22, 2013

## Slide 3: Accident Analysis
Assessment :
systematic process aimed at ensuring that all relevant safety requirements are met, including:
    principal requirements
    plant equipment requirements
    plant systems design requirements
Notes:   the principal requirements: (e.g. sufficient defense in depth, accounting for the operating experience and safety research),
  plant equipment requirements (e.g. equipment qualification and consideration of the ageing and reliability of systems through redundancy and diversity)
  plant systems design requirements (e.g. specific equipments on the reactor core, reactor coolant system, containment and engineered safety features).

## Slide 4: Accident Analysis
According to the probability of its occurrence and potential consequences, an event may be classified as:
Anticipated Operational Occurrence (transient)
Design Basis Accident (DBA).

## Slide 5: Accident Analysis
Design-basis accident (DBA):
A postulated accident that a nuclear facility must be designed and built to withstand without loss to the systems, structures, and components necessary to ensure public health and safety.*
Beyond design-basis accidents (BDBA):
Accident sequences that are possible but were not fully considered in the design process because they were judged to be too unlikely.
Notes: As the regulatory process strives to be as thorough as possible, "beyond design-basis" accident sequences are analyzed to fully understand the capability of a design. *
*http://www.nrc.gov/reading-rm/basic-ref/glossary/design-basis-accident.html

## Slide 6: Accident Analysis
Complementary methods of safety analysis are used jointly in evaluating the safety of an NPP:
Deterministic
Probabilistic

## Slide 7: Accident Analysis
Deterministic safety analysis:
predicts the response of an NPP in specific predetermined operational states to postulated initiating events.
applies a specific set of rules and specific acceptance criteria.
focused on neutronic, thermohydraulic, radiological and structural aspects,

## Slide 8: Accident Analysis
Probabilistic safety analysis (PSA) combines
the likelihood of an initiating event
potential scenarios in the development of the event
its consequences into an estimation of core damage frequency
source term
overall risk arising from operation of the NPP.
number of event sequences can be very large.

## Slide 9: Accident Analysis
Two classes of radiation exposure effects:
1. Deterministic effects
  certain to occur under given conditions
2. Stochastic effects
  where the effect may or may not occur
Notes:   DE: certain to occur under given conditions (e.g. individuals exposed to several grays over a short period of time will definitely suffer Acute Radiation Syndrome); and
SE: where the effect may or may not occur (e.g. an increase in radiation exposure may or may not induce a cancer in a particular individual but if a sufficiently large population receive a radiation exposure above a certain level, an increase in the incidence of cancer may become detectable in that population).

## Slide 10: Federal Oversight
In the U.S.
  104 commercial nuclear power reactors are licensed to operate
  65 sites
  31 States.
Onsite and offsite emergency plans
Shared by the NRC and Federal Emergency Management Agency (FEMA).
  facilitated through a Memorandum of Understanding (MOU).
  The MOU is responsive to the President's decision of December 7, 1979:
    FEMA-- lead in overseeing offsite planning and response,
    NRC assist FEMA.
Notes: In the U.S.
  104 commercial nuclear power reactors are licensed to operate
  65 sites
  31 States.
For each site, there are onsite and offsite emergency plans to assure that adequate protective measures can be taken to protect the public in the event of a radiological emergency. Federal oversight of emergency preparedness for licensed nuclear power plants is shared by the NRC and Federal Emergency Management Agency (FEMA). This sharing is facilitated through a Memorandum of Understanding (MOU). The MOU is responsive to the President's decision of December 7, 1979, that FEMA take the lead in overseeing offsite planning and response, and that NRC assist FEMA in carrying out this role. The NRC has statutory responsibility for the radiological health and safety of the public by overseeing onsite preparedness and has overall authority for both onsite and offsite emergency preparedness.*
http://www.nrc.gov/reading-rm/doc-collections/fact-sheets/emerg-plan-prep-nuc-power-bg.html
retrieved March 22, 2013

## Slide 11: Federal Oversight
Reactor Oversight Process:
  NRC reviews emergency planning procedures and training.
    Regular drills
    Exercises
  Each plant owner is required to exercise its emergency plan once every two years
  Regular self-testing of emergency plans
Notes: s part of the Reactor Oversight Process, the NRC reviews licensees’ emergency planning procedures and training. These reviews include regular drills and exercises that assist licensees in identifying areas for improvement, such as in the interface of security operations and emergency preparedness. Each plant owner is required to exercise its emergency plan with the NRC, FEMA, and offsite authorities at least once every two years to ensure state and local officials remain proficient in implementing their emergency plans. Licensees also self-test their emergency plans regularly by conducting drills. Each plant’s performance in drills and exercises can be accessed through the NRC Web site at this address: http://www.nrc.gov/reading-rm/doc-collections/fact-sheets/emerg-plan-prep-nuc-power-bg.html

## Slide 12: Final Safety Analysis Report
FSAR is provided by applicant
Supports the NRC's approval and certification of the standard U.S. EPR design,
Divided into two parts (called "tiers"):
  The Tier 1 material :
    high-level information on the plant design.
  The Tier 2 document :
    more-detailed information on the plant design.
Notes: he applicant's final safety analysis report (FSAR) provides information to support the NRC's approval and certification of the standard U.S. EPR design, under the provisions of Title 10, Part 52, of the Code of Federal Regulations (10 CFR Part 52), "Licenses, Certifications, and Approvals for Nuclear Power Plants." The FSAR is divided into two parts (called "tiers"):
The Tier 1 material, which is derived from the more-detailed Tier 2 document, provides high-level information on the plant design. As such, it includes the principal performance characteristics and safety functions of the plant's structures, systems, and components (SSCs). It also includes inspections, tests, analyses, and acceptance criteria (ITAAC) to provide reasonable assurance that the as-built plant will operate in conformance with the combined license (COL), the provisions of the Atomic Energy Act, and applicable NRC regulations. In addition, the Tier 1 document identifies significant site parameters and requirements for significant interfaces between the standard U.S. EPR design and those aspects of the plant design that are site-specific.
The separate Tier 2 document provides more-detailed information on the plant design. This information is to be approved, but not certified, by the NRC.
Retrieved http://www.nrc.gov/reactors/new-reactors/design-cert/epr/reports.html March 22, 2013

## Slide 13: Accident management
1. set of actions during the evolution of a beyond design basis accident:
  (a) To prevent the escalation of the event into a severe accident;
  (b) To mitigate the consequences of a severe accident;
  (c) To achieve a long term safe stable state.
2. severe accident management:
mitigate the consequences of a severe accident
Accident management is essential to ensure effective defense in depth
Notes: http://www-pub.iaea.org/MTCD/publications/PDF/Pub1376_web.pdf

## Slide 14: Emergency Planning Zones
NRC defines two EPZ around each nuclear power plant.
  The plume exposure pathway EPZ extends about 10 miles in radius around a plant.
    Exposure and inhalation of the public to airborne radioactive contamination.
  The ingestion pathway EPZ extends about 50 miles in radius around a plant.
    ingestion of food and liquid that is contaminated by radioactivity.
Notes: For planning purposes, the NRC defines two emergency planning zones (EPZs) around each nuclear power plant. The exact size and configuration of the zones vary from plant to plant due to local emergency response needs and capabilities, population, land characteristics, access routes, and jurisdictional boundaries. The two types of EPZs are:
The plume exposure pathway EPZ extends about 10 miles in radius around a plant. Its primary concern is the exposure of the public to, and the inhalation of, airborne radioactive contamination.
The ingestion pathway EPZ extends about 50 miles in radius around a plant. Its primary concern is the ingestion of food and liquid that is contaminated by radioactivity.

## Slide 15: Protective Actions
The NRC's regulations are designed:
  to mitigate accident consequences
  to minimize radiation exposure
When a radiological emergency occurs, nuclear power plant:
  evaluate plant conditions
  make protective action recommendations.
  the state or local government agencies are responsible for making decisions on the actions
Notes: Protective Actions
The NRC's regulations are designed to mitigate accident consequences and minimize radiation exposure to the public through protective actions. When a radiological emergency occurs, nuclear power plant personnel evaluate plant conditions and make protective action recommendations to the state and local government agencies on how to protect the population. Based on the recommendation and independent assessment of other local factors, the state or local government agencies are responsible for making decisions on the actions necessary to protect the public and for relaying these decisions to the public.
Factors that affect protective action decisions include plant conditions, competing events, weather, evacuation times, shelter factors, how quickly an incident develops, how short-lived a release of radiation may be, and other conditions.

## Slide 16: Protective Actions
Factors that affect protective action decisions include:
  plant conditions,
  competing events,
  weather,
  evacuation times,
  shelter factors,
  how quickly an incident develops,
  how short-lived a release of radiation may be,
  other

## Slide 17: Evacuation, Sheltering
Protective measures :
    evacuation,
    sheltering,
    the prophylactic use of potassium iodide (KI), as appropriate.
  Under most conditions, evacuation may be preferred
  Under some conditions, people may be instructed to take shelter
  sheltering can significantly reduce a person’s dose
  Evacuations should be mapped to anticipate the path of the release.
Notes: Protective actions considered for a radiological emergency include evacuation, sheltering, and, as a supplement to these, the prophylactic use of potassium iodide (KI), as appropriate. Under most conditions, evacuation may be preferred to remove the public from further exposure to radioactive material. However, under some conditions, people may be instructed to take shelter in their homes, schools, or office buildings. Depending on the type of structure, sheltering can significantly reduce a person’s dose compared to remaining outside. In certain situations, KI is used as a supplement to sheltering.
Evacuation does not always call for completely emptying the 10-mile zone around a nuclear power plant. In most cases, the release of radioactive material from a plant during a major incident would move with the wind, not in all directions surrounding the plant. The release would also expand and become less concentrated as it travels away from a plant. Therefore, evacuations should be mapped to anticipate the path of the release. Generally as a minimum, in the event of a General Emergency, a two-mile ring around the plant is evacuated, along with people living in the 5-mile zone directly downwind and slightly to either side of the projected path of the release. This “keyhole” pattern (Figure 1) helps account for potential wind shifts and fluctuations in the release path (Figure 2). Evacuation beyond 5 miles is assessed as the accident progresses. Also in response to a General Emergency, people living in the remainder of the 10-mile zone will most likely be advised to go indoors to monitor Emergency Alert System broadcasts.

## Slide 18: Evacuation, Sheltering
General Emergency:
  Evacuation:
    a two-mile ring around the plant,
    the 5-mile zone directly downwind
    slightly to either side of the projected path of the release.
    Evacuation beyond 5 miles is assessed as the accident progresses.
  Sheltering:
    people living in the remainder of the 10-mile zone

## Slide 19: “Keyhole” covering 2-mile radius and downwind sectors
Notes: http://www.nrc.gov/reading-rm/doc-collections/fact-sheets/emerg-plan-prep-nuc-power-bg.html
Retrieved March 22, 2013

## Slide 20: Original and revised keyhole following wind shift
Original
Revised
Notes: http://www.nrc.gov/reading-rm/doc-collections/fact-sheets/emerg-plan-prep-nuc-power-bg.html
Retrieved March 22, 2013

## Slide 21: Use of Potassium Iodide
Another protective action in the 10-mile EPZ:
  potassium iodide KI:
    helps prevent the thyroid from absorbing radioactive iodine
    blocks the radioactive iodine from being absorbed by the thyroid gland
    reduces the risk of thyroid cancers and other diseases.
    does not protect against inhaled radioactive materials,
    does not offer protection from external exposure to radiation.
    risks and potential side effects:
      gastrointestinal disturbances, allergic reactions, and iodide goiter and hypothyroidism.
Notes: Another protective action in the 10-mile EPZ involves KI, a compound that helps prevent the thyroid from absorbing radioactive iodine, one of several radioactive materials that could be present in a release from a nuclear power plant accident. If taken within the appropriate time and at the appropriate dosage, KI blocks the radioactive iodine from being absorbed by the thyroid gland and reduces the risk of thyroid cancers and other diseases. KI does not protect against any other inhaled radioactive materials, nor will it offer protection from external exposure to radiation. The Food and Drug Administration (FDA) has determined that KI is a safe and effective drug when used for this purpose. However, there may be risks and potential side effects in using KI, including gastrointestinal disturbances, allergic reactions, and iodide goiter and hypothyroidism. Please consult your physician if you have questions on the potential side effects.
In January 2001, the NRC modified its regulations to include considering the use of KI, and, later that year, the FDA issued guidance on using the drug. As of February 28, 2005, 20 states have received KI tablets from the NRC for their populations within 10 miles of a nuclear power plant. These states are: Alabama, Arizona, California, Connecticut, Delaware, Florida, Maryland, Massachusetts, Mississippi, New Hampshire, New Jersey, New York, North Carolina, Ohio, Pennsylvania, South Carolina, Tennessee, Vermont, Virginia, and West Virginia. Illinois has its own KI program in place; therefore, 21 of the 34 states with populations within the 10-mile EPZ have KI. Further information on KI is available on the NRC Web site at:http://www.nrc.gov/about-nrc/emerg-preparedness/about-emerg-preparedness/potassium-iodide-use.html .

## Slide 22: Use of Potassium Iodide
NRC modified its regulations, January 2001
FDA issued guidance on using the drug.
As of February 28, 2005, 20 states received KI tablets from the
Illinois has its own KI program in place;
21 of the 34 states with populations within the 10-mile EPZ have KI.
Notes: NRC modified its regulations, January 2001,
FDA issued guidance on using the drug.
As of February 28, 2005, 20 states received KI tablets from the NRC Alabama, Arizona, California, Connecticut, Delaware, Florida, Maryland, Massachusetts, Mississippi, New Hampshire, New Jersey, New York, North Carolina, Ohio, Pennsylvania, South Carolina, Tennessee, Vermont, Virginia, and West Virginia. Illinois has its own KI program in place; therefore, 21 of the 34 states with populations within the 10-mile EPZ have KI. Further information on KI is available on the NRC Web site at:http://www.nrc.gov/about-nrc/emerg-preparedness/about-emerg-preparedness/potassium-iodide-use.html .

## Slide 23: Safety limit
Definition:
  “A restriction or range placed upon important process variables that are necessary to reasonably protect the integrity of the physical barriers that guard against the uncontrolled release of radioactivity.” *
Notes: http://www.nrc.gov/reading-rm/basic-ref/glossary/safety-limit.html

## Slide 24: Limiting safety system settings
Definition:
    Settings for automatic protective devices related to those variables having significant safety functions. Where a limiting safety system setting is specified for a variable on which a safety limit has been placed, the setting will ensure that automatic protective action will correct the abnormal situation before a safety limit is exceeded.
Notes: http://www.nrc.gov/reading-rm/basic-ref/glossary/limiting-safety-system-settings.html

## Slide 25: Safety Limits
Prevention of unacceptable releases of radioactive materials from the plant
Limits imposed on:
  temperatures of fuel and fuel cladding,
  coolant pressure,
  pressure boundary integrity
  other operational characteristics influencing the release of radioactive material from the fuel.
Protect the integrity of certain physical barriers
Notes: The concept of safety limits is based on the prevention of unacceptable releases
of radioactive materials from the plant through the application of limits imposed on the
temperatures of fuel and fuel cladding, coolant pressure, pressure boundary integrity
and other operational characteristics influencing the release of radioactive material from
the fuel. Established safety limits are to protect the integrity of certain physical barriers
that guard against the uncontrolled release of radioactive material. The safety limits
should be established by means of a conservative approach to ensure that all the uncertainties of safety analyses are taken into account. This implies that exceeding a single
safety limit does not always lead to the unacceptable consequences mentioned earlier.
Nevertheless if any safety limit is exceeded, the reactor should be shut down and normal power operation restored only after appropriate evaluation has been performed and
approval for restarting has been given in accordance with established plant procedures.*
http://www-pub.iaea.org/MTCD/Publications/PDF/Pub1100_scr.pdf March 22 2013

## Slide 26: Safety Limits
if any safety limit is exceeded:
the reactor should be shut down
normal power operation restored only
  after appropriate evaluation
  in accordance with established plant procedures.