## Slide 1
ACADs (08-006) Covered
Keywords
Gate, ball, butterfly, diaphragm, globe, regulate, throttle, back flow, relief, check valve, actuator, positioner, limit switch, bench set, valve stroke, positive seat.
Description
Supporting Material
1.3.1.7 | 1.3.9.2 | 2.1.6.1 | 2.1.6.2 | 2.1.6.4. | 2.1.7.1 | 2.1.7.2 | 2.1.7.6
5.2.1.10 | 5.4.1.4 | 5.4.3.5 |  |  |  |  | 
Notes: <number>

## Slide 2: Pneumatic Control Valves
Air Operated Valves
Motor Operated Valves
Manual Valves
Gate Valves
Globe Valves
Check Valves
Plug Valves
Butterfly Valves
Instrumentation
&
Controls
AOV Group
Mechanical
Motor Operated Valve Group
Electrical

## Slide 3: Prevent Events / Hazard Awareness for Air Operated Valves
Hazards include:
  Highly loaded springs, missile hazards
  Heavy parts, rigging issues
  Pinch points created by moving equipment
  Pneumatic loads
  Chemicals
  System pressure and heat
  Noisy, dirty and poorly lit work environments
  System interactions
  Configuration control
  Tagging issues

## Slide 5
Standards & Expectations
Procedure Use & Adherence

## Slide 6
Operation of the numerous
Valves in a Power Plant in
cases are far more dangerous
than fully realized, therefore
exercise the greatest care
when operating any Valve.
General Safety Rules

## Slide 7
Never stand directly in
front of a valve being
opened or closed
Escaping steam, air, or
Fluid may cause injury.
General Safety Rules
Packing may blow out.

## Slide 8
Valves located in difficult
access areas should
have considerations for a
means of escape.
General Safety Rules

## Slide 9
When turning Handwheel
of a Valve make certain the
Wheel and Stem only are
turning.
Bonnet may blow off
causing bodly injury.
General Safety Rules
Screwed Bonnet type
may turn with the Stem.

## Slide 10
Never use brute force to
close a Valve
Can damage Valve Disc or Seat.
General Safety Rules
Can break parts.

## Slide 11
Four principles functions of valves.

## Slide 12: Starting & Stopping
Gate Valves are the type best suited for this purpose. When open gate Valves permit fluid to move in a straight line through the Valve with a minimum restriction of flow and loss of pressure.
Notes: <number>

## Slide 13: Regulating or Throttling Flow
Globe Valves. The Disc construction of a globe valve permits closer regulation.
MAXIMUM
80
Notes: <number>

## Slide 14: Preventing Back Flow
Check Valves perform the single function of preventing flow in one direction. Positive flow keeps these valves open, and reverse flow closes the check automatically.
Notes: <number>

## Slide 15: Relieving Pressure
Safety or Relief Valves. They are usually spring loaded valves which open automatically when pressure exceeds a set limit.
Exit
Notes: <number>

## Slide 16: Types of valves
Globe Valves
Gate Valves
Plug valves
Check valves
Needle Valves
Ball Valves
Butterfly Valve

## Slide 17
Open and Close
Designed to regulate and throttle
Globe Valve

## Slide 18
Flow Path
SEATING IS PARALLEL TO LINE OF FLOW. SEAT AND DISC

## Slide 19
Gate Valve
Solid Wedge Disc

## Slide 20
Gate Valve
Split Wedge Disc

## Slide 21
Allows flow in one direction only.
Automatic in operation.
Check Valve

## Slide 22
Most Popular design
Very little resistance to flow.
Used where pressure drop is prime importance.
Not recommended were reversal of flow is frequent.
Swing Check Valve
Notes: <number>
a. Disc Slam - Sudden flow reversal which exerts shock on valve disc and seating surfaces.
b. Valve chatter - Fluctuation of disc due to change in differential pressure.

## Slide 23
Check Valve
Notes: <number>

## Slide 24
Needle Valve

## Slide 25
Butterfly Valves

## Slide 26
Open/close Operation
Low Head Loss
Not Designed for Throttling
Notes: <number>

## Slide 27: Valve Components
The area where disc/wedge closes on the valve body to stop or reduce flow.
Directs flow, and attachment component to system
Provides a seal between the stem and bonnet. Keeps pressure off packing when valve is open.
Body to bonnet seal.
Upper part of valve. Support for, yoke actuator, handwheel, etc..
Seal between the stuffing box and stem.
The location for packing to be placed.
Compresses packing..
Gland Flange is a one piece unit used to compress packing.
Follower consists of two separate pieces.
Bolted or threaded.
Support element connection between bonnet and handwheel.
Transfer motion of Handwheel to the disc.
Attached to disc by: Split Joint
Threaded
One piece
Pins/cotter keys.
Backseat
Stem
Gasket
Stuffing Box
Gland
Handwheel
Yoke bushing or stem nut
Yoke
Bonnet
Body
Wedge/Disc
Seat
Gland Flange/ Follower
Packing
Controls the movements of the disc.
Component part of the valve that opens or closes against the seat to start or stop flow.
Notes: <number>

## Slide 28
Plug Disc
Most Control Valves Are Globe Valves
Ball Disc
Composition Disc

## Slide 29
Valve
Actuator
Positioner
3 Major Parts of an Air Operated Valve

## Slide 30
Notes: <number>
Valve Flow Characteristics

## Slide 31: Diaphragm Actuators
The diaphragm type usually consists of a spring which opposes the air pressure applied against the diaphragm
Spring-less types of diaphragm actuators, in which controlled air pressure is applied to either side of the diaphragm, are also quite common. The piston type actuators are usually without springs.

## Slide 32
In which direction does this actuator fail?
What must you do before removing this?
Notes: <number>
The spring loaded diaphragm actuator consists of a diaphragm and a diaphragm plate connected to an actuator stem. The diaphragm is enclosed in a case into which the air pressure from a controller or positioner is applied. The air pressure on the diaphragm is opposed by a spring and the unbalanced force on the valve plug. The spring repositions the actuator stem and valve plug when the air pressure on the diaphragm decreases, until the force on the diaphragm, due to the air pressure, is equal to the force exerted by the spring and valve plug.
The adjusting spring allows external setting or adjustment of the initial spring compression. The spring force is adjusted so that the valve starts to open or close at the desired minimum pressure. The diaphragm areas must be large enough so that sufficient force is created to overcome the spring force and also the force on the valve plug. The actuator shown in Figure 7 is called direct-acting or "air to close" operation. If system safety requires the opposite action, "air to open" or failed closed, a reversed actuator is used and referred to as reverse-acting.

## Slide 33
Which way do each of these actuators fail?

## Slide 34
Which way does this valve fail?

## Slide 35
Arrangement of a Typical Air Supply for Pneumatic Actuators
Notes: <number>
Many control-valve actuators using positioners or volume boosters, receive air from a source separate from that supplying the controller. In such instances, a filtering system might be installed at the valve. The sump collects condensed moisture which can be drained out the bottom petcock. The filter, which is often a part of a pressure-reducing regulator, prevents the passage of viscous oils and particles of dirt.

## Slide 36: Purpose of a Valve Positioner
Convert low volume control air signal to a proportionally higher volume air pressure which is applied to an actuator to position the valve
Improves valve response time
Can be used to characterize valve response
The volume of air output from pneumatic controllers or I/P converters may not be sufficient to position the valve
More on positioners later

## Slide 37
Typical Piston Actuators: Piston actuators are usually smaller and slightly faster than diaphragm actuators but require higher pressure air. They can also handle hotter environments.
Notes: <number>
Piston actuators Piston actuators are generally used where the stroke of a diaphragm actuator would be too short or the thrust is too small. The compressed air is applied to a solid piston contained within a solid cylinder. Piston actuators can be single acting or double acting, can withstand higher input pressures and can offer smaller cylinder volumes, which can act at high speed.

## Slide 38
Notes: <number>
Pneumatic or Hydraulic Piston Actuators
Pneumatic or hydraulic piston actuators are used when the force required to position a valve or a damper is higher than that which can be provided by a diaphragm.
Usually no spring is required to absorb the force of the piston. Instead, the piston is double-acting (when fluid is admitted to one side of the piston, the fluid from the other side is allowed to pass out of the cylinder).
Since higher air or hydraulic pressures can be applied, a lower volume has to be displaced to and from the piston, thus causing an increase in speed of response to a control signal. They can also provide a much greater stem movement than a diaphragm actuator.
For on-off positioning, the cylinder can be loaded and unloaded by a simple solenoid valve but when it is desired to position the valve plug at any intermediate position, a positioner is required as is shown in the actuator on the left-hand side.

## Slide 39: Theory of Positioner Operation
Inputs are:
  Valve position
  Supply air (usually 20PSI)
  A valve position signal
    Either 3-15PSI or
    4-20ma
Output is a valve position
  Actually output is air pressure to the actuator

## Slide 40: Fisher 3582i Positioner

## Slide 41
Fisher 3582
Most common valve positioner at Palo Verde
Input: Either 3-15PSI or 4-20ma (if using a 3582i)
Feedback: Mechanical linkage with valve stem
Output: a valve position

## Slide 43
As with most valve operators, the 3582 can be set up for normally open valves, normally closed valves, and valves with a variety of flow characteristics depending on which cam is selected and how the positioner is calibrated.

## Slide 44: Valve Limit Switches
Provide remote indication of valve position
We use mostly Namco Snaplok Limit Switches
Environmentally qualified
Generally 2 switches per valve
Open switch – switch closed from the time the valve leaves open until about 95% open and powers the green light
Closed Switch – switch closed from the time the valve is about 5% open until full open and powers the red light

## Slide 45
Valve Position:
Fully closed

## Slide 46
Valve Position: Intermediate

## Slide 47
Valve Position:
Full Open

## Slide 48
Valve Position:
Fully closed
Valve Position: Intermediate
Valve Position:
Full Open

## Slide 49
Valve Limit Switches
The convention at Palo Verde:
Red light = Valve open
Green light = valve shut
Both lights lit = valve intermediate position
Limit switches are usually set up at 90% or 95% open and 5% or 10% open.
Be careful when working on limit switches as they work backward from what you may think.

## Slide 50
Valve Limit Switches
The convention at Palo Verde:
Red light = Valve open
Green light = valve shut
Both lights lit = valve intermediate position
Limit switches are usually set up at 90% or 95% open and 5% or 10% open.
Be careful when working on limit switches as they work backward from what you may think.

## Slide 51
Click to run a program to demonstrate valve limit switch configurations

## Slide 52: How to Stroke & Bench Set a Valve
Procedure: 30MT-9ZZ22 Calibration of Control Valves
Procedure: 39DP-9ZZ02 Air Operated Valve Program
Procedures: 39DP-9ZZ31 & ZZ33, AOV Diagnostic Testing & Analysis

## Slide 53: Bench Set
Refers to the spring compression setting required to ensure the actuator matches the given valve service conditions; initial force, unbalance force, seat load, travel
Bench Set is performed with the actuator stem disconnected from the valve stem

## Slide 54: Valve Stroke
The distance the plug or stem moves in order to go from a full-closed to a full-open position
A valve may be capable of traveling further than its nameplate ‘stroke’ distance

## Slide 55: Positive Seat
The process of ensuring the valve plug is securely positioned in the valve seat prior to setting stroke length
This establishes one of the two positive stops in setting valve stroke.
Bubble Tight is a term used in the industry to describe the ability of a control valve to completely shut off flow, but it is not a realistic standard
Control valves are not isolation valves

## Slide 56: Bench Set Precautions
Valve must be assembled with proper packing adjustment and no system pressure
Do not rotate the valve plug against the valve seat
Do not drop the valve plug on the valve seat
Disengage the hand jack
Personell Safety precautions

## Slide 57: Bench set a valve in class

## Slide 58: Industry Events
SOER 85-02 Valve Mispositioning Events
SOER85-03 Excessive Personnel Radiation Exposure

## Slide 59: Lab Exercises