## Slide 1: Class Problem 2a-1
Solve , for , if and .

## Slide 2: Ohm’s Law

## Slide 3: Ohm’s Law
Derive units for voltage and current
Define resistance
Define circuit
Recognize schematic diagrams of voltage sources and resistors
Define Ohm’s Law and use it to find the current passing through a resistor.
https://www.khanacademy.org/science/ap-physics-1/ap-circuits-topic/current-ap/v/circuits-part-1

## Slide 4: Electricity Review
-
Voltage (V) – potential difference between the strength of the electron supply and the electron shortage
Current (I) – net flow of electrons through a material
Resistance (R) – a measure of a material’s opposition to the passage of electric current
electron supply
electron shortage
+
What are the three components of electricity?

## Slide 5: Units for electric current: Amperes (Amps), A
The electric current, I, is the amount of charge passing a point per unit time.
Therefore,

## Slide 6: Units for voltage: Volts, V
Voltage is the measure of the amount of potential energy per electric charge or Coulomb.
Therefore,

## Slide 7: Energy is a measure of work (Units = Joules)
Recall:
One coulomb flows through each bulb
Voltage is doubled when two batteries are used.
The work done when two batteries are used is twice as much as the work done when one battery is used, even though the same number of electrons flow through each bulb.
Doubling the voltage doubles the work and gives off much more light.
3V
V
V
V

## Slide 8
Voltage / Water Pressure Analogy
depth of water between surface
of lake and surface of river
Glen Canyon Dam in Arizona, USA
The work done per gallon of water passing through a turbine will double (theoretically) when the water depth (pressure) is doubled.
Wikipedia
Likewise, the work done per Coulomb of charge passing through a resistor will double (theoretically) when the voltage is doubled.
voltage & pressure are both measures of a potential difference

## Slide 9: Current, Voltage and Resistance
Current (i): the quantity of electrons passing a given point in a given time. Coulombs/second = Amperes (A)
Voltage (v): electromotive force (emf) /pressure that drives the flow of charge. Arises from having a supply of electrons at a different energy state that that of the electron’s destination. Joules/Coulomb = Volts (V)
Resistance (r): the property of a material that describes how easily charge may pass through it. Volts / Ampere = Ohms ()
Rate of Flow
(like current)
Valve Partially Open
(like resistance)
Height (creating pressure)
(like voltage)

## Slide 10: Units for resistance: Ohms, Ω
Resistance is a measure of the frictional resistance encountered by electrons as they attempt to pass through a material.

## Slide 11: Units: Voltage, Current, Resistance
Component | Symbolic Representation | Unit | 
Voltage | V | Volts | 
Current | I | Amperes | 
Resistance | R | Ohms | Ω
Component | Symbolic Representation | Unit | 
Voltage | V | Volts | 
Current | I | Amperes | 
Resistance | R | Ohms | Ω

## Slide 12: Circuits
To induce current flow you must give it a path or closed circuit.
Creating a closed circuit:
  Causes the voltage to push the electrons to move.
  Tells electrons where to go (electron supply to electron shortage).
Components like resistors are included along the path.
  Incandescent bulbs act as resistors.
Circuit Diagrams
  We can draw diagrams to represent circuit components.
  Simple circuit: power source, resistive element, and conductive material.

## Slide 13: Circuit Diagrams
Power Source
DC power source
Resistor
Orientation does not matter. Can be in either direction
Conductor
Assumed resistance is zero
Schematic Diagrams & Symbols, Electrical Circuits (17:58): https://www.youtube.com/watch?v=Dl1gFBNa0Ik

## Slide 14: Ohm’s Law
Ohm’s Law relates voltage, current, & resistance to each other.
Consider a circuit that has the following values:
  Voltage = 5V
  Resistance = 100Ω
  Current = 0.05A
Do you see a relation among the values? (looking just at the numbers)
  V = 5V
  R = 100Ω
  I = 0.05A
Intro to Ohms Law (5:25): https://www.youtube.com/watch?v=_-jX3dezzMg

## Slide 15
Class Problem 2a-2: For the given circuit,
  Draw the circuit shown symbolically.
    Label voltage, current and resistance. The incandescent bulb can be treated as a resistor.
    The batteries are AA, and the bulb provides a 12Ω resistance.
  Determine the current delivered to the resistor.

## Slide 16: Solution
a.
b.
  6V
  (4 x 1.5V)
  12Ω
  I=?
So this circuit would have one-half an amp of current flowing through it.

## Slide 17: Ohm’s Law Summary
A Volt (a.k.a. Potential Difference) is a Joule of energy per Coulomb of charge.
An Ampere is a Coulomb per second.
Resistance is a measure of a material’s opposition to the passage of electric current. (measured in Ohms)
A circuit is a closed path that will allow current to flow.
Schematic diagrams are used to illustrate circuits.
Ohm’s Law states that voltage is equal to current (I) x resistance (R): V = IR