## Slide 1: Kirchhoff’s Voltage Law

## Slide 2: DISCLAIMER & USAGE
  This material is based upon work supported by the National Science Foundation's Advanced Technological Education Program under Grant No. 1801177.
  Any opinions, findings, and conclusions or recommendations expressed in this material are those of the author(s) and do not necessarily reflect the views of the National Science Foundation.
2

## Slide 3: Build the Series Circuit
color | digit
black | 0
brown | 1
red | 2
orange | 3
yellow | 4
green | 5
blue | 6
violet | 7
gray | 8
white | 9
470Ω
220Ω
9V
LOOP
Find a yellow, violet, brown resistor and a red red brown resistor.
470Ω
220Ω
Do you have to use the same rows as shown in the picture?
No, you can use any rows as long as the components are connected properly.
One loop, the resistors are in series
Build the circuit below, powered by the 9V power source (Vin).

## Slide 4: Use Multimeter to Measure Voltages Around Loop
(1) Measure across the power source and write down the value.
Dial set to DCV
What value for voltage do you expect?
Will it be exactly 9V?
Does everyone have the exact same value? Why or Why not?
Did anyone measure a negative value? Why?
Red and black leads of the multimeter are backwards. Recall, voltage is a measure of the potential difference between the strength of the electron supply and shortage. When the leads are backwards, you are measuring the difference in the wrong direction.

## Slide 5: Use Multimeter to Measure Voltages Around Loop
220Ω
470Ω
9V
Across the Power Source
Across the 220Ω Resistor
Across the 470Ω Resistor
ΔV1 ≈
ΔV2 ≈
ΔV3 ≈
ΔV1 - ΔV2 – ΔV3 ≈
A POWER SOURCE is a voltage RISE
A RESISTOR is a voltage DROP
(1)
(2)
(3)
Rises must balance drops
8.31V
2.65V
5.65V
0V
LOOP

## Slide 6: Build the Parallel Circuit
+
-
220kW
470W
9V
LOOP 1
LOOP 2

## Slide 7: Measure Voltages around Loops
+
-
220W
470W
9V
ΔV1 ≈
ΔV2 ≈
ΔV3 ≈
8.28V
8.28V
8.28V
LOOP 1
LOOP 2
ΔV1 - ΔV2 ≈
0V
ΔV1 – ΔV3 ≈
0V
(1) Across the Rise (Loop 1 & 2)
Rises balance drops in each loop
(2) Across the 470Ω Drop (Loop 1)
(3) Across the 220Ω Drop (Loop 2)

## Slide 8: Kirchhoff's Voltage Law (KVL)
220Ω
470Ω
9V
The algebraic sum of voltages around any closed loop in a circuit is zero.
Closed Loop:
Series Circuits:
ΔV = 2.87V
ΔV = 6.13V
9V is split between the two resistors
Larger voltage drop occurs at the larger resistor
Parallel Circuits:
9V is supplied to each loop
Resistor size does not influence how much voltage is around loop.
+
-
220W
470W
9V
ΔV = 9V
ΔV = 9V

## Slide 9: Implications of KVL
+
-
1000Ω
6V
500Ω
500Ω
500Ω
1000Ω
ΔV1
ΔV2
ΔV3
ΔV4
ΔV5
The voltage rise and drop are the same through each loop
Voltage splits for resistors in series
  If resistors are the same, voltage splits evenly
  If resistors are different, larger resistor has larger voltage drop

## Slide 10
Class Problem: For the circuit given find
  The overall voltage drop over the resistor in Loop1 and Loop 2
  The current that passes through the 20Ω resistor
  Equivalent resistance of the resistors only in Loop 2
  Current passing through the resistors in Loop 2 (Hint: use Ohm’s Law and the Req of the two resistors in the loop)
  The voltage drops across the 10Ω and the 15Ω resistors (Hint: current stays the same through both resistors)
10Ω
15Ω
20Ω
a. According to KVL
b.
c.
d.
e.