## Slide 1: Troubleshooting Your Multimeter

## Slide 2: DISCLAIMER & USAGE
  This material is based upon work supported by the National Science Foundation's Advanced Technological Education Program under Grant No. 1801177.
  Any opinions, findings, and conclusions or recommendations expressed in this material are those of the author(s) and do not necessarily reflect the views of the National Science Foundation.
2

## Slide 3: Is the dial set to the correct setting?
DCV – Measures DC Volts
ACV – Measures AC Volts
Ω – Measures Resistance
ACmA – Measures AC Current in mA (0-200mA)
– Tests Diodes
– Tests Continuity Between Two Points
Battery Load Test – Tests small batteries
DCmA – Measures DC Current in mA (0-200mA)
DC10A – Measures DC Current in MA (0-10A)
Red lead plugged in here to measure everything but DC10A
Black lead plugged into COM
Red lead plugged in here only when measuring current larger than 200mA

## Slide 4: Are the leads plugged in correctly?
Black lead should be plugged into the “COM” input jack. This is referring to ground.
Use this input jack when measuring or testing voltage (AC/DC), batteries, resistance, continuity, diodes, and small currents up to 200mA. This jack is more commonly used in our classes.
Use the “DC10A” input jack when measuring larger currents up to 10A. Dial should be turned to DC10A position.

## Slide 5: Did you blow a fuse?
Fuses get blown often when measuring current. It is okay if you blow a fuse; just replace it with a new one!
Fuses are blown most often when measuring current given these scenarios:
Current is greater than 200mA, but settings were used for less than 200mA.
Current is measured improperly (e.g., if measured like voltage across components instead of through the circuit).
Good Fuse
(Wire is straight)
Blown Fuse
(Wire is Broken)

## Slide 6: Pinchers vs Probes
Pinchers
Probes
Probes
Must hold with hands
Touch end of probe on wire/metal being measured
Pinchers
Hands free
Clip end of pinchers on on wire/metal being measured