## Slide 1: Using Flowcharts
Designing and Documenting Processes, Control Algorithms and Software

## Slide 2: Flow Charts
Definition / Types of Flow Charts / Examples
Flow Charting Symbols
Working with PowerPoint (to generate Flowcharts / Project Documentation)
Flow Chart Cooling Control Program

## Slide 3: Flow Charts
A flowchart is a type of diagram that represents a workflow or process.
A flowchart can also be defined as a diagrammatic representation of an algorithm, a step-by-step approach to solving a task.
Flowcharts are used in designing and documenting simple processes or programs.
https://en.wikipedia.org/wiki/Flowchart

## Slide 4
Refrigeration System Control Logic

## Slide 5: Program Flow Chart Symbols / Layout
Compute
Temperature
> Setpoint ?
Y
N
Read Thermistor
Void Loop
Turn Heater On
Loop
Start/End
Terminal
Connector/
Program Flow
Input / Output
Process/
Operation
Decision
1
Connector
1
See ANSI & ISO Standards

## Slide 6: Working in PowerPoint
Opening, Closing, Saving, Retrieving…
Chart Types / Formatting
Slide Size
Slide Master
Views: Normal, Slide Sorter
Header/Footer
Selecting Graphics, Text Boxes
Using Connectors
Grouping, Layering (Bring to Front, Send to Back…)
Windows Snip & Sketch Tool
Hot Links
Font Sizes

## Slide 7: Flow Chart the Cooling Control Program
int val;
float tempF;
float setpoint = 74.0;
void setup() {
Serial.begin(9600);
pinMode(7,OUTPUT);
Serial.print(setpoint);Serial.println("degf");
}
void loop() {
val = analogRead(5);
tempF = 0.2063*val-26.428;
Serial.print(" Analog = "); Serial.print(val);
Serial.print(" = "); Serial.print(tempF,3);Serial.println(" degF");
if (tempF > setpoint){
digitalWrite(7,HIGH);
Serial.println("The temperature is too hot! The fan is ON");
}
if (tempF <= setpoint) {
digitalWrite(7,LOW);
Serial.println("The temperature is comfortable. The fan is OFF");
}
}
Compute
Temperature
Initialize
Variables
Analog Read Thermistor
tempF > Setpoint ?
Void Setup
Setup
Print Fan Status
Turn Fan ON

## Slide 8: Rubric
Flow Chart Symbols used properly 10
Connectors indicate program flow 10
All major elements of the program captured 20
  Setup
  Void Setup
  Void Loop
  Inputs
  Outputs (to Serial Monitor, to/rom circuits)
  Decisions

## Slide 9
Compute
Temperature
> Setpoint ?
Y
N
Read Thermistor
Void Loop
Turn Fan ON
Loop
Void Setup
Set int, tempF and setpoint variables
Initialize Serial Monitor
Set Pin 7 Output – Fan Control
Print Temperature
Turn Fan OFF
<= Setpoint ?
Y
N