## Slide 1: Moving The Setpoint

## Slide 2: DISCLAIMER & USAGE
  This material is based upon work supported by the National Science Foundation's Advanced Technological Education Program under Grant No. 1801177.
  Any opinions, findings, and conclusions or recommendations expressed in this material are those of the author(s) and do not necessarily reflect the views of the National Science Foundation.
2

## Slide 3: Moving the Setpoint
Add a potentiometer to our cooling system to adjust the setpoint
Run sample code to verify that we can change the set point at which the cooling system turns on or off.

## Slide 4: Changing the Range
Right now we have to go into the Arduino to change our target value
We are going to wire a potentiometer that will tell the Arduino to change the range
VS

## Slide 5: Potentiometer Review
A potentiometer will change the amount of voltage across it.
3 pins
  V In
  Signal
  Ground
5V
Signal

## Slide 6: Adding a Potentiometer to the Cooling Circuit
We will add a potentiometer to allow us to adjust the temperature.
potentiometer
5V
Analog 3

## Slide 7: Cooling Control System
Build the circuitry and write a sketch that will accomplish these tasks:
  Use a potentiometer to set a setpoint value (74.0°F). The potentiometer should allow for a small range of setpoint values.
    Use the setpoint equation from earlier with a gain of 15% and an offset of 550.
    Convert the analog setpoint value into °F when you print it to your serial monitor for an easier to understand value. You also need it to be in °F for use throughout your sketch. You cannot compare an analog value to a °F value.
      For example: if (tempF > setpoint) where tempF is in °F and setpoint is in analog, the Arduino will not know the difference. It only sees values.
  When your thermistor reads a temperature value > the setpoint, turn a fan on.
  When your thermistor reads a temperature value < or = to the setpoint, turn the fan off.
  Use potentiometer to change the setpoint to 80.0°F. Everything else in your sketch should automatically update accordingly.
Remember to print all values on your serial monitor (setpoint, current temperature, etc)

## Slide 8: Cooling Control System Circuitry
5V
C
B
E
Digital pin 7
1kΩ
coil
normally open contacts
SPST relay
+
-
Vin
M
5V
analog input 5
10kW
transistor, relay, and motor
potentiometer
thermistor
5V
analog input 3

## Slide 9: Cooling Control System Circuitry
int val;
float tempF;
float setpoint = 74.0;
void setup() {
Serial.begin(9600);
pinMode(7,OUTPUT);
Serial.print(setpoint);Serial.println("degf");
}
void loop() {
val = analogRead(5);
tempF = 0.2063*val-26.428;
Serial.print(" Analog = "); Serial.print(val);
Serial.print(" = "); Serial.print(tempF,3);Serial.println(" degF");
if (tempF > setpoint){
digitalWrite(7,HIGH);
Serial.println("The temperature is too hot! The fan is ON");
}
if (tempF <= setpoint) {
digitalWrite(7,LOW);
Serial.println("The temperature is comfortable. The fan is OFF");
}
}
5V
C
B
E
Digital pin 7
1kΩ
coil
normally open contacts
SPST relay
+
-
Vin
M
5V
analog input 3
10kW
5V
analog input 5
R2
R1
transistor, relay, and motor
potentiometer
thermistor
Old Fan Cooling Program
Handout

## Slide 10
int val;
float tempF;
float setpoint = 74.0;
void setup() {
Serial.begin(9600);
pinMode(7,OUTPUT);
Serial.print(setpoint);Serial.println("degf");
}
void loop() {
val = analogRead(5);
tempF = 0.2063*val-26.428;
Serial.print(" Analog = "); Serial.print(val);
Serial.print(" = "); Serial.print(tempF,3);Serial.println(" degF");
if (tempF > setpoint){
digitalWrite(7,HIGH);
Serial.println("The temperature is too hot! The fan is ON");
}
if (tempF <= setpoint) {
digitalWrite(7,LOW);
Serial.println("The temperature is comfortable. The fan is OFF");
}
}
Modify this program we used to read the thermistor and turn the fan on and off previously per the directions below.
 Read potentiometer, compute with offset and gain, then convert to temperature
 Change logic to turn heat on when below setpoint and off when above setpoint (and turn on LED when heater is on).

## Slide 11: Cooling Control System Programming Tips
What is the first thing in your program?
What variables do you think you need? You may add more as you build the program.
Declaring variables
int val – for the value read in by the thermistor
float tempF – the temperature in °F that is converted from val
int dial – the value related to the position of the dial on the potentiometer
int setpointA – analog value of the setpoint that is set using potentiometer
float setpointF – converted value of the setpoint into °F
What needs to be put in the setup() function?
What components do you need to have in your loop() function?
Serial.begin(9600); & pinMode(7, OUTPUT);
Potentiometer and setpoint
Thermistor
Conditional statement if the temperature is greater than setpoint
Conditional statement if the temperature is less than or equal to setpoint

## Slide 12: Cooling Control System Programming Tips
What do you need to include in your sketch for the potentiometer and setpoint?
Read in analog value from the potentiometer dial.
Adjust the dial value to fit your narrowed setpoint range using gain (15%) and offset (500).
Convert the analog setpoint value to a °F value using inverted calibration equation.
Print the analog and °F values of setpoint onto your serial monitor (with labels).
What do you need to include in your sketch for the thermistor?
Read in analog value from the thermistor.
Convert the analog thermistor value to a °F value using inverted calibration equation.
Print the analog and °F values of temperature onto your serial monitor (with labels).
Variables associated with each section are provided in blue. You can use different variable names in your sketch.
dial
setpointA
setpointF
val
tempF

## Slide 13: Cooling Control System Programming Tips
What do you need to include in your sketch for the conditional statement if the temperature is greater than setpoint?
Conditional statement comparing the tempF and the setpointF.
Statement printed to the serial monitor that the temperature is too hot and the fan is on.
Turn the digital pin connected to the cascading switch circuit HIGH.
What do you need to include in your sketch for the conditional statement if the temperature is greater than setpoint?
Conditional statement comparing the tempF and the setpointF.
Statement printed to the serial monitor that the temperature is too hot and the fan is off.
Turn the digital pin connected to the cascading switch circuit LOW.
If (tempF > setpointF)
digitalWrite(7 , HIGH)
If (tempF <= setpointF)
digitalWrite(7 , LOW)

## Slide 14: Cooling Control System Sketch

## Slide 15
int val;
float tempF;
int dial;
int setpointA;
float setpointF;
void setup() {
Serial.begin(9600);
pinMode(7,OUTPUT);
}
void loop() {
dial = analogRead(5);
setpointA = 0.15*dial+500.0;
setpointF = 0.2063*setpointA-26.428;
Serial.print("setpoint = "); Serial.print(setpointA);
Serial.print(" = "); Serial.print(setpointF);Serial.println(" degF");
val = analogRead(3);
tempF = 0.2063*val-26.428;
Serial.print("thermistor val = "); Serial.print(val);
Serial.print(" = "); Serial.print(tempF);Serial.println(" degF");
if (tempF > setpointF){
digitalWrite(7,HIGH);
Serial.println("The temperature is too hot! The fan is ON");
}
if (tempF <= setpointF) {
digitalWrite(7,LOW);
Serial.println("The temperature is comfortable. The fan is OFF");
}
delay(500);
}
Cooling Control System Sketch