## Slide 1: Warehouse Operations
Warehouse and Inventory
Management – LOG 104
http://www.youtube.com/watch?v=Z2Bs0nqVyqs
Notes: <number>

## Slide 2: Typical Warehousing Activities
Receiving (unloading, verifying, inspecting)
Putaway, cross-docking
Order picking, replenishment
Sortation, packing
Shipping (verifying, loading)
http://www.youtube.com/watch?v=UFqgJhZbZsg&feature=related
Notes: <number>
In most warehouses, products are received and, if they cannot be cross-docked and immediately shipped out, are putaway into storage until they are needed to fill a customer’s order, at which time they are picked from storage, packed, sorted, and unitized, if necessary, and then shipped to customers.
A separate forward picking storage area can be used to enable more efficient order picking. It is replenished from a reserve storage area.
Periodically, partially filled storage locations containing the same type of item are consolidated into a single location to improve space utilization, items are moved to different storage locations to improve handling efficiency in a process termed rewarehousing, and the contents of storage locations are counted in order to verify the accuracy of inventory records in a process termed cycle counting.
Glossary:
Receiving. The process of unloading, verifying, inspecting, and staging of material transported to a warehouse in preparation for putaway or cross-docking, sometimes including sorting and repackaging of the material.
Putaway. The process of moving material from a receiving area to a storage location.
Cross-docking. The process of moving material from a receiving area directly to a shipping area without the storage of the material.
Reserve storage. An area intended for the storage of material in full pallet load sizes from which both forward picking areas are replenished and pallet orders and some case orders are picked.
Replenishment. The process of moving material from reserve storage to a forward picking area.
Forward picking. A storage area designed for efficient piece and case order picking that is usually replenished from reserve storage but sometimes directly from receiving.
Order picking. The process of removing material from storage in response to specific customer orders.
Sortation. The process of merging, identifying, inducting, and separating material to be conveyed to specific destinations.
Packing. The process of preparing a container for shipment.
Unitizing. The process of combining multiple smaller containers into a larger container that can be handled as a single unit load.
Shipping. The process of staging, verifying, and loading orders to be transported from a warehouse.
Rewarehousing. The process of moving items to different storage locations to improve handling efficiency.
Cycle counting. The process of counting the contents of storage locations in order to verify the accuracy of inventory records.

## Slide 3: Typical Warehousing Activities
Notes: <number>
Receiving
Unloading, verifying, inspecting and staging of material, disbursing material to storage
Prepackaging
Optional - Material broken down for storage/merchandising
Kitting
Putaway
Putaway to primary or reserve storage, materials handling, location verification, product placement
Storage
Physical containment of merchandise while it is awaiting demand
Replenish items in forward picking area
Order picking
Process of removing items from storage to met demand
Single order picking, batch picking, zone picking, wave picking
Packaging and/or Pricing
Optional part of picking process: combining items for shipment in containers, pricing with current prices
Sortation
Sorts batch picks, combines distributed picks
Unitizing and shipping
Checking orders for completeness, packaging in appropriate shipping containers, preparing shipping documentation, determining shipping charges, loading trucks

## Slide 4: Traditional Warehouse
Notes: May include all steps depending on configuration – forward picking area/reserve storage
<number>

## Slide 5: Receiving
Receiving introduces inventory into the warehouse and prepares it for storage or customer order fulfillment.
It is the process of unloading, verifying, inspecting, and staging of material transported to a warehouse in preparation for putaway or cross-docking, sometimes including sorting and repackaging of the material.
Physical receiving processes are largely driven by the nature of the goods being received, as well as the ultimate mission of the facility.
Initial processing of goods on the receiving dock generally consists of check-in and receipt verification. The degree of processing depends on the design of upstream and downstream processes and is driven by the relative capacity and productivity of the various processes.
Notes: <number>
Purchase orders (including shop orders and return authorizations) are sent to suppliers to authorize the shipment of material to the warehouse. In response to a purchase order, a supplier sends an advance shipment notice (ASN) to the WMS. The ASN contains information about the material contained in each movable unit (case, carton, pallet, etc.) contained in the shipment. Using SSCC, unique serial numbers can be assigned to each component at the time of its manufacture so that re-labeling is not required as part of the receiving function even when the material is not stored in the top-level container in which it is received.

## Slide 6: Receiving – 11 steps
Inbound trucker provides info about product and gets appointment for delivery
Advance shipping notice (ASN) received by warehouse
Trucker arrives and is assigned to receiving door
Vehicle is safely secured at dock
Seal is inspected and broken in presence of carrier representative
Load is inspected and either accepted or refused
Unitized merchandise unloaded
Loose merchandise unloaded
All unloaded material staged for count and final inspection
Proper disposal is made of damaged material
Load is stored in assigned location
Notes: 11 sequential steps – not all required, but should be considered
Inbound trucker provides info about product and gets appointment for delivery – advantages for warehouse? Obligation for trucker
Advance shipping notice (ASN) received by warehouse – ensures correct product delivered to correct place, putaway and pick tasks can be pre-planned, helps identify cross-docking opportunities
Trucker arrives and is assigned to receiving door
Vehicle is safely secured at dock
Seal is inspected and broken in presence of carrier representative – seal number on ASN
Load is inspected and either accepted or refused – initial inspection; example of fast-food chain testing fat content of hamburger;
Unitized merchandise unloaded
Loose merchandise unloaded
All unloaded material staged for count and final inspection
Proper disposal is made of damaged material – by previous agreement, may send back, or keep to recoup damages
Load is stored in assigned location
Some variations:
Blind receiving – receiver writes down quantity w/o looking at ASN; then compares to ASN; reconciliation required
Bar-code/RFID technology – inbound packages scanned and compared to ASN
Moving directly from vehicle to storage – no staging; used when experience show few problems with inbound vendors
Cross-docking
<number>

## Slide 7: Where is receiving
For production warehouse, receiving and shipping may be at different ends of building
For non-production warehouse separation of shipping and receiving not justified
  Dock space more flexible
  Good for crossdocking – adjacent doors or corner of building
  May be decentralized to be close to storage
Notes: <number>

## Slide 8: Receiving problems
Damage
In-transit theft
Collusion theft
Recycling pallets or other load unitizing devices
Improper handling of cross-docking
Failure to balance workload between receiving and other activities
http://crimeprevention.rutgers.edu/crime/emp_theft/warehouses/receiving/receiving.htm
Notes: Damage – refuse or segregate goods, camera good for this
In-transit theft /collusion theft - http://crimeprevention.rutgers.edu/crime/emp_theft/warehouses/receiving/receiving.htm
Recycling pallets or other load unitizing devices – procedure for doing this
Improper handling of cross-docking – moving materials into storage then immediately removed instead – waste of time and labor
Failure to balance workload between receiving and other activities – scheduling receiving and other functions to avoid “hurry up and wait”
<number>

## Slide 9: Receiving - Crossdocking
Part of a special type of Supply Chain
  Cross-dock is NOT an isolated entity
Principles:
  Where goods are received from suppliers
  Sorted without storage,
  Then efficiently moved to downstream customers in the supply chain
Cross—docking
The recipes for Success
John Vogt Pat ByrnesWWBC CorpSupply Chain Partners
28th Annual WERC Conference
May 3, 2005
Notes: A cross-dock is a facility in a supply chain, which receivesgoods from suppliers and sorts these goods into alternative groupings based on the downstream delivery point. No reserve storage of the goods occurs, and staging occurs only for the short periods required to assemble a consolidated, economical load for immediately onward carriage via the same mode as the receipt or a different mode.
<number>

## Slide 10: Why use Crossdocks
Most efficient method of moving goods from source to consumer
Least inventory method
Cost effective transport
Smallest space requirement and capital investment in facilities
Incorporates inbound delivery period into the order to delivery time.
With correct data input and real-time communications –allows for even more efficient continuous replenishment
Candidates:
  Single SU unit loads (per pallet/per case)
  Backorders
  Special orders
  Inter-DC transfers
  Customer-ready loads i.e store-ready pallets
Notes: <number>

## Slide 11: Crossdocking at Consolidated Freightways
Like many LTL crossdocks, this one is a narrow rectangle surrounded by doors at which trailers are parked to exchange freight.
Freight has been docked in the center of the floor, while forklift trucks drive along the walls to carry freight to the appropriate departing trailers.
Copyright © John J. BARTHOLDI, III. All Rights Reserved. Last modified: Sun Mar 26 09:56:22 EST 2006

## Slide 12: Crossdocking at Costco
Pallets in Receiving queue
Store numbers above shipping doors
The transfer area

## Slide 13: Crossdock shapes
FEDEX Freight in Atlanta
H shape in Detroit
Roadway Chicago
Notes: Less than 150 dock doors – best configuration is rectangle – minimizes labor costs and loses no door capacity to inside corners
150-250 dock doors – best configuration T-shape – forfeits some of its best door positions to inside corners, worst doors are closer to the center than I the I-shape
250+ - H-shape best – worst doors are not too far from the center
<number>

## Slide 14: Putaway
Putaway is the process of moving material from the receiving area to a warehouse's storage, replenishment, or pick area or, in the case of cross-docking, directly to the shipping area.
Direct putaway is most efficient
Secondary putaway involves staging then putaway
Notes: <number>

## Slide 15: Putaway methodologies – informal system
Product stored wherever there is space, no record of where stored
Warehouse personnel need to have good memory
May be good for small warehouse with small number of SKU’s, few storage locations, few # of employees
Notes: May be arranged so that each person is responsible for single product area – problems?
Advantages: no maintenance, no cost, flexible
Disadvantages: Difficult to locate product, Dependent on one person’s knowledge, inefficient
<number>

## Slide 16: Putaway methodologies – Fixed Location System
Every part has location and every location has its part
Each SKU has unique and specific location in warehouse
Best suited to small warehouse, small # of SKU’s, and small # of employees
Notes: Advantages: easy to establish and maintain
Disadvantages: poor space utilization
must leave space for products not in stock
must size locations for maximum stock
difficult to expand
difficult to memorize storage locations
<number>

## Slide 17: Putaway methodologies – Part number system
Hybrid of fixed location methodology
Products assigned locations based on sequence of part numbers (A12 comes before B12)
Suited for companies with consistent part number and part number demand
Good for operations where volume and frequency distributed among products
Notes: Advantages:
easy to find product
product readily accessible
easy to set-up
Disadvantages:
not flexible
difficult to adjust for demand volumes
addition of products requires shifting of all subsequent items
poor space utilization
<number>

## Slide 18: Putaway methodologies – Commodity System
Groups items by product type
Within each group, products arranged by fixed, random, or part number
Good for warehouse where there is “shopping” of products
Notes: Advantages:
products grouped in logical manner
can increase picking efficiency
improved flexibility
Disadvantages:
easy to pick right type but wrong product
must have commodity knowledge to retrieve products
space utilization is better but not optimal
difficult to categorize some products
<number>

## Slide 19: Putaway methodologies – Random Location system
Product located in various places in warehouse where there is room (may be limited by physical constraints or storage zones)
Formal records must be kept and maintained!
Good for warehouses with dynamic demands and SKU offerings
Notes: Advantages:
space utilization is excellent
most flexible of all systems
Easy to expand
Easy to understand
Disadvantages:
requires detailed records
discipline to maintain records
<number>

## Slide 20: Putaway methodologies – Combination Method
Utilize combination of all methods to meet demands of different types of products
E.g. in same warehouse
  Store hazardous chemicals away from other products using fixed location system
  Store other items where space is constrained using fixed location system
Notes: Advantages:
flexible
uses best of all methodologies
can customize based on the warehouse
control is good
expansion is easy
Disadvantages:
more than one system can confuse users
space utilization can be compromised
<number>

## Slide 21: Product slotting
Item Activity Profile optimizes product placement for putaway, order-picking and retrieval.
Slotting involves grouping products by
  Storage environment families – by temperature, flammability, hazardous storage
  Order completion zones - Can create a warehouse within a warehouse for highly efficient order picking
  Storage modes – determine least cost storage mode for item picking productivity, density, picking error rates, system investment
  Activity zones – assign the most popular items to the most accessible warehouse locations
    Fast movers are placed nearest the receiving/shipping truck docks, or closest to the floor. This minimizes the distances traveled daily by material handling equipment.
    Slow movers are located at points furthest from outbound shipping docks or farthest from the floor. This insures that lengthy horizontal moves by material handling equipment are minimized.
    Within a storage mode, activity suggests the location of the items in a storage mode, fastest moving items located in the golden zone (close to the aisle or near waist level), medium movers in the silver zone, and slow movers in the remaining spaces
  Ongoing process – products must be continually reslotted as activity changes
Notes: The Pareto principle (also known as the 80-20 rule, the law of the vital few and the principle of factor sparsity) states that, for many events, 80% of the effects comes from 20% of the causes. Business management thinker Joseph M. Juran suggested the principle and named it after Italian economist Vilfredo Pareto, who observed that 80% of income in Italy went to 20% of the population. It is a common rule of thumb in business; e.g., "80% of your sales comes from 20% of your clients."
It is worthy of note that the usual applications of the Pareto principle are appeals to a pseudo-scientific "law of nature" usually relied upon to bolster non-quantifiable or non-verifiable assertations that are "painted with a broad brush". The fact that hedges such as the 90/10, 70/30, and 95/5 "rules" exist is sufficient evidence of the non-exactness of the Pareto principle. On the other hand, there is adequate evidence that "clumping" of factors does occur in most phenomena.
The Pareto principle is only tangentially related to Pareto efficiency, which was also introduced by the same economist, Vilfredo Pareto. Pareto developed both concepts in the context of the distribution of income and wealth among the population.
The observation was in connection with income and wealth. Pareto noticed that 80% of Italy's wealth was owned by 20% of the population. He then carried out surveys on a variety of other countries and found to his surprise that a similar distribution applied.
It also applies to a variety of more mundane matters: we wear our 20% most favoured clothes about 80% of the time[citation needed], we spend 80% of the time with 20% of our acquaintances[citation needed] etc.
The Pareto principle has many applications in quality control. It is the basis for the pareto chart, one of the key tools used in total quality control and six sigma. The Pareto principle serves as a baseline for ABC-analysis and XYZ-analysis, widely used in logistics and procurement for the purpose of optimizing stock of goods, as well as costs of keeping and replenishing that stock.
In computer science the Pareto principle can be applied to resource optimization by observing that 80% of the resources are typically used by 20% of the operations[citation needed]. In software engineering, it is often a better approximation that 90% of the execution time of a computer program is spent executing 10% of the code (known as the 90/10 law in this context).
<number>

## Slide 22: The golden zone – a forward-pick area of a warehouse
A fast-pick or forward pick area is one from which it is most efficient to pick, but which must be restocked from a reserve or overflow or bulk storage area. Here are some examples of forward pick areas:
  Carton flow rack that is restocked from bulk storage
  The ground floor of pallet rack that is restocked by moving pallets down from higher levels
  Carousels, A-frames, or any other specialized equipment that must be replenished from elsewhere in the warehouse
The forward-pick area is the most important real estate in a warehouse because it is the most convenient from which to pick. Moreover, it may represent considerable capital investment for special equipment.

## Slide 23: Replenishment
Replenishment is the process of moving material from reserve storage to a forward picking area so that it is available to fill customer orders efficiently.
Other types of in-plant moves include:
  Consolidation: the process of combining several partially filled storage locations containing the same type of item into a single location or several orders into a single shipment.
  Rewarehousing: the process of moving items to different storage locations to improve handling efficiency.

## Slide 24: Order Picking
Usually driven by a order processing function which generates picking order
Includes any retrieval of goods from storage
  Pallet picking
  Layer picking
  Case picking
  Split case picking
  Broken case picking

## Slide 25: Why is Order Picking Important?
Order picking is the most critical activity in most warehouses because it is the point at which customer expectations are actually filled.
Order picking represents 55% of all operating costs in a typical warehouse
Notes: <number>
While the process of placing the fewer large unit loads into a warehouse is usually mechanized, the process of picking the many small items from a warehouse is often very labor intensive. This makes order picking the most costly warehousing activity.

## Slide 26: Pick Slot Storage Types
System | Description | Pros | Cons
Static Storage Pallet Rack Shelving | System in which the product does not move on its own. The most common storage equipment used is the selective pallet rack (single deep) and the steel shelving unit. Storage by size and popularity is critical. | appropriate for the storage and picking of all but the most popular products, initial low investment | excessive travel time, ineffective control system
Dynamic Storage Carton Flow Pallet Flow | System in which the product flows by gravity (gravity conveyor or air flotation rails) to present a unit of material to the picker at a specified location. There are two basic variations: Carton Flow, used for broken case picking and Pallet Flow Rack, used for case picking. | relatively small picking face, reduced size of zone and travel distance | substantial equipment costs, replenishment costs (labor)
Example
Carton Flow
Example
Pallet Rack
Replenish
Pick

## Slide 27: Order Picking Handling Systems
Man-to-Part: Traditional material handling approach to order picking that requires the picker to travel to the storage location
System | Description | Pros | Cons
Pick to pallet | The picker operates an industrial truck with a pallet and commonly used for case picking and broken case picking. | access to hi-rise shelving | least productive order picking method
Pick to cart | The picker operates a push cart or powered cart. | improved productivity with computer control and radio communication capabilities, able to handle large orders and long distances | restricted access to storage levels that can be reached from the floor
Pick to belt | The picker is assigned a zone along a. conveyor where he places picked items. Commonly used with flow rack storage and requires sortation by customer order before shipping |  | 
Man-aboard Storage / Retrieval | The picker rides a captive aisle storage/retrieval machine that rides on a rail and is powered by an electric bus overhead. | reduces travel time | flexibility of being able to move between storage aisles
Example
Carton Flow & Pick to Belt
Broken Case
Full Case

## Slide 28: Order Picking Handling Systems (continued)
Part-to-Man: Material handling system in which the part is delivered via carousels, conveyors, and storage/retrieval systems to the picker
System | Description | Pros | Cons
Horizontal Carousels | Storage bins that rotate horizontally on a track under electric motor power | improved cube utilization, full utilization (no waiting, no traveling) | substantial equipment costs; cannot pick & replenish simultaneously
Vertical Carousels | Storage shelves that rotate vertically, always presenting a shelf to the picker at waist level. | excellent for space utilization and organization when storing small volume, small items | substantial equipment costs; cannot pick & replenish simultaneously
Automatic Storage & Retrieval System | Hybrid of the carousel and S/R modules that store and retrieve containers under computer or operator directed control |  | substantial equipment costs
Example
Horizontal Carousel

## Slide 29: Picking Control Methods
System | Description | Pros | Cons
Paper Picking | A printed pick list that includes SKU’s and locations |  | higher likelihood of picking errors; requires manual pick confirmation
Label Picking | A bar coded label is printed for each SKU or full case with correct location address, SKU identity, and customer order number. | reduces likelihood of counting errors, improves productivity | 
Pick-to-Light | The use of a visual display/audio instructions to visually lead the picker through the process of picking each line in the assigned zone. | paperless picking, order accuracy | 
Voice-directed picking | Audio instructions on items to pick | paperless picking, order accuracy, multi-lingual | 
Radio Frequency (RF) Units | The use of onboard and hand-held terminals displaying picking instructions via RF data communication links from the picker to the control computer in real-time. Also provides a means of confirming or correcting picking orders. | reduced travel time and delays, high order accuracy | 
http://www.bing.com/videos/watch/video/warehouse-pick-pick-by-light-picking-system-warehouse-order/495729193633b3bc508f495729193633b3bc508f-612978852498?q=order-picking&FROM=LKVR5&GT1=LKVR5&FORM=LKVR13
http://www.youtube.com/watch?v=KWUfpznbb5k&feature=related
http://www.youtube.com/watch?v=lWsMdN7HMuA&feature=related

## Slide 30: Order Picking Methodologies
Release Method | Description | Pickers Per Order | Line Items Per Pick | Periods per Shift | Pros | Cons
Discrete Picking | One person picks one order, one product at a time. Orders are not scheduled and may be picked at any time on a particular day. | Single | Single | Single | simple, risk of picking errors of omission is reduced, provides fastest response in a service window environment, picking accuracy accountable to a single person, little coordination with other pickers required, no space required for order consolidation, and relatively low control system sophistication required | least productive, excessive travel time, relatively low number of orders picked simultaneously, greater risk of picking area congestion
Zone Picking | The total pick area is organized into distinct zones managed by one person responsible for picking all lines for each order for that zone. Two variations of zone picking include: Sequential zone picking, when the order is passed from one zone to the next, one at a time. Simultaneous zone picking, when the order is consolidated in a designated location after zone picking is done from all applicable zones independently. | Multiple | Single | Single | flexible with different skills or equipment associated with a hybrid warehouse, reduced travel time/congestion/delays due to the ability to further subdivide zones, relatively high number of orders picked simultaneously, reduced picking area congestion | Multiple pickers accountable for picking accuracy, high coordination with other pickers required, space and coordination required for order consolidation
Notes: Discrete – One person picks one order, one line at a time, one order period per shift; orders not scheduled – may be picked at any time
Advantages: Simplest – one picking document
Errors of omission reduced
service window – provides fastest response
accountability clear-cut
Disadvantages: least productive
travel time might be excessive
Zone – Total pick area organized into zones – 1 person assigned to each zone; picker in each zone picks one line item at a time for each order in zone, working on only one order at a time; lines from each zone brought to order consolidation area; can be sequential (pick and pass) or independent picking then consolidation
Often used because of different equipment in a warehouse with multiple types of equipment. One order may include items from static high-rise shelving + picking from horizontal carousels (Honda distribution warehouse)
Batch – One picker picks a group of orders at the same time, one line at a time. A product on more than one order is picked all at one time, then segregated by order. Segregation may happen while picking into totes, or transported to a designated area where they are sorted by individual order
Advantages: High productivity due to reduced travel time
best candidates are orders with 1-4 lines and small cube
Disadvantages: measures need to be taken to minimize picking and sorting errors
computer control systems and auto sortation almost necessary but very effective
Wave picking – similar to discrete picking except that a selected group of orders are scheduled during a specific planning period, good for coordinating picking and shipping functions
Zone-Batch picking – each picker assigned a zone and picks a part of one or more orders, one scheduling period in each shift
Zone-wave picking – each picker assigned a zone and picks al lines for all orders stocked in the assigned, one order at a time, multiple periods per shift
Zone-Wave-Batch picking – each picker assigned zone and picks all lines for all orders stocked in the assigned zone, picking more than one order at a time with multiple scheduling shifts per period
<number>

## Slide 31: Order Picking Methodologies (continued)
Release Method | Description | Pickers Per Order | Line Items Per Pick | Periods per Shift | Pros | Cons
Batch Picking | One picker picks a group of orders at the same time, one line at a time. | Single | Multiple | Single | greater productivity, best for orders with few (1-4) lines and small cube, reduced travel time, drastically reduced picker travel time, very high number of orders picked simultaneously | risk of picking and sorting errors, coordination required between bulk picking and individual order sortation , individual order processing time dependent upon total batch processing time, space required for individual order sortation, residual product handling can be relatively high, relatively high control system sophistication
Wave Picking | One picker picks one order one line at a time however a selected group of orders are scheduled to be picked during a specific planning period | Single | Single | Multiple | better coordination with shipping | Risk of productivity loss if shipping schedule is unbalanced
Notes: Discrete – One person picks one order, one line at a time, one order period per shift; orders not scheduled – may be picked at any time
Advantages: Simplest – one picking document
Errors of omission reduced
service window – provides fastest response
accountability clear-cut
Disadvantages: least productive
travel time might be excessive
Zone – Total pick area organized into zones – 1 person assigned to each zone; picker in each zone picks one line item at a time for each order in zone, working on only one order at a time; lines from each zone brought to order consolidation area; can be sequential (pick and pass) or independent picking then consolidation
Often used because of different equipment in a warehouse with multiple types of equipment. One order may include items from static high-rise shelving + picking from horizontal carousels (Honda distribution warehouse)
Batch – One picker picks a group of orders at the same time, one line at a time. A product on more than one order is picked all at one time, then segregated by order. Segregation may happen while picking into totes, or transported to a designated area where they are sorted by individual order
Advantages: High productivity due to reduced travel time
best candidates are orders with 1-4 lines and small cube
Disadvantages: measures need to be taken to minimize picking and sorting errors
computer control systems and auto sortation almost necessary but very effective
Wave picking – similar to discrete picking except that a selected group of orders are scheduled during a specific planning period, good for coordinating picking and shipping functions (Peapod example)
Zone-Batch picking – each picker assigned a zone and picks a part of one or more orders, one scheduling period in each shift
Zone-wave picking – each picker assigned a zone and picks al lines for all orders stocked in the assigned, one order at a time, multiple periods per shift
Zone-Wave-Batch picking – each picker assigned zone and picks all lines for all orders stocked in the assigned zone, picking more than one order at a time with multiple scheduling shifts per period
<number>

## Slide 32: Order Picking Methodologies (continued)
Release Method | Description | Pickers Per Order | Line Items Per Pick | Periods per Shift | Pros | Cons
Zone-Batch Picking | Each picker is assigned a zone, and will pick a part of one or more orders, depending on which lines are stocked in the assigned zone. | Multiple | Multiple | Single | Potential for higher productivity | requires more control due to complexity in nature
Zone-Wave Picking | Each picker is assigned a zone, and picks all lines for all orders stocked in the assigned zone. | Multiple | Single | Multiple | Potential for higher productivity | requires workload balancing between pick zones
Zone-Batch-Wave Picking | Each picker is assigned a zone, and picks all lines for orders stocked in the assigned zone. | Multiple | Multiple | Multiple | Potential for higher productivity | requires more control due to complexity in nature
Notes: Discrete – One person picks one order, one line at a time, one order period per shift; orders not scheduled – may be picked at any time
Advantages: Simplest – one picking document
Errors of omission reduced
service window – provides fastest response
accountability clear-cut
Disadvantages: least productive
travel time might be excessive
Zone – Total pick area organized into zones – 1 person assigned to each zone; picker in each zone picks one line item at a time for each order in zone, working on only one order at a time; lines from each zone brought to order consolidation area; can be sequential (pick and pass) or independent picking then consolidation
Often used because of different equipment in a warehouse with multiple types of equipment. One order may include items from static high-rise shelving + picking from horizontal carousels (Honda distribution warehouse)
Batch – One picker picks a group of orders at the same time, one line at a time. A product on more than one order is picked all at one time, then segregated by order. Segregation may happen while picking into totes, or transported to a designated area where they are sorted by individual order
Advantages: High productivity due to reduced travel time
best candidates are orders with 1-4 lines and small cube
Disadvantages: measures need to be taken to minimize picking and sorting errors
computer control systems and auto sortation almost necessary but very effective
Wave picking – similar to discrete picking except that a selected group of orders are scheduled during a specific planning period, good for coordinating picking and shipping functions
Zone-Batch picking – each picker assigned a zone and picks a part of one or more orders, one scheduling period in each shift
Zone-wave picking – each picker assigned a zone and picks al lines for all orders stocked in the assigned, one order at a time, multiple periods per shift
Zone-Wave-Batch picking – each picker assigned zone and picks all lines for all orders stocked in the assigned zone, picking more than one order at a time with multiple scheduling shifts per period
<number>

## Slide 33
Procedure | Pickers per Order | Line items per pick | Periods per shift
Discrete | Single | Single | Single
Zone | Multiple | Single | Single
Batch | Single | Multiple | Single
Wave | Single | Single | Multiple
Zone-Batch | Multiple | Multiple | Single
Zone-Wave | Multiple | Single | Multiple
Zone-Batch-Wave | Multiple | Multiple | Multiple
Order-Picking Methodologies
Notes: Discrete – One person picks one order, one line at a time, one order period per shift; orders not scheduled – may be picked at any time
Advantages: Simplest – one picking document
Errors of omission reduced
service window – provides fastest response
accountability clear-cut
Disadvantages: least productive
travel time might be excessive
Zone – Total pick area organized into zones – 1 person assigned to each zone; picker in each zone picks one line item at a time for each order in zone, working on only one order at a time; lines from each zone brought to order consolidation area; can be sequential (pick and pass) or independent picking then consolidation
Often used because of different equipment in a warehouse with multiple types of equipment. One order may include items from static high-rise shelving + picking from horizontal carousels (Honda distribution warehouse)
Batch – One picker picks a group of orders at the same time, one line at a time. A product on more than one order is picked all at one time, then segregated by order. Segregation may happen while picking into totes, or transported to a designated area where they are sorted by individual order
Advantages: High productivity due to reduced travel time
best candidates are orders with 1-4 lines and small cube
Disadvantages: measures need to be taken to minimize picking and sorting errors
computer control systems and auto sortation almost necessary but very effective
Wave picking – similar to discrete picking except that a selected group of orders are scheduled during a specific planning period, good for coordinating picking and shipping functions
Zone-Batch picking – each picker assigned a zone and picks a part of one or more orders, one scheduling period in each shift
Zone-wave picking – each picker assigned a zone and picks al lines for all orders stocked in the assigned, one order at a time, multiple periods per shift
Zone-Wave-Batch picking – each picker assigned zone and picks all lines for all orders stocked in the assigned zone, picking more than one order at a time with multiple scheduling shifts per period
<number>

## Slide 34: Order picking in CD Warehouse
The 48 bays of flow rack contain only about 10 percent of the sku's but these account for about 65 percent of the picking.
Most of the warehouse floor space is occupied by static-shelving, from which about 13,000 different labels (sku's) are picked. This represents about 90 percent of all sku's but only about 35 percent of all picks.
Copyright © John J. BARTHOLDI, III. All Rights Reserved. Last modified: Sun Mar 26 09:56:22 EST 2006
Notes: Most of the warehouse floor space is occupied by static-shelving, from which about 13,000 different labels (sku's) are picked. This represents about 90 percent of all sku's but only about 35 percent of all picks.
Order pickers push carts through the aisles, much like shoppers at a grocery store. Since these are the less popular sku's, there is a lot of walking per pick.
The top of the shelves are used to store "overstock" so that the shelves can be restocked without having to travel all the way to the pallet rack (visible at the far left).
The 48 bays of flow rack contain only about 10 percent of the sku's but these account for about 65 percent of the picking. You can see as many workers in this area than in all of the static-shelving area. Instead of pushing shopping carts the pickers are operating like an assembly line, where the products to be assembled are the customer orders.
<number>

## Slide 35: Sortation and Packing
Sortation is the process of merging, identifying, inducting, and separating items to be conveyed to specific destinations.
Packing is the process of unitizing orders for shipment.
Sortation and packing is only required after piece and case batch order picking.
Notes: <number>

## Slide 36: Shipping
The process of staging, verifying, and loading orders to be transported from a warehouse.
The ASN for each order is generated during the picking process and is sent to the customer.

## Slide 37: Packing / Shipping
  Order verification
  Packing
    Master packs / consolidation
    Palletization
    Freight / postage determination
  Labeling
    Content labeling
    Compliance labeling
    Shipping labeling
    Packing slips
  Shipping
    Manual Pallet Build, Stage & Load
    Carton Sortation to Pallets, Stage & Load
    Direct Carton Load
    Automated Loading
    Pack & Hold
The shipping function creates unit loads (pallets or containers) for shipping, as well as preparing shipments for delivery to customers. The shipping area is typically responsible for closing out order activity and confirming distribution activities.

## Slide 38: Distribution Operations: Warehouse Planning & Design
 | Excellent | Advanced | Common | Outdated
Parameters Used in Layout and Equipment Decisions | Use of computer based layout and work-flow simulation modeling is used. The model is stand-alone or part of a “Tier-One” WMS solution. It considers slotting by SKU velocity and optimization of work flow and travel paths. | Use of PC based spreadsheet models for layout and equipment needs and cost are used. Some velocity loading is considered for SKU placement. | No models exist. Sizing is based on an estimate of bin, rack and floor space needed for current and future needs, derived from past examples. | No models exist. Layout and equipment are based on past methods and product groupings. Velocity and travel optimization not considered.
Methods and tools for Layout and Equipment Decisions | Layout and Equipment design carried out by using a modeling tool to optimize space, SKU slotting, and travel optimization of the warehouse vs. cost, service and profit targets. | SKU quantities and volumes are used to estimate storage types and space needs. Numerous storage and retrieval methods are evaluated to determine equipment needs. | SKU quantities and volumes are used to estimate storage types and space needs. Past storage and retrieval methods are assumed while determining equipment needs. | Sizing is done based on a comparison of material and quantities to be stored to past examples.
Evaluation of Warehouse Configuration | Dynamic SKU slotting is used to continually optimize warehouse space. Rearrangements are based on changing stock movement patterns. | Frequent, periodic rearrangements of the warehouse (SKU static slotting) when movement patterns of stock changed significantly. | Ad-hoc and infrequent rearrangements of the warehouse. | No optimization of the warehouse. Material is moved only when space needs to be freed up for more material or when earlier such actions are reversed.
Process Automation | Processes are managed via integrated WMS system, are RF-driven and include RFID technologies. Conveyor systems and automated sortation are integrated with WMS. Other automation (e.g. ASRS, carousels, etc.) may be utilized to satisfy specific requirements. | Processes are managed via WMS system and are mostly RF driven. Conveyor systems and automated sortation are utilized. Other automation (e.g. ASRS, carousels, etc.) may be utilized to satisfy specific requirements. | Paper or Radio Frequency (RF) driven processes. Some utilization of conveyors to transport orders to packing & shipping. | Paper driven processes with some reporting.
Notes: <number>

## Slide 39: Distribution Operations: Operational Processes
 | Excellent | Advanced | Common | Outdated
Receiving | Statistical sampling of ASN’s is used to verify accuracy of receipts. No physical counting of receipts is required for consistently accurate vendors. Use of Cross docking with the use of ASN to allocate in-transit prior to actual receipt. | Receipts are verified against ASN and entered into warehouse system via RF terminal. Use of Cross docking from receiving to shipping– allocate upon ASN. | Receipts are verified via physical counts and entered into warehouse system via RF terminal or manually. | Receipts are verified via physical counts compared to receiver document. Receipts are manually entered into warehouse system.
Put-away | WMS directs put away and interleaves putaway tasks with other warehouse tasks (e.g. replenishment, stock transfers, order picking, etc.) | WMS directs put away to optimal storage location. | Putaways are non-directed and updated into the warehouse system via RF terminal or manually. | Paper-based put-away process where inventory moves are updated into the warehouse system by clerical, after the fact.
Order Picking | Mixture of products cross-docked and pick from stock. Batch and wave picking with automated sortation are utilized to optimize productivity and shipping capacity. Conveyor system includes inline weighing and manifesting. | Mixture of products cross-docked and pick from stock. Batch picking and automated sortation is utilized to optimize productivity. | Mixture of single order and batch picking. Batch picked orders are manually sorted. | Single orders are picked from storage racks.
Replenishment | Replenishment tasks are interleaved with other warehouse tasks. Wave based replenishment to multiple pick zones based on material handling types. WMS system automatically increases priority of replenishment tasks when pick slot quantities fall below demand. | Replenishment tasks are interleaved with other warehouse tasks. Wave based replenishment may be used. WMS system automatically increases priority of replenishment tasks when pick slot quantities fall below demand. | Replenishment needs are generated from warehouse system report. Stockers use report to fulfill pick slot needs. Emergency pick slot needs are manually communicated. | Replenishment needs are manually tracked and communicated to stockers.
Notes: <number>

## Slide 40
Multiple processes at Baxter Global
Multiple processes at International Truck and Engine

## Slide 41: Peapod
Picking aisle
Picking cart
Shipping queues