## Slide 1: Warehouse Safety and Ergonomics
Warehouse and Inventory Management
LOG 103

## Slide 2: Are warehouses unsafe?
• More than 145,000 people work in over 7,000 warehouses.
• The fatal injury rate for the warehousing industry is higher than the national average for all industries.
• Potential hazards for workers in warehousing:
  • Unsafe use of forklifts;
  • Improper stacking of products;
  • Failure to use proper personal protective equipment;
  • Failure to follow proper lockout/tagout procedures;
  • Inadequate fire safety provisions; or repetitive motion injuries.
Warehouse Safety

## Slide 3: Warehouse potential hazards
For warehousing establishments, the 10 OSHA standards most frequently included in the agency’s citations were:
  1. Forklifts
  2. Hazard communication
  3. Electrical, wiring methods
  4. Electrical, system design
  5. Guarding floor & wall openings
  and holes
  6. Exits
  7. Mechanical power transmission
  8. Respiratory protection
  9. Lockout/tagout
  10. Portable fire extinguishers
Warehouse Safety

## Slide 4: Warehouse potential hazards
Docks: Injuries happen here when forklifts run off the dock, products fall on employees or equipment strikes a person.
Forklifts: About 100 employees are killed and 95,000 injured every year while operating forklifts in all industries. Forklift turnovers account for a significant percentage of these fatalities.
Conveyors: Workers can be injured when they are caught in pinch points or in the in-going nip points, are hit by falling products or develop musculoskeletal disorders associated with awkward postures or repetitive motions.
Manual Lifting/Handling: Back injuries may occur from improper lifting or overexertion.
Hazard Communication: Chemical burns are possible if spills of hazardous materials occur.
Charging Stations: Fires and explosion risks are possible unless proper guidelines are followed.
Poor Ergonomics: Improper lifting, repetitive motion or poor design of operations can lead to musculoskeletal disorders in workers.
Other hazards: Inadequate fire safety provisions, improper use of lockout procedures and failure to wear personal protective equipment also create hazards in the warehouse workplace.
Warehouse Safety

## Slide 5
Warehouse Safety

## Slide 6
Warehouse Safety

## Slide 7: Early Truck Departure

## Slide 8: Trailer Pop-Ups
The dangers of uneven weight distribution.

## Slide 9: Tilted Trailer

## Slide 10
Warehouse Safety

## Slide 11: 2 main categories of hazards
Mechanical Hazards • Confined spaces • Electrical hazards • Falling objects • Hazardous Material • Improper storing of material • Outside truck traffic • Packaging/Processing machines • Powered Industrial Vehicles | Employee Hazards • Crush hazards/Pinch points • Cutting Tools • Housekeeping • Improper Lifting • Pedestrian Safety • PPE use • Material Handling • Slips, trips & falls
Warehouse Safety

## Slide 12
MECHANICAL HAZARDS
• Confined spaces
• Electrical hazards
• Falling objects
• Hazardous Material
• Improper storing of material
• Outside truck traffic
• Packaging/Processing machines
• Powered Industrial Vehicles
Warehouse Safety

## Slide 13: Confined spaces 29 CFR 1910
An OSHA permit-required confined space is one that has—or has the potential for—one or
more of these hazards:
A hazardous atmosphere that could cause a person inside to become ill,
incapacitated, unable to escape without aid, or even to die. The atmosphere
may be hazardous due to:
Flammable gas, vapor, or mist levels more than 10 percent above the
substance's lower flammable limit.
Airborne combustible dust at or above the substance's lower flammable limit,
making it hard to see things less than five feet away.
Atmospheric oxygen concentration below 19.5 percent or above 23.5 percent.
Just 16 percent oxygen can make you drowsy, nauseated, and speed up
breathing and heartbeat. At 12 percent, you'll lose consciousness; a 6 percent
oxygen level will kill you.
Any other atmospheric condition immediately dangerous to life or health (IDLH)
a condition that threatens life, could cause irreversible health problems, or limit
your ability to escape the space without help.
Warehouse Safety

## Slide 14: Confined spaces
Engulfment potential applies to a space that contains a liquid or a flowing solid
(such as sand or grain) that could immerse and bury or smother you.
Entrapping design refers to walls that converge inward or a floor that slopes
and tapers down. In a space like that, you could slip or fall into an area too small
to escape from or get pushed into machinery.
Other recognized serious health or safety hazards could include:
  • Combustibility. If something can burn or explode, it is more likely to do so, and
  do it instantly, in a confined space.
  • Falls. If you fall in a confined space, you could get trapped or asphyxiated,
  especially if the space has too little oxygen or contains toxic gases.
  • Heat. Heat can build up quickly in a confined space, making you tired, dizzy,
  and ill.
  • Noise. Sounds reverberate in a confined space, and you could fail to hear
  important instructions or warnings.
Warehouse Safety

## Slide 15: Electrical Hazards CFR 1910 Subpart S
Electrical equipment shall be free from recognized hazards that are
likely to cause death or serious physical harm to employees.
  • No frayed, cracked or damaged insulation on any wiring
  • No bare wires or open electrical boxes (covers and knock outs in place)
  • Extension cords cannot be used for a permanent connection
  • Consider possible arcing effects
  • Do not block electrical panels – minimum of 30” clearance
  • Each disconnect switch or circuit breaker must be clearly labeled with a
  durable label or marking.
  • Live parts of electric equipment operating at 50 volts or more shall be
  guarded against accidental contact by an approved enclosure
  • Workspace around electrical equipment must not be less than 6’6” in
  height or 30” wide.
  • At least one entrance not less than 24” wide and 6’6” high shall be
  provided to give access to the workspace
Warehouse Safety

## Slide 16: Falling Objects
Some safe guards against falling objects should be put in place:
If you are working above other employees:
  • Be careful so that material will not fall from your workspace
  • Use trash containers or other means to keep debris from falling on persons below
  • Use the safety equipment and practices that are required for the job. For
  example, if operating a Pick Truck, you should be wearing a body harness and
  lanyard to prevent falls.
  • Never deliberately throw or sweep material from above.
  • Don’t work, or allow others to work, under obviously unsafe conditions.
If you are working on the ground or below other employees:
  • Store material safely so it won’t fall on someone just walking by
  • Wear safety equipment like hard hats or safety glasses if required
  • Pay attention to what is going on around you especially if cranes are being used to hoist materials into the air
Warehouse Safety

## Slide 17: Hazardous Material 29 CFR 1910.1200
Hazardous Communication (HazCom) Program also known as the “Right
to Know” law is required – Sample programs are available on
www.osha.gov
  • You must share information and train your employees on what Hazardous
  Material they are working with
  • You must maintain a Hazardous Material inventory of all chemicals used in
  your facility
  • You must have a Material Safety Data Sheet (MSDS) for every chemical in
  your facility
  • Chemical manufacturers, importers, and distributors of hazardous chemicals
  are all required to provide the appropriate labels and material safety data
  sheets to the employers to which they ship the chemicals.
  • Every container of hazardous chemicals you receive or use in your facility
  must be labeled, tagged, or marked with the required information.
  • Your suppliers must also send you a properly completed material safety data
  sheet (MSDS) at the time of the first shipment of the chemical, and with the
  next shipment after the MSDS is updated with new and significant
  information about the hazards.
Warehouse Safety

## Slide 18: Hazardous Waste Operations and Emergency Response
If your company produces any hazardous waste, you need a HAZWOPER program.
1910.120(b)(1)(i) Employers shall develop and implement a written safety and health
program for their employees involved in hazardous waste operations. The program shall be
designed to identify, evaluate, and control safety and health hazards, and provide for
emergency response for hazardous waste operations.
1910.120(b)(1)(ii)(A-G) The written safety and health program shall incorporate the following:
  An organizational structure – the chain of command and responsibilities 1910.120(b)(2)(i)(A) –
  1910.120(b)(2)(i)(D)
  A comprehensive workplan - shall address the tasks and objectives of the site operations and identify
  the methods for accomplishing those tasks and objectives.
  A site-specific safety and health plan - shall address the safety and health hazards of each phase of site
  operation and include the requirements and procedures for employee protection.
  The safety and health training program shall address employee training assignments to assure
  compliance with paragraph (e) of this section. See 1910.120(e)(1) – (9)
  The medical surveillance program shall be instituted by the employer for a list of employees and records
  must be kept for duration of employment plus 30 years. 1910.120(f)(1) – (8)
  The employer's standard operating procedures for safety and health.
  Any necessary interface between general program and site specific activities.
Warehouse Safety

## Slide 19: Proper storing of materials
  • 1910.176(a) Use of mechanical equipment. Where mechanical handling equipment is
  used, sufficient safe clearances shall be allowed for aisles, at loading docks, through
  doorways and wherever turns or passage must be made. Aisles and passageways shall be
  kept clear and in good repair, with no obstruction across or in aisles that could create a
  hazard. Permanent aisles and passageways shall be appropriately marked.
  • 29 CFR 1910.176(b) Secure storage. Storage of material shall not create a hazard. Bags,
  containers, bundles, etc., stored in tiers shall be stacked, blocked, interlocked and limited in
  height so that they are stable and secure against sliding or collapse.
  • 29 CFR 1910.176(c) Housekeeping. Storage areas shall be kept free from accumulation of
  materials that constitute hazards from tripping, fire, explosion, or pest harborage.
  Vegetation control will be exercised when necessary.
  • Check what you're storing to determine if it needs certain conditions—dry, dark, ventilated,
  etc.
  • Check that shelves and racks are sturdy and in good condition, these should be labeled
  for capacity.
  • Place heavier objects close to the floor, lighter/smaller objects higher.
  • Don't stack items so high that they could block sprinklers, come in contact with overhead
  lights or pipes or become unstable and fall over.
Warehouse Safety

## Slide 20: Improper storing of material….
Warehouse Safety

## Slide 21: ….causes damage
Warehouse Safety

## Slide 22: Outside Truck Traffic
Trucks and pedestrians don’t mix well – keep them separate with designated
areas
  • Don’t allow personal vehicles to use the same area as your shipping & receiving
  traffic if at all possible. Eliminate the contact, eliminate the hazard! It can also
  help reduce theft.
  • Trucks may have hazardous material on them other than your delivery. No spill,
  no problem. If they have a hazmat spill, you must keep it away from any storm
  drains
  • If a truck or it’s load leaks onto your property, you could be held responsible for
  any environmental damage
  • Truck drivers need to drive at a safe posted speed limit. One suggestion
  is10mph, otherwise accidents may happen . . . .
Warehouse Safety

## Slide 23: Outside Truck Accident
Warehouse Safety

## Slide 24: Outside Truck Safety Practices
GOAL – Get Out and Look
Spotters – with safety vests
Chocks and cones
Nose gear if trailer is dropped at dock
Scheduled deliveries
Clean dock areas

## Slide 25: Safety – Company-Owned Fleet
Safety Meetings - Morning and Evening
Thorough Training and Frequent Road Tests
Backing Certification Training
Distance Measuring Equipment
Back-up Cameras
GPS
Don’t Force Speed
Take Note of Different Sized Trucks

## Slide 26: Packaging/Processing Machines
Machine guarding standard - 29 CFR 1910.212(a)(1) One or more methods
  of machine guarding shall be provided to protect the operator and other
  employees in the machine area from hazards such as those created by pointof-
  operations, ingoing nip-points, rotating parts, flying parts, flying chips and
  sparks. Examples of machine guarding are barrier guards, two-handed tripping
  devices, and electronic safety devices.
• Walking / working surfaces - 29 CFR1910.22(a)(2) The floor of every
  workroom shall be maintained in a clean and, so far as possible, a dry
  condition. Where wet processes are used, drainage shall be maintained, and
  false floors, platforms, mats, or other dry standing places should be provided
  where practicable.
• Walking / working surfaces - 29 CFR 1910.22(a)(3) To facilitate cleaning,
  every floor, working place, and passageway shall be kept free from protruding
  nails, splinters, holes, or loose boards.
Warehouse Safety

## Slide 27: Packaging/Processing Machines
LockOut/TagOut (LO/TO) standard – also known as the Control of Hazardous
  Energy. Once your employee performs a lock out on a machine they should
  push the start button to test it!
29 CFR 1910.147(a)(2)(i) This standard applies to the control of energy during
  servicing and/or maintenance of machines and equipment.
29 CFR 1910.147(a)(2)(ii) Servicing and/or maintenance which takes place
  during normal production operations is covered by this standard only if:
29 CFR 1910.147(a)(2)(ii)(A) An employee is required to remove or bypass a
  guard or other safety device; or
29 CFR 1910.147(a)(2)(ii)(B) An employee is required to place any part of his or
  her body into an area on a machine or piece of equipment where work is
  actually performed upon the material being processed (point of operation) or
  where an associated danger zone exists during a machine operating cycle.
Warehouse Safety

## Slide 28: Powered Industrial Vehicles 29 CFR 1910.178
Only trained and authorized employees may operate powered industrial vehicles
• Must be trained by a competent person
• 1910.178(l)(2)(i)(A)(B) Trainees may operate a powered industrial truck only:
  - Under the direct supervision of persons who have the knowledge, training, and experience
  to train operators and evaluate their competence; and
  - Where such operation does not endanger the trainee or other employees.
• Must be renewed/retrained every 3 years minimum
• Must include an evaluation, both medical and hands on evaluations
• 1910.178(l)(4)(ii)(A)-(E) Refresher training in relevant topics shall be provided to the
operator when:
    (A) The operator has been observed to operate the vehicle in an unsafe manner;
    (B) The operator has been involved in an accident or near-miss incident;
    (C) The operator has received an evaluation that reveals that the operator is not operating
    the truck safely;
    (D) The operator is assigned to drive a different type of truck; or
    (E) A condition in the workplace changes in a manner that could affect safe operation of the
    truck.
• Be sure to document all training and evaluations
Warehouse Safety

## Slide 30
EMPLOYEE HAZARDS
• Crush hazards/Pinch points
• Cutting Tools
• Housekeeping
• Improper Lifting
• Pedestrian Safety
• PPE use
• Material Handling
• Slips, trips & falls
Warehouse Safety

## Slide 31: Crush Hazards/Pinch Points
Crush Hazards and Pinch Points are not a hazard IF employees do not put their body parts in them.
• Train employees what the crush hazards and pinch points are related to their job.
• Keep machine guards in place to prevent body parts from entering the
machine.
• Machine guarding is one area strongly looked at by OSHA.
• Teach employees not to wear any loose clothing or loose jewelry such as
necklaces or dangly earrings when working around machinery.
• Long hair can also be a hazard if it gets caught in a pinch point. Someone
could lose their scalp. Long hair should be tied back or up to prevent the
hazard.
Warehouse Safety

## Slide 32: Cutting Tools
Teach your employees the dangers of cutting tools:
• That improper use leads to injuries
• Dull blades cut people but not boxes
• Use safety knives to help prevent injuries
• Use cut resistant gloves if necessary
• Use the right tool for the job, don’t use a knife for a screwdriver
Warehouse Safety

## Slide 33: Housekeeping
Good housekeeping is not an option, it is a regulation!
• 29 CFR 1910.22(a)(1) All places of employment, passageways, storerooms, and service rooms shall be kept clean and orderly and in a sanitary condition.
• 29 CFR1910.22(a)(2) The floor of every workroom shall be maintained in a cleanand, so far as possible, a dry condition. Where wet processes are used, drainage shall be maintained, and false floors, platforms, mats, or other dry standing places should be provided where practicable.
• 1910.22(b)(1) Where mechanical handling equipment is used, sufficient safe clearance s shall be allowed for aisles, at loading docks, through doorways andwherever turns or passage must be made. Aisles and passageways shall be kept clear and in good repairs, with no obstruction across or in aisles that could create a hazard.
Warehouse Safety

## Slide 34: Improper Lifting
Train your employees how to lift properly and the dangers of a back injury if they lift improperly!
• Lift with your legs and not your back
• Keep it close and keep the curves in your back
• Move your feet when turning
• When you can, build a bridge to pick something up to support your back
• Use your free hand or your legs to support yourself
• Check the ergonomics of the job task. Ask yourself, can it be done differently?
Warehouse Safety

## Slide 35: Pedestrian Safety
You should have clearly designated areas for employees to walk
• Pedestrians need to be aware of their surroundings.
• Employees on foot or on a Powered Industrial Vehicle (PIV) should not use a cell phone while traveling through your facility. Develop a cell phone policy.
• All visitors should be shown where pedestrians should walk or be
escorted by an employee.
• All PIV operators should yield right-of-way to pedestrians
• Teach all PIV operators to use their horns at blind intersections and
anytime they are near pedestrians. The PIV operators should not
assume the pedestrians can see them and the pedestrians should not assume PIV operators can see them either.
Warehouse Safety

## Slide 36: PPE Use
OSHA has issued its final rule on employer payment for Personal ProtectiveEquipment (PPE). Under the new rule, all required PPE, with a few exceptions, must be provided at no cost to the employee.
• This requirement addresses PPE of many kinds such as hard hats, gloves,goggles, safety shoes, safety glasses, welding helmets and goggles, faceshields,chemical protective equipment, fall protection equipment, and so forth.
• The new rule went into effect on Feb. 13, 2008, and employers must implement its provisions by May 15, 2008.
• Be sure to do a Job Safety Analysis (JSA) on all jobs in your facility to determine the proper PPE for that job. The job may not need any PPE.
• When some sort of PPE is required, train your employees how to use it properly and make sure they do.
Warehouse Safety

## Slide 37: Material Handling
Be sure material handling equipment is in good working condition
• Train employees how to use equipment properly
• Make sure any straps, slings & hooks are visually inspected monthly
• Overhead cranes should be visually inspected monthly
• Overhead cranes should be on a Preventative Maintenance schedule
• Document annual inspections on straps, slings, hooks & overhead cranes
• Pull any damaged material handling equipment out of service until repaired ore replaced
Warehouse Safety

## Slide 38: Slips, Trips & Falls
Keep walking/working surfaces clear of all debris
• Keep them dry as much as possible
• Watch out for trip hazards in the warehouse and offices
• Trip hazards include such things as extension cords, throw rugs, door mats, loose steps, open desk or file cabinet drawers, skids, parts, boxes and all other packing materials just to name a few
• Wet spills are probably the biggest slip hazard, teach employees to clean them up as soon as they come across a spill.
Warehouse Safety

## Slide 39: Programs that may be needed in a warehouse
Emergency Action Plan – 29CFR 1910.38
• Hazard Communication Program (HazCom) – 29 CFR 1910.1200
• HAZWOPER - 29CFR 1910.120
• Permit Required Confined Space – 29 CFR 1910.146
• Occupational Noise Exposure – 29 CFR 1910.95
• Occupational Exposure to Bloodborne Pathogens – Multiple standards
• Personal fall protection. 29CFR 1910.66(j)
• Safety & Health Program
Warehouse Safety

## Slide 40: Emergency Action Plan 29 CFR 1910.38
The Emergency Action Plan should address emergencies that the employer mayreasonably expect in the workplace. Examples are: fire; toxic chemical releases; tornadoes;blizzards; floods; and others.
• Emergency Evacuation - At the time of an emergency, employees should know what typeof evacuation is necessary and what their role is in carrying out the plan. In some caseswhere the emergency is very grave, total and immediate evacuation of all employees isnecessary. The use of floor plans or workplace maps which clearly show the emergencyescape routes should be included in the emergency action plan. Color coding will aidemployees in determining their route assignments.
• Emergency Action Plan training - The employer should assure that an adequate numberof employees are available at all times during working hours to act as evacuation wardensso that employees can be swiftly moved from the danger location to the safe areas.Generally, one warden for each twenty employees in the workplace should be able toprovide adequate guidance and instruction at the time of a fire emergency.
• Fire Prevention Housekeeping - The standard calls for the control of accumulations of flammable and combustible waste materials.
• Maintenance of equipment under the fire prevention plan - Certain equipment is often installed in workplaces to control heat sources or to detect fuel leaks. An example is a temperature limit switch often found on deep-fat food fryers found in restaurants.
Warehouse Safety

## Slide 41: Occupational Noise Exposure 29 CFR 1910.95
Not every workplace will need this type of program. Only if your employees are exposed to an 8-hour time-weighted average of 85 decibels or greater
  • If you are found to have an 8-hour time-weighted average of 85 decibels or more then you must develop a Hearing Conservation program - 1910.95(c)
The Hearing Conservation Program must include:
  • A monitoring program - 1910.95(d)
  • An Audiometric testing program - 1910.95(g)
  • A Baseline audiogram - 1910.95(g)(5)
  • Testing to establish a baseline audiogram shall be preceded by at least 14 hours without exposure to workplace noise. Hearing protectors may be used as a substitute for the requirement that baseline audiograms be preceded by 14 hours without exposure to workplace noise - 1910.95(g)(5)(iii)
Warehouse Safety

## Slide 42: Occupational Noise Exposure 29 CFR 1910.95
• Each employee's annual audiogram shall be compared to that employee's baseline audiogram to determine if the audiogram is valid and if a standard threshold shift as defined in paragraph (g)(10) of this section has occurred. This comparison may be done by a technician - 1910.95(g)(7)(i)
• The audiologist, otolaryngologist, or physician shall review problem audiograms and shall determine whether there is a need for further evaluation - 1910.95(g)(7)(iii)
• If you have a standard threshold shift of 10dB or more that is determined to be work related it must go on your OSHA 300 log - 1904.10(a)–(b)(1)
• A standard threshold shift is a change in hearing threshold relative to the baseline audiogram of an average of 10 dB or more at 2000, 3000, and 4000 Hz in either ear. - 1910.95(g)(10)
• There is a list of follow up procedures provided under - 1910.95(g)(8)
• One important procedure is that employers shall ensure that hearing protectors are worn by any employee who is exposed to an 8-hour time-weighted average of 85 decibels or greater, and who:
  Has not yet had a baseline audiogram established or
  Has experienced a standard threshold shift.
Warehouse Safety

## Slide 43: Fall Protection Program
Employees on working platforms shall be protected by a personal fall arrest
system meeting the requirements of appendix C, Section I, of this standard, and as otherwise provided by this standard - 29CFR 1910.66(j)
• Appendix C gives all definitions and pertinent information for a personal fall arrest system 1910.66 App C
• For General Industry a body belt is permitted. However, a full body harness is much safer than a body belt. It is also a lot less strain on the body during a fall.
• Standard weight limit on lanyards and harnesses is 310lbs.
• When you do Powered Industrial Vehicle operator physical evaluations, check their height and weight. If they are 300lbs or more, consider getting higher weight rated fall protection.
• Anchor points to which personal fall arrest equipment is attached shall be capable of supporting at least 5,000 pounds per employee attached
Warehouse Safety

## Slide 44: Safety & Health Program
The benefits of a strong Safety & Health Program include: • Reducing the pain and suffering associated with workplace injuries, illnesses and accidents • A very positive impact on the bottom line • Lower workers’ compensation costs • Increased productivity • Increased employee morale • Lower absenteeism • Lower employee turnover | The elements of a strong Safety & Health program could include: • A Wellness program including such things as: • Weight loss program • Smoking Cessation • Exercise & fitness on site • Health clubs Safety Committee who’s duties may include: • Safety Audits • Behavioral Audits • Accident Investigations • Develop an incentive program or a behavior based program
Warehouse Safety