## Slide 1: Warehouse Layout and Design
Warehouse and Inventory Management
LOG 104

## Slide 2
Once a organization has decided where a warehouse facility will be located, the next important decision is the arrangement of equipment and people within the facility.

## Slide 3: Facility Layouts:
A Decision that Encompasses:
  Placement of ‘Departments’
  Placement of Workstations/Machines
  Placement of Stockholding points within Factory or Warehouse
  Development of Controlled Traffic Patterns to generate smooth workflow throughout
The layout decision will certainly affect the Flow of materials, in-plant Transportation cost, equipment utilization, and general productivity and effectiveness of the business.
Therefore, layout should be carefully arranged, AND It must satisfy specific objectives.

## Slide 4: Facility Layouts:
Usually the layout is planned to minimize a particular criterion:
For example, minimizing total traveling time, total cost, total delays, etc.
There are also situations in which the layout may be designed to maximize a criterion:
For example, maximize quality, flexibility, or space utilization.

## Slide 5: Warehouse design and layout criteria:
Be designed based on current and future needs.
  Facilitate changes in business/agency growth, and size/population of office and warehouse spaces within the building. Warehouse space should be easily adapted to new functions such as office (on ground or upper levels), computer centers, or light industrial/fabrication.
  Accommodate need for future loading docks, truck space, and car parking spaces if space configuration changes through effective site design.
  Address material handling technologies and business practice, such as "just-in-time" storage, which have fundamentally changed operation of warehouses and distribution centers, and will continue to do so.
  Include roof design with built-in extra structural capacity to handle addition of future rooftop equipment.
  Be designed with fire protection capacity to accommodate storage of materials with a greater fire hazard, especially needed with high plastic product content or packaging, and plastic shrink-wrapped pallets.
Maximize utilization of space while providing adequate circulation paths for personnel and material handling equipment such as forklift trucks.
  Use higher bays to take advantage of height allowances in the space.
Optimize layout and configuration for the warehouse operation, including efficient circulation and material handling and storage processes.
Relate interior and exterior receiving and shipping operations to the process flow of goods through the warehouse.

## Slide 6: Material handling criteria
A process controlled environment - process steps follow on in a logical sequence that can be seen by walking the floor.
Visible flows and floors for each of the process steps.
Maximum use of available space.
Optimised racking & storage space that is flexible in its design.
Easy put away and retrieval of products .
Optimised work flows ensuring the shortest travel distances for put away and picking routines.
Picking routines that group products by type or stock location sequencing.
Predictable processing times

## Slide 7: Three distinct phases
Pre-engineering
  Overall purpose of facility: distribution center w/storage vs cross-dock vs fulfullment center vs reverse logistics center
  Data collection -> calculate gross storage
  Conceptual design
  Layout planning
  Compare tradeoffs for storage, equipment, environmental, safety and health, flexibility, reliability
Engineering
  Detailed system layout drawings – aisles, storage
  Requirements for electrical, lighting, computers
Implementation

## Slide 8: What data is needed
Number of SKUs
Design specifications of SKUs
Annual, Monthly, Seasonal throughput
Growth Projections
Receiving Characteristics
Order Characteristics
Shipping Characteristics
Storage Characteristics

## Slide 9: Most Typical Warehouse Layouts
U-shaped
Straight-thru
Modular

## Slide 10: U-shaped Layout
Receiving
Shipping
Reserve Storage
and
Pallet Picking
Case
Picking
Broken
Case
Picking
Accumulation, Sortation & Packing
Cross-docking
Direct
putaway
to reserve
Direct
putaway
to primary
Replenishment
Replenishment

## Slide 11: Some key advantages of the U-shaped layout
Excellent utilization of dock resources since the receiving and shipping processes can share dock doors.
Facilitates cross-docking since the receiving and shipping docks are adjacent to each other and may be co-mingled.
Excellent lift-truck utilization since
  put-away and retrieval trips are easily combined
  storage locations closest to shipping and receiving docks are natural locations to house fast-moving items.
=> U-shaped layout/flow is the benchmark upon which all other layouts/flows should be compared.

## Slide 12: Straight-thru Layout (Primarily for cross-docking facilities)
SHIPMENT STAGING
RECEIVING CHECK-IN
RECEIVING
SHIPPING
TEMPORARY
HOLDING
AREA
SORTING AND
ASSEMBLY
AREA

## Slide 13: Modular Layout
Appropriate for large-scale operations in which the individual processes are so large that they merit stand-alone and uniquely designed buildings
E.g.,
  a rack-supported building for unit-load AS/RS;
  an air-conditioned low-bay building for customizing operations such as monogramming, pricing and marking;
  a low-bay shipping building equipped with high-speed sortation equipment.

## Slide 14: Systematic Layout Planning
Systematic Layout Planning (SLP) is an organized approach to facility Layout planning.

## Slide 15: Systematic Layout Planning (SLP) (R. Muther, 1961)
Input Data and Activities
Material
Flow
Activity
Relationships
Relationship
Diagram
Space
Requirements
Space
Availability
Space
Relationship
Diagram
Modifying
Considerations
Practical
Limitations
Develop
Layout
Alternatives
Evaluation
Analysis
Search
Selection

## Slide 16: Systematic Layout Planning
The heart of SLP is the Activity Relationship Chart and Diagrams that neatly summarize vast amounts of quantitative and Qualitative information.

## Slide 17: Typical Activity Relationship Chart:
These charts are often called an AEIOUX chart – the letters used to explain relationships that are learned during our facility studies:

## Slide 18: Completing the Activities Relationship Chart:
After listing all departments on chart, Conduct Surveys to assess relationships with each department’s staff
Interpret results of surveys as closeness needs – itemize and record closeness requirements to support assessed relationship
Establish the relationships:
    A – absolutely necessary
    E – Especially Important
    I – Important
    O – “ordinary” closeness okay
    U – Unimportant
    X – Undesirable
Allow all concerned parties to review proposed chart for accuracy of closeness settings

## Slide 19: Using Activity Relationship Chart to build Designs:
Using Pure SLP ideas we develop a “Meatball” diagram and move departments around to shorten A & E lines while increasing length of X lines

## Slide 20: Using Activity Relationship Chart to build Designs

## Slide 21: Using Activity Relationship Chart to build Designs
An alternative approach begins with looking at each department as equal sized rectangles listing letter relationship with all departments in the Facility
Receiving: A -; X-; E-B; I-D; O-C,E; U- F,G
Milling: A -; X-; E-A,D; I-E,F; O-; U- C,G
Press: A -; X-; E-; I-; O-A,F; U- B,D,E,G
Sc. Machine: A -; X-; E-B; I-A,E; O-; U-C,F,G
Plating: A -E; X-; E-G; I-B; O-C; U- A,D
Shipping: A -; X-; E-F; I-E; O-; U- A, B, C,D
Assembly: A -F; X-; E-; I-B,D,G; O-A; U- C

## Slide 22: Using Activity Relationship Chart to build Designs
Select template with highest number of A relationships; tied templates selected subject to hierarchy: most E’s, Most I’s, fewest X’s
    Here select Plating department (F)
Next template chosen should have A relationship w/ 1st chosen – any ties broken as above
    Here Assembly, department E
Next template chosen should have the highest joint relationship with first two chosen
    Here is Shipping – G
This continues until all departments are chosen

## Slide 23: In doing the Design:
F
E
G
B
D
A
C
By This Order:
Place F in Center. Then follow in order keeping Ideas (AEIOUX) of arrangements:
F
E
G
B
D
A
C

## Slide 24: A Final Step: now we consider actual departmental areas:
Code | Function | Area Ft2 | # Units (2000 per)
A | Receiving | 12,000 | 6
B | Milling | 8,000 | 4
C | Press | 6,000 | 3
D | Sc. Machines | 12,000 | 6
E | Assembly | 8,000 | 4
F | Plating | 12,000 | 6
G | Shipping | 12,000 | 6

## Slide 25: Leads to the following Proposed Layout:
When equal sizes are replaced with scaled sizes we develop these layouts:
Obviously, many variants would be possible (no X’s and few A and E’s)
We determine appropriate layout only after quantitative analysis is applied to the proposed arrangements

## Slide 26: Example
A small accounting Firm, GUNTAŞ Accounting, has rented Space in a new one-floor building.
The firm has allocated 6000 square meters to its seven departments as follows:

## Slide 27: Example

## Slide 28: Example
In the first step of Systematic Layout Planning, we analyze interactions between departments AND we assess the desirability of placing departments together.

## Slide 29: Example
The firm has carefully analyzed its operations to Determine the importance of Locating specific departments Close Together.
The results of this analysis are summarized in the following Activity Relationship Chart:

## Slide 30: Example

## Slide 31: Example

## Slide 32: Example
This Activity Relationship Diagram is essentially an Illustration of the Information Contained in the Activity Relationship Chart.
All departments in this diagram are Represented by equal size boxes.
The next step is to anticipate the space required for each Department.

## Slide 33: Example
Since the space assignments are given before, the following Activity Relationship Diagram shows the relative Sizes of Each Department:

## Slide 34: Example

## Slide 35: Example
In this stage, there are no restrictions on the length and width of each department
In the final step, we should develop and evaluate several alternative layouts, while keeping in mind the Practical Limitations.

## Slide 36: Example
Some examples of Practical Limitations in this case were as follows:
1- It is considered that offices for partners (2), the meeting room (7) and the reception area (1) should be close to each other.
2- It is important that the juniors (4) and the managers (3) be close together.

## Slide 37: Example
As a result of these limitations, An alternative floor plan is developed as follows:

## Slide 38: Example

## Slide 39: Example
This floor plan may be revised many times until the best layout has been found.
Usually departments are positioned one by one, Beginning with the department with the Highest A or E ratings.
Systematic Layout Planning is essentially an organized Trial-and-Error Approach.

## Slide 40: Example
Therefore, unless all possible layouts are considered, There is no way to know if an Optimal Solution been Reached.
There are a variety of computer software packages and methods to do this.
http://www.hpcinc.com/rma/guides/RMA%201146%20SLP%20Overview%20Mfg.pdf

## Slide 41: What’s next?
Engineering
  Detailed system layout drawings – aisles, storage
  Requirements for electrical, lighting, computers
Implementation