## Slide 1: Examine On/Off and Studio 5000
Learning Objectives
Examine On instruction
Examine Off instruction
Studio 5000 software
  Opening
  Communication
  Upload/Download
  Controller Organizer
  Simple program
  Data Types

## Slide 2: Examine On Instruction
Looks like
2 parts
  Address
    Example: Local:1:I.data.1
  Instruction
    Asking the question
      Is Local:1:I.Data.1 ON? True or False
Path of TRUE’s to the output!!!

## Slide 3: Examine On Instruction

## Slide 4: Examine Off Instruction
Looks like
2 parts
  Address
    Example: Local:1:I.data.0
  Instruction
    Asking the question
      Is Local:1:I.Data.0 OFF? True or False
Path of TRUE’s to the output!!!

## Slide 5: Examine Off Instruction

## Slide 6: Studio 5000
Allen Bradley’s/Rockwell’s Software to program the Control Logix and Compact Logix PLC’s.
  Open it
  Choose processor
  Upload/download
  Create a program

## Slide 7: Studio 5000
Ladder Diagram location
Inputs used as many times as you want (limited by memory of the processor)
Outputs can be used ONCE as an output unless it is a latch/unlatch bits
Output can be used as an input as many times as you want
Tags
  Create a tag in controller
  Alias a tag to a local address
  Create an internal bit
  Explain data types

## Slide 8: Studio 5000
Tags
  Create a tag in controller
  Alias a tag to a local address
  Create an internal bit
  Explain data types

## Slide 9: Studio 5000
Data Types
  Bit = on (1) or off (0) = 2 states
  Byte = SINT = Single Integer = 8 bits = 256 states
  Word = INT = Integer = 16 bits = 65,536 states
  Double word = DINT = 32 bits = a lot of states