## Slide 1: Timers and Counters
Learning Objectives
Timers
  Types
  Data associated with them
Counters

## Slide 2: Timers
Types
  On Delay
    Non-retentive - resets when path of true is lost
    Retentive - remembers the accumulated value. Resets with a separate instruction.
    Off Delay

## Slide 3: Timers
Data Types
  Bits = On or Off
    Enable bit - EN - NO timing function! Simply means the rung in front of the timer is TRUE.
    Done bit - DN - Goes on when the Accumulated is equal to the Preset.
      Math formula ACC = PRE
    Timer Timing bit - TT - Goes on when the timer is enabled and the Accumulated is less than the Preset.
      Math formula ACC < PRE

## Slide 4: Timers
Data Types
  DINT = Double Integer 32 bits Lots of possibilities
    Preset - PRE - This is the value in which the timer will turn on the done bit.
    Accumulated - ACC - This is the current value of the timer.
  Both PRE and ACC can be written to and read from by other instructions in the program.
  When creating the tag choose TIMER data type.

## Slide 5: Counters
Data Types
  Bits = On or Off
    Count UP bit - CU - The counter is counting up.
    Count Down bit - CD - The counter is counting down.
    Done bit - DN - Goes on when the Accumulated is equal to or greater than the Preset.
      Math formula ACC => PRE
    Overflow - OV - The counter has been asked to count higher than it is capable.
    Underflow - UN - The counter has been asked to count lower than it is capable.

## Slide 6: Counters
Data Types
  DINT = Double Integer 32 bits Lots of possibilities
    Preset - PRE - This is the value in which the counter will turn on the done bit.
    Accumulated - ACC - This is the current value of the counter.
  Both PRE and ACC can be written to and read from by other instructions in the program.
  When creating the tag choose COUNTER data type.
  It is acceptable to use the same address for an up and down counter output!

## Slide 7: Present to the students how to enter a timer and counter in the program.