## Slide 1
ACADs (08-006) Covered
Keywords
Historical perspective, significant actions, ALARA. CFR 19, CFR 20, CFR 21, CFR 34, CFR 50, CFR 61, CFR 71
Description
Supporting Material
3.3.5.1 | 3.3.5.2 | 3.3.5.4 | 3.3.5.5 | 3.3.5.6.1 | 3.3.5.6.2 | 3.3.5.6.3 | 3.3.5.6.4
3.3.5.6.5 | 3.3.5.6.6 | 3.3.5.6.7 | 3.3.7.6.1 | 4.14.1 | 4.14.2 | 4.14.4 | 4.14.5
4.14.6.1 | 4.14.6.2 | 4.14.6.3 | 4.14.6.4 | 4.14.6.5 | 4.14.6.6 | . 4.14.6.7 | 
license21
Notes: <number>

## Slide 2: Historical
X-Rays Discovered by Roentgen – 1895
Roentgen’s Radiation Protection Standards
X-Ray Injuries led to Protection Standards
First Therapeutic Use of X-Rays – 2/1896

## Slide 3: Historical
Realization of Harmful Effects – 10/1896
X-Ray Machines in Major U.S. Cities – 1897
First Known Death From X-Rays – 1904
First Radiation Exposure Guidelines - 1915

## Slide 4: Significant Actions
1954 – Atomic Energy Act
1968 – Radiation Control Health & Safety Act
Industrial & Medical Diagnostic X-Rays
1974 – Atomic Energy Commission Split: 1. Nuclear Regulatory Commission (NRC) 2. Energy Research & Development Administration (ERDA)

## Slide 5: Significant Actions
1977 – ERDA Becomes the Department of Energy
NRC Regulates Radiation Safety
Agreement States Established

## Slide 6: Advisory Organizations - History
1915 – Design Criteria for X-Ray Devices
1920-1921 – Operating Requirements Considered
1925 – 1st Exposure Level Recommended
1925 – ICRU Formed
1928 – Roentgen Used as Unit of Radiation Measurement

## Slide 7: Advisory Organizations - History
1928 – ICRP Formed
1929 – Advisory Committee on X-Ray and Radiation Protection Formed in U.S.
1934 – ICRP First Dose Recommendation 0.2 R/day (50 R/yr)
1946 – Advisory Council Becomes NCRP

## Slide 8: Advisory Organizations - History
1947 – NCRP Lowers Dose a. ‘Permissible Dose’–0.3 R/wk b. As Low As Practical-ALAP
1956 – Permissible Dose Reduced to 0.1 R/wk (5 R/yr)
1957 – IAEA Established by UN
1959 – Federal Radiation Council (FRC)

## Slide 9: Advisory Organizations - History
1964 – NCRP Chartered by Congress
1966 – American National Standards Institute Established
1983 - Committee for Interagency Radiation Research and Policy Coordination Established in Office of Science & Technology

## Slide 10: Radiation Protection Standards and Guidelines
10 CFR 20 governs Radiation Protection
Awareness of the requirements necessary

## Slide 11: Philosophy
Risk based approach to radiation protection
  Limits stochastic effects of radiation exposure
  Avoids non-stochastic effects of radiation exposure
Combines internal and external dose
Annual dose limits only
5 (N-18) is N/A!

## Slide 12: Risk Based Approach
Stochastic risk is comparable to that for workers in other safe industries
  Assumes ALARA program is effective
  Cannot expose all workers to 5 Rem/year
Non-stochastic risk is ZERO

## Slide 13: Stochastic Effects
No dose threshold
Severity is NOT a function of dose
Probability of occurrence is a function of dose
Examples are:
  Cancer
  Genetic effects

## Slide 14: ALARA
As Low As Reasonably Achievable The Licensee shall use, to the extent practical, procedures and engineering controls based upon sound radiation protection principles to achieve occupational doses and doses to members of the public that are As Low As Reasonably Achievable (ALARA)

## Slide 15: Non-stochastic Effects
Well-defined dose threshold
Severity is a function of dose
Examples are:
  Cataracts
  Sterility
  Skin reddening

## Slide 16: Interrelationships
License Condition – Specific Requirement
NUREG – Supporting Information
Recommendation - Suggestions
Regulation – (CFR) - Legal Statement
Regulatory Guide – Technical Aid
Technical Specification – ‘Contract’

## Slide 17: 10 CFR 19 Notices, Instructions & Reports
19.11 - Posting of Notices to Workers 1. 10 CFR 19 & 20 (Available) 2. Operating License (Available) 3. Operating Procedures (Available) 4. Notice of Violations (Available) 5. Form NRC-3 (Posted)

## Slide 18: 10 CFR 19 Notices, Instructions & Reports
19.12 – Instructions to Workers
19.13 – Notices & Reports to Individuals

## Slide 19: 10 CFR 20 Standards for Protection Against Radiation; Final Rule

## Slide 20: 10 CFR 20 Subpart A
20.1001 – Purpose:
20.1002 – Scope:
20.1003 – Definitions (Almost 100)

## Slide 21: Important Terms
ALARA
ALI (Annual Limit on Intake)
CDE (Committed Dose Equivalent)
CEDE (Committed Effective Dose Equivalent)
DDE – (Deep Dose Equivalent)
DAC – (Derived Air Concentration)
DAC Hour – (DAC Times Exposure Time)

## Slide 22: Important Terms
Declared Pregnant Woman
Eye Dose Equivalent (LDE)
Fetus/Embryo Dose
Generally Applicable Environmental Radiation Standards (Issued by EPA)
Nonstochastic Effect

## Slide 23: Important Terms
Planned Special Exposure (PSE)
SDE (Shallow Dose Equivalent)
Stochastic Effect
TEDE (Total Effective Dose Equivalent) (DDE + CEDE)
TODE (Total Organ Dose Equivalent) (DDE + CDE)

## Slide 24: 10 CFR 20 Subpart B
Radiation Protection Programs Requirements 1. Radiation Protection Program 2. ALARA Program 3. Annual Review of Programs

## Slide 25: 10 CFR 20 Subpart C
20.1201 - Occupational Dose Limits
20.1202 – Sum Internal & External Doses
20.1203 – External Dose for Airborne
20.1204 – Determine Internal Exposure
20.1206 – Planned Special Exposures
20.1207 – Occupational Dose Limits for Minors
20.1208 – Dose to Embryo/Fetus/Worker

## Slide 26: 10 CFR 20
Subpart D – Radiation Dose for Individual Members of the Public Limited to 100 mrem (1 mSv) per year.
Subpart F – Surveys & Monitoring
Subpart G – Control of Exposure External Sources in Restricted Areas
Subpart L – Records
Subpart M - Reports

## Slide 27: OE16645
Improper Posting
Causes: - Inadequate Training - Inadequate Communications
Error Prevention Tools: - Two Minute Rule - Effective Communications - Self-Checking - Questioning Attitude

## Slide 28: 10 CFR 20 Subpart L - Records
20.2102 – Radiation Protection Program
20.2104 – Prior Occupational Dose
20.2105 – Planned Special Exposures
20.2106 – Individual Monitoring Results (NRC Form 5)
20.2107 – Dose to Member of the Public

## Slide 29: 10 CFR 20 Subpart M - Reports
20.2202 – Immediate & 24-hour Notifications to NRC
20.2203 – Reports Documenting Exceeding Limits
20.2204 – Reports of Planned Special Exposures
20.2206 – Reports of Individual Monitoring (NRC Form 5)

## Slide 30: Occupational Adult Dose Limits
Category NRC Limit
TEDE (External + Internal) 5 rem/year
TODE (External + Organ) 50 rem/year
Skin or Extremities 50 rem/year
Lens of Eye 15 rem/year

## Slide 31: Additional Dose Limits
Category NRC Limit
Occupational Dose Limits -10 % of Limit
For Minors for adults
Declared Pregnant Worker -500 mrem for
Gestation
Lifetime -No Limit
Member of Public -100 mrem/
year

## Slide 32: TVA’s Administrative Dose Levels
Up to 0.5 rem/year (5 mSv) 1. Current Year Estimate 2. No Authorization Required
To Exceed 0.5 rem/year (5 mSv) 1. Initiate Form 4 2. Attempt to Verify Current Year Dose 3. No Authorization Required

## Slide 33: TVA’s Administrative Dose Levels
To Exceed 1.0 rem/year (1 cSv) 1. Initiate Form 4 2. Attempt to Verify Current Year Dose 3. Approvals: Site RadCon Manager/RSO

## Slide 34: TVA’s Administrative Dose Levels
To Exceed 5.0 rem/year (5 cSv) 1. Initiate Form 4, Verify Information 2. Initiate Planned Special Exposure 3. Authorizations: a. Site RadCon Manager b. Plant Manager c. Site or Applicable VP d. VP, Nuclear Operations e. Senior VP, Nuclear Operations

## Slide 35: TVA’s Administrative Dose Levels
To Exceed 1N (TEDE shall not exceed 1N rem, where N = Individual’s age) 1. Form 4, Must be Verified 2. Authorizations: a. Site RadCon Manager b. Plant Manager c. Site VT d. VP, Nuclear Operations

## Slide 36: EPA Guidance for Nuclear Incidents
EPA Dose Equivalent Remarks
< 0.1 rem (< 0.1 cSv) No Sheltering
1 rem (1 cSv) Sheltering Initiated
1-5 rem (1-5 cSv) Public Evacuation
25 rem (25 cSv) Administer Stable
Iodine
> 25 rem (> 25 cSv) Save Lives/Protect Large Populations

## Slide 37: Planned Special Exposures
Annual Limits: a. 10 rems TEDE (5 Routine & 5 PSE); or 100 rems to any organ (50 Routine and 50 PSE); and b. 30 rems LDE (15 Routine & 15 PSE); and c. 100 rems Skin or Extremity (50 Routine & 50 PSE)

## Slide 38: Planned Special Exposures
Lifetime Dose Limits a. 25 rems TEDE or 250 rems to Organ or Tissue; and b. 75 rems to the Eye (LDE); and c. 250 rems to the Skin or Extremity

## Slide 39: Conditions for PSEs
An Exceptional Situation
Written Authorization Before Exposure
Individual Informed of Dose/Risk
Instructed in ALARA Techniques
Document all Prior Doses
Special Records Maintained
Limits: Annual – 5 rem; Lifetime – 25 rem

## Slide 40: Voluntary Prenatal Exposure Program
Training by RadCon to all Employees
Minimize Risk to Embryo/Fetus
Counseling Services Upon Request
Strictly Voluntary – Written Records Kept
Dose to Embryo/Fetus Should be: 1. ALARA 2. ≤ 50 mrem/mo. & 500 mrem/Gestation 3. Excluded from PSE Activities

## Slide 41: ALARA: Concepts
Law – Balance Exposure & Economics
Lead to Lower Dose Limits
ALARA guidelines: 1. Regulatory Guide 8.8 2. Regulatory Guide 8.10 3. Regulatory Guide 8.13
Respiratory Protection – Reg Guide 8.15
TVA’s Radiation Exposure Tracking

## Slide 42: ALARA: Bases
Any Change in Body from Ionizing Radiation Potentially Detrimental
Any Dose in Any Amount is Potentially Harmful
Cells Part of Delicate, Balanced System, Easily Disrupted by Radiation

## Slide 43: ALARA: Implementation
Management Commitment & Support
Careful Design of Facilities & Equipment
Well Trained, Committed & Aware Workers

## Slide 44: ALARA: Organizational Responsibilities
Plant RadCon Staff: - Implementation - Operation - Planning - Protection - Training
Plant Supervision: - Procedures & Work Orders

## Slide 45: ALARA: Individual Responsibilities
Individual Employee - Most Important: - Reduce own Dose - Follow Procedures - Report Radiological Hazards

## Slide 46: ALARA: Program Elements
ALARA Policy/Management Commitment
Worker/Line Management Commitment
Collective Dose Data Base System
ALARA Job Reviews
ALARA Design Reviews

## Slide 47: ALARA: Program Elements
ALARA Coordinator
Goals & Associated Tracking System
Employee Incentives to Reduce Dose
Management Incentives to Reduce Cost

## Slide 48: Other Regulations - 1
10 CFR 21 – Reporting Noncompliance
10 CFR 30 – Byproduct Materials License
10 CFR 31 – General Licenses

## Slide 49: OE15307
Leak Test Not Performed
Causes: - Inadequate Attention to Detail - Inadequate Communications
Error Prevention Tools: - Effective Communications - Self-Checking - Peer-Checking - Questioning Attitude

## Slide 50: Other Regulations - 2
10 CFR 34 – Radiography
10 CFR 50 – Power Production Facilities
10 CFR 61 – Radioactive Waste
10 CFR 71 – Transporting Rad Materials
49 CFR 100-199 – Transportation Regs

## Slide 51: 10 CFR 50
50.5 - Deliberate Misconduct Subject to fine
50.7 - Employee Protection “Whistleblower” protection
50.9 - Completeness and Accuracy Of Information (Provided to the NRC)
50.36- Technical Specifications

## Slide 52: Completeness and Accuracy of Information
Requirement – 10 CFR 50.9 Information must be: 1. Complete 2. Accurate
Implementation – TVAN Business Practice-213
Interface – Nuclear Licensing 1. Licensing Documents 2. Meetings 3. Conversations with NRC

## Slide 53: Rule Violation
The Requirement that all Information be Complete and Accurate may be Violated even though the Incorrect Information Submitted was: 1. Not in Writing 2. Not Under Oath 3. Not Intentional

## Slide 54: Incomplete or Inaccurate Information
False Statements
Omission
Inadequate Review
Failure to Review
Careless Disregard or Deliberateness
Negligence not Careless Disregard
Inadvertent Error
Failure to Correct or Update

## Slide 55: Responsibilities for Accurate Information
Chief Nuclear Officer/Executive VP Receive Material from NRC & Assign
Nuclear Licensing 1. Log Correspondence 2. Review Commitments 3. Responsible Organization for each Commitment
Responsible Organizations Evaluate Compliance with Commitments

## Slide 56: Responsibilities for Accurate Information
Organization Managers Assign Technical Lead
Technical Lead 1. Coordinate on Specific Input Data 2. Monitor Performance vs. Schedule 3. Provide Documentation 4. Prepare Response; Submit to Licensing

## Slide 57: Error Prevention Tools
Pre-Task Briefings
Research Bases and History
Follow Procedures
Verify Non-Routine Information
Ensure Independent Technical Review
Use Self-Checking or Peer-Checking

## Slide 58: Responsibilities of All Employees
TVAN Personnel 1. Document Commitments 2. Maintain Procedures 3. Coordinate NRC Contacts with Nuclear Licensing

## Slide 59: Technical Specifications
Safety Limits
Limiting Conditions for Operation
Surveillance Requirements
Design Features
Administrative Controls
Decommissioning
Initial Notification
Written Reports

## Slide 60: OE11952
Improper Control of Sources in Transit
Causes: - Inadequate Attention to Detail - Inadequate Communications
Error Prevention Tools: - Effective Communications - Self-Checking - Peer-Checking - Questioning Attitude

## Slide 61: TVA Documents
Radiation Protection Plan 1. Minimum Requirements and Management Controls for Radiation Protection 2. Verbatim Compliance Not Required
Plant RadCon Manuals 1. Implement Radiation Protection Plan 2. Verbatim Compliance Required

## Slide 62: Summary
Significant Advisory Organizations: 1. ICRU 2. ICRP 3. NCRP 4. FRC (EPA)
Significant Regulatory Agencies: 1. AEC 2. ERDA 3. NRC 4. DOE

## Slide 63: Questions
How much radiation is required to redden the skin (ESD)?
Why is there a need for radiation dose limits and guidelines?
What is the function of the NRC?
What is meant by an “Agreement State?”
What information is given in Title 10 Code of Federal Regulations Part 20, and what organization has the responsibility for regulating it?
What does ALARA mean?