## Slide 1
ACADs (08-006) Covered
Keywords
Plastic scintillator, flow-through ionization, end-window G-M tube.
Description
Supporting Material
Continuous Air Monitors
3.2.3.28.3 | 3.2.4.5.1 |  |  |  |  |  | 

## Slide 2: CAMs
Continuous air monitors are used to maintain a watch on the level air activity in an area such as the inside of a reactor containment shell.
Many varieties.
The collecting devices and detectors use depend on
  the nuclides
  levels of interest.
Several systems can be incorporated in parallel:
  flow-through ionization chamber may be used to monitor gases,
  while an end-window G-M tube looks at the particulates collected on a filter.

## Slide 3: CAMs
Other designs use:
  surface barrier detectors for ɑ ,
  plastic scintillators for β,
  NaI crystals for γ

## Slide 4: CAMs
CAM-5 was originally designed at ANL
The device uses the equilibrium counting ratio of radon daughters by simultaneously counting the β and α activity built up on a fixed filter.
The activities are each counted separately in two stacked gas proportional counters (piggyback probe) and read out on charts.
The unique feature is a third channel, which reads out the difference between the alpha counting rate and an arbitrarily selected fraction of the betta counting rate