## Slide 1
ACADs (08-006) Covered
Keywords
Dose, line, point, deep, eye, shallow, effective, committed, total, total organ, rad, gray.
Description
Supporting Material
External Exposure Control
1.1.8.3.1 | 1.1.8.3.2 | 1.1.8.3.3 | 3.3.1.8 | 3.3.1.9.1 | 3.3.1.9.2 | 3.3.1.9.3 | 3.3.1.9.4
3.3.1.9.5 | 3.3.1.9.6 | 3.3.1.10 | 3.3.3.4 | 3.3.3.13 | 3.3.3.14 | 3.3.4.11 | 3.3.7.2
3.3.7.5 | 3.3.7.6.2 | 3.3.7.6.3 | 3.3.1113.3 | 4.9.8 | 4.9.9.1 | 4.9.9.2 | 4.9.9.3
4.4.9.4 | 4.9.9.5 | 4.9.9.6 | 4.9.9.7 | 4.9.9.8 | 4.9.10 | 4.121.3 | 4.12.2

## Slide 2
Absorbed Dose
  Measures energy deposited in some given mass
  Originally defined as “rad” (Roentgen Absorbed Dose)

## Slide 3
Dose Equivalent (and equivalent dose)
  Modifying absorbed dose by quality factor produces dose equivalent
  Dose equivalent (HT) = rad X quality factor

## Slide 5
Sample problem
  While covering a job, a technologist receives 5 rad γ, 0.015 Gy β-, and .004 Gy nth. What was the equivalent dose for the job?

## Slide 6
Effective Dose Equivalent (and effective dose)
  Quantity used to assess risk from BOTH uniform whole-body and non-uniform partial body exposures
  Uses weighting factors, wT, to take into account reduced risk of cancer mortality and genetic effects when only some body organs receive a dose

## Slide 8
What is wT for the whole body?
Why?

## Slide 9
Sample problem
  An average diagnostic x-ray study of the thoracic spine delivers 0.115 Gy to patient’s thyroid and 0.040 Gy to the red marrow. What is the effective dose equivalent?

## Slide 10
Committed Dose Equivalent
  Applies to radioactivity deposited internally
  Given symbol HT,50
  Represents total cumulative dose to organ or tissue for a 50-yr period beginning the instant uptake occurs
Committed Effective Dose Equivalent
  Given symbol HE,50
  Represents radiation risk from internal radioactivity equivalent to risk from uniform whole body external exposure of same size

## Slide 12
Exposure Rate Determination
  To control exposure must know what it is
  Can estimate γ dose from known activity
  To determine field intensity (I) in R/hr at 1 ft. from a point source
  Accurate to within + 20% for energies 50 keV and 3 MeV
where: I = dose rate in Rem/hr @ 1 ft.
C = source activity in Curies (Ci)
E = gamma energy in MeV
N = % photon yield in decimal form

## Slide 13
  If N not given, assume 100%
  If > 1 photon energy given, each one taken into consideration
  For distances given in meters, use

## Slide 14
Sample problem
  Calculate the dose rate at 1 ft. for a 2.5 Ci point source of 99Mo, which emits the following gammas: 442.8 keV (82.4%), 133.1 keV (16.4%), and 289.7 keV (1.14%)

## Slide 16
Sample problem
  Calculate the dose rate at 1 ft. for a 5 Ci point source of 140Ba, which emits the following gammas: 537.3 keV (24.4%), 162.7 keV (6.2%), 304.9 keV (4.3%), and 423.7 keV (3.2%)

## Slide 17
Time
  Since Dose = DR X t, minimizing time in radiation field reduces dose
  Stay time is the maximum time allowed in a radiation field to preclude exceeding an allowable dose. Calculated as follows:

## Slide 18: External Exposure Control
Example problem
  A worker must enter a 1.7 R/hr γ radiation field to perform assigned work. Her accumulated dose equivalent for the month is 133 mrem. If the monthly ALARA guideline is 750 mrem, what is her stay time in the area?

## Slide 19
Distance
  Intensity of radiation field decreases as distance from the source increases
  Point source—an imaginary point in space from which all radiation is assumed to be emanating
  Radiation intensity point source  according to Inverse Square Law
    As distance from point source changes, dose rate  or  by square of ratio of distances from the source
    Becomes inaccurate close to source (i.e., about 10 times the diameter of the source)

## Slide 20
  Inverse Square Law
Where: I1 = Exposure rate at distance 1 (d1)
I2 = Exposure rate at distance 2 (d2)
d1 = Distance 1
d2 = Distance 2

## Slide 21
Example problem
  A point source of 60Co has a γ exposure rate of 6.2 R/hr at 5 ft. What would the exposure rate be at 2 ft?

## Slide 22
Example problem
  A 5 Ci point source of 60Co has a γ exposure rate of 5.0 R/hr at 1 m. At what distance would the dose rate be 100 mr/hr?

## Slide 23
  Line Source
    Line source treated as a series of point sources side by side along length of source
    Relationship between distance and exposure rate can be written mathematically as:
    Valid to point 1/2 of longest dimension of the line source (L/2), beyond which the point source formula should be used

## Slide 24
Example problem
  A small diameter tank containing radioactive sludge is 12 ft. long. The exposure rate at 1 foot is 22.4 R/hr. What is the exposure rate at 5 ft?

## Slide 25
Example problem
  A small pipe tank containing radioactive effluent is 18 ft. long. Exposure rate at 22 ft. is 1.5 R/hr. What is the exposure rate at 3 ft?

## Slide 26
  Plane Source
    Plane or surface sources can be floor, wall, large cylindrical or rectangular tank, or any other geometry where width or diameter is not small compared to length
    Requires calculus to calculate accurate dose rates

## Slide 27
    Relationship can be described for how exposure rate varies with distance from the source
      When distance to plane source is small compared to longest dimension, exposure rate falls off a little slower than 1/d (i.e. not as quickly as a line source)
      As distance from plane source increases, exposure rate drops off at a rate approaching 1/d2

## Slide 28
10 ft.
10 ft.
 @ < 1/d
>10 ft.
 @ < 1/d2

## Slide 29
Shielding Calculations
  Half-value layer —amount of shielding material required to reduce radiation intensity to 1/2 the unshielded value
  Calculated by the formula

## Slide 30
  Tenth-value layer — amount of shielding material required to reduce radiation intensity to 1/10 the unshielded value
  Calculated by the formula
  Both HVL and TVL depend on photon energy

## Slide 31
Photon Energy (keV) | HVL (cm) |  |  | 
 | Lead (11.35 g/cm3) | Iron (7.86 g/cm3) | Concrete (2.4 g/cm3) | Water (1.0 g/cm3)
500 | 0.38 | 1.0 | 3.3 | 7.2
1000 | 0.86 | 1.5 | 4.5 | 9.8
1500 | 1.2 | 1.8 | 5.6 | 12.0
2000 | 1.3 | 2.1 | 6.4 | 14.0
3000 | 1.5 | 2.4 | 7.9 | 17.5
Half-Value Layers

## Slide 32
    Attenuation can also be calculated based on HVL or TVL if HVL or TVL values are known, along with shielding thickness, using one of the following formulas
    or
    where:
    I = Shielded dose rate
    I0 = Unshielded dose rate
    x = No. of HVLs or TVLs (shield thickness divided by HVL or TVL)

## Slide 33
Buildup
  HVL and TVL approach works well for routine operational questions.
  If a high activity source and thick shielding are involved, problems arise
  Compton Scattering and Pair Production do not remove all photon energy

## Slide 34
  Residual, lower-energy Compton photons and annihilation gammas still transporting energy through the shield
  If shield is thick, stray photons can interact 2nd time and scatter in different direction producing exposure rate outside the shield > primary transmitting beam

## Slide 36
  The thicker and taller the shield, the greater the buildup
  Since Compton scatter and Pair Production are likely only for medium and high energy photons, respectively, photon energy will affect scatter contribution to dose rate
  Shield material (i.e., Z) also affects buildup
  Problem solved by introducing “buildup factor” into the gamma attenuation equation
  becomes

## Slide 37
  Buildup factor depends on shield Z, gamma energy, and the size and shape of the shield

## Slide 38
  Buildup factor depends on shield Z, gamma energy, and the size and shape of the shield
B | L | XL/X0 = Be-µL | L (cm) | μ’ (cm-1) | μ’/μ | μ’/μen
3 | 1.7 | 0.548 | 24 | 0.025 | 0.35 | 0.81
6 | 4.0 | 0.110 | 57 | 0.039 | 0.55 | 1.26
10 | 6.3 | 1.84E-2 | 89 | 0.045 | 0.64 | 1.46
20 | 10.9 | 3.69E-4 | 154 | 0.051 | 0.72 | 1.65
30 | 14.6 | 1.34E-5 | 207 | 0.054 | 0.76 | 1.75

## Slide 39
Sky Shine
  Room air not normally thought of as providing significant shielding for gammas, but air provides atoms with which gammas can Compton scatter
  Thus, gammas appear to turn corners
  Phenomena called “sky shine”

## Slide 40
  Name coined to reflect (no pun intended) fact that gammas appear to shine down from the sky if there is inadequate shielding above the source
  If an open-topped cell is used to contain high activity source, can produce significant radiation field outside cell wall

## Slide 42
Dose Compliance Reporting
  Designed to protect occupational workers
  Requires reporting annual dose and total lifetime dose to
    Worker
    NRC (in specific cases)
  Uses two forms – NRC Forms 4 and 5
  NRC Form 4
    Summary of lifetime dose history, year by year, by employer
    Includes internal and external doses for current year and TEDE for past years

## Slide 43
    Captures routine doses and those received as “Planned Special Exposures”
  NRC Form 5
    Detailed report of all doses of regulatory interest for the current year
    Together, Forms 4 and 5 constitute complete up-to-date worker dose history
  Not eligible for PSEs until Forms 4 and 5, or equivalent, are presented to employer

## Slide 44
Deep Dose Equivalent
Eye Dose Equivalent
Shallow Dose Equivalent – Whole Body
Shallow Dose Equivalent – Skin of Extremity
Committed Effective Dose Equivalent
Committed Dose Equivalent
Total Effective Dose Equivalent
Total Organ Dose Equivalent
No Record – No PSE!
Allowable dose  1.25 Rem for each quarter of no records

## Slide 45
Symbol for nuclide resulting in internal exposure in format
Xx-###x (Cs-137 or Tc-99m)
Clearance class (10CFR20.1001-2401, App. B)
Mode of intake: H=inhalation; B=skin absorption; G=ingestion; J=injection
Intake of each nuclide in µCi/ml
Deep Dose Equivalent
Eye Dose Equivalent
Shallow Dose Equivalent – Whole Body
Shallow Dose Equivalent – Skin of Extremity
Committed Effective Dose Equivalent
Committed Dose Equivalent
Total Effective Dose Equivalent
Total Organ Dose Equivalent
Additional info needed to determine compliance with limits (e.g., SDE,ME result of exposure from a discrete hot particle)

## Slide 46
Planned Special Exposures
  Cannot be used just to reduce collective dose
  One clear use – emergency lifesaving actions
  Dose limits
    0.05 Sv (5 rem) per year
    0.25 Sv (25 rem) per lifetime
  Must follow specific guidelines

## Slide 48
  Before worker can participate in PSE
    Lifetime dose history must be available
    Includes all doses for which annual limits exist
  Licensee must “attempt to obtain” this info
  Worker must provide signed statement or can request info from most recent radiation employer

## Slide 49
  PSE requires
    Exceptional circumstances
    Manager that approved
    Actions as part of PSE
    Why PSE was necessary
    ALARA steps taken to mitigate exposure
    Projected doses
    Actual doses received
  NRC must receive report within 30 days of any PSE