## Slide 1
ACADs (08-006) Covered
Keywords
ALI, DAC, total effective dose, whole body, internal organ, ingestion, inhalation.
Description
Supporting Material
Internal Exposure Control
3.3.7.1.1 | 3.3.7.1.2 | 3.3.7.1.3 | 3.3.7.1.4 | 3.3.7.2 | 3.3.7.3 | 3.3.7.4 | 3.3.7.5
3.3.7.6.2 | 3.3.7.6.3 | 3.3.7.7 | 3.3.7.8 | 3.3.10.5 | 4.9.9.5 | 4.9.9.6 | 4.9.9.7
4.9.9.8 | 4.9.10 |  |  |  |  |  | 

## Slide 2
Internal Exposure Control

## Slide 3: Internal Exposure Control
ALIs, and DACs, and CEDs, OH My!!!!!!!!!!!

## Slide 4: Internal Exposure Control
Annual Limit on Intake (ALI)
  50-yr CEDE found by comparing intake activity with the annual limit on intake
  1 ALI = amount of activity necessary to produce exactly:
    CED – 50 mSv (5 rem) – Body
    CD – 500 mSv (50 rem) – Organ

## Slide 5: Internal Exposure Control
  If > 1 nuclide taken in, various activities divided by respective ALI values cannot add to fraction > 1

## Slide 6: Internal Exposure Control

## Slide 7: Internal Exposure Control
Derived Air Concentration (DAC)
  Concept introduced by ICRP to assist in determining hazard with air concentration
  Expressed in μCi/ml (USA) or Bq/m3 (elsewhere)

## Slide 8: Internal Exposure Control
  Derived by referring back to reference man
    Reference Man breathes 2.4E9 ml or 2400 m3 during 2000-hr work year
    Based on not exceeding ALI in a year

## Slide 9: Internal Exposure Control
Sample Problem
A laboratory technician is exposed to airborne 40K. What is the calculated DAC for this case?

## Slide 10: Internal Exposure Control
Derived Air Concentration-hour (DAC-hr)
  Product of
    Concentration of radioactive material in the air
    Length of exposure to that nuclide, in hours
  Licensee allowed to use 2000 hrs to represent 1 ALI

## Slide 11: Internal Exposure Control
Problem
A DOE weapons facility worker is exposed for 8 hours to an air concentration of 6E-11 μCi/ml of PuO2. What is the dose (CED) from this exposure?

## Slide 12: Internal Exposure Control
Solution
ALI = 0.02 μCi = 2E-2 μCi
Air Concentration

## Slide 13: Internal Exposure Control
Cumulative Exposure
(7.5 DAC)(8 hrs) = 60 DAC-hrs
Resulting Dose

## Slide 14: Internal Exposure Control
Solubility Class
  Deals with biological clearance half-life
    Class D — < 10 days
    Class W — 10 – 100 days
    Class Y — > 100 days

## Slide 15: Ingestion
Blood
(Body Fluids)
GI
Tract
Feces
Other
Organs
Skin
Kidneys
Liver
Bile
Hair
Sweat
Urine

## Slide 16: Inhalation
Exhalation
Blood
(Body Fluids)
Lymph Nodes
GI
Tract
Respiratory
Tract
Feces
Other
Organs
Skin
Kidneys
Liver
Bile
Hair
Sweat
Urine

## Slide 17: Injection and Absorption
17
Blood
(Body Fluids)
GI
Tract
Wound Site
Feces
Other
Organs
Skin
Kidneys
Liver
Bile
Hair
Sweat
Urine

## Slide 18: Internal Exposure Control
Internal Dose Assessment
  Determine body or organ burden
    Bioassay
    Whole or partial body count
  Compute initial intake at t=0 or intake history
  Choose dose model
  Calculate internal CEDE

## Slide 19: Internal Exposure Control
Bioassay – In Vitro Techniques
  Basic Principles
    Refers to analysis for determining nature and activity of internal contamination by taking measurements of body excretion product
    Assumes concentration of activity in elimination products is proportional to activity in body

## Slide 20: Internal Exposure Control
    Sample activity concentration measured by conventional techniques.
    “Guess” made regarding proportionality constant based on previously measured behavior of the isotopes under similar conditions
    This is called “Body Burden”
    Bioassay measurements give burden at time of measurement, not intake

## Slide 21: Internal Exposure Control
    Number of elimination products have been used
    Urinalysis most commonly used – ease of collection and aesthetics
    Nasal swabs and exhaled air samples also commonly used

## Slide 22: Internal Exposure Control
  Contaminants loosely classified as soluble and insoluble
  Route of intake must also be specified
  Material Behavior
    Human body is essentially a chemical processing plant
      Food broken down chemically
      Identified chemically
      Utilized based on body’s needs

## Slide 23: Internal Exposure Control
  Behavior based on three factors:
    Chemical form / solubility
    Intake location / metabolic pathway
    Metabolic need / uptake vs elimination
  Routes of Entry

## Slide 24: Internal Exposure Control
    Inhalation and Ingestion most common
    Percutaneous refers to absorption directly through skin (common for 3H)
  Insoluble more difficult
    With ingestion, can pass through GI tract relatively unscathed
    If nuclide emits radiation that can’t be detected outside body, must use fecal analysis

## Slide 25: Internal Exposure Control
    For inhaling insoluble nuclides, clearance rates depend on pulmonary rates and size of particles
  Soluble contaminants further subdivided into three cases:
    Dissolve uniformly into body water
    Seeks a target organ
    Seeks bone

## Slide 26: Internal Exposure Control
  Urine considered body fluid, so [nuclideurine] considered equal to [nuclidebody water]
  Use Reference Man and Reference Woman to calculate
    Physiological makeup of average man and woman in terms of metabolic processes and mass and size of organs
    Total body water reference man = 42 kg
    Total body water reference woman = 29 kg

## Slide 27: Internal Exposure Control
  Body burden found by:
  Based on water having density of 1 kg/l

## Slide 28: Internal Exposure Control
  Sample Problem
  A female worker submits a urine sample with 0.01 μCi of 3H. Calculate her body burden, in Bq, at the time of sampling.

## Slide 29: Internal Exposure Control
  Sample Problem
  What would be the results if the sample were from a male instead of a female?

## Slide 30: Internal Exposure Control
Organ-Deposited Contaminants
  Chemical elements or compounds concentrated into certain body organs (target organs) based on metabolic activity
Bone Seekers
  Extremely long retention times after incorporation into bone tissue

## Slide 31: Internal Exposure Control
Intake Calculations
  Single Uptake Event
    Easiest calculational method uses Intake Retention Factors
    IRF gives fraction of initial intake activity present in whole body, organ, or excreta at various times after intake.
    Example: IRF for 24-hr urine sample is 10% on day 6. If collected and assayed on day 6, intake activity is 10 times total urine sample activity.

## Slide 32: Internal Exposure Control
    Formula
    Where:
    At = Measured activity in body or organ
    IRFt = IRF at corresponding time t

## Slide 33: Internal Exposure Control
Sample Problem
  A worker has an annual whole body count that shows 0.014 μCi of 137Cs and 0.052 μCi of 60Co.
  What is the estimated intake for this worker.

## Slide 34: Internal Exposure Control
  Because intake date is unknown, NUREG 8.9 suggests using mid-point of time span (i.e., 6 months ago)
  Linear interpolation of between day 300 and 400 listings for radionuclides listed in NUREG/CR-4884 gives following IRFs:
  137Cs – 5.93E-2
  60Co – 9.37E-2 or 1.16E-2 (depending on chem form)

## Slide 35: Internal Exposure Control

## Slide 36: Internal Exposure Control
    Better accuracy can be obtained from several successive in vitro counts
    Particularly true if date of intake is known
    NRC recommends using “minimum chi-squared statistic” formula
    Formula becomes
    “i” subscript represents the sequential measurement at some time “I”

## Slide 37: Internal Exposure Control
Sample Problem
  A research worker inhales a 32P labeled compound following a broken flask accident. A series of 24-hr urine samples, corrected for decay since sampling, showed the following concentrations, in μCi/ml: Day 2=1.5; Day 10= 0.13; and Day 20=0.06
  What was the 32P intake activity?

## Slide 38: Internal Exposure Control
  IRF values are 0.0417, 0.00434, and 0.00155 for days 2, 10 and 20, respectively.

## Slide 39: Internal Exposure Control
  Multiple or Continuous Uptakes
    Single intake usually the result of an accident
    More common is regular intake of small amounts or continuous exposure
    If multiple intakes are separated by >4 Τeff each intake can be treated as “single intake” and results added together
    Multiple intakes closer together than <4 Τeff treated as continuous by NRC

## Slide 40: Internal Exposure Control
Mathematics of Clearance
  Involves two independent and separate processes
    Radiological decay
    Biological removal
  Both biological and radiological clearance are assumed to follow exponential laws

## Slide 41: Removal Mechanisms
Radiological clearance
At = activity at some time (t)
A0 = activity original
e = Euler’s constant 2.71828…
λR = Radiological decay constant (ln 2/T1/2)
t = time allowed for decay
Biological clearance
At = activity at some time (t)
A0 = activity original
e = Euler’s constant 2.71828…
λB = Biological decay constant (ln 2/T1/2)
t = time allowed for decay

## Slide 42: Internal Exposure Control
  Can write equation for equation for body burden vs. time, At, due to combined effects of both biological and radiological clearance as follows:

## Slide 43: Internal Exposure Control
  Can write equation for equation for body burden vs. time, At, due to combined effects of both biological and radiological clearance as follows:

## Slide 44: Effective Half-Life
Te = Effective half-life
Tb = Biological half-life
Tp = Physical (radiological) half-life
λe = Effective removal constant
λb = Biological elimination constant
λp = Physical (radiological) decay constant

## Slide 45: Effective Half-Life
This valve will drain half the tank in 4 hrs.
This valve will drain half the tank in 2 hrs.
How long will it take to drain half the tank if both valve are open?

## Slide 46: Effective Half-Life

## Slide 47: Effective Half-Life
Nuclide | Tp | Tb | Te
Am-241 | 432.7 y | 204.8 y | 139 y
Co-60 | 5.27 y | 10 d | 10 d
Cs-137 | 30 y | 70 d | 70 d
Ir-192 | 74 d | very long | 74 d
Ra-226 | 1600 y | 45 y | 44 y
Sr-90 | 29 y | 15 d | 15 d

## Slide 48: Internal Exposure Control
Bioassay – In Vivo Techniques
  Involves placing external radiation detector near body to measure radiation from internally deposited nuclides.
  Works only for nuclides that can be detected externally
  Like in vitro, also gives burden at time of measurement, not at intake

## Slide 49: Internal Exposure Control

## Slide 50: Internal Exposure Control
Intake Calculations
  Single Uptake Events
    Number of methods used over the years
    Some use commercially available computer programs
    Others allow hand calculations and employ complicated models that allow many variables to be specified

## Slide 51: Internal Exposure Control
    Easiest method uses intake retention factors or IRFs
    IRF gives fraction of initial intake activity present in whole body, organ, or in excreta at various times after intake
    For example, if IRF for 24-hr urine sample is 10% on day 6, collecting and assaying urine on day 6 and multiplying by 10 will result in

## Slide 52: Elimination Mechanisms
Blocking agent
Diluting agent
Mobilizing agent
Chelating agent
Diuretics
Expectorants / Inhalants
Lung Lavage

## Slide 53: Elimination Mechanisms
Blocking agent
  Saturates a specific tissue with a stable element to minimize uptake of the radioactive element.
  Must be administered before, or immediately after the intake for maximum effectiveness.

## Slide 54: Elimination Mechanisms
Diluting agent
  Also known as displacement therapy. The body is given a large inventory of the stable element to choose from, thereby decreasing the chance of incorporating the radioactive element.

## Slide 55: Elimination Mechanisms
Mobilizing agent
  Increases the natural turnover process of the radioactive element.

## Slide 56: Elimination Mechanisms
Chelating agent
  Causes insoluble particles to remain in circulation until removed by the urinary system.

## Slide 57: Elimination Mechanisms
Diuretics
  Increase urinary excretion.

## Slide 58: Elimination Mechanisms
Expectorants / Inhalants
  Increase respiratory excretion.

## Slide 59: Elimination Mechanisms
Lung Lavage
  A ventilator tube is inserted into one lung while the other lung is repeatedly filled and drained with saline to remove material.
  Normally used only when acute effects of radiation threaten the patient’s life.