## Slide 1
ACADs (08-006) Covered
Keywords
Trending, incident, incident response, off-scale dosimeter, exposure to public, plume.
Description
Supporting Material
Off-Normal and Emergency Response
3.3.2.3 | 3.3.12.1 | 3.3.12.3 | 3.3.12.6 | 3.3.12.8 | 3.3.12.9 | 3.3.12.10 | 3.3.12.11
3.3.12.12 | 3.3.12.13 | 3.3.12.14 | 3.3.12.14 | 3.3.12.16 | 3.3.12.18 | 3.3.12.19 | 3.3.12.22
3.3.13.6 | 3.3.13.8 | 3.3.13.11 | 3.3.13.12 | 3.3.13.13 | 3.3.13.15 | 3.3.13.19 | 
Notes: RPT-243-6
Off-Normal and Emergency Response
ACAD-08-006: 3.3.2.3; 3.3.12.1; 3.3.12.3; 3.3.12.6; 3.3.12.8; 3.3.12.9; 3.3.12.10; 3.3.12.11; 3.3.12.12; 3.3.12.13; 3.3.12.14; 3.3.12.16; 3.3.12.18; 3.3.12.19; 3.3.12.22; 3.3.13.6; 3.3.13.8; 3.3.13.11; 3.3.13.12; 3.3.13.13; 3.3.13.15; 3.3.13.19
DOE: 2.13.01; 2.13.03; 2.13.04; 2.13.05; 2.13.06; 2.13.07; 2.13.08 ;2.13.10; 2.13.13; 2.13.14; 2.14.01; 2.14.02; 2.14.03; 2.14.04; 2.14.05; 2.15.01; 2.15.02; 2.15.03; 2.15.04
Duration: 3 hours
Material Resources Needed: none
Equipment/Supplies: Overhead display for PowerPoint
Assessment/Evaluation: The learning outcomes should be reviewed at the beginning of the class and should be reviewed periodically and at the conclusion. Examination number 3 (Final) will provide a formal assessment of these learning outcomes.
References Used in Development:
Basic Radiation Protection Technology, 5th and 6th edition, Gollnick; ISBN 0-916339-11-4
Nuclides and Isotopes/Chart of the Nuclides, 16th edition, Baum, Knox, Miller; ASIN: B000BUNFS8
Operational Health Physics Training, Moe; ANL-88-26 (1988)
DOE Health Physics Training, DOE-HDBK-1122-99 & DOE-HDBK-1122-2009
10CFR20 & 10CFR835 – current revisions

## Slide 2: Review Learning Outcomes
Previously Covered Outcomes
Notes: These learning outcomes have been addressed at least one other time. They are here to help ensure the student has achieved them by the end of the course. They are related to the topic of this lecture and thus review of them will help set the stage. The technical content pertaining to the outcomes is not repeated here.
The instructor should use some form of interactive activity to engage the class in covering the outcomes before starting new material.

## Slide 3: Review Prior Learning Outcomes Upon completion of this lesson, the student will be able to:
Identify the radiological consequence that may result from various incidents, such as:
  a sudden increase in dose rate,
  the uncontrolled spread of contamination,
  a leak or spill of contaminated liquid,
  an injury to an individual performing radiological work,

## Slide 4: Review Prior Learning Outcomes Upon completion of this lesson, the student will be able to:
Describe methods used for decontamination of areas within the plant, such as:
  mopping,
  using oil-impregnated wipes (masslin),
  wiping with damp rags,
  vacuuming, and
  scrubbing with brushes.

## Slide 5
Select the appropriate personnel decontamination techniques for various levels of contamination and the degree to which contamination is fixed.
  • removing particles with tape
  • scrubbing gently with soft brush
  • shaving contaminated hair
  • sweating and chemical decontamination
  • washing with lukewarm water and mild detergent
Review Prior Learning Outcomes Upon completion of this lesson, the student will be able to:

## Slide 6
Identify techniques available for the decontamination of tools and equipment, including the advantages, disadvantages, and limitations of each: • carbon-dioxide-pellet blasting • chemical decontamination • electropolishing • grit blasting • high-pressure water blasting • ice-pellet blasting • low-pressure water blasting • mechanical removal (grinding, machining, filing)
Review Prior Learning Outcomes Upon completion of this lesson, the student will be able to:

## Slide 7
Identify techniques available for the decontamination of tools and equipment, including the advantages, disadvantages, and limitations of each (cont’d): • spray washing • steam cleaning • ultrasonic cleaning • use of strippable coatings • washing in non-ionic detergent • wiping with lint-free cloth or oil-impregnated wipes
Review Prior Learning Outcomes Upon completion of this lesson, the student will be able to:

## Slide 8
Identify situations in which personnel decontamination is to be referred to other appropriate personnel:
  contaminated wounds;
  contaminated eyes, ears, nose, or throat; and
  contamination that cannot be removed through the use of approved techniques.
Describe special procedures for decontamination of radioiodines.
Review Prior Learning Outcomes Upon completion of this lesson, the student will be able to:

## Slide 9: Review Prior Learning Outcomes Upon completion of this lesson, the student will be able to:
Describe the procedure to be followed when an individual is contaminated, including performing a contamination survey (whole-body) by radiological protection personnel; recording contamination levels, location, date, and time on the personnel contamination report; (plant specific) direct decontamination of areas above the plant limit; identifying when nasal smears and/or a whole-body count are required; documenting the final results of decontamination; and interviewing the individual to identify the source of contamination.

## Slide 10
Describe why some areas of the plant are not to be decontaminated, such as:
  filter galleries,
  high radiation areas, and
  hallways between contaminated areas frequently traveled by operations personnel.
Review Prior Learning Outcomes Upon completion of this lesson, the student will be able to:

## Slide 11: New Learning Outcomes

## Slide 12: Off-Normal Response

## Slide 13
Explain the importance of using trending to identify the causes of individual incidents and the common causes of multiple incidents.
Discuss how reports of incidents at one plant can be useful in preventing similar incidents at another plant.
Identify work practices, instrument responses, and alarms that indicate the potential for a radiological incident.
Learning Outcomes (cont’d) Upon completion of this lesson, the student will be able to:

## Slide 14
Identify the immediate actions to be taken to control and minimize the extent of radiological incidents such as the following: • alarm on electronic dosimeter • area radiation monitor alarm • contaminated injured personnel • contaminated personnel • continuous air monitor alarm • fire in the radiologically controlled area
Learning Outcomes (cont’d) Upon completion of this lesson, the student will be able to:

## Slide 15
Identify the immediate actions to be taken to control and minimize the extent of radiological incidents such as the following (cont’d): • off-scale pocket dosimeter • contaminated liquid or resin spill • dry contaminated material spill • unmonitored release of radioactivity to the environment
Learning Outcomes (cont’d) Upon completion of this lesson, the student will be able to:

## Slide 16
Identify the radiological consequence that may result from various incidents, such as:
  a fire in the radiologically restricted area,
  the loss of a high-activity radiation source,
  a degraded core, and
  uncontrolled or unsecured high radiation areas.
Identify radiological surveys to be taken as a result of an incident and the purpose of each.
Learning Outcomes (cont’d) Upon completion of this lesson, the student will be able to:

## Slide 17
Evaluate radiological incidents to identify the scope and cause. Identify follow-up actions to correct the causes of the incidents.
Describe recent significant radiological incidents at this plant or at other nuclear power plants.
Learning Outcomes (cont’d) Upon completion of this lesson, the student will be able to:

## Slide 18: Emergency Response

## Slide 19: Learning Outcomes Upon completion of this lesson, the student will be able to:
Describe, in general terms, the expected response to radiological incidents, including:
  precedence given to treating injuries,
  mitigation and minimization of exposure to plant personnel and the public,
  mitigation and minimization of damage to equipment, and
  notification of appropriate personnel.
Discuss emergency dose limits for life-saving and the control of plant safety.

## Slide 20
Identify and quantify potential sources of exposure to the public from the plant liquid and gaseous effluent releases, transportation of radioactive materials, and major accidents.
Identify isotopes expected to be present in the event of a radiological incident.
Describe how to locate and track a radioactive plume.
Learning Outcomes (cont’d) Upon completion of this lesson, the student will be able to:

## Slide 21
Estimate the activity released during an incident using the following:
  airborne activity levels in a plume
  contamination levels and extent of area contaminated
  gaseous/particulate-specific activity and volume released
  liquid-specific activity and volume released
  prerelease and postrelease radiation surveys (for example, pipe, valves, tanks)
Learning Outcomes (cont’d) Upon completion of this lesson, the student will be able to:

## Slide 22
Outline
Introduction
Off- Normal Events and Response
Emergency Planning and Response
Notes: 2/13/2013
22

## Slide 23: Introduction
Notes: 2/13/2013
23

## Slide 24: Introduction
Lessons learned from the earliest accidents can and do still apply today.
The RPT plays an critical role in responding to off-normal events and all phases of any emergency.
It’s important to understand when an off-normal event moves to an accident and when an accident moves from an emergency to consequence management.
Off-normal events and emergency events will happen, so you must be prepared to respond.

## Slide 25: Introduction
There are many instances within the daily operations of a nuclear facilitiy that may occur which might be classified as an off-normal or abnormal event.
These are events which do not meet the criteria of an emergency necessarily; however, failure to mitigate them may result in a situation being reached which may lead to regulatory violation or an emergency event.

## Slide 26: Introduction
NRC Licensees are also required to report events which meet certain criteria – specified in 10CFR 50.72 and .73 . Specific significant criteria for reporting are specified in 10CFR20.2202
  These start as Event Notification Reports and may elevate to more detailed reports depending on the event.
  Licensee Event Reports (LERs) are more detailed requiring detailed investigations and corrective actions.

## Slide 27: Introduction
The DOE also has a formal program conducted under the auspice of Environmental Protection, Sustainability Support & Corporate Safety Analysis (SESA) – Office of Analysis

## Slide 28: Introduction
Most facilities have pre-established procedures to address the actions required to be taken in order to mitigate the events.
Also, normally, the facility will have an event reporting process in which the event is documented, investigated, root cause determined and corrective actions specified to prevent recurrence.
By evaluating and understanding why events happen, steps can be taken to prevent their recurrence.

## Slide 29: Introduction
These event reports and investigations are shared within the industry as Operating Experience Reports.
By sharing lessons learned, facilities can take proactive measures to prevent the same type of event from occuring at their facilitiy.
The NRC, DOE, and the Institute of Nuclear Powwer Operations (INPO) and the World Association of Nuclear Operations (WANO) all have mechanisms for sharing these reports.

## Slide 30: Introduction
Nuclear Emergencies, in the US, are managed according to the Federal Radiological Emergency Response Plan (FRERP) approved in 1985, revised 1991
  Federal Radiological Emergency Response Plan
The objective of the Federal Radiological Emergency Response Plan (FRERP) is to establish an organized and integrated capability for timely, coordinated response by Federal agencies to peacetime radiological emergencies.

## Slide 31: Introduction
The FRERP:
  Provides the Federal Government's concept of operations based on specific authorities for responding to radiological emergencies
  Outlines Federal policies and planning considerations on which the concept of operations of this Plan and Federal agency specific response plans are based and
  Specifies authorities and responsibilities of each Federal agency that may have a significant role in such emergencies.

## Slide 32: Introduction
There are two Sections in this Plan.
  Section I contains background, considerations, and scope.
  Section II describes the concept of operations for response.
This plan designates lead federal agency

## Slide 33: Introduction
Lead Federal Agency – Responsible for the protection of the public and environment at the accident site.
  NRC for domestic licenses
  EPA – domestic unregulated or originating in a foreign country
  Agreement States
Actual response is performed in accordance with individual facilities’ formal Emergency Plans.

## Slide 34: Off-Normal Events

## Slide 35: Generic Response
Each facility will develop station specific procedures for responding to off-normal and emergency radiological events.
The steps presented here are generic and are used to illustrate actions taken in response to the events.

## Slide 36: Early Warning
There may often be indications detected which serve as early warning signs of a developing radiological event or one already in progress.
An RPT with a sharp sense of situational awareness will often times be the first alert in such situations.
In any case, RP will always be involved in identifying, confirming, quantifying, and resolving all radiological events.

## Slide 37: Early Warning
At times, work events will be the early indicators (or initiators) of the event.
  Facility processes such as waste processing, system alignments and activites such as tank filling or system flushing may result in off-normal radiological conditions such as elevated radiation levels in the facility.
  A work crew performing maintenance requiring the opening of a radioactive system may cause airborne radioactivity or the spread of radioactive contamination if performed improperly.

## Slide 38: Early Warning
At times, elevated RP instrument readings may be the indicator alerting the station to a developing event
At times, the radiological conditions may reach the warning or alarm setpoints of installed area or process radiation monitors or on ventilation airborne concentration monitors.

## Slide 39: Immediate Actions
In general all radiological events can be classified into one of four categories:
  Elevated radiation levels
  Spread of contamination
  Airborne radioactivity
  Loss of control of radioactive material
The immediate actions taken by Radiation Protection can help to quantifiy and mitigate the event from a radiological standpoint.

## Slide 40: Immediate Actions
Note that supervisory personnel are notified as part of the immediate actions associated with the discovery of an event. They will provide immediate oversight and direction as the event unfolds.
Ultimately as appropriate, the position on site who has overall command and control of the facility will be notified and will provide oversight in the facility’s response to the event.

## Slide 41: Immediate Actions Elevated Radiation Levels
Elevated radiation levels can first be suspected by the occurrence of one or more alarms:
  Personal Alarming Dosimeter (PAD) dose or dose rate alarm (or off-scale pocket dosimeter)
  Area Radiation Monitor (ARM) goes into alert warning (amber) or alarm (red)
  High readings on portable survey instrument

## Slide 42: Immediate Actions Elevated Radiation Levels
In the case of an alarming PAD:
  If the alarm is a dose rate alarm – the individual should back out of the area causing the alarming.
  If the alarm continues or if the dose rates are excessive beyond what was expected for the area:
    the individual should be instructed to exit the area and
    an RPT should perform a general area radiation survey to identify the cause of the eleveated dose rates.

## Slide 43: Immediate Actions Elevated Radiation Levels
In the case of an alarming PAD:
  If the alarm is a dose alarm (or off-scale SRD) – the individual should exit the area immediately and report to RP.
  RP will investigate the cause of the alarm which may include conducting a radiation survey on the area

## Slide 44: Immediate Actions Elevated Radiation Levels
In the case of an alarming ARM:
  Depending on the remote readout, RP maybe directed to conduct a survey of the area covered by the ARM.
  If performed, this will confiorm the validity of the alarm and will also be used to identify the cource of the radiation causing the alarm.
  If the remote readout is excessive, RP may be directed to take dose rate readings in adjacent areas.

## Slide 45: Immediate Actions Spread of Contamination
Spread of contamination can be detected in several different ways.
  Personnel alarming a personnel contamination monitor (PCM)
  Contamination detected on an individual during a hand frisk
  Contamination detected on a survey of a normally clean area
  Detection of uncontained leakage from a known contamination source
  Spillage of contaminated liquid or dry material

## Slide 46: Immediate Actions Spread of Contamination
Specific immediate actions will be dictated by the event.
In events involving personnel:
  As discussed previously:
    If personnel injury is involved, treating the injury takes priority over normal contamination control. Medical personnel will provide direction.
    If injury is not an issue, the RPT will survey or direct the survey of the individual to identify location, quantity, and cause of the contamination

## Slide 47: Immediate Actions Spread of Contamination
In the case of finding contamination on a survey:
  RPT will establish those controls necessary to contain the area and prevent the continued spread of contamination.
  Another survey will be conducted in an atteempt to identify the source of the contamination and the exent of the spread of the contamination.

## Slide 48: Immediate Actions Spread of Contamination
In the case of a spill of radioactive liquid, resin or dry material the standard SWIMS accronym should be used to direct the immediate actions:
  S – Stop the spill if possible and cover the spill
  W – Warn others
  I – Isolate the area – barricade, posting etc.
  M –Minimize the spread and monitor the area
  S – secure or redirect local ventilation
If the spill involves dry material, ensure ventilation is redirected and the material is covered.

## Slide 49: Immediate Actions Spread of Contamination
If the spill involves highly radioactive material such as expended resin, then dose considerations must be observed and may take priority in the recovery effort.

## Slide 50: Immediate Actions Airborne Radioactivity
There are various potential causes for airborne radioactivity in a facility depending upon the nature of the operations that occur at the facility.
RP may be alerted to the presence of airborne radioactivity by:
  The initiation of a continuous air monitor (CAM) alert or alarm
  High activity detected on a job coverage, breathing zone, or routine grab sample
  Several personnel exiting and alarming a PCM

## Slide 51: Immediate Actions Airborne Radioactivity
Depending on the indications alerting the RP to the event, immediate actions can include:
  Obtaining back-up air samples
  Checking installed and temporary ventilation flow in process areas
  Inspecting the area looking for airborne causing activities sucah as:
    cutting or grinding contaminated surfaces
    opening, venting, or draining radioactive systems

## Slide 52: Immediate Actions Unmonitored Release
Any pathway to the environment that is not monitored by calibrated instrumentation is considered an unmonitored pathway.
The spill of radioactive liquids, resin, or solid material and the occurrence of airborne radioactivity can also lead to an unmonitored release of radioactivity to the environment.

## Slide 53: Immediate Actions Loss of Control of Radioactive Material
Anytime a licensed source is not where it is supposed to be, some amount of control has been lost.
If that licensed source leaves the confines of the normal owner controlled area without the required controls being in place, then members of the general public have been placed at risk.
In addition to making the required state and federal notifications, the licensee is tasked with taking all steps necessary to location and restore the source to their control.

## Slide 54: Immediate Actions Loss of Control of Radioactive Material
Obviously, RP will play a central role in searching for and recovering the lost source.

## Slide 55: Immediate Actions Fire in an RCA
Any fire in an industrial setting is significant.
A fire in a radiologically controlled area (RCA) multiplies that significance.
Depending on the speccifics, a fire can result in:
  Airborne radioactivity
  An unmonitored release
  An increase in contamination
  An increase in local dose rates

## Slide 56: Immediate Actions Fire in an RCA
The RPT’s role in response to a fire focuses on providing radiological protection to the fire fighters and first responders
  Monitoring dose rates
  Obtaining and analyzing air samples
  Performing contamination surveys

## Slide 57: Immediate Actions Uncontrolled or Unsecured High Radiation Area
Any area identified as a High Radiation Area (greater than or equal to 100 mrem/hr at 12” (30cm)) is required to have some level of controls established.
As a minimum, this is normally accomplished with posting.
In some applications when the dose rate reaches 1000 mrem/hr, the area must also be maintained in a locked area with administrative controls placed on access.

## Slide 58: Immediate Actions Uncontrolled or Unsecured High Radiation Area
In the event a High Radiation Area is found which is not properly controlled, the RPT must take control of the area immediately, evacuate unecessary personnel, notify supervision, and obtain a survey of the area.

## Slide 59: Operating Experiences
NOTE TO INSTRUCTOR – Find 2-3 OE Events to review to understand how OE is published and lessons that can be learned from others experiences.

## Slide 60: Emergency Response

## Slide 61: Introduction
Many of the off-normal conditions discussed earlier may actually be indication of the on-set of a more serious condition in the facility.
  High dose rates
  Alarming dosimetry
  Alarming ARMs or CAMs
Because of this, all off-normal conditions are promptly reported to station management and are evaluated in light of other idications in the facility.

## Slide 62: Introduction
Also, since these events often seem to occur in the off hours, your response to the early indicators may be some of the first and, arguably, most important at diagnosing the problem and implementing early mitigating actions.

## Slide 63: Introduction
In this section, we will look:
  first - at the reporting and classification categories
  second - at the general phases associated with emergencies
  third - at the emergency response and actions

## Slide 64: Reporting and Classification

## Slide 65: Reporting and Classification
Emergencies can be classified by:
  Dose, Injury, and Damage
  Location Relative to the Facility
  Exposure Conditions
As discussed earlier, incidents and events are reported under a formalized program specific to the organization and stipulated in the applicable regulatory requirements.

## Slide 66: 10CFR20.2202 Criteria Classification by Injury, Damage and Dose
Immediate Notification Required (within 30 minutes):
  TEDE 250 mSv (25 rem) or more
  Eye dose of 750 mSv (75 rem)
  Skin/extremities dose of 2.5 Gy (250 rads) or more
  Release of material in a quantity of 5 ALI
  Loss of 1 work week of facility operations
  Property damage exceeding $200,000

## Slide 67: 10CFR20.2202 Criteria Classification by Injury, Damage and Dose
Twenty-four Hour Notification:
  TEDE 50 mSv (5 rem) or more
  Eye dose of 150 mSv (15 rem)
  Skin/extremities dose of 0.5 Sv (50 rem) or more
  Release of material in a quantity of 1 ALI
  Loss of 1 work day of facility operations
  Property damage exceeding $2,000

## Slide 68: 10CFR20.2202 Criteria Classification by Injury, Damage and Dose
Thirty Day Written Notification:
  All of the above events
  Doses in excess of occupational limits
  Doses in excess of public limits
  Dose rates or concentrations > restricted area limits
  Dose rates or concentrations > 10 X unrestricted area limits

## Slide 69: Classification by Location
Onsite
  Occurs within the legal geographical boundary of a license and all the consequences are confined within that location. Members of the general public are not affected
Offsite
  Occurs at a location outside the facility boundary or occurs as a result of the escape of radioactive material from within the facility to public areas. This will involve members of the general public.

## Slide 70: Classification by Exposure Conditions
Non-Contaminating/Observable –
  no release,
  exposure of personnel to an external radiation source for a finite period of time.
  priority is to securing the source of exposure and determining the dose received by involved personnel.

## Slide 71: Classification by Exposure Conditions
Non-Contaminating/Undiscovered -
  no release,
  source of exposure potential for long period of time before discovery,
  extent of number of personnel exposed not known initially,
  priority is:
    to secure the source
    determine the population of workers involved
    evaluate doses received

## Slide 72: Classification by Exposure Conditions
Contaminating/Observable –
  release involved
  momentary loss of control of radioactive material
  spill or airborne
  ingestion or inhalation may be involved
  priority is:
    personnel safety
    control of material
    evaluation

## Slide 73: Classification by Exposure Conditions
Contaminating/Undiscovered –
  release involved
  initially undetected
  initial source unknown
  population affected unknown
  priority is:
    identify source and secure it
    identify population affected
    quantify and evaluate

## Slide 74: Accident Phases

## Slide 75: Accident Phases
Occurrence Phase –
  the events immediately preceding the accident and the physical happenings of the accident
  usually the shortest of four phases
  usually details are only known after the fact and are a result of the post-accident investigation.
Notes: (Gollnick pp 610-612, fig. 6)
Any given accident can be expected to display and progress through the four phases shown here. Some are very short in duration - others are protracted and dependent upon the specific accident, location, etc.

## Slide 76: Accident Phases
Emergency Phase –
  immediate life and property saving actions taken by personnel in the near vicinity
  relatively short
  personnel accountability
  emergency first aid
  implementation of formal E-Plan and activation of the emergency response organization (ERO)
  Emergency Dose Guidelines maybe initiated
Notes: (Gollnick pp 610-612, fig. 6)
Any given accident can be expected to display and progress through the four phases shown here. Some are very short in duration - others are protracted and dependent upon the specific accident, location, etc.

## Slide 77: Accident Phases
  Emergency Dose Guidelines can be initiated in conjunction with the E-Plan on a voluntary basis as the need directs:
    Up to 10 rem for major property saving actions
    Up to 25 rem for life-saving actions or protection of large populations
    Above 25 rem for life saving actions or protection of large populations only for specific volunteers briefed on the consequences and risks associated with this dose.
Notes: (Gollnick pp 610-612, fig. 6)
Any given accident can be expected to display and progress through the four phases shown here. Some are very short in duration - others are protracted and dependent upon the specific accident, location, etc.

## Slide 78: Accident Phases
Recovery Phase –
  mobilization of larger pool of personnel for assistance
  regulators and off-site public health authorities notified and activated
  conclusion of this phase occurs when the extent of the impact has been determined and controls are established
Notes: (Gollnick pp 610-612, fig. 6)
Any given accident can be expected to display and progress through the four phases shown here. Some are very short in duration - others are protracted and dependent upon the specific accident, location, etc.

## Slide 79: Accident Phases
Restoration Phase –
  most time intensive
  involves all clean-up activities – restored to pre-event levels (minimum)
  medical treatment and follow-up activities
  all litigation has been resolved
  decision made to either decommission and dismantle or restore to full operation
Notes: (Gollnick pp 610-612, fig. 6)
Any given accident can be expected to display and progress through the four phases shown here. Some are very short in duration - others are protracted and dependent upon the specific accident, location, etc.

## Slide 80: Emergency Planning and Response

## Slide 81: Emergency Plan Components
The different sectors of the nuclear industry have varying requirements regarding the formulation of the required emergency plan.
A nuclear power plant will have an extensive multiple volume plan which is required by 10CFR50.47 as a part of the licensing process and actually becomes a part of the license.
A small warehouse storing limited quantities may have a very simple four or five page document.
Notes:   Gollnick Page 612, fig. 7

## Slide 82: Emergency Plan Components
Regardless, each E-Plan will contain at least a reference to the following components:
  On-Site Authority
  Off-site Agency Contacts
  Credible Site Emergencies
  Warning Monitor Specifications and Locations
  Emergency Action Levels
  Emergency Facilities and Equipment
  Employee Training/Retraining Programs
  Public Relations and Legal Assistance
  Other Hazards Related to Radiological
  Provision for Updating and Exercising the Plan
Notes:   Gollnick Page 612-615, fig. 7
On-Site Authority - A list of persons that have the authority to call in outside
help, evacuate the site, initiate entry into a contamination zone and take other emergency
related actions should be prepared and maintained up to date.
  Off-site Agency Contacts – State and federal agencies needed as well as qualified expert vendors for assistance
  Credible Emergencies – those events which have a reasonable chance of occurring at the station – earthquakes, tsunamis, fire, flooding, etc.
Warning Monitor Specifications – based on the credible accident analysis able to detect the isotopes and the quantity expected
Emergency Action Levels (next slides)
Facilities and Equipment – needed to handle the needs of the response crews
Train and Retraining (10CFR19.12 requires all employees be trained to a minimum level to properly respond to warnings and alarms. Also detailed implementation training for all responders
Public Relations and Legal –
  Other Hazards Related to Radiological – other concerns to consider such as a biohazard as well as radioactivity
  Provision for Updating and Exercising the Plan – practice, review, critique, change, train, practice and review. An on-going and continuous cycle of reflection and improvement.

## Slide 83: Emergency Plan Components
10CFR50.47 and EPA Manual for Protective Action Guidelines establish the requirement for designating two concentric emergency planning zones (EPZs) around each plant centered on the reactor building:
  10 mile EPZ – referred to as the plume exposure pathway. The majority of general population exposure due to direct plume exposure and ground contamination
  50 mile EPZ – referred to as the ingestion exposure pathway. The majority of general public dose will be received through ingestion of drinking water, vegetation, other food supplies
Notes:   Gollnick Page 612-615,

## Slide 84: Emergency Plan Components
Further, the law requires:
  The electric utility be able to:
    classify an emergency into one of four standardized cases,
    notify off-site authorities, and
    recommend public protective actions.
  The responsible off-site authorities must be able to:
    determine the proper protective actions,
    alert and notify the general public within 15 minutes, and
    assist the public in carrying out the recommended protective actions.
Notes:   Gollnick Page 612-615,

## Slide 85: Emergency Plan Components
The NRC has standardized nuclear power plant emergencies into four classes or Emergency Action Levels (EAL) according to severity:
  Unusual Event – an abnormal condition in plant operation that does not pose any public health hazard. Appropriate notifications are made and the event will be addressed used standard processes and procedures.
Notes:   Gollnick Page 612-615

## Slide 86: Emergency Plan Components
  Alert – next higher severity level. An event involving an unknown or significant decrease in the level of protection for the public or on-site personnel. When an alert is declared, the state of readiness of the on-site and off-site response organizations is increased and additional assessments are made.
Notes:   Gollnick Page 612-615
  http://www.iaea.org/ns/tutorials/regcontrol/intro/glossarye.htm accessed 9/28/2011
  The incident results in actual or potential reduction of plant safety, e.g., an accident involving handling of spent fuel. Off-site response is
  called for. Local agencies would activate their emergency operations centers to operational status. They would then await further developments. No public action would be necessary.

## Slide 87: Emergency Plan Components
Site Emergency - An event resulting in a major decrease in the level of protection for the public or on-site personnel. This includes:
  a major decrease in the level of protection provided to the reactor core or large amounts of spent fuel; or
  conditions where any additional failures could result in damage to the reactor core or spent fuel; or
  high doses on-site.
  When a site area emergency is declared, preparations should be made to take protective actions off-site and to control the doses to on-site personnel.
Notes:   Gollnick Page 612-615
  http://www.iaea.org/ns/tutorials/regcontrol/intro/glossarye.htm accessed 9/28/2011
The event would not, however, require protective actions beyond the plant boundary. A leak in the primary coolant system greater than the capacity to replace the water would be an example of this level of emergency.

## Slide 88: Emergency Plan Components
General Emergency - An event resulting in an actual release, or substantial probability of a release, requiring implementation of urgent protective actions off-site. This includes:
  actual or projected damage to the reactor core or large amounts of spent fuel; or
  releases off-site resulting in doses exceeding intervention levels for urgent protective actions within hours.
  When a general emergency is declared, urgent protective actions are recommended immediately for the public near the facility.
Notes:   Gollnick Page 612-615
  http://www.iaea.org/ns/tutorials/regcontrol/intro/glossarye.htm accessed 9/28/2011
This requires complete mobilization of the off-site emergency organizations and probable alert of the general public within the 10 mile EPZ. The loss of integrity of 2 out of three of the barriers to fission product release – fuel cladding, pressure vessel, and containment building – along with potential loss of the third would constitute a General Emergency.

## Slide 89: Initial Accident Responses (RPT)
  Your initial response as an RPT on-site or off-site will be directed by the actual event but in general keep the following priorities in mind:
  Life saving first aid always has the highest priority
  Familiarize yourself with the area – situational awareness
  Evacuate/relocate personnel to safe area
  Call for help
  Minimize spread of contamination
  Screen and segregate personnel by conditions
Notes: Gollnick 617, Fig 9

## Slide 90: Initial Accident Responses (RPT)
Screen and Segregate
  Contaminated/injured
  Contaminated/not injured
  Not contaminated
  Activated?
  Chelation?
  KI?
Notes: Gollnick 619-626, Fig 9

## Slide 91: Additional Accident Responses (RPT)
As the situation dictates, off-site monitoring teams may be dispatched within the 10 mi EPZ to position themselves to monitor the impact of the accident on the zone.
Requires airborne sampling, dose rate monitoring, as well as vegetation sampling for further analysis
The field teams will be used to track the plume and to validate the computer model being used to calculate off-site doses.
Notes: Gollnick 617, Fig 9

## Slide 92: Additional Accident Responses (RPT)
Plume tracking and monitoring is a coordinated effort where the command center will direct the field teams to run parallel to the plume track.
At a specified location, the team will proceed to traverse the plume – stopping at centerline to obtain dose rate information and collect an air sample.
The dose rate information is communicated back via radio and the air sample is field counted and then delivered to an analysis location.
This field data is then correlated with the computer model to validate the information.
Notes: Gollnick 617, Fig 9

## Slide 93: Additional Accident Responses (RPT)
The model’s parameters are determined based on measured release rate, measured or calculated activity levels (based on postulated concentrations derived from isotopic ratios assuming a certain amount of core damage and power history)
The model permits very complicated dose calculations which in turn may be used to formulate protective action recommendations to the local health officials.
Notes: Gollnick 617, Fig 9

## Slide 94: Beyond the Facilities’ Organization
As noted in the beginning of this lesson, nuclear emergencies, in the US, are managed according to the Federal Radiological Emergency Response Plan (FRERP) approved in 1985, revised 1991
  Federal Radiological Emergency Response Plan
The objective of the Federal Radiological Emergency Response Plan (FRERP) is to establish an organized and integrated capability for timely, coordinated response by Federal agencies to peacetime radiological emergencies.

## Slide 95: Beyond the Facilities’ Organization
The FRERP:
  Provides the Federal Government's concept of operations based on specific authorities for responding to radiological emergencies
  Outlines Federal policies and planning considerations on which the concept of operations of this Plan and Federal agency specific response plans are based and
  Specifies authorities and responsibilities of each Federal agency that may have a significant role in such emergencies.

## Slide 96: Beyond the Facilities’ Organization
There are two Sections in this Plan.
  Section I contains background, considerations, and scope.
  Section II describes the concept of operations for response.
This plan designates lead federal agency

## Slide 97: Beyond the Facilities’ Organization
Lead Federal Agency (LFA) – Responsible for the protection of the public and environment at the accident site.
  NRC for domestic licenses
  EPA – domestic unregulated or originating in a foreign country
  Agreement States
Actual response on station is performed in accordance with individual facilities’ formal Emergency Plans.

## Slide 98: Beyond the Facilities’ Organization
Once an emergency has occurred, either the state officials or the LFA can activate the FRMAC (Federal Radiological Monitoring and Assessment Center) – an interagency asset under auspice of the DOE.
Notes: Gollnick Ed 6, pp 637-641

## Slide 99: Beyond the Facilities’ Organization
Some of the available Federal Assets (partial listing) that may be activated based on the incident:
  RAP – Radiological Assistance Program (DOE) Teams stationed at eight strategic locations around the US at DOE facilities (SRS has one)
  NEST – DOE Nuclear Emergency Search Teams – Nevada Operations Office in Ls Vegas, respond to nuclear terrorism
  RERT – Radiological Emergency Response Team – EPA – response to unregulated sources such as lost sources or sources of unknown origin.
Notes: Gollnick Ed 6, pp 637-641
The RAP team acts as the Advance Party following FRMAC activation. Based on it’s on-scene assessment, a FRMAC Phase I response can be in place on-scene in 8 hours if appropriate. A FRMAC Phase II response can follow in 11 hours and a Full-Field FRMAC can be setup in 24 to 36 hours.
NEST consists of a group of volunteer scientists and technicians from the nuclear weapons development program who are on call in the event of an incident. The NEST response includes the search, detection, and identification of lost or stolen nuclear weapons or special nuclear materials or sources involved in radiation threats. They can be deployed within 2 hours. Their equipment includes briefcase gamma-neutron monitors, airplane mounted detectors, and roadblock monitors that scan traffic in and out of an incident area. They can provide on-site support in disarming or disabling nuclear devices. The team was used for three months in 1978 in the Canadian Northwest Territory to locate and recover hundreds of parts from the fallen Soviet Cosmos 954 satellite containing a nuclear reactor.
RERTs - The Environmental Protection Agency staffs two Radiological Emergency Response Teams, RERTs, one of which is on continuous standby alert at all times. They can reach any point in the U.S. within 24 hours. They are supported by three
EPA radiological labs and a fleet of mobile counting laboratories that can provide complete radioanalytical services and communications support. The EPA is the lead agency in accidents involving unregulated rad material, e.g., lost sources, sources of unknown origin or NORM material.

## Slide 100: Beyond the Facilities’ Organization
Some of the available Federal Assets (partial listing) that may be activated based on the incident (cont’d):
  NRC/DOT – both maintain emergency response centers available 24/7 for assistance requests
  REACT/TS – Radiation Emergency Assistance Center/Training Site – operated by Oak Ridge Institute for Science and Education – assistance where human exposures are involved
Notes: Gollnick Ed 6, pp 637-641
REAC/TS - If the nuclear accident involves human exposures, competent medical assistance must be made available to the victims immediately. One of the best sources is the Radiation Emergency Assistance Center Training Site or REAC/TS, operated by the Oak Ridge Institute for Science and Education in Oak Ridge, TN. REAC/TS has physicians available, around the clock, who are experienced in handling
radiation accident victims. They can consult by phone with local doctors who are treating accident victims and provide them with a wealth of information. REAC/TS also maintains a registry of world-wide accidents involving radiation exposure or intake of radioactive materials. Details of treatments used in previous accidents can be very useful in planning for current victim treatment.

## Slide 101: What Are Your Questions?