## Slide 1
ACADs (08-006) Covered
Keywords
Description
Supporting Material
3.3.5.6.8 | 3.3.13.10 | 3.3.14.7.6 |  |  |  |  | 
Notes: <number>

## Slide 2: Personnel Monitoring
HTP001.012
TP-<number>
Notes: <number>

## Slide 3: Course Overview
Introduction
Terms & Definitions
Regulations, Exposure Limits &
Guidelines
External Exposure Monitoring
Internal Exposure Monitoring
Dose Terms & Dose Calculations
Dose Tracking & Reporting
TP-<number>

## Slide 4: Enabling Objectives: 1
Identify Dose Terms
State Regulations & Limits
Familiar with Radiation Monitoring Devices
Describe Operation of Various Dosimeters
Explain Dosimetry Administrative Controls
Use of Multiple & Extremity Dosimeters
Dosimetry for Various Situations
TP-<number>

## Slide 5: Enabling Objectives: 2
Describe Actions for Abnormal Situations
Explain Concepts of Internal Dosimetry
Primary Radionuclides of Concern
Describe Biological Effects & Risks
Explain Dose Calculation Methods
Assessment of Radioactivity Uptake
Dose Tracking and Reporting
TP-<number>

## Slide 6: Units of Radiation Dose: Absorbed Dose
Gray – The SI Unit of Absorbed Dose 1 Gray = 1 Joule/Kilogram (1 gray = 100 rads)
Rad – The Special Unit of Absorbed Dose 1 rad = 100 ergs/gram or 0.01 Joule/kg (1 rad = 0.01 gray)
TP-<number>

## Slide 7: Units of Radiation Dose: Dose Equivalent
Rem – The Special Unit of Any Quantities expressed as Dose Equivalent (DE) DE = Absorbed Dose times Quality Factor (1 rem = 0.01 sievert)
Sievert (Sv) – The SI Unit of Quantities expressed as Dose Equivalent (DE) (1 Sv = 100 rems)
TP-<number>

## Slide 8: Quality Factors
Type of Radiation Quality Factor X-Rays, γ, or β 1 Alpha, Fission Fragments, etc. 20 Neutrons (Unknown Energy) 10 High-Energy Protons 10
TP-<number>

## Slide 9: Personnel Monitoring: Required by 10CFR20.1501
TP-<number>

## Slide 10: Purposes for Monitoring
Regulations Comply with
Evaluate:
- Magnitude & Extent of Radiation Levels
- Quantities of Radioactive Materials
- Potential Radiological Hazards
TP-<number>

## Slide 11: Conditions Requiring External Monitoring
Dose > 10% of 10CFR20.1201 Limits
DDE > 0.1 rem (1 mSv) for Minors
LDE > 0.15 rem (1.5 mSv) for Minors
SDE/Extremity Dose > 0.5 rem for Minors
DDE > 0.1 rem (1 mSv) During Pregnancy
Entering High or Very High Radiation Area
TP-<number>

## Slide 12: Conditions Requiring Monitoring for Internal Exposures
Greater than 10% of Applicable ALI
CEDE > 0.1 rem (1 mSv) for Minors
CEDE > 0.1 rem (1 mSv) During Pregnancy
TP-<number>

## Slide 13: Exposure Limits & Guidelines
TEDE </= 5 rems (0.05 Sv), or DDE + CDE </= 50 rem (0.5 Sv)
LDE </= 15 rem (0.15 Sv)
SDE/Extremity </= 50 rem (0.5 Sv)
DE </= 0.5 rem (5 mSv) to Embryo/Fetus
TVA Administrative Limit: TEDE </= 1 rem (0.01 Sv)
TP-<number>

## Slide 14: Planned Special Exposures (PSE)
Conditions:
- Authorized in Writing Before Exposure Occurs
- Individuals Informed of Purpose
- Individuals Informed of Doses - Individuals Instructed in Measures to Keep Doses ALARA
TP-<number>

## Slide 15: Emergency Dose Limits
Voluntary Only
Individuals Informed of Risk
- 10 Rem TEDE to Prevent:
Serious Damage to the Plant
Serious Hazard to Personnel
- 25 Rem TEDE to Save a Life
TP-<number>

## Slide 16: Exposure to Pregnant Women
DDE </= 0.5 rem (5 mSv) to Embryo/Fetus
Copy of Regulatory Guide 8.13
No Airborne or Contaminated Areas
Initial Whole Body Count Performed
TP-<number>

## Slide 17: Modes of Exposure
External Exposure
Internal Exposure
Combination of the Two
TP-<number>

## Slide 18: External Exposure Monitoring
Whole Body TLDs
Multiple Partial Body TLDs
Extremity TLDs
Whole Body DRDs
Dose Rate Measurements
TP-<number>

## Slide 19: Thermoluminescence
Thermo – Hot
Luminescent - Light
TP-<number>

## Slide 20: Electron Trapping
TP-<number>

## Slide 21: TLDs
Li2B4O7:Cu and
CuSO4:Tm
TP-<number>

## Slide 22: Li2B4O7:Cu TLD
Wide Range (10 mR to 100,000R)
Long Data Retention (Low Fading)
Linear Response
Sensitive to β, γ, X-Rays, and Neutrons
Reusable and Economical
Not Susceptible to Radiofrequency Interference
TP-<number>

## Slide 23: Lithium Borate Response Curves
Radiation Response
per Roentgen
TP-<number>
Phoon
Photon Energy (MeV)
0
1
2
0
1
2
Element 1
Element 2
0.01
0.1
1
10

## Slide 24: CuSO4:Tm TLDs
Range: 1 mR to 1,000 R
Linear up to about 200 R
Sensitive to β, γ, and X-Rays
Over responds to Low Energy X-Rays
Useful for Environmental Measurements
TP-<number>

## Slide 25: Calcium Sulfate Response Curves
Radiation Response
per Roentgen
TP-<number>
Phoon
Photon Energy (MeV)
0
5
10
0
1
2
0.01
0.1
1
10
Element 3
Element 4

## Slide 26: Limitations of Both Types
Sensitive to Heat, Moisture, and Shock
Can be Shielded by the Body
Subject to Improper Wear by Workers
Misuse Results in Incorrect Data
Errors from Logistical/Recordkeeping
TP-<number>

## Slide 27: Panasonic TLDs
TP-<number>

## Slide 28
TP-<number>
Thermoluminescent Dosimeter

## Slide 29
TP-<number>
TLD Badge
Assembly

## Slide 30
TP-<number>
TLD Badge

## Slide 31: Panasonic 802 TLD
Element # TLD Material Filtration
1 Li2B4O7:Cu 14 mg/cm2
2 Li2B4O7:Cu 160 mg/cm2
3 CuSO4:Tm 160 mg/cm2
4 CuSO4:Tm 0.7 mg Lead
TP-<number>

## Slide 32: Measuring Neutrons with TLDs
Use 6Li and 10B Rather Than 7Li and 11B
Fast Neutrons not Directly Measured
Neutrons Moderated by the Body
Slower Recoil Neutrons Measured
“Albedo Effect”
TP-<number>

## Slide 33: Panasonic 802 TLD
Element # TLD Material Filtration
1 Li2B4O7:Cu 14 mg/cm2
2 Li2B4O7:Cu 160 mg/cm2
3 CuSO4:Tm 160 mg/cm2
4 CuSO4:Tm 0.7 mg Lead
TP-<number>

## Slide 34: Reading Panasonic TLDs
TP-<number>

## Slide 35: System Calibration
Routine Calibration
Daily QC Check
Calibration TLDs
On-Line QC TLDs Daily
TP-<number>

## Slide 36: System QC/QA
TEDS Accredited by NIST and NVLAP
Intercomparison Tests
Review & Verification Checks
Statistical Review Technology
Assessed by External Organizations
Quality Manager Assessment
Routine Internal Evaluations
TP-<number>

## Slide 37: Badge Issue & Collection
Issued & Collected by RADCON
Computer Assigns a TLD Number
Issued for a 3-Month Period
Processed by TEDS
Background TLDs Maintained
TP-<number>

## Slide 38: Special Pulls
Administrative Dose Limits Exceeded
DRD Off Scale or Displays Error
Termination/Relocation of Employee
Quality Control Check
Multiple Badge or Neutron Processing
TP-<number>

## Slide 39: Wearing the TLD
Front of Body, Neck to Waist
Conditions May Require Change
Wear Inside Coveralls in Contaminated Area
Do Not Open or Pamper With the Badge
TP-<number>

## Slide 40
Proper
Wearing
of
Dosimetry
TP-<number>

## Slide 41: Multiple Badging
Nonuniform Radiation Field
Whole Body Dose >/= 100 mrem/h & Variable
Highest Dose Location Unknown
Radiation Levels Unknown and
  Gradient Nonuniform
TP-<number>

## Slide 42: Multi-Badge Placement
Forehead
Chest
Back
Gonads
Right Arm
Left Arm
Right Femur
Left Femur
Control (Not Worn)
TP-<number>

## Slide 43: Extremity Badges
>/= 500 mrem to Extremity
Handling Unshielded Beta Sources
Whole Body (Except Hands) Shielded
Handling Small Non-Shielded γ Sources
Decontamination of Beta
Glove Box Operations
Handling I-125
TP-<number>

## Slide 44: Extremity Dosimeter
TP-<number>

## Slide 45: Wearing Extremity Badge
TP-<number>

## Slide 46: Secondary Dosimetry
In Any RCA
Includes:
- EDs
-DADs
Read Periodically During Job Assignment
Wear on Front of Person
Wear Inside in Contamination Area
TP-<number>

## Slide 47
TP-<number>
Electronic Dosimeter

## Slide 48
TP-<number>
Electronic Dosimeter Display

## Slide 49
TP-<number>
Pocket
Chamber

## Slide 50
TP-<number>

## Slide 51: Dosimetry Requirements for Work Areas: 1
Restricted Area – TLD
Radiation Area – TLD
RCA – TLD & DAD/ED
Nonuniform Radiation Fields – Multiple TLDs
High Doses to Extremities – Extremity TLDs
TP-<number>

## Slide 52: Dosimetry Requirements for Work Areas: 2
Neutron Areas –Process TLD for Neutrons
High Radiation Area – Secondary and Supplemental Dosimetry
Very High Radiation Area – Secondary and Supplemental Dosimetry
Planned Special Exposure –Per RADCON
Visitors – Same as Escort
TP-<number>

## Slide 53: Dosimeter Discrepancies
Dosimeter Investigative Report (DIR) For:
- Lost or Damaged TLD
- Lost/Damaged/Malfunctioning DRD
- Suspect Results
- Secondary Dosimeter </= 100 mrem and </= 25% Difference in Values
- Customer Complaints & Concerns
TP-<number>

## Slide 54: Internal Exposure Pathways
Inhalation
Ingestion
Absorption
Open Wounds
TP-<number>

## Slide 55: Reducing Internal Exposures
No Eating, Drinking, Smoking, Chewing, or Dipping in RCA
Wear Protective Clothing Correctly
Cover All Wounds
Respirators in Airborne Areas
Good Work Practices
TP-<number>

## Slide 56: Elimination of Internal Radioactivity
Biological Processes
Radiological Decay
Combination of the Two
TP-<number>

## Slide 57: Potential Health Effects and Risks
TP-<number>

## Slide 58: Naturally Occurring Radioactive Materials
K-40 about 18 mrem/y
C-14 about 1 mrem/y
Rn-222 about 200 mrem/y
TP-<number>

## Slide 59: Potential Health Effects
None from < 10,000 mrem (100 mSv)
Denver, CO, Background 1,000 mrem
- No Adverse Biological Effects
Cancer Associated with > 50,000 mrem
- Leukemia, Lung, Colon & Others
Long Latent Period
Indistinguishable from Cancers from Non-Radiation Causes
TP-<number>

## Slide 60: Other Influences
Chemical & Physical Hazards Contribute to the Same Diseases
- Smoking
- Alcohol
- Diet
TP-<number>

## Slide 61: Internal Exposure Terms 1
Concentration – Activity/Volume of Air (ex. µCi/cc)
Intake – Curies of Radioactive Material Taken into the Body
Class – (10CFR20, Appendix B, Table 1) Retention of Radioactive Material in the Pulmonary Region of the Lungs (D=Days, W=Weeks, Y=Years)
TP-<number>

## Slide 62: Internal Exposure Terms 2
Annual Limit on Intake (ALI) – Radioactive Material Taken into the Body in 1 year (2000 h) Resulting in a CEDE (Total Body Dose) of 5 rem (0.05 Sv) or a CDE (Organ Dose) of 50 rem (0.5 Sv)
ALI Fraction (fALI) – Fraction of ALI from a Specific Intake, or
fALI = Intake (µCi)/ALI (µCi)
TP-<number>

## Slide 63: Sample Problem # 1
Find the ALI(s) for Co-60 (10CFR20 Appendix B, Table 1)
Solution: ALI for Class W = 200 µCi ALI for Class Y = 30 µCi
TP-<number>

## Slide 64: Internal Exposure Terms 3
Derived Air Concentration (DAC) – Concentration of Air (µCi/ml) if Breathed for 2000 h at 1.2 m3/h (20,000 ml/min) Results in an Intake of 1 ALI (10CFR20, Appendix B, Table 1)
TP-<number>

## Slide 65: Relationship Between DAC and ALI
DAC = ALI (µCi)/(h/y)(60 min/h) (Breathing Rate), or
DAC = ALI (µCi)/(2000 h/y)(60 min/h) (20,000 ml/min), or
DAC = ALI (µCi)/(2.4 E 9 ml)
TP-<number>

## Slide 66: Internal Exposure Terms 4
DAC Fraction (fDAC) – Fraction of DAC Resulting from Exposure to a Specific Airborne Concentration of Radioactive Material, or fDAC = Conc. (µCi/ml)/DAC (µCi/ml)
DAC-hour – The fDAC Multiplied by the Time of Exposure, or DAC-h = (fDAC)(h)
TP-<number>

## Slide 67: Sample Problem # 2
Calculate the DAC Fraction (fDAC) for an Exposure to 1 E -9 µCi/ml of Co-60 (Oxide Form)
Solution: DAC for Co-60 (Oxide Form) = 1 E -8 µCi/ml, and fDAC = (1 E -9 µCi/ml)/(1 E -8 µCi/ml), or, fDAC = 0.1
TP-<number>

## Slide 68: Sample Problem # 3
Calculate the DAC-h for Sample Problem # 3 Where the Exposure Time is 3 hours
Solution: DAC-h = (0.1)(3 h), or DAC-h = 0.3 h
TP-<number>

## Slide 69: Relationship of DAC-h and ALI
Since the ALI is Based on an Exposure of 5 rem (5,000 mrem) in 2,000 hours/y, Then, 5,000 mrem/2000 h = 2.5 mrem/DAC-h or, 1 DAC-h = 2.5 mrem Internal Dose
TP-<number>

## Slide 70: Sample Problem # 4
Using the Concept of ALI and DAC, Determine if a Worker Should Wear a Respirator for a Specific Task Where:
TP-<number>

## Slide 71: Sample Problem # 4
Dose Rate = 24 mrem/h, Plus some Airborne Exposure
Job Time: With Respirator = 2 h, 20 min, or 2.33 h Without Respirator = 2 h
Without Respirator = 2 DAC-h Internal Dose
TP-<number>

## Slide 72: Sample Problem # 4
Solution: a. Dose Wearing a Respirator: (24 mrem/h)(2.33 h) = 56 mrem from Direct Radiation No Exposure from Airborne Radioactivity (Respirator)
TP-<number>

## Slide 73: Sample Problem # 4
Solution: b. Not Wearing a Respirator: (24 mrem/h)(2 h) = 48 mrem, Direct (2 DAC-h)(2.5 mrem/DAC-h) = 5 mrem from Airborne Radioactivity
Total = 48 mrem + 5 mrem = 53 mrem
TP-<number>

## Slide 74: Sample Problem # 4
Conclusion: By NOT Wearing a Respirator, the Worker Will Receive LESS Total Effective Dose Equivalent, Therefore, No Respirator Should be Worn for This Job.
TP-<number>

## Slide 75: Measuring Internal Radioactivity (Bioassay)
10CFR20.1204 Requires Measurements to be Taken of:
- Concentrations of Radioactive Materials in Air in Work Areas, or;
- Quantities of Radionuclides in the Body,
- Quantities of Radionuclides Excreted From the Body, or;
- Combinations of these Measurements
TP-<number>

## Slide 76: Compliance
Principle Means Used at TVA to Demonstrate Compliance:
- Air Sampling, and
- Tracking DAC-hours
TP-<number>

## Slide 77: Internal Dose Monitoring
Internal Dose Monitoring Required for:
- Intake >0.1 ALI or 200 DAC-h/year (Adult)
- CEDE >/= 100 mrem or 40 DAC-h/year (Pregnant Women)
TP-<number>

## Slide 78: Bioassay Requirements
Before Initial Entry to Contamination or Airborne Areas
Contamination on Face Indicates Uptake
Nasal Contamination Detected
Ingestion or Suspected Ingestion
Contamination of Open Wound
Randomly (Evaluate Controls)
Termination
TP-<number>

## Slide 79: Whole Body Counting (In-Vivo Bioassay)
Primary Bioassay Technique
May use Bed, Chair, Booth, or Room
Radiation Detectors Placed Near Body
Data Accumulated by Multichannel Analyzer
Data Analyzed by Computer System
Performed if Exposure > 20 DAC-h/year
TP-<number>

## Slide 80
TP-<number>
NaI Detectors
Thyroid Detector
Germanium
Detector

## Slide 81
Booth Whole
Body Counter
TP-<number>

## Slide 82
Multichannel Analyzer System Used for Whole Body Counting
TP-<number>

## Slide 83: WBC Measurement Quality Assurance
Measurement Performance Verification (MQA) Testing
- Sources Traceable to NIST
- Includes Expected Nuclides
WBC MQA Intercomparison
- Blind Phantoms
- Compare Results with Known Values
TP-<number>

## Slide 84: Actions Taken for Positive Results: 1
Decontaminate and Follow-up Count
Repeat Until:
- No Activity Found
- No More Decrease
Diagnostic Count if Radioactivity Continues
TP-<number>

## Slide 85: Actions Taken for Positive Results: 2
Follow-up Bioassay:
- Whole Body Count (WBC), or;
- Urine Sample, or;
- Fecal Sample
WBC Trend Report
TP-<number>

## Slide 86: In-Vitro Bioassay
Urine and Fecal Samples
Samples Taken for:
- Initial
- Annual
- Termination
- Relocation
- Incident
- Special
TP-<number>

## Slide 87: In-Vitro Bioassay Results
Analyzed by ERM&I
Results in Individual’s Exposure Record
Summary Trend Report
TP-<number>

## Slide 88: Required Actions: Results >/= 0.01 ALI or 20 DAC-h
Follow-Up Investigation
Sum Internal & External
Follow-Up Bioassay
Assess Intake & CEDE
Record on NRC Form 5
TP-<number>

## Slide 89: Dose Terms & Calculations
Committed Effective Dose Equivalent-(CEDE)
CEDE a Function of:
- CDE, or;
- Nuclide Intake & ALI, or;
- Airborne Concentration & DAC, or;
- Nuclide Intake & Dose Conversion Coefficient
TP-<number>

## Slide 90: CEDE From CDE
CEDE = ∑(WT * CDE), Where:
- CEDE = Committed Effective Dose Equivalent
- WT = Weighting Factor (rem) for each Organ or Tissue
- CDE = Committed Dose Equivalent (rem)
TP-<number>

## Slide 91: CEDE From Nuclide Intake & ALI
CEDE = ∑(5Ii/ALIi), Where;
- CEDE = Committed Effective Dose Equivalent (rem)
- 5 = Annual Stochastic Limit (rem)
- Ii = Inhalation or Ingestion Intake of Nuclide I (µCi)
- ALIi = Stochastic ALI for Nuclide i (µCi)
TP-<number>

## Slide 92: CEDE From Airborne Concentration & DAC
CEDE = ∑(5Ci * t)/(2,000 DACi), Where;
- CEDE = Committed Effective Dose Equivalent
- 5 = Annual Stochastic Limit (5 rem)
- Ci = Airborne Concentration (µCi/ml)
- t = Time of Exposure (hours)
- 2000 = Hours in a Work Year
- DACi = Stochastic DAC for Nuclide i
TP-<number>

## Slide 93: CEDE From Nuclide Intake & Dose Conversion Coefficient
Methodology Used by HIS-20
CEDE = ∑(Ii * Di,t), Where;
- CEDE = Committed Effective Dose Equivalent, (rem)
- Ii = Inhalation or Ingestion Intake of Nuclide i (µCi)
- Di,t = Stochastic Dose Conversion
Coefficient for Tissue t & Nuclide i (EPA Report No. 11), rem/µCi
TP-<number>

## Slide 94: Committed Dose Equivalent
The Organ or Tissue Specific Committed Dose Equivalent (CDE) Must be Calculated When the CEDE >/= 1.0 rem or an Overdose has Occurred
TP-<number>

## Slide 95: Federal Guidance Report No. 11
Federal Guidance Report No. 11 (EPA Report No. 11) Provides Conversion Factors for CDE per Unit Intake by:
- Inhalation (Table 2.1)
- Ingestion (Table 2.2)
Conversion Factors:
- Sv/Bq * 3.7 E 6 = rem/µCi
- Sv/Bq * 3.7 E 9 = mrem/µCi
TP-<number>

## Slide 96: CDE From Intake & ALI
CDE = ∑(50Ii/ALIi), Where;
- CDE = Committed Dose Equivalent (rem)
- 50 = Annual Nonstochastic Limit (rem)
- Ii = Inhalation Intake for Nuclide i (µCi) - ALIi = Nonstochastic ALI for Nuclide i (µCi)
TP-<number>

## Slide 97: CDE From Airborne Concentration & DAC
CDE = ∑[50Cit/(2,000 DACi)], Where;
- CDE=Committed Dose Equivalent (mrem)
- 50 = Annual Nonstochastic Limit (rem)
- Ci = Airborne Concentration of Nuclide i (µCi/ml)
- t = Duration of Exposure (hours) - 2000 = Hours in a Work Year
- DACi = DAC for Nuclide i (µCi/ml)
TP-<number>

## Slide 98: CDE From Intake & Dose Conversion Coefficient
CDEt = ∑(Ii * Dni,t), Where;
- CDEt = Committed Dose Equivalent to Organ or Tissue t (rem)
- Ii = Intake for Nuclide i (µCi)
- Dni,t = Nonstochastic Dose Conversion
Coefficient for Tissue t and Nuclide I (rem/µCi) from Federal Guidance Report No. 11
TP-<number>

## Slide 99: Dose to Embryo/Fetus
FDE = ∑[(Ii)(FDCFi,t)(TFi)(1,000), Where;
- FDE = Dose Equivalent (mrem) to Fetus
- Ii = Intake (µCi) for Nuclide i
- FDCFi,t = Fetal Dose Conversion Coefficient (rem/µCi) for Mother’s
Assimilation of Radionuclide i at Fetal Age t (Regulatory Guide 8.36)
TP-<number>

## Slide 100: Dose to Embryo/Fetus: 2
FDE (Continued)
- t = Fetal Age at time of Intake
- TFi = Transfer Coefficient of Assimilated Radioactivity from Regulatory Guide 8.36
- 1000 = mrem/rem
TP-<number>

## Slide 101: Doses From Contamination
Surface (Skin) Dose Equivalent (SDE) = Dose to a depth of 0.007 cm (7 mg/cm2)
Deep Dose Equivalent (DDE) = Dose to a depth of 1 cm (1,000 mg/cm2)
Lens of Eye Dose Equivalent (LDE) = Dose to a depth of 0.3 cm (300 mg/cm2)
TP-<number>

## Slide 102: Contamination Dose Calculations Required for:
SDE >/= 100 mrem (54,000 cpm-h) Measured with 15.5 cm2 Frisker Area = 10 cm2 Dose Depth = 7 mg/cm2
DDE >/= 10 mrem (170,000 cpm-h) Measured with 15.5 cm2 Frisker Area = 1 cm2 Dose Depth = 1,000 mg/cm2
TP-<number>

## Slide 103: Activity-Hour Concentration
A = (Ch)/(2.22 E 6)(Eff.)(Area), Where;
- A = Activity-h Concentration (µCi-h/cm2)
- Ch=Counts per Minute-hour Total, cpm-h - 2.22 E 6 = Conversion: 2.22E6 dpm/µCi - Eff = Detector Counting Efficiency, cpm/dpm (0.10 for 15.5 cm2 Frisker) - Area = Surface Area (10 cm2 for SDE; 1 cm2 for DDE or LDE)
TP-<number>

## Slide 104: Shallow (Skin) Dose Equivalent (SDE)
SDE = (DF)(A), Where;
- SDE = Surface (Skin) Dose Equivalent (mrad) for Beta or Gamma - DF=SDE Dose Factor (mrad-cm2/µCi-h) (3,700 mrad-cm2/µCi-h for Beta, or 185 mrad-cm2/µCi-h for Gamma) - A = Activity-hour Concentration (µCi-h/cm2)
TP-<number>

## Slide 105: Deep Dose Equivalent (DDE)
DDE = (DF)(A), Where;
- DDE = Deep Dose Equivalent (mrad) for Gamma - DF =DDE Dose Factor (mrad-cm2/µCi-h)
(11 mrad-cm2/µCi-h for Gamma) - A = Activity-hour Concentration (µCi-h/cm2)
TP-<number>

## Slide 106: Doses From Hot Particles
Particles Usually < 100 micron
Activity Usually At Least 0.1 µCi
Any Discrete Particle >/= 20,000 cpm
Dose Calculation Same as DDE
TP-<number>

## Slide 107: Total Organ Dose Equivalent (TODE)
Sum of DDE & CDE
or
TODE = DDE + CDE
TP-<number>

## Slide 108: Total Effective Dose Equivalent (TEDE)
Sum of Internal (CEDE) and External (DDE) Exposures
TEDE = CEDE + DDE
If TEDE =/> Workers Age (Years), Worker Limited to 1,000 mrem/y
TP-<number>

## Slide 109: Dose Tracking and Reporting
80 % of Limit – Dose Extension
90 % of Limit – Dose Extension or Restricted Access to RCA
Determination of Prior Dose –NRC Form-4
Annual Exposure Report – NRC Form-5
TP-<number>

## Slide 110: Summary - 1
Radioactivity – It’s Everywhere!
Occupational Exposure – ALARA
Radiation Effects & Risks
Somatic Effects
Genetic Effects
Risks Low for Low Doses
Dose Limits – 10CFR20
TP-<number>

## Slide 111: Summary - 2
Personnel Monitoring – External
TLDs
Electronic Dosimeters
Personnel Monitoring – Internal
Whole Body Counting
Excreta Sampling
TP-<number>

## Slide 112: Summary - 3
Dose Terms and Calculations
Absorbed Dose - rad, Gy
Dose Equivalent - rem, Sv
ALI & DAC
Whole Body Dose
Organ/Tissue Dose – Committed
Dose Tracking & Reporting
TP-<number>