## Slide 1
ACADs (08-006) Covered
Keywords
Gas-filled detector, ionization chamber, proportional detector, Geiger-Mueller detector scintillation detector, semiconductor, thermoluminescent detector, characteristics, operating principles, advantages, disadvantages.
Description
Supporting Material
Rad Measurements Instrument Instructor Notes
1.1.8.1.1 | 1.1.8.1.2 | 1.1.8.1.3 | 1.1.8.1.4 | 1.1.8.4.5 | 1.1.8.1.6 | 1.1.8.1.7
3.2.2.1.1 | 3.2.2.2 | 3.2.2.33.2.3.2 | 3.2.3.17 | 3.2.3.18 | 3.3.3.1 | 4.4.3
4.5.3 | 4.5.6 | 5.4.1.5a | 5.4.1.5b | 5.4.1.5c | 5.4.1.5d | 5.4.1.5e
Notes: <number>

## Slide 2
Simple Gas Filled Detector
Anode +
Cathode -
To meter
Notes: <number>
Discuss how the chamber is filled with gas (sometimes air) with a central electrode well insulated from the chamber walls.
Anode - center electrode (positive charge)
Cathode - chamber wall (negative charge)
A potential difference is applied between the wall and the central electrode to produce an electric field in the chamber.
Next slide

## Slide 3: Simple Gas Filled Detector
Anode
Cathode -
To meter
e-
+
e-
+
e-
+
e-
+
e-
+
e-
+
y
y
y
Notes: <number>
Discuss how ionization is the process by which a neutral atom or molecule acq uires a negative or positive charge.
Radiation causes ion pairs to be produced in the gas within the chamber (this is shown on the slide)
The electric field between the cathode and anode draws the ions toward the electrodes.
Next slide

## Slide 4
Simple Gas Filled Detector
Anode +
Cathode -
To meter
e-
e-
e-
e-
e-
e-
+++++++
e-
e-
Notes: <number>
The positive ions are drawn to the cathode.
The negative ions are drawn to the anode.
The speed at which the ions move toward the electrodes is a function of the field strength and the nature of the gas.
A charge collects on the anode causing a voltage change in the circuit (pulse). This pulse causes a current to flow in the internal meter circuit.
This is a simple radiation detector.
Next slide

## Slide 5: Gas Amplification Curve
Recombination
Ionization
Limited Proportional
Proportional
Geiger Mueller
Number of Ions Collected
Continuous Discharge
Voltage
Fission product Alpha Beta Gamma
Notes: <number>
Don’t bring in the build which actually shows the gas amplification curve.
Play the draft game where there are four teams and each team has to draft players to make up the perfect team.
Before the teams are made up, ask the class recall the names of the six regions of the gas amplification curve.
All of the points in the lesson plan will be covered by the various laminated pages for each of the regions.
After the game is played bring in the build (which shows the regions) and give them each a handout on which to capture the main points for each of the regions.
Ask each team to review their pages and allow participants to fill in their handout for each of the regions.
Next slide

## Slide 6
RO-2, 2A
Ion Chamber
Notes: <number>

## Slide 7
RO-7
Ion Chamber
Notes: <number>

## Slide 8
RSO-50E, 5, 50, 500
Ion Chamber
Notes: <number>

## Slide 9
PCM-1B
Gas Proportional
Notes: <number>

## Slide 10
PCM-2
Gas Proportional
Notes: <number>

## Slide 11
PNR-4 & Ludlum 12-4
Gas Proportional
Notes: <number>

## Slide 12
Ludlum 14C
GM
Notes: <number>

## Slide 13
Ludlum 177 with pancake probe
GM
Notes: <number>

## Slide 14
Ludlum 375
GM
Notes: <number>

## Slide 15
Surveyor-50
GM
Notes: <number>

## Slide 16: Teletector
GM

## Slide 17
Surveyor M
Scintillation
Notes: <number>

## Slide 18
Microanalyst
Scintillation
Notes: <number>

## Slide 19
PM-7 (Portal Monitor)
Scintillation
Notes: <number>

## Slide 20
SAM 11
Scintillation
Notes: <number>

## Slide 21
ED (DMC 2000)
Solid State Detector
Notes: <number>