## Slide 1
ACADs (08-006) Covered
Keywords
Radiographic testing, x-ray, natural radiation, curie, becquerel, personnel monitoring, decay, half-life, intensity, exposure limits, inverse square, stochastic, nonstochastic, radiation safety officer.
Description
Supporting Material
Augusta Technical College 2011
1.1.8.1.2 | 1.1.8.3.1 | 3.3.1.8 | 3.3.2.4.5 | 3.3.3.14 | 3.3.4.3 | 3.3.5.6.1 | 3.3.5.6.2
3.3.5.6.4 | 3.3.6.1 | 3.3.7.5 | 4.9.1 | 4.9.8 | 4.10.4.5 | 4.12.1.1 | 4.12.1.2
4.12.1.3 | 4.12.1.4 | 4.12.2 | 4.14.6.1 | 4.14.6.2 | 4.14.6.4 |  | 
Notes: <number>

## Slide 2
Radiographic Testing
Prepared by:
Chattanooga State Community College
Notes: <number>

## Slide 3: Topics
  History of RT
  Science of Radiation
  Radiation Terminology
  Radiation Safety
Notes: <number>

## Slide 4: Radiographic Testing (RT)
Definition: An NDT method that utilizes x-rays or gamma radiation to detect discontinuities in materials, and to present their images on recording medium.
Notes: <number>

## Slide 5: History – X-Rays
X-rays discovered in 1895 by Wilhelm Roentgen
1896 – used by physicians to locate bullets in wounded soldiers
1913 – development of high vacuum x-ray tubes enabled voltages of 100,000 V
  Increased penetrating power of x-rays led to industrial applications
1931 – GE developed 1,000,000 V x-ray generator
  ASME approved use of x-ray to test fusion-welded pressure vessels
Notes: <number>

## Slide 6: History – Natural Radiation
1896 – Henri Becquerel identified uranium as radioactive material
1898 – Pierre and Marie Curie discovered polonium, followed by radium (“shining” element)
  Radium capable of filming through 10-12” thick steel castings
  Used extensively during WWII as part of U.S. Navy shipbuilding program
1946 – cobalt and iridium became available
  Both stronger and cheaper than radium
Notes: <number>

## Slide 7: What is radiation?
X-rays and gamma rays are types of electromagnetic radiation of shorter wavelengths than visible light:
  λvisible = 600 Angstroms, λx-rays = 1 A, λgamma rays = 0.0001 A
  shorter wavelengths permit penetration through materials
  high energy levels break chemical bonds
    *Leads to destruction of living tissue
X-rays and gamma rays differ only in source of origin
Notes: <number>

## Slide 8: Radiation Properties
Undetectable by human senses
  Cannot be seen, felt, heard, or smelled
Possesses no charge or mass
  Referred to as photons (packets of energy)
Generally travels in straight lines (can bend at material interfaces)
Characterized by frequency, wavelength, and velocity
Part of electromagnetic spectrum but not influenced by electrical or magnetic fields
Notes: <number>

## Slide 9: Atoms
Atom - the smallest particle of any element that retains the characteristics of that element
Subatomic particles – protons, electrons, neutrons
Notes: <number>

## Slide 10: Atoms Continued
Nucleus of atom – contains the positively-charged protons and neutrally-charged neutrons
Electrons – negatively-charged particles that travel at high speed around the nucleus
Atomic number – based on an element’s number of protons
  Ex. Carbon (C) has atomic number 6, Potassium (K) has atomic number 19
Isotopes – atoms of the same element with different number of neutrons
Atomic mass – approximately equal to sum of protons and neutrons
Notes: <number>

## Slide 11: Radioactivity
Defined as the release of energy and matter that results from changes in the nucleus of an atom
An atom that contains additional neutrons is unstable
In order to move to a more stable state, the nucleus seeks to remove the extra neutrons, thereby emitting radiation
Atoms with atomic numbers > 83 referred to as radioisotopes – they have unstable nuclei and are radioactive
Notes: <number>

## Slide 12: Radioactive Decay
Defined as the spontaneous breakdown of an atomic nucleus resulting in the release of energy and matter from the nucleus
Occurs by:
  Alpha decay (emits 2 protons and 2 neutrons from the nucleus)
  Beta decay (a neutron split into a proton and an electron)
  Gamma decay (energy in the form of gamma radiation emitted from the nucleus)
Alpha and beta decay involve particles
Example nuclear reaction:
  92U238 90Th234 + 2He4 + gamma rays
Notes: <number>

## Slide 13: Radioactive Decay Continued
When an atom undergoes radiographic decay, it emits one or more forms of radiation with sufficient energy to ionize the atoms with which it interacts
Ionizing radiation – high speed subatomic particles ejected from the nucleus, or gamma rays emitted by the either the nucleus or orbital electrons
Ionization – complete removal of an electron from an atom following the transfer of energy from a passing charged particle
Notes: <number>

## Slide 14: Radioactive Decay Continued
Activity – quantity which expresses the degree of radioactivity or the radiation-producing potential of a given amount of radioactive material
  Given in units of Curie (English system) or Becquerel (SI)
  One Curie is quantity of radioactive material in which 3.7 * 1010 atoms disintegrate per second (move to a more stable state)
  1 Becquerel = quantity of radioactive material in which 1 atom disintegrates per second
  1 Curie = 3.7 * 1010 Becquerel
Specific activity – activity per unit mass or volume
Notes: <number>

## Slide 15: Half-Life
Defined as the time required for the activity of a particular radioisotope to decrease to half of its original value
  Varies for different radioisotopes
  Ranges from microseconds to billions of years (uranium)
Half-life of Cobalt-60 = 5.3 years
Half-life Iridium-192 = 74 days
Carbon-14 dating
  used to approximate the age of fossils
  Decays with a half-life of 5730 years
Notes: <number>

## Slide 16: Half-Life Example
Example: You originally have a 30-Curie source of Cobalt-60.
  How many Curies will you have in 5.3 years?
  Answer: The source will have decayed by one half-life in 5.3 years, therefore half of the original source will remain, or 15 Curies.
  How long will it take for the source to decay to 3.75 Curies?
  Answer: Every 5.3 years the source will be reduced by half. In 1 half-life, the source will be reduced to 15 Curies. In 2 half-lives, the source will be down to 7.5 Curies. Finally, in 3 half-lives, the source will be 3.75 Curies. Therefore, it will take a total of 3 half-lives (or 15.9 years) for the source to decay to 3.75 Curies.
Notes: <number>

## Slide 17: Penetrating Power of Radiation
Only x-rays and gamma rays can penetrate solid materials to a significant extent (alpha and beta particles can penetrate skin only up to 8 mm)
Transmission of radiation depends on:
    Material thickness
    Material density
    Energy of the photons
Photons that are not transmitted are attenuated (absorbed or scattered)
Notes: <number>

## Slide 18: Radiation Safety
Science of radiation protection (also called health physics) developed to address acceptable radiation levels to reduce risk of injury to humans
Primary health concern (for chronic, not acute exposure) is increased risk for cancer
Depends on amount of radiation dose, duration of dose, and specific body parts exposed
Possession and use of radioactive materials strictly regulated by the Nuclear Regulatory Commission (NRC) as specified in Title 10 of the Code of Federal Regulations (CFR)
Notes: <number>

## Slide 19: Radiation Safety Continued
By 1900 it was understood that use of x-rays and gamma radiation required safety precautions to protect one’s health
1920’s – routine use of film badges for personnel monitoring begun, genetic effects of radiation recognized
Origin of radiation
  Natural (sun, radon gas)
  Man-made (x-rays, gamma rays)
Notes: <number>

## Slide 20: Radiation Energy
Different radioactive materials and x-ray generators produce radiation at different energies
Energy of radiation – responsible for the ability to penetrate matter
  Measured in electronvolts (eV) or kiloelectronvolts (keV)
  An electronvolt is the energy gained by an electron passing through a potential difference of 1 volt
  Energy adjustable on an x-ray generator
  Energy an unchangeable characteristic of a radioisotope
Notes: <number>

## Slide 21: Radiation Intensity
Amount of energy passing through a given area (perpendicular to the direction of radiation travel) in a given unit of time
Survey meter – used to measure intensity or radiation dose rate
  Units in mRem/hr or Rem/hr
  Frequently referred to as the most important tool a radiographer has to determine the presence and intensity of radiation
Per the inverse square law, the intensity varies inversely with the square of the distance
Notes: <number>

## Slide 22: Dose
Exposure – measure of the strength of a radiation field
  Units of Roentgen or R
Dose (also called absorbed dose) – amount of ionizing energy absorbed by an object
  Units of Rad (“radiation absorbed dose”)
Dose equivalent relates absorbed dose to biological effect of dose – equals absorbed dose times a quality factor (quality factor = 1 for x-ray and gamma radiation in humans)
  Units of Rem (“Roentgen equivalent in man”)
For humans, 1 R = 1 Rad = 1 Rem
Notes: <number>

## Slide 23: Dose vs. Dose Rate
Dose rate – measure of how fast a radiation dose is being received
  dose rate = dose / time
  Units of R/hr, mR/hr, Rem/hr, mRem/hr (same units as intensity)
To calculate a person’s dose, multiply the dose rate (measured with a survey meter) by the duration of exposure
  dose = dose rate * time
Example: If the radiation intensity in a particular area is 5 mRem/hr, and the person remains in that area for 30 minutes, what is the person’s radiation dose?
  dose = 5 mRem/hr * 0.5 hr = 2.5 mRem
Notes: <number>

## Slide 24: Biological Effects of Radiation
Absorbed dose depends on:
  Intensity of radiation source
  Distance from source
  Time of exposure
Ionization of living tissue causes molecules in cells to be broken apart
Biological effects vary with:
  Type of radiation (penetrating ability)
  Size of dose received
  Dose rate
  Body part exposed (extremities can handle more exposure than blood-forming organs)
  Age of individual (cell divisions slow with age – older people less sensitive to ionizing radiation)
Notes: <number>

## Slide 25: Stochastic and Nonstochastic Effects
Stochastic effects are delayed and difficult to specifically correlate to radiation exposure (cancer)
Nonstochastic effects are acute effects
  Directly proportional to size of dose
  Symptoms
    Skin reddening
    Skin and tissue burns
    Cataract formation
    Sterility
    Radiation sickness (nausea, vomiting, diarrhea, headache, fever, dizziness, weakness, hair loss)
    Death
Notes: <number>

## Slide 26: Important NRC Codes
10CFR19 – Notices, Instructions, and Reports to Workers: Inspection and Investigations
10CFR20 – Standards for Protection Against Radiation
10CFR34 – Licenses for Industrial Radiography and Radiation Safety Requirements for Industrial Radiographic Operations
Guidelines established to both prevent acute exposure and limit chronic exposure to “acceptable” levels
Desire to maintain all exposure “as low as reasonably achievable” – referred to as ALARA
BANANA – “build absolutely nothing anywhere near anyone”
Notes: <number>

## Slide 27: Exposure Limits
Effect of exposure (dose received in a 24-hour period):
  0-25 Rem – no evident injury (blood changes detectable at 5 Rem)
  400-500 Rem – results in death in 50% of cases
  1000+ Rem – results in death in ALL cases
Annual Occupational Limits
  Total effective dose – 5 Rem
  For pregnant women - 0.5 Rem during gestation period
  For people younger than age 18 – 0.5 Rem
Notes: <number>

## Slide 28: Exposure Limits Continued
Annual Non-Occupational Limits (for general public exposure to industrial ionizing radiation)
  0.1 Rem (2% of occupational limit)
  Doesn’t include natural background radiation (0.3 Rem) or radiation from man-made sources, such as medical x-rays (0.05 Rem)
Full-body X-ray Scanners at Airports
  According to the FAA web-site, the effective dose per scan is less than 0.0001 mSv (milliSievert)
  0.01 Sievert = 1 Rem, therefore 0.0001 mSv = 0.01 mRem
  The Health Physics Society (HPS) recommends 0.25 mSv (25 mRem) max annual dose from single source
  This corresponds to 2500 exposures per year
Notes: <number>

## Slide 29: Controlling Radiation Exposure
Remember: TIME, DISTANCE, and SHIELDING
Recall that dose = dose rate * time
Collimator – device used to direct radiation onto a part and shield the radiation in other directions
In general, the denser the material the greater the shielding
  Most effective shielding by depleted uranium – used to shield the source in gamma ray cameras
  Lead and concrete commonly used for shielding
Notes: <number>

## Slide 30: Controlling Radiation Exposure
Recall inverse square law – “the radiation intensity varies inversely with the square of the distance”
I1*D12 = I2*D22
Example: If the intensity at 1’ from the source is 500 Rem/hr, at what distance is the intensity 2 mRem/hr?
  Solution: Let I1 = 500 Rem/hr; D1 = 1 foot; I2 = 2 mRem/hr
  Solve for D2.
  D2 = Square root (I1*D12 / I2) = 500 feet
Signs must be posted at intensity boundaries (usually 2 mRem/hr and 100 mRem/hr) to warn individuals that radiographic testing is in progress
Notes: <number>

## Slide 31: Half-Value Layer
Defined as the thickness of a material needed to reduce the radiation intensity to ½ of its original value
  To provide shielding
  Depends on radioisotope used for gamma radiation (or voltage if radiation source is an x-ray)
  Depends on voltage if radiation source if an x-ray
 | Half-Value Layer, mm (inch) |  |  |  | 
Source | Concrete | Steel | Lead | Tungsten | Uranium
Iridium-192 | 44.5 (1.75) | 12.7 (0.5) | 4.8 (0.19) | 3.3 (0.13) | 2.8 (0.11)
Cobalt-60 | 60.5 (2.38) | 21.6 (0.85) | 12.5 (0.49) | 7.9 (0.31) | 6.9 (0.27)
Notes: <number>

## Slide 32: Radiation Safety Officer
Radiation Safety Officer (RSO) - individual authorized by company to ensure radiation activities performed safely and per approved procedures and regulations
Radiographers required to wear personnel monitoring devices to aid in tracking and minimizing their radiation exposure
Notes: <number>

## Slide 33: Personnel Monitoring Devices
Pocket dosimeter
  Similar in appearance to small marker
  Reads radiation dose (not dose rate)
  Allows workers to track daily dose received (reset at the start of each shift)
Audible alarm rate meter
  Sounds an alarm at a preset dose rate (typically 500 mRem/hr)
  NOT a replacement for a survey meter!
  Gamma Exposure Video.mov
Notes: <number>

## Slide 34: Personnel Monitoring Devices - Continued
Film badge
  Piece of radiation-sensitive film that provides a permanent record of radiation dose received
TLD (thermoluminescent dosimeter)
  Often used instead of a film badge (may be reused)
  Both film badges and TLDs typically worn for 1-3 months before being processed to determine dose
Notes: <number>

## Slide 35: Radiography Equipment – X-Ray Generators
X-rays are generated by directing a stream of high-speed electrons at a target material, such as tungsten, which has a high atomic number
Interaction with the tungsten atoms slows or stops the electrons, and x-rays are produced
Major components of an x-ray machine
  Tube – contains a cathode (coiled wire) and an anode (target) – operates in a vacuum
  High voltage generator
  Control console (to adjust output)
  Cooling system
Notes: <number>

## Slide 36: X-Ray Generators Continued
X-ray control console
  Increasing current (or milliamperage) increases number of electrons that flow from the cathode to the anode – thus increases the x-ray intensity
  Increasing the voltage increases the speed at which the electrons travel – thus increasing the energy or penetrating power of the x-ray
Notes: <number>

## Slide 37: Radiography Equipment – Gamma Sources
Man-made radioactive sources produced by introducing an extra neutron to atoms of the source material by neutron bombardment
As the atoms shed the neutron energy is released in the form of gamma ray
Co-60 and Ir-192 common industrial gamma ray sources due to:
  high energies
  Portability (as opposed to x-ray machines)
Disadvantage of gamma sources – cannot be turned off, therefore source must be isolated and shielded within an exposure device (camera)
Notes: <number>

## Slide 38: Radiography Equipment – Gamma Sources
Sources typically consist of multiple pellets loaded into a stainless steel capsule to obtain desired activity level (number of Curies)
Capsule sealed by welding
Attached to a short flexible cable called a pigtail
Housed in a shielding device referred to as an exposure device or camera
Activity of source governs amount of shielding required
  Co-60 has a higher activity (1.25MeV) than Ir-192 (460keV)
  Co-60 cameras typically weigh 500 lbs vs. ~45 lbs for Ir-192 cameras
Notes: <number>

## Slide 39: Performing Radiography
Exposure device connected to source tube on one end and a crank-out mechanism on the other end
Source tube in positioned as needed to obtain radiograph of component (with the source itself safely housed in the exposure device)
From as far away as possible, the radiograph turns the crank to move the source from the camera to the tip of the source tube
After the proper exposure time (calculated based on source strength, source to film distance, and thickness of the component), the radiographer cranks the source back into the camera
The radiographer must use the survey meter to confirm the source fully extracted back into the camera
Notes: <number>

## Slide 40: Radiograph Image Properties
Sensitivity – a measure of the quality of the image in terms of the smallest detail that may be detected
  Image Quality Indicators (IQIs or penetrameters) – devices used to indicate the quality level or sensitivity of the radiograph (plaque type or wire type)
  Depends on contrast and definition
Contrast – degree of density difference between two areas on a radiograph
Definition – degree of sharpness of the radiographic image
  Codes require a minimum “unsharpness”
Notes: <number>

## Slide 41: Radiograph Image Properties
Density – degree of film darkening
  If 0.01% of transmitted light reaches far side of film the density is 4.0 (based on an exponential equation)
  If 1.0% of transmitted light reaches far side of film the density is 2.0
  Many governing codes require densities of 2-4% (don’t want image too light or too dark)
Densitometer – device used to measure film density
  Density through the IQI must meet code (2-4%)
  Also, the density in the area of interest (the weld perhaps), must satisfy plus/minus criteria
    Darkest area must have a density of not more than 30% of the density under the IQI
    Lightest area must have a density of not less than 15% of the density under the IQI
Notes: <number>

## Slide 42: Assignment…
RT Worksheet/Calculations
Densitometersa
Notes: <number>