## Slide 1
ACADs (08-006) Covered
Keywords
Description
Supporting Material
Water Grades
4.20.1.18 |  |  |  |  |  |  | 

## Slide 2: Overview of Lab Water Grades
Norms define different laboratory water grades for:
  technical reasons
  economical reasons
The purpose
  To ensure that the right water quality is used for a specific application

## Slide 3: Grades of water
Grade 3 water:
  Lowest lab water grade
  Recommended for:
      Glassware rinsing, heating baths feed type 1 lab water systems
2. Grade 2 water:
  General lab applications
  Preparation of reagents for chemical analysis or synthesis
3. Grade 1 water:
  critical laboratory applications
  production of reagents for molecular biology applications preparation of solutions for electrophoresis and blotting.
Notes: Lab applications: buffers, pH solutions and microbiological culture media preparation; as feed to Type 1 water systems, clinical analyzers, cell culture incubators and weatherometers;
Critical lab applications: such as HPLC mobile phase preparation, blanks and sample dilution in GC, HPLC, AA, ICP-MS and other advanced analytical techniques; preparation of buffers and culture media for mammalian cell culture and IVF;

## Slide 4: Laboratory Water Specifications
Published norms:
  ASTM® and ISO® 3696 for laboratory applications;
  CLSI guidelines for clinical laboratories.
Some laboratories will also use norms defined in the European or the US Pharmacopoeia.

## Slide 5: Water specifications
Contaminant | Parameter and unit | Type 3 | Type 2 | Type 1
Ions | Resistivity (MΩ•cm @ 25°C) | >0.05 | >1.0 | >18.0
Organics | TOC (ppb) | <200 | <50 | <10
Pyrogens | (Eu/ML) | NA | NA | <0.03
Particulates | Particulates > 0.2 µm (units/mL) | NA | NA | <1
Colloids | Silica (ppb) | <1000 | <100 | <10
Bacteria | Bacteria (cfu/mL) | <1000 | <100 | <1
Notes: Retrieved from: http://www.millipore.com/lab_water/clw4/tutorial&tabno=4 on March 21, 2013

## Slide 6: Lab grade water production
Filtration technologies:
  Reverse osmosis, nanofiltration, ultrafiltration, microfiltration and particle filtration
  Filtration is often the first step in producing type I and II water.
UV radiation
  for eliminating bacteria and other microorganisms in water,
  does not remove particulate matter
  Does not produce water with the pH or conductivity levels required for some applications.
Other purification methods:
  distillation, deionization filtration and activated carbon adsorption.
Notes: UV light is often used in conjunction with filtration or other purification methods to such as distillation, deionization filtration and activated carbon adsorption