## Slide 1
ACADs (08-006) Covered
Keywords
Atoms, molecules, acids, bases, states of matter, conductivity, pH, Periodic Table of Elements, elements, mixtures, solutions, compounds, properties, analysis methods, states of matter, units of measure, vapor pressure, corrosion, basic water chemistry control, water treatment, sources of impurities, control methods, cation.
Description
Supporting Material
1.1.4.1 | 1.1.6.1.1 | 1.1.6.1.4 | 1.1.6.1.5 | 1.1.6.1.6 | 1.1.6.1.7 | 1.1.6.1.8 | 1.1.6.1.9
1.1.6.1.10 | 1.1.6.2.1 | 1.1.6.2.2 | 1.1.6.2.4 | 1.1.6.2.5 | 1.1.6.2.6. | 1.1.6 .2.7 | 1.1.6.3.2
1.1.6.3.3 | 1.1.6.3.7 | 4.20.1.1 | 4.20.1.3 | 4.20.1.4 | 4.20.1.11 | 4.20.1.12 | 4.20.1.12b
4.20.1.13 | 4.20.1.14 | 4.20.1.15 |  |  |  |  | 
Notes: <number>

## Slide 2: Power Plant Chemistry Overview
IRSC EE 1580
Notes: <number>

## Slide 3: Desired Outcome (Terminal Obj.)
The student will be able to explain and apply the basic concepts of chemistry fundamentals, including water chemistry control and reactor water chemistry.
Notes: <number>

## Slide 4: Enabling Statements: Competency 6
Explain the basic fundamentals of chemistry including:
  Atoms
  Molecules
  Acids and Bases
  States of Matter
  Conductivity
  pH
Notes: <number>

## Slide 5: Enabling Statements: Competency 6
Explain how to read and interpret information from the Periodic Table of Elements.
Notes: <number>

## Slide 6: Enabling Statements: Competency 6
Define:
  Elements
  Mixtures
  Solutions
  Compounds
Notes: <number>

## Slide 7: Enabling Statements: Competency 6
Explain Properties and Analysis Methods
Notes: <number>

## Slide 8: Enabling Statements: Competency 6
Explain States of Matter
  Gases
  Liquids
  Solids
Notes: <number>

## Slide 9: Enabling Statements: Competency 6
Define units of measure:
  Atomic Number
  Atomic Weight
  AMU
Notes: <number>

## Slide 10: Enabling Statements: Competency 6
Explain characteristics of gases
Notes: <number>

## Slide 11: Enabling Statements: Competency 6
State the relationship between the temperature of a liquid and its vapor pressure
Notes: <number>

## Slide 12: Enabling Statements: Competency 6
Explain corrosion chemistry and monitoring, including
  Types of corrosion
  Characteristics, and
  Prevention.
Notes: <number>

## Slide 13: Enabling Statements: Competency 6
Explain primary and secondary water chemistry control, including:
  Types, sources and effects of impurities
  Sampling methods
  Parameters monitored
  Principles of water treatment
Notes: <number>

## Slide 14: Enabling Statements: Competency 7
Explain basic water chemistry control fundamentals, including the following:
  Effects of impurities (such as increased corrosion rates, reduction in heat transfer area, tube failure in Steam Generators)
Notes: <number>

## Slide 15: Enabling Statements: Competency 7
Explain basic water chemistry control fundamentals, including the following:
  Ion Exchange Theory (Anion, Cation, Mixed Bed, Bed Exhaustion, Decontamination Factor)
Notes: <number>

## Slide 16: Enabling Statements: Competency 7
Explain basic water chemistry control fundamentals, including the following:
  Parameters monitored: pH, Conductivity, Sodium, Chlorides, Flourides, Sulfates, hardness, silica, etc.
Notes: <number>

## Slide 17: Enabling Statements: Competency 7
Explain basic water chemistry control fundamentals, including the following:
  Principles of water treatment (Filters, RO, IX)
Notes: <number>

## Slide 18: Enabling Statements: Competency 7
Explain basic water chemistry control fundamentals, including the following:
  Sources of impurities (e.g. tube leaks)
Notes: <number>

## Slide 19: Enabling Statements: Competency 7
Explain basic water chemistry control fundamentals, including the following:
  The corrosion process including types, characteristics and prevention
  Water chemistry control methods (such as IX), O2 control with chemistry (hydrazine or N2) and, pH Control.
Notes: <number>

## Slide 20: Enabling Statements: Competency 7
Explain reactor water chemistry fundamentals, including the following:
  Control/removal of impurities (such as IX, Chemical addition, hydrogen addition, hydrazine and degassing)
  Effects of impurities (such as increase in corrosion rates, total gases, local radiation levels)
Notes: <number>

## Slide 21: Enabling Statements: Competency 7
Explain reactor water chemistry fundamentals, including the following:
  Hydrogen gas in reactor water for Oxygen control
  Radiolysis and recombination (Such as water/ammonia and the effects on pH)
Notes: <number>

## Slide 22: Enabling Statements: Competency 7
Explain reactor water chemistry fundamentals, including the following:
  Sources of impurities (Such as air intrusion, IX exhaustion
  Types of impurities (Such as Chlorides, Flourides, Oxygen and Hydrogen)
Notes: <number>

## Slide 23: Enabling Statements: Competency 6
Explain the basic fundamentals of chemistry including:
  Atoms
  Elements
  Molecules
  Acids and Bases
  States of Matter
  Conductivity
  pH
  Units of Measure.
Notes: <number>

## Slide 24: Explain the basic fundamentals of chemistry: Atoms
All matter is composed of atoms, existing individually or in combination with each other.
An atom is an extremely small electrically-neutral particle.
It is the smallest unit involved in the chemical change of matter
Notes: <number>
CHARACTERISTICS OF ATOMS DOE-HDBK-1015/1-93 Fundamentals of Chemistry, Vol 1, page 2
All matter is composed of atoms, existing individually or in combination with each other. An
atom is an extremely small electrically-neutral particle. It is the smallest unit involved in the
chemical change of matter. Atoms can be treated as distinct particles because they behave as
such chemically, but atoms themselves are composed of even smaller subparts. Understanding these atomic subparticles is important in understanding chemistry.
An atom is composed of a positively-charged nucleus orbited by one or more negatively-charged particles called electrons. A simplified schematic representation of this arrangement is illustrated
in Figure 1. The nucleus is the core of an atom. It has a positive charge because it usually
consists of two particles, the neutron and the proton (hydrogen is the exception with only a
proton in the nucleus). The neutrons are electrically neutral, and the protons are electrically
positive. A nucleus with one proton has a charge of +1 (or simply 1), and a nucleus with two
protons has a +2 charge. Together the neutrons and protons give the nucleus its mass, but the
proton alone gives the nucleus its positive charge.
Neutrons and protons are relatively massive and are essentially equal in mass.

## Slide 25: Explain the basic fundamentals of chemistry: Atoms
Atoms themselves are composed of even smaller subparts.
An atom is composed of a positively-charged nucleus orbited by one or more negatively-charged particles called electrons
Notes: <number>
CHARACTERISTICS OF ATOMS DOE-HDBK-1015/1-93 Fundamentals of Chemistry, Vol 1, page 2
All matter is composed of atoms, existing individually or in combination with each other. An
atom is an extremely small electrically-neutral particle. It is the smallest unit involved in the
chemical change of matter. Atoms can be treated as distinct particles because they behave as
such chemically, but atoms themselves are composed of even smaller subparts. Understanding these atomic subparticles is important in understanding chemistry.
An atom is composed of a positively-charged nucleus orbited by one or more negatively-charged particles called electrons. A simplified schematic representation of this arrangement is illustrated
in Figure 1. The nucleus is the core of an atom. It has a positive charge because it usually
consists of two particles, the neutron and the proton (hydrogen is the exception with only a
proton in the nucleus). The neutrons are electrically neutral, and the protons are electrically
positive. A nucleus with one proton has a charge of +1 (or simply 1), and a nucleus with two
protons has a +2 charge. Together the neutrons and protons give the nucleus its mass, but the
proton alone gives the nucleus its positive charge.
Neutrons and protons are relatively massive and are essentially equal in mass.

## Slide 26: Atoms

## Slide 27: Elements
The number of PROTONS in an atom define the ELEMENT (e.g., Hydrogen, Oxygen, Sodium)
All isotopes of the same ELEMENT have the same number of protons.

## Slide 28: Explain the basic fundamentals of chemistry: Atoms  Elements
An atom is classified chemically by the number of protons in its nucleus.
Atoms that have the same number of protons in their nuclei have the same chemical behavior.
Atoms that have the same number of protons are grouped together and constitute a chemical element.
Notes: <number>
CHARACTERISTICS OF ATOMS DOE-HDBK-1015/1-93 Fundamentals of Chemistry, Vol 1, page 2
All matter is composed of atoms, existing individually or in combination with each other. An
atom is an extremely small electrically-neutral particle. It is the smallest unit involved in the
chemical change of matter. Atoms can be treated as distinct particles because they behave as
such chemically, but atoms themselves are composed of even smaller subparts. Understanding these atomic subparticles is important in understanding chemistry.
An atom is composed of a positively-charged nucleus orbited by one or more negatively-charged particles called electrons. A simplified schematic representation of this arrangement is illustrated
in Figure 1. The nucleus is the core of an atom. It has a positive charge because it usually
consists of two particles, the neutron and the proton (hydrogen is the exception with only a
proton in the nucleus). The neutrons are electrically neutral, and the protons are electrically
positive. A nucleus with one proton has a charge of +1 (or simply 1), and a nucleus with two
protons has a +2 charge. Together the neutrons and protons give the nucleus its mass, but the
proton alone gives the nucleus its positive charge.
Neutrons and protons are relatively massive and are essentially equal in mass.

## Slide 29: Explain the basic fundamentals of chemistry: Molecules
Molecules are groups or clusters of atoms held together by means of chemical bonding.
There are two types of molecules;
  molecules of an element and
  molecules of a compound.
Notes: <number>
CHARACTERISTICS OF ATOMS DOE-HDBK-1015/1-93 Fundamentals of Chemistry, Vol 1, page 7
Molecules are groups or clusters of atoms held together by means of chemical bonding. There
are two types of molecule; molecules of an element and molecules of a compound.
Molecules of an Element
In certain cases, two single atoms of an element can be attracted to one another by a
bond to form a molecule. Examples of this are hydrogen, oxygen, and bromine. The
molecular formulas for these are H , O , and Br . Most gaseous elements exist as 2 2 2
molecules of two atoms.
Molecules of a Compound
Two atoms of different elements held together by a bond form a compound. The
molecule is the primary particle of a chemical compound. Some examples of this type of
molecule include hydrogen chloride (HCl), water (H O), methane (CH ), and 2 4
ammonia (NH ). 3
Molecular Weight
The weight of a molecule, the molecular weight, is the total mass of the individual
atoms. Therefore, it is fairly simple to calculate the mass of any molecule if its formula
is known (that is, the elements and the number of each that make up the molecule). Note
that the terms mass and weight are used interchangeably in chemistry.

## Slide 30: Explain the basic fundamentals of chemistry: Molecules
Molecules of an ELEMENT:
In certain cases, two single atoms of an element can be attracted to one another by a bond to form a molecule.
Notes: <number>
CHARACTERISTICS OF ATOMS DOE-HDBK-1015/1-93 Fundamentals of Chemistry, Vol 1, page 7
Molecules of an Element
In certain cases, two single atoms of an element can be attracted to one another by a
bond to form a molecule. Examples of this are hydrogen, oxygen, and bromine.. Most gaseous elements exist as molecules of two atoms.

## Slide 31: Explain the basic fundamentals of chemistry: Molecules
Molecules of Compounds:
Two or more atoms of different elements held together by bonds form a compound.
The molecule is the primary particle of a chemical compound.
Notes: <number>
CHARACTERISTICS OF ATOMS DOE-HDBK-1015/1-93 Fundamentals of Chemistry, Vol 1, page 7
Molecules of a Compound
Two atoms of different elements held together by a bond form a compound. The
molecule is the primary particle of a chemical compound. Some examples of this type of molecule include hydrogen chloride (HCl), water (H2O), methane (CH4 ), and ammonia (NH3 ).
The weight of a molecule, the molecular weight, is the total mass of the individual atoms. Therefore, it is fairly simple to calculate the mass of any molecule if its formula is known (that is, the elements and the number of each that make up the molecule).
Note that the terms mass and weight are used interchangeably in chemistry.

## Slide 32: Explain the basic fundamentals of chemistry: Molecules
Molecules of Compounds:
Notes: <number>
CHARACTERISTICS OF ATOMS DOE-HDBK-1015/1-93 Fundamentals of Chemistry, Vol 1, page 7
Molecules of a Compound
Two atoms of different elements held together by a bond form a compound. The
molecule is the primary particle of a chemical compound. Some examples of this type of molecule include hydrogen chloride (HCl), water (H2O), methane (CH4 ), and ammonia (NH3 ).
The weight of a molecule, the molecular weight, is the total mass of the individual atoms. Therefore, it is fairly simple to calculate the mass of any molecule if its formula is known (that is, the elements and the number of each that make up the molecule).
Note that the terms mass and weight are used interchangeably in chemistry.

## Slide 33: Explain the basic fundamentals of chemistry: Molecules
Examples of Molecules of compounds:
hydrogen chloride (HCl),
water (H2O),
ammonia (NH3 ).
Notes: <number>
CHARACTERISTICS OF ATOMS DOE-HDBK-1015/1-93 Fundamentals of Chemistry, Vol 1, page 7
Molecules are groups or clusters of atoms held together by means of chemical bonding. There
are two types of molecule; molecules of an element and molecules of a compound.
Molecules of an Element
In certain cases, two single atoms of an element can be attracted to one another by a
bond to form a molecule. Examples of this are hydrogen, oxygen, and bromine. The
molecular formulas for these are H , O , and Br . Most gaseous elements exist as 2 2 2
molecules of two atoms.
Molecules of a Compound
Two atoms of different elements held together by a bond form a compound. The
molecule is the primary particle of a chemical compound. Some examples of this type of
molecule include hydrogen chloride (HCl), water (H O), methane (CH ), and 2 4
ammonia (NH ). 3
Molecular Weight
The weight of a molecule, the molecular weight, is the total mass of the individual
atoms. Therefore, it is fairly simple to calculate the mass of any molecule if its formula
is known (that is, the elements and the number of each that make up the molecule). Note
that the terms mass and weight are used interchangeably in chemistry.

## Slide 34: Explain the basic fundamentals of chemistry: Acids and Bases
Notes: <number>
ACIDS, BASES, SALTS, AND pH DOE-HDBK-1015/1-93 Fundamentals of Chemistry
CH-01 Page 46 Rev. 0
ACIDS, BASES, SALTS, AND pH
Different substances respond differently in solution. How substances behave
in water is of special interest to the power industry. The interactions of
water and acids, bases, or salts are of special interest because water is used
in many industries. This chapter will introduce the student to the general
behavior of these substances.

## Slide 35: Acids and Bases:
Different substances respond differently in solution. How substances behave in water is of special interest to the power industry. The interactions of water and acids, bases, or salts are of special interest because water is used in many industries.
Notes: <number>

## Slide 36: Acids:
Acids are substances that dissociate in water to produce hydrogen (H+).
Strong Acids have LOW pH values.
Notes: <number>
Examples of acids are vinegar, aspirin, and lemon juice.
These substances share the following common properties.
1. Acid solutions taste sour (acid means "sour" in Latin).
2. Acids react with many metals to form hydrogen gas.
3. Acids turn litmus paper red.
4. Acid solutions conduct electricity.
5. Acids react with bases to form a salt and water.
6. Acids react with carbonates to form CO (carbon dioxide gas).

## Slide 37: Acids:
An example of a common acid is sulfuric acid, H2 SO4 . In solution, H2SO4 dissociates to form hydrogen and sulfate ions
Notes: <number>
Examples of acids are vinegar, aspirin, and lemon juice.
These substances share the following common properties.
1. Acid solutions taste sour (acid means "sour" in Latin).
2. Acids react with many metals to form hydrogen gas.
3. Acids turn litmus paper red.
4. Acid solutions conduct electricity.
5. Acids react with bases to form a salt and water.
6. Acids react with carbonates to form CO (carbon dioxide gas).

## Slide 38: Bases:
Bases are substances that produce hydroxide ions (OH-) in water solutions.
Strong Bases have HIGH pH values
Notes: <number>
Common types of bases are lye, household ammonia, and most soaps. The following are four
characteristic properties of bases.
1. Basic solutions taste bitter and feel slippery to the touch.
2. Bases turn litmus paper blue.
3. Basic solutions conduct electricity.
4. Bases neutralize acids.

## Slide 39: Bases:
An example of a common base is sodium hydroxide, NaOH. In solution, it dissociates to form sodium ions and hydroxide ions
Notes: <number>
Common types of bases are lye, household ammonia, and most soaps. The following are four
characteristic properties of bases.
1. Basic solutions taste bitter and feel slippery to the touch.
2. Bases turn litmus paper blue.
3. Basic solutions conduct electricity.
4. Bases neutralize acids.

## Slide 40: Acids and Bases
When an acid reacts with a base, two products are formed; water and a salt. A salt is an ionic compound composed of positive ions and negative ions.
The ionic bond is what keeps salts in their molecular form.
Notes: <number>

## Slide 41: States of Matter
The term states of matter refers to the physical forms in which matter exists: solid, liquid, and gas.
Notes: <number>
Characteristics of Matter
The term states of matter refers to the physical forms in which matter exists: solid, liquid, and
gas. Solids are characterized as having both a definite shape and a definite volume. In a solid,
the forces that keep the molecules or atoms together are strong. Therefore, a solid does not
require outside support to maintain its shape.
Liquids have definite volumes but indefinite shapes and are slightly compressible. Liquids take
the shape of their containers. The forces that keep a liquid's molecules or atoms together are
weaker than in the solids.
Gases are readily compressible and capable of infinite expansion. They have indefinite shape and
indefinite volume. Of the three states, gases have the weakest forces holding their molecules or
atoms together.
The different states of matter have one thing in common; they can all be broken down into
fundamental units called atoms.

## Slide 42: States of Matter
Solids are characterized as having both a definite shape and a definite volume. In a solid, the forces that keep the molecules or atoms together are strong. Therefore, a solid does not require outside support to maintain its shape.
Notes: <number>
Characteristics of Matter
The term states of matter refers to the physical forms in which matter exists: solid, liquid, and
gas. Solids are characterized as having both a definite shape and a definite volume. In a solid,
the forces that keep the molecules or atoms together are strong. Therefore, a solid does not
require outside support to maintain its shape.
Liquids have definite volumes but indefinite shapes and are slightly compressible. Liquids take
the shape of their containers. The forces that keep a liquid's molecules or atoms together are
weaker than in the solids.
Gases are readily compressible and capable of infinite expansion. They have indefinite shape and
indefinite volume. Of the three states, gases have the weakest forces holding their molecules or
atoms together.
The different states of matter have one thing in common; they can all be broken down into
fundamental units called atoms.

## Slide 43: States of Matter
Liquids have definite volumes but indefinite shapes and are slightly compressible. Liquids take the shape of their containers. The forces that keep a liquid's molecules or atoms together are weaker than in the solids.
Notes: <number>
Characteristics of Matter
The term states of matter refers to the physical forms in which matter exists: solid, liquid, and
gas. Solids are characterized as having both a definite shape and a definite volume. In a solid,
the forces that keep the molecules or atoms together are strong. Therefore, a solid does not
require outside support to maintain its shape.
Liquids have definite volumes but indefinite shapes and are slightly compressible. Liquids take
the shape of their containers. The forces that keep a liquid's molecules or atoms together are
weaker than in the solids.
Gases are readily compressible and capable of infinite expansion. They have indefinite shape and
indefinite volume. Of the three states, gases have the weakest forces holding their molecules or
atoms together.
The different states of matter have one thing in common; they can all be broken down into
fundamental units called atoms.

## Slide 44: States of Matter
Gases are readily compressible and capable of infinite expansion. They have indefinite shape and indefinite volume. Of the three states, gases have the weakest forces holding their molecules or atoms together.
Notes: <number>
Characteristics of Matter
The term states of matter refers to the physical forms in which matter exists: solid, liquid, and
gas. Solids are characterized as having both a definite shape and a definite volume. In a solid,
the forces that keep the molecules or atoms together are strong. Therefore, a solid does not
require outside support to maintain its shape.
Liquids have definite volumes but indefinite shapes and are slightly compressible. Liquids take
the shape of their containers. The forces that keep a liquid's molecules or atoms together are
weaker than in the solids.
Gases are readily compressible and capable of infinite expansion. They have indefinite shape and
indefinite volume. Of the three states, gases have the weakest forces holding their molecules or
atoms together.
The different states of matter have one thing in common; they can all be broken down into
fundamental units called atoms.

## Slide 45: Conductivity
Conductivity is a measure of the ability of a substance to allow electron flow.
Notes: <number>
Conductivity is a measure of the ability of a substance to allow electron
flow. In the context of corrosion, conductivity indicates the amount of ions in solution, which relates directly to the potential of corrosion taking place.

## Slide 46: Conductivity
Conductivity of reactor facility water is measured to provide an indication of dissolved ionic substances in the coolant
Notes: <number>
Conductivity is a measure of the ability of a substance to allow electron
flow. In the context of corrosion, conductivity indicates the amount of ions in solution, which relates directly to the potential of corrosion taking place.

## Slide 47: Conductivity
In the context of corrosion, conductivity indicates the amount of ions in solution, which relates directly to the potential of corrosion taking place.
Notes: <number>
Conductivity is a measure of the ability of a substance to allow electron
flow. In the context of corrosion, conductivity indicates the amount of ions in solution, which relates directly to the potential of corrosion taking place.

## Slide 48: Conductivity
Treating the water by softening and demineralization removes the dissolved solids and reduces the conductivity.
Notes: <number>
Conductivity is a measure of the ability of a substance to allow electron
flow. In the context of corrosion, conductivity indicates the amount of ions in solution, which relates directly to the potential of corrosion taking place.

## Slide 49: pH
pH is defined as the negative logarithm of the hydrogen concentration, represented as [H+] in moles/liter in a solution.
The pH of pure water at 25 C is 7.
pH values less than 7 indicate an acidic solution and values greater than 7 indicate a basic or alkaline solution.
Notes: <number>
Many compounds dissolve in water and alter the hydrogen ion concentration. Compounds that produce hydrogen ions directly when dissolved in water are called acids, and those that produce hydroxyl ions directly when dissolved in water are called bases. To treat these aspects of chemistry more precisely, a quantitative system of expressing acidity or basicity (alkalinity) is needed. This need could be met by using the value of [H+], where [H+] is expressed in moles/liter, as a measure of acidity. But, in most cases [H+] is in the range of 1.0 E-1 to1.0E-14 moles/liter. Because numbers of this magnitude are inconvenient to work with, an alternate system for expressing the acidity of dilute solutions has been devised. This system is based on a quantity called pH. ph is defined as the negative logarithm of the hydrogen concentration, represented as [H+] in moles/liter.
pH = -log [H+]
The negative logarithm is specified because the logarithm of any number less than 1 is negative; thus multiplication by -1 causes the values of pH to be positive over the range in which we are interested. (The term pH was first defined by a Danish chemist and is derived from p for the Danish word potenz (power) and H for hydrogen.)

## Slide 50: pH and Corrosion
The corrosion rate of iron in high temperature water is lower in the pH range of 7 to 12 than (Neutral to slightly basic) it is at either lower or higher pH values
Notes: <number>
Many compounds dissolve in water and alter the hydrogen ion concentration. Compounds that produce hydrogen ions directly when dissolved in water are called acids, and those that produce hydroxyl ions directly when dissolved in water are called bases. To treat these aspects of chemistry more precisely, a quantitative system of expressing acidity or basicity (alkalinity) is needed. This need could be met by using the value of [H+], where [H+] is expressed in moles/liter, as a measure of acidity. But, in most cases [H+] is in the range of 1.0 E-1 to1.0E-14 moles/liter. Because numbers of this magnitude are inconvenient to work with, an alternate system for expressing the acidity of dilute solutions has been devised. This system is based on a quantity called pH. ph is defined as the negative logarithm of the hydrogen concentration, represented as [H+] in moles/liter.
pH = -log [H+]
The negative logarithm is specified because the logarithm of any number less than 1 is negative; thus multiplication by -1 causes the values of pH to be positive over the range in which we are interested. (The term pH was first defined by a Danish chemist and is derived from p for the Danish word potenz (power) and H for hydrogen.)

## Slide 51: Units of Measure
Atomic Nomenclature:
Where:
A = atomic mass number (protons and neutrons)
X = element symbol
Z = atomic number (protons)

## Slide 52: Units of Measure
Atomic Mass:

## Slide 53: Review Questions:
What is the smallest unit involved in the chemical change of matter?
The ATOM!

## Slide 54: Review Questions:
Are atoms electrically neutral?
Yes!

## Slide 55: Review Questions:
An atom is composed of a ________ charged nucleus orbited by one or more ________ charged particles called electrons
Positively
Negatively

## Slide 56: Review Questions:
Groups or clusters of atoms held together by means of chemical bonding are known as
Molecules

## Slide 57: Review Questions:
Two or more atoms of different elements held together by bonds form a
Compound

## Slide 58: Review Questions:
Acids are substances that dissociate in water to produce
H+ ions

## Slide 59: Review Questions:
Strong Acids have _____ pH values
Low

## Slide 60: Review Questions:
Bases are substances that produce hydroxide ions _______ in water solutions.
OH- ions

## Slide 61: Review Questions:
Strong Bases have _________pH values.
High

## Slide 62: Review Questions:
The two (2) products formed when acids and bases neutralize each other are ______
Water and Salt

## Slide 63: Review Questions:
What are the three (3) states of matter?
Solid, Liquid and Gas

## Slide 64: Review Questions:
__________ is a measure of the ability of a substance to allow electron flow.
Conductivity

## Slide 65: Review Questions:
Conductivity indicates the amount of ions in solution, which relates directly to the potential of ________ taking place.
Corrosion

## Slide 66: Enabling Statements: Competency 6
Explain how to read and interpret information from the Periodic Table of Elements.
Notes: <number>

## Slide 67: Periodic Table
Over many years of chemical investigation, scientists have discovered a remarkable feature of the elements.
If the elements are arranged in the order of their atomic numbers, the chemical properties of the elements are repeated somewhat regularly.

## Slide 68: Periodic Table
Each horizontal row is called a period.

## Slide 69: Periodic Table
Elements with similar chemical properties appear in vertical columns called groups.

## Slide 70: Periodic Table
The number directly below each element is its atomic number (# of protons in the nucleus = Z)

## Slide 71: Periodic Table
The number the number above each element is its atomic weight (A).

## Slide 72: Periodic Table

## Slide 73: Periodic Table
Chemical activity can also be determined from position in the periodic table. The most active metals are the members of the Alkali Family, e.g., cesium (Cs) and francium (Fr).
The most active nonmetals are the members of the Halogen Family, e.g., fluorine (F) and chlorine (Cl).
The Noble Gases in Group 0 are inert.

## Slide 74: Review Question:
In the Periodic Table of elements, how are elements of similar chemical characteristics aligned?
In VERTICAL GROUPS

## Slide 75: Enabling Statements: Competency 6
Define:
  Elements
  Mixtures
  Solutions
  Compounds
Notes: <number>
Combining Elements
The Laws of Definite Proportions and Multiple Proportions and the related portions of atomic
theory form the bases for most quantitative calculations involving chemical reactions. Applying
the basic chemical laws to chemical bonding will help the reader to understand the probability
and proportions involved in chemical reactions. Regardless of the type of bond (ionic, covalent,
coordinate covalent, or metallic), specific amounts of one element will react with specific
amounts of the element(s) with which it is combined.
If two substances are placed together in a container, in any ratio, the result is a mixture. When
a teaspoon of sugar is added to a glass of water, it will slowly dissolve into the water and
disappear from view. As a result, the molecules of sugar are evenly distributed throughout the
water and become mixed with the water molecules. Because the sugar and water mixture is
uniform throughout, it is said to be homogeneous. A homogeneous mixture of two or more
substances is called a solution. The reason solutions are classified as mixtures rather than as
compounds is because the composition is not of fixed proportion.
All solutions consist of a solvent and one or more solutes. The solvent is the material that
dissolves the other substance(s). It is the dissolving medium. In the water-sugar solution, the
water is the solvent. The substances that dissolve in the solution are called solutes. In the
water-sugar solution, sugar is the solute. It is not always easy to identify which is the solvent
and which is the solute (for example, a solution of half water and half alcohol).
Solutions can exist in any of the three states of matter, solid, liquid, or gas. The earth's
atmosphere is a gaseous solution of nitrogen, oxygen, and lesser amounts of other gases. Wine
(water and alcohol) and beer (water, alcohol, and CO ) are examples of liquid solutions. Metal 2
alloys are solid solutions (14-karat gold is gold combined with silver or copper).
One factor that determines the degree and/or rate at which a reaction takes place is solubility.
Solubility is defined as the maximum amount of a substance that can dissolve in a given amount
of solvent at a specific temperature. At this point, the solution is said to be saturated. A
solution is saturated when equilibrium is established between the solute and the solvent at a
particular temperature. Equilibrium is the point at which the rates of the forward and reverse
reactions are exactly equal for a chemical reaction if the conditions of reaction are constant.
Kinetics is the study of the factors which affect the rates of chemical reactions. There are five
principle factors to consider: concentration, temperature, pressure, the nature of the reactants,
and the catalyst.

## Slide 76: Elements:
An atom is classified chemically by the number of protons in its nucleus.
Atoms that have the same number of protons in their nuclei have the same chemical behavior.
Atoms that have the same number of protons are grouped together and constitute a chemical element.

## Slide 77: Mixtures:
Mixtures consist of two or more substances intermingled with no constant percentage composition. Each component retains its original properties.
Notes: <number>

## Slide 78: Mixtures:
If two substances are placed together in a container, in any ratio, the result is a mixture.
Notes: <number>

## Slide 79: Solutions:
A homogeneous mixture of two or more substances is called a solution.
Notes: <number>

## Slide 80: Solutions:
All solutions consist of a solvent and one or more solutes. The solvent is the material that dissolves the other substance(s).
Notes: <number>

## Slide 81: Compounds:
A chemical compound is a pure chemical substance consisting of two or more different chemical elements.
Notes: <number>
A chemical compound is a pure chemical substance consisting of two or more different chemical elements[1][2][3] that can be separated into simpler substances by chemical reactions.[4] Chemical compounds have a unique and defined chemical structure; they consist of a fixed ratio of atoms[3] that are held together in a defined spatial arrangement by chemical bonds. Chemical compounds can be molecular compounds held together by covalent bonds, salts held together by ionic bonds, intermetallic compounds held together by metallic bonds, or complexes held together by coordinate covalent bonds. Pure chemical elements are not considered chemical compounds, even if they consist of molecules which contain only multiple atoms of a single element (such as H2, S8, etc.),[5] which are called diatomic molecules or polyatomic molecules.

## Slide 82: Compounds:
Chemical compounds have a unique and defined chemical structure; they consist of a fixed ratio of atoms that are held together in a defined spatial arrangement by chemical bonds
Notes: <number>
A chemical compound is a pure chemical substance consisting of two or more different chemical elements[1][2][3] that can be separated into simpler substances by chemical reactions.[4] Chemical compounds have a unique and defined chemical structure; they consist of a fixed ratio of atoms[3] that are held together in a defined spatial arrangement by chemical bonds. Chemical compounds can be molecular compounds held together by covalent bonds, salts held together by ionic bonds, intermetallic compounds held together by metallic bonds, or complexes held together by coordinate covalent bonds. Pure chemical elements are not considered chemical compounds, even if they consist of molecules which contain only multiple atoms of a single element (such as H2, S8, etc.),[5] which are called diatomic molecules or polyatomic molecules.

## Slide 83: Review Question:
Define “Mixture”
Mixtures consist of two or more substances intermingled with no constant percentage composition. Each component retains its original properties.

## Slide 84: Review Question:
Define “Solution”
A homogeneous mixture of two or more substances is called a solution.

## Slide 85: Review Question:
What is a “Compound”
A chemical compound is a pure chemical substance consisting of two or more different chemical elements

## Slide 86: Enabling Statements: Competency 6
Gas Properties

## Slide 87: Explain the Characteristics of gases
Gases are readily compressible and capable of infinite expansion.
They have indefinite shape and indefinite volume.
Of the three states, gases have the weakest forces holding their molecules or atoms together.

## Slide 88: Enabling Statements: Competency 6
State the relationship between the temperature of a liquid and its vapor pressure.

## Slide 89: Temperature vs. Vapor Pressure
As Temperature INCREASES
Vapor Pressure INCREASES

## Slide 90: Temperature vs. Vapor Pressure
The vapor pressure of any substance increases non-linearly with temperature

## Slide 91: Enabling Statements: Competency 6
Explain corrosion chemistry and monitoring, including types of corrosion, characteristics and prevention.

## Slide 92: What is Corrosion?
Corrosion is the deterioration of a material due to interaction with its environment.

## Slide 93: How does it happen?
In general corrosion is the process whereby the surface of a metal undergoes a slow, relatively uniform; removal of material due to electro-chemical processes.

## Slide 94: How does it happen?
The two conditions typically required for a metal to undergo general corrosion are:
  metal and water in the same environment, and
  a chemical reaction between the metal and water that forms an oxide.

## Slide 95: How does it happen?
OXIDE
FILM
OXIDE-WATER
INTERFACE
METAL-OXIDE
INTERFACE
IRON METAL
WATER
FeO
Fe3O4
Fe2O3

## Slide 96: Different Types of Corrosion
Galvanic
Pitting
Intergranular Stress

## Slide 97: Galvanic Corrosion
Dissimilar Metals:

## Slide 98: Pitting/Crevice

## Slide 99: Intergranular Stress

## Slide 100: What problems does that create?
Corrosion of the nuclear fuel cladding may cause the cladding to fail.
Corrosion of Steam Generator Tubes can cause tube failure.
Corrosion of heat exchanger tubes can cause tube failure.

## Slide 101: What problems does that create?
Corrosion products reduce heat transfer capabilities
Reactor Coolant System corrosion leads to higher dose rates and more contamination.

## Slide 102: Enabling Statements: Competency 7
Explain basic water chemistry control fundamentals, including:
Effects of impurities
Ion exchange theory
Parameters monitored
Principles of water treatment

## Slide 103: Enabling Statements: Competency 7
Explain basic water chemistry control fundamentals, including:
Sources of impurities
The corrosion process
Water chemistry control methods

## Slide 104: Effects of Impurities
Reduction in heat transfer capability
Increased corrosion rates
Tube failures
  Steam Generators
  Heat exchangers – primary and secondary
Ion exchanger fouling – decontamination
Increased radiation source term
Notes: <number>
As discussed earlier, corrosion buildup reduces heat transfer capability, can create hot spots and cause fuel damage, and can lead to tube failures in heat exchanges, one of the most important being the Steam generators which provide the separation of primary and secondary systems.
Other important primary to secondary interfaces – CCW heat exchangers

## Slide 105: Ion Exchange Theory
Ion Exchange is a reversible exchange of ions from a liquid and a solid
Used to remove undesirable ions from a liquid and substitute acceptable ions from the solid (resin)

## Slide 106: Ion Exchange Theory
Two general types of ion exchange resins:
Cation – exchange positive ions
Anion – exchange negative ions
Notes: <number>
Related to home water conditioners
Na exchanged from resin for Mg, Mn, Ca – Cation resin

## Slide 107: Ion Exchange Theory
Common cations include Ca++, Mg++, Fe++, and H+
Common anions include Cl-, SO4-, and OH-
Notes: <number>
Related to home water conditioners
Na exchanged from resin for Mg, Mn, Ca – Cation resin

## Slide 108: Ion Exchange Theory
Resins - made of polymers
Ion selection based on ‘relative affinity’ – preferential attraction of resin to specific ions
Cation Affinities
Ba+2 > Sr+2 > Ca+2 > Co+2 > Ni+2 > Cu+2 > Mg+2 > Be+2
Anion Affinities
SO4 > I > NO3 > Br > HSO3 > Cl > OH > HCO3 > F
Notes: <number>
Related to home water conditioners
Na exchanged from resin for Mg, Mn, Ca – Cation resin

## Slide 109: Ion Exchange Theory
STORAGE
TANK
H
+
R
-
-
H
+
CATION
EXCHANGER
OH
-
R
+
-
OH
-
ANION
EXCHANGER
RAW WATER
PURE WATER
HCO
3
-
SO
4
=
CI
-
NO
3
-
Ca
++
Mg
++
Na
+
HCO
3
-
SO
4
=
Cl
-
NO
3
-
H
2
O
H
+
H
+
OH
-
H
2
O
Ca
++
Mg
++
Na
+
HCO
3
-
SO
4
=
Cl
-
NO
3
-
H
2
O
MIXED BED
EXCHANGER
H
2
O
R
+
-
OH
-
R
-
-
H
+

## Slide 110: Ion Exchange Theory
Monitoring DF
Channeling
Breakthrough
Exhaustion

## Slide 111: Chemistry Parameters Monitored
Notes: <number>
Reactor Coolant System parameters

## Slide 112: Chemistry Parameters Monitored / Control of Impurities

## Slide 113: Sources of Impurities
Make-up water
Tube Leaks
  Condenser
  Heat exchangers
Maintenance activities