## Slide 1
ACADs (08-006) Covered
Keywords
Demineralization, reverse osmosis, evaporation, distillation, oil separation, condensate polishing, boiler protection.
Description
Supporting Material
1.1.6.2.4 | 1.1.6.3.2 | 4.2.7.6 | 4.20.1.16 | 4.22.1.4 | 4.22.1.5 | 5.2.2.6 | 
Notes: <number>

## Slide 2
Power Plant Construction and QA/QC
Section 2.6– Water Treatment
Engineering Technology Division

## Slide 3
Overview
Section 2.6– Water Treatment
Introduction
Chemistry Basics
Pretreatment
Demineralization
Condensate Polishing
Boiler Protection

## Slide 4
Introduction
Section 2.6– Water Treatment
Water Treatment is the attempt to remove anything that is not water molecules.
Chemicals and compounds in water create corrosive environments.
pH is a measure of acidity or alkalinity.
Failure to maintain chemistry control can lead to reduced efficiency and/or premature failure.
Understanding the source water chemistry is the key to determining Water Treatment requirements.

## Slide 5
Section 2.6– Water Treatment
Chemistry Basics – Water Source

## Slide 6
Section 2.6– Water Treatment
Chemistry Basics – Water Source

## Slide 7
Chemistry Basics – River Water
Section 2.6– Water Treatment

## Slide 8
Section 2.6– Water Treatment
Chemistry Basics – Tap Water

## Slide 9
Section 2.6– Water Treatment
Chemistry Basics – Industrial Contaminants

## Slide 10
Section 2.6– Water Treatment
Chemistry Basics – Other Contaminants

## Slide 11
Section 2.6– Water Treatment
Chemistry Basics – Other Contaminants

## Slide 12: Oil separation
Oil and water separators are commonly used in electrical substations.
The transformers found in substations use a large amount of oil for cooling purposes.
Moats are constructed surrounding unenclosed substations to catch any leaked oil, but these will also catch rainwater. Oil and water separators therefore provide a quicker and easier cleanup of an oil leak.
Notes: http://en.wikipedia.org/wiki/API_oil-water_separator
<number>

## Slide 13: Oil separation
Objective: Recognize the components, functions and operation of the Chemical and Oily Waste Water Systems.
Notes: Chemical and Oily Waste Water Systems
PALO VERDE NUCLEAR GENERATING STATION
Instrumentation & Controls Training
Classroom Lesson
EO 1.1
Identify the functions of the Chemical and Oily Waste Water Systems.
1.1.1 Main Idea
<PG 11663:OB 79503(1114)><<A. Overview
1. Drainage and Leakage are facts of life for a power station. At a Nuclear Power Station, we have to consider types of drains.
a. Chemical Waste Drains
1) high amounts of dissolved solids
2) corrosive
3) environmental pollutants
b. Oily Waste Drains
1) leakage from heavy equipment, hydraulics
2) damages water purification media - resins
3) environmental pollutant
4) flammable
c. Radioactive Drains
1) represent a large portion of systems at plant; many are or have potential to be radioactive
2) complicate segregation of other drains (chemical, oily, etc.)
a) while others can be treated and released to environment easily, radioactive contamination complicates treatment and release.
d. Pure or low dissolved solid drains
1) ideal - can be released to environment easily
2) easy to reclaim by some means – demin. water is expensive
2. We need means of segregating these.
a. Separate out known
1) Radioactive drains - sent to Liquid Radwaste low TDS holdup tanks. Includes drains from:
a) Aux. Building Sump
b) Containment Drainage Sumps
2) Radioactive - Chemical Drains sent to Chem Drain Tank then to either Solid or Liquid Radwaste. Includes:
a) Decon Station Drains
b) Laboratory Drains
3) Potentially Contaminated Chemical Drains - sent to Cooling Water Holdup Tank. Include:
a) Essential Cooling Water Room Drains
b) Various Radwaste Room Drains
4) High dissolved solid wastes -sent to Chemical Waste Neutralizing Tank. Includes:
a) Condensate Demineralizer Regeneration Waste
b) Blowdown Demineralizer Regeneration Waste
5) Oily Waste - sent to Oily Waste Separator. Include various sump drains that usually contain oil.
3. Three systems to discuss are:
a. Cooling Water Waste Drain System
b. Condensate Polisher Waste and Drain System
c. Oily and Non-Radioactive Waste Drain System
d. (Radioactive Drains are discussed in the Radwaste Systems lecture.)
<number>

## Slide 14: Oil separation
Drainage and Leakage are facts of life for a power station. At a Nuclear Power Station, we have to consider types of drains.
Oily Waste Drains:
1) leakage from heavy equipment, hydraulics
2) damages water purification media - resins
3) environmental pollutant
4) flammable
Notes: Chemical and Oily Waste Water Systems
PALO VERDE NUCLEAR GENERATING STATION
Instrumentation & Controls Training
Classroom Lesson
<number>

## Slide 15: Oil separation
Oily and Non-Radioactive Waste Drains
Functions:
1. Collect and transport liquid waste from equipment and floor drains of the:
a. Turbine Bldg.
b. Control Bldg.
c. Diesel Generator Bldg.
d. Plant yard areas
2. Remove entrailed oil from the waste for disposal and transfer the oil free water to the retention basin and then to the evaporation pond.
Notes: Chemical and Oily Waste Water Systems
PALO VERDE NUCLEAR GENERATING STATION
Instrumentation & Controls Training
Classroom Lesson
<number>

## Slide 16: Oil separation
Oily and Non-Radioactive Waste Drains
Description:
1. System consists of:
a. various sumps and respective pumps
b. oily waste separator
c. Retention Basins
d. Evaporation Pond
Notes: Chemical and Oily Waste Water Systems
PALO VERDE NUCLEAR GENERATING STATION
Instrumentation & Controls Training
Classroom Lesson
<number>

## Slide 17
Section 2.6– Water Treatment
Pretreatment

## Slide 18
Pretreatment – Waste Water
Section 2.6– Water Treatment
Varies by use

## Slide 19
Section 2.6– Water Treatment
Negative Valance
Positive Valance
Demineralization – Resin Type

## Slide 20
Section 2.6– Water Treatment
Demineralization – Reverse Osmosis Process

## Slide 21
Section 2.6– Water Treatment
Demineralization – Reverse Osmosis

## Slide 22
Section 2.6– Water Treatment
Demineralization – Evaporation
Typically operates in a vacuum to reduce source heat.

## Slide 23
Section 2.6– Water Treatment
Demineralization –Distillation

## Slide 24
Condensate Polishing
Section 2.6– Water Treatment

## Slide 25
Section 2.6– Water Treatment
Condensate Polishing

## Slide 26
Boiler Protection
Section 2.6– Water Treatment
When source water is properly analyzed and water treatment address the impurities, then Boiler Protection is provided.
To Improve protection, additional chemicals can be added (Oxalates, pH controls, H2, etc)
Oxygen and Carbon Dioxide reduction in the De-aeration process reduces corrosive environments.

## Slide 27
Questions?
Section 2.6– Water Treatment