## Slide 1
ACADs (08-006) Covered
Keywords
Rigging, hoist, crane.
Description
Supporting Material
Hoists and Cranes
1.3.4.2 | 1.3.4.5 | 5.1.2.19 | 5.1.2.20 | 5.2.1.9b |  |  | 

## Slide 2
Hoists and Cranes

## Slide 3: Terminal Objective
Understand the basic terminology and safety associated Hoists, cranes, and rigging

## Slide 4: Enabling Objectives
Identify a number of DO’s and DONT’s around rigging
Explain the uses of various types of hoists
Be able to identify some basic crane hand signals

## Slide 5
Basic RIGGING Practices
All personnel shall be kept clear of lifted or suspended loads.
Keep all personnel and body parts clear of the rigging hardware.
Keep all personnel and body parts from under the load.
Shocking the load is prohibited.
A sling shall not be pulled from a load when the load is resting on the sling.

## Slide 6
Prior to use the slings and all rigging hardware, fastenings and attachments shall be inspected for damage or defects.
Additional inspections shall be performed during sling use.
When warranted, damaged or defective slings shall be removed from service.

## Slide 7
Basic Sling Utilization Practices
Keep sling angles as close to vertical as possible.
Ensure sling capacity is enough for load.
Protect slings from abrasions or sharp edges.
Do not misuse slings.

## Slide 8: Standards and Expectations
Leather gloves are required during rigging activities.
Notes: OBJECTIVE 9. STATE the safety precautions, responsibilities, and expectations to be observed during rigging activities IAW applicable standards, procedure and Conduct of Maintenance Guide.
Instructor Note:
Reinforce to the students the safety aspects and management expectations of when
utilizing wire rope and or rigging equipment. Remember SAFETY is number one!
Wire ropes must be inspected prior to use. Insure inspection tag is with in date specified.
Always use suitable leather gloves during rigging activities.
Personal Protective Equipment must be worn in all rigging and work activities.
Gloves may be excluded for hand signals only.

## Slide 9: Common Types of Hooks
Swivel
Duplex
Eye
Eye
Grab Eye
Notes: Objective 5.
Commonly used hooks:
• Eye hooks – The wire rope or a shackle is attached to the hook through the hook’s eye. The
eye and the hook are on the same plane. These hooks have the eye with the plane of the
hook.
The capacity of bronze, high-strength eye hooks ranges from 1/2 to 6.5 tons.
• Shank hooks – Shank hooks are specifically design to swivel 360º. The shank end is threaded
for a special nut that holds the hook on the face of a thrust bearing. They range in capacities
from 3/4 to 200 ton. Above 200 ton, a single-throat design is difficult to use because of its
unbalanced shape. For this reason, a duplex or sister hook is preferred above 60 ton and
becomes almost mandatory above 200 ton.
In general, small hoists range in capacity up to 20 ton; therefore, the only types of hooks
normally used are the eye and shank single hooks.
For safety reasons and to prevent slings from being unhooked, shank single hooks are
required to have spring-loaded safety latches.

## Slide 10: Types of Shackles
Screw Pin
Round Pin
Safety Type
Chain
Anchor
Screw Pin
Round Pin
Safety Type
Notes: Objective 5. DESCRIBE rigging hardware to include characteristics, functions and inspection criteria.
Instructor Note: Explain to students
Safe working load is for new or like-new condition; any change in this condition
will lessen the load the fitting can safely withstand.
1. Must be inspected prior to use and has certain precautions that must be considered.
Cotter pins must be installed on round pin shackles.
Never use screw-type pin shackles if the pin can roll under load and unscrew.
Shackle pulled at an angle greatly reduce capacity; use washers or spacers to centralize
the load.
Never exceed the safe working load on a shackle. (or any rigging equipment)
Do not abuse shackles by throwing them down or hammering, etc..
Clean and inspect for damage that might have occurred during usage.
Return to proper storage area and the area should be a clean dry place free of corrosives.
2. Function.
Used to couple slings to hooks, slings to eyes, and hooks to eyes.
Used to make choker with single-leg sling.
Connectors used to support the lift load.

## Slide 11: Eyebolts Characteristics
Plain
Shoulder
Straight Pull Only
Angle Pulls Allowed
Notes: Objective 5.
Eyebolts characteristics:
A bolt with a looped head made of forged steel. May or may not be shouldered above the
threaded portion.
Two common types:
Plain (shoulder less) type eyebolts are designed for straight pulls only and will bend or break if
pulled at an angle. They are not designed for any side loading.
Shoulder type can be pulled at an angle up to 45o, but safe working load declines drastically as
angle of lift increases.
Installation depth:
Both types of eyebolts must have 1 1/2 times their thread diameter engaged into the object to
be picked up for a safe lift.
Must be inspected prior to use and has special considerations for usage.
1. Do not pull on plain eyebolts at any angle.
2. Be sure that shoulder eyebolts are properly seated; use washers to shim if
necessary to align eyebolts with lifting slings.
3. If two eyebolts are used, be sure that eyes are oriented with each other.
4. Ensure correct thread size and type for engagement prior to use.
Example Sight Specific Event: STPNOC once had issues with personnel inserting metric eyebolts into standard National Course threaded floor plugs. They pulled out under load due to poor thread engagement – dropping the load.
CONTINUED ON NEXT SLIDE.

## Slide 12: Rigging Equipment
Hoists or Cranes
“the Muscle to make things move”

## Slide 13: Rigging Equipment
Hoists and Cranes
Come-a-longs
- Pulling, lifting or leveling loads
- cable, chain
- capacity on side
- safety latches on hooks

## Slide 14: Rigging Equipment
Hoists and Cranes
Chain Hoists
- Pulling, lifting or leveling loads
- capacity on side
- safety latches on hooks
- pull chain and load chain
are different grades

## Slide 15: Chain Hoist / Chain fall
Pull Chain
Load Chain
Body/block
Assembly
Notes: Instructor Note:
Explain that the three types of chain hoists commonly utilized are Differential, Screw-gear, and Spur-gear.
(To launch/activate video with cursor click on video window at appropriate time.)
Differential chain hoist - characteristics:
Simplest but least efficient of the three kinds of chain hoists and consists of:
Upper block, Lower block assembly and a Endless chain.
Upper block:
Has a hook which attaches block to overhead/crane.
Contains two sheaves which have pockets to fit chain links which keep chain from slipping.
Sheaves are mounted on same shaft which rotate at same rate as the shaft.
One sheave has more pockets than the other.
The hook on lower block attaches to load.
Least efficient of three kinds of hoists.
Requires more work to lift given load with differential hoist than other types.
It is light and relatively inexpensive.
The difference in the number of pockets on the larger sheave and the smaller sheave is
called the hoist's differential.
Hoist with differential of two will shorten load loop by two links every time sheaves rotate,
raising load a distance equal to one link (half of differential).
Hand loop of chain moves through fairly large distance while load raised only a small amount.

## Slide 16: Beam Trolley
5 Ton
Inspection Criteria
Notes: Objective 5. DESCRIBE rigging hardware to include characteristics, functions and inspection criteria.
Beam trolleys use and their characteristics:
Beam trolleys are devices that fit on the lower flange of a horizontal beam that allow a hoist or
lug to move axially along the length of the horizontal beam.
Two types of beam trolleys are commonly employed in power plants: the push trolley and the
geared trolley.
Typically, they are sized according to the width of the beam on which they are to be installed,
with no more than 1/4-inch side movement (1/8 inch on each side).
Beam trolleys can be equipped with a number of different lifting/rigging devices. Many times,
trolleys are equipped with a hook.
CAUTION NOTE: Beam trolleys should be removed from service if:
They can no longer move freely along the flange of the beam or if the attachment device
(hook, hoist, shackle) no longer meets the inspection criteria established for each of these
devices.
The trolley should also be removed if there is any evidence of damage or permanent
deformation (cracking, corrosion, bending) of the faceplates or axles or if the load rating/safety
plates are missing or illegible.
Extreme care required during installation to ensure lifting is point directly below.
“I” of beam, wheels are equally spaced for proper I-beam flange contact and bolted securely.

## Slide 17: Mobile Crane Signals
Notes: Objective 7. IDENTIFY hand signals used for control of hoisting and crane operations in accordance with criteria for hand signals as specified by the ASME B30.5 standards.

## Slide 18: Slow signals
Notes: Objective 7. IDENTIFY hand signals used for control of hoisting and crane operations in accordance with criteria for hand signals as specified by the ASME B30.5 standards.

## Slide 19: Stop Signal
Notes: Objective 7. IDENTIFY hand signals used for control of hoisting and crane operations in accordance with criteria for hand signals as specified by the ASME B30.5 standards.