## Slide 1
Power Plant Science- Residual Heat & Reactor Operation
ACADs (08-006) Covered
Keywords
Heat, decay heat, reactivity, reactivity coefficients, fuel temperature coefficient, void coefficient, background radiation, reactor vessel, pressurizer, containment, cooling towers, control rods, fission product poisons.
Description
This PowerPoint presentation is an overview of basic power plant science concepts including residual heat and decay heat as pertaining to reactor operations.
Supporting Material
1.1.4.4 | 1.1.4.6.3 | 1.1.4.6.4 | 1.1.4.6.5 | 5.2.3.7 | 5.2.3.8

## Slide 2: Power Plant Science
Power Plant Science

## Slide 3: Residual Heat & Heat Decay (1.1.4.4)
Objectives
  Students should have a basic understanding of how heat effects Nuclear reactors including the importance of:
    Sources of decay heat
    Identify major sources of background radiation

## Slide 4: Decay Heat (1.1.4.4.1)
Decay heat production is a particular problem associated with nuclear reactors.
Even though the reactor is shut down, heat is produced from the decay of fission fragments.
Limits for each particular reactor are established to prevent damage to fuel assemblies due to decay heat.

## Slide 5: Spent Fuel Pool

## Slide 6: Decay Heat
A problem peculiar to power generation by nuclear reactors is that of decay heat.
In fossil fuel facilities, once the combustion process is halted, there is no further heat generation, and only a relatively small amount of thermal energy is stored in the high temperature of plant components.

## Slide 7: Decay Heat
In a nuclear facility, the fission of heavy atoms such as isotopes of uranium and plutonium results in the formation of highly radioactive fission products.
Some radioactive atoms will decay while the reactor is operating and the energy released by their decay will be removed from the core along with the heat produced by the fission process.

## Slide 8: Decay Heat
All radioactive materials that remain in the reactor at the time it is shut down and the fission process halted will continue to decay and release energy.
This release of energy by the decay of fission products is called decay heat.

## Slide 9: Significance of Decay Heat
Reactor decay heat can be a major concern. In the worst case scenarios, it can cause melting of and/or damage to the reactor core, as in the case of Three Mile Island.
The degree of concern with decay heat will vary according to reactor type and design.

## Slide 10: Three Mile Island

## Slide 11: Significance of Decay Heat
Each reactor will have some limits during shutdown that are based upon decay heat considerations.
These limits may vary because of steam generator pressure, core temperature, or any other parameter that may be related to decay heat generation.
Even during refueling processes, heat removal from expended fuel rods is a controlling factor.
For each limit developed, there is usually some safety device or protective feature established.

## Slide 12: Major Sources of Natural Background Radiation (1.1.4.5)
Background radiation is the ionizing radiation constantly present in the natural environment of the Earth, which is emitted by natural and artificial sources.

## Slide 13: Background Radiation

## Slide 14: Background Radiation
Natural background radiation comes from two primary sources: cosmic radiation and terrestrial sources.
The worldwide average background dose for a human being is about 2.4 millisievert (mSv) per year.
This exposure is mostly from cosmic radiation and natural radionuclides in the environment (including those within the body).

## Slide 15: Background Radiation
Natural background radiation is far greater than human-caused background radiation exposure, which in the year 2000 amounted to an average of about 5 μSv (0.005 mSv) per year from historical nuclear weapons testing, nuclear power accidents and nuclear industry operation combined.
This is greater than the average exposure from medical tests, which ranges from 0.04 to 1 mSv per year.

## Slide 17: Background Radiation
Older coal-fired power plants without effective fly ash capture are one of the largest sources of human-caused background radiation exposure

## Slide 18: Basic Reactor Operations (1.1.4.6)
  Objectives:
    Reactor types
    Reactor Parameters
    Reactivity
    Response to control rods
    Boron
    Fission Product poisons
    Reactor Startup/shutdown
    Reactivity events
    Design concepts
    Core Parameters
    Control methods

## Slide 19: Basic Reactor Design (1.1.4.6.1)
The Following slides show the basic design for nuclear power plants in the in the United States.
Important note: American facilities are the premier nuclear reactors in the world. They are among the safest and most expensive. Reactor design vary greatly around the world.

## Slide 22: Reactor Vessel & Internals
Notes: Core
217 fuel assemblies
Approx. 8” square and 13’ tall
Stacked side by side in the center of the reactor
Uranium Dioxide pellets
Vessel
41’ tall 18’ in diameter
Made of high strength steel
Walls 8” thick

## Slide 23
Refueling:

## Slide 24
Refueling:

## Slide 25: Nuclear Reactor
157 Fuel
Elements
Notes: Artist’s sketch of a Westinghouse nuclear reactor.
The fuel is shown in red in the heart of the reactor.
Hot leg and Cold leg nozzles are shown.
Control Rod drive shafts are readily visible at the top.

## Slide 26: Reactor Vessel Fabrication
Notes: Just wanted you to see a great photo.
This reactor is about to be annealed in the furnace shown at the right.
This is part of the fabrication process and relieves internal stresses.

## Slide 27: Reactor Vessel Delivery
Notes: This reactor vessel, shown being delivered to the site on a sled, shows the relative size of a reactor.
Wall thickness of this high grade carbon steel is 8”. The vessel also has an inner liner made of stainless steel.

## Slide 28: Steam Generator
Steam
Generator
Tubes
Notes: The Steam Generator is the interface between the Reactor Coolant System and the Secondary System.
RCPs force RCS water through the 3,200+ tubes of the Steam Generators (3 S/Gs for Turkey Point).
This RCS water never comes in contact with the secondary system water but transfers its heat energy across the tube surface to turn the water on the outside of the tubes into saturated steam.
The Steam Generator is essentially a very large heat exchanger.

## Slide 29: Pressurizer
Electrical
Heaters
Notes: The Pressurizer is the only place in the RCS where a steam/water interface exists.
The rest of the RCS, including the reactor core, is all immersed in subcooled water.
Water in the Pressurizer is heated with electrical heaters to approximately 653°F. Because the conditions are saturated, this defines the Pressurizer and RCS pressure at 2235 psig.

## Slide 30: Reactor Coolant Pump
Notes: The RCPs are huge (6,000 HP) pumps that force the Reactor Coolant through the core and around the loops.
There are 3 RCPs for each reactor, one in each loop. Their function is to cool core and transport the heat energy (7 billion BTU’s per hour) from the reactor core to the 3 Steam Generators.

## Slide 31: Containment
Notes: The Containment structure houses the primary systems.
At Turkey Point it is approximately 150 feet tall.
The walls are made out of steel reinforced concrete and have a steel liner. For added strength, pre-stressed cables encircle the sides and top dome.
The minimum wall thickness is 3 and 1/2 feet thick and in some places approaches 7 feet thick.
The Containment is designed to withstand any plausible accident (nuclear accident, airplane crash, hurricane).
There is a myth that containments have to be strong enough to contain a nuclear explosion from the reactor. The Uranium fuel in commercial reactors is only 3 - 4% enrichment. This causes the U-235 to be so diffuse, it is physically impossible for a reactor to explode like an atom bomb.

## Slide 32: Containment Reinforcement
Notes: This photo is a Containment under construction.
The steel rebar is as thick as a person’s arm.
Note that containments are just one of six barrier to the release of radiation (shields) at a nuclear power plant.
The four barriers are:
Fuel Pellet
Fuel Cladding
RCS Water
Reactor vessel and Reactor Coolant System
Shield walls inside Containment
Containment walls
Its interesting to note that the Chernobyl nuclear power plant was built without a Containment.

## Slide 33: Main Turbine
Turbine
Blading
Notes: This is a partially disassembled main turbine.
The smaller high pressure blading is shown in the foreground.
The larger low pressure blading is in the background.
The common turbine shaft that connects all of this blading is 74 meters long.
Not shown here is the electrical generator which will also be attached to the common shaft, beyond the low pressure blading.

## Slide 34: Cooling Towers
Notes: These are natural draft cooling towers that are associated with the tertiary system. The really big ones can be as high as 1,000 feet and dwarf a typical containment at 200 feet tall.
People often associate these with nuclear power plants but they can be used with any type of power plant, fossil or nuclear, that does not have a large body of water available to use as a heat sink.

## Slide 35: Turkey Point Cooling Canals
Notes: For the ultimate heat sink, Turkey Point uses a cooling canal system.
There are 32 south flowing canals and 7 north flowing canals….More than 150 total miles.
Transit time for this closed cooling loop is approximately 2 days.
As a result, Turkey point has not relied on Biscayne Bay for cooling since 1973.

## Slide 36: Reactivity (1.1.4.6.3)
Reactivity is a measure of the departure of a reactor from criticality.
The reactivity is related to the value of k.
Reactivity is a useful concept to predict how the neutron population of a reactor will change over time.

## Slide 37: Reactivity
The amount of reactivity (ρ) in a reactor core determines what the neutron population, and consequently the reactor power, are doing at any given time.
The reactivity can be effected by many factors (for example, fuel depletion, temperature, pressure, or poisons).

## Slide 38: Reactivity Coefficients
To quantify the effect that a variation in parameter (that is, increase in temperature, control rod insertion, increase in neutron poison) will have on the reactivity of the core, reactivity coefficients are used.
Reactivity coefficients are the amount that the reactivity will change for a given change in the parameter.

## Slide 39: Reactivity Coefficients
For example, an increase in moderator temperature will cause a decrease in the reactivity of the core.
The amount of reactivity change per degree change in the moderator temperature is the moderator temperature coefficient.

## Slide 40: Temperature Coefficient of Reactivity
The change in reactivity per degree change in temperature is called the temperature coefficient of reactivity.
Because different materials in the reactor have different reactivity changes with temperature and the various materials are at different temperatures during reactor operation, several different temperature coefficients are used.

## Slide 41: Temperature Coefficient of Reactivity
Usually, the two dominant temperature coefficients are the moderator temperature coefficient and the fuel temperature coefficient.

## Slide 42: Void Coefficient
In systems with boiling conditions, such as boiling water reactors (BWR), the pressure coefficient becomes an important factor due to the larger density changes that occur when the vapor phase of water undergoes a pressure change.
Of prime importance during operation of a BWR, and a factor in some other water-moderated reactors, is the void coefficient.

## Slide 43: Void Coefficient
The void coefficient is caused by the formation of steam voids in the moderator.
The void coefficient of reactivity is defined as the change in reactivity per percent change in void volume.

## Slide 44: Void Coefficient
As the reactor power is raised to the point where the steam voids start to form, voids displace moderator from the coolant channels within the core.
This displacement reduces the moderator-to-fuel ratio, and in an under moderated core, results in a negative reactivity addition, thereby limiting reactor power rise.
The void coefficient is significant in water-moderated reactors that operate at or near saturated conditions.

## Slide 45: Fuel Temperature Coefficient
Another temperature coefficient of reactivity, the fuel temperature coefficient, has a greater effect than the moderator temperature coefficient for some reactors.
The fuel temperature coefficient is the change in reactivity per degree change in fuel temperature. This coefficient is also called the "prompt" temperature coefficient because an increase in reactor power causes an immediate change in fuel temperature.

## Slide 46: Control Rods (1.1.4.6.4)
Rods of neutron-absorbing material are installed in most reactors to provide precise, adjustable control of reactivity.
These rods are able to be moved into or out of the reactor core and typically contain elements such as silver, indium, cadmium, boron, or hafnium

## Slide 47: U-235 Fission
neutron
U-235
Fission Fragments
neutrons
Notes: This is the nuclear reaction that we are counting on!
Uranium-235 absorbs a thermal neutron. Soon the nucleus splits into two unequal size fission fragments, 2 to 3 new neutrons, and some gamma radiation.
The fission fragments have high kinetic energy which they transmit to the surrounding fuel material to produce heat energy.
The gamma radiation is a hazard which must be shielded.
The neutrons slow down to be absorbed by other U-235 nuclei to repeat the process.

## Slide 48: Uranium Fuel Pellets
Notes: Each pellet is approximately 5/8” high and is made of Uranium Dioxide.
The pellets and are stacked inside fuel pins to a height of 12 feet.
Each pellet contains the energy equivalent of 3 barrels of oil.
There are 7 million pellets in each reactor.
(1 pellet) X (144”) X (204 pins) X (157 elements) = >7,000,000
(0.625”) (pin) (element) (reactor)

## Slide 49: Moderator & Control Rods
Notes: Neutrons are born from fission in the fuel pins and migrate into the water moderator.
Approximately 18 collisions are needed to thermalize a neutron at which time it is ready to migrate back into the fuel and be absorbed by a Uranium-235 nucleus to repeat the process.
If a control rod (80% Silver/15% Indium/ 5%Cadmium) is inserted, the neutrons life is cut short and will be absorbed by the control rod before it makes it back to the fuel.
Note that there is dissolved Boron in the moderator. By regulating the boron concentration, operators can control reactor power and shutdown the reactor, independent of the control rods.

## Slide 50: Fuel Assembly
Notes: There are 157 fuel elements inside each reactor.
Each element weighs 1443 pounds and stands approximately 13 feet tall and is 8 and one half inches on a side.
15X15 fuel array with 21 guide sheathes.
Each element will spend three 18 month cycles before it is exhausted.

## Slide 51: Spent Fuel Element
Cerenkov
Radiation
Notes: This is what a fuel element looks like after it has been in the reactor.
The blue glow is called cerenkov radiation and is named after the Russian scientist who identified it as electrons that are moving faster than the speed of light through the water the element is immersed in.

## Slide 52: Spent Fuel Pool
Notes: This is a spent fuel pool. It is designed for long term storage of spent fuel elements.
The surface area is smaller than an Olympic size pool and it is 40 feet deep.
There are two spent fuel pools at Turkey Point. Each can hold 1400 spent fuel elements which is enough capacity store all of the fuel used at Turkey Point since plant inception through the year 2012.

## Slide 53: Fission Product Poisons
Fission fragments generated at the time of fission decay to produce a variety of fission products.
Fission products are of concern in reactors primarily because they become parasitic absorbers of neutrons and result in long term sources of heat.

## Slide 54: Fission Product Poisons
Although several fission products have significant neutron absorption cross sections, xenon-135 and samarium-149 have the most substantial impact on reactor design and operation.
Because these two fission product poisons remove neutrons from the reactor, they will have an impact on the thermal utilization factor and thus and reactivity.

## Slide 55: Reactor Operations: Startup (1.1.4.6.5)
When starting up a nuclear reactor with un-irradiated fuel the source neutron population will be very low.
In some reactors, the neutron population is frequently low enough that it cannot be detected by the nuclear instrumentation during the approach to criticality.
This is a major safety risk. Installed neutron sources are frequently used to provide a safe, easily monitored reactor startup.

## Slide 56: Reactor Operations: Startup
The neutron source, together with the subcritical multiplication process, provides a sufficiently large neutron population to allow monitoring by the nuclear instruments allowing for a safe startup of the reactor.

## Slide 57
Reactor Operations: Shutdown
A reactor is considered to be shut down when it is subcritical and sufficient shutdown reactivity exists so there is no immediate probability of regaining criticality.
Shutdown is normally accomplished by insertion of some (or all) of the control rods, or by introduction of soluble neutron poison into the reactor coolant.

## Slide 58: Questions???
Students: Now is your chance to have unclear concepts clarified. Please take advantage of this time to ask any questions pertaining to this material or material previously covered!