## Slide 1
ADAS Training for Truck Driver Students
This material is based on work supported by the National Science Foundation Grant DUE #2054997; any opinions, findings, conclusions, or recommendations expressed in this material are those of the author(s) and do not necessarily reflect the views of the National Science Foundation

## Slide 2
Levels of Vehicle Automation

## Slide 3
Pre/Post-Trip Inspections
Radar
Camera
In-cab Displays

## Slide 4
Pre/Post-Trip Inspections - Radar
Ensure unit is not cracked, broken, missing, or damaged.
Radar should be free of debris (i.e. excessive bugs).
Unit should not be blocked (i.e. snow, ice, added accessories or guards, etc.)

## Slide 5
Pre/Post-Trip Inspections - Camera
Ensure unit is not cracked, broken, missing, or damaged.
Camera should be free of obstructions (excessive bugs, cracked windshield, snow, ice, etc.).

## Slide 6
Pre/Post-Trip Inspections – In-Cab Displays
Ensure Wabco display cycles through the images to the right.

## Slide 7
Pre/Post-Trip Inspections – In-Cab Displays (Continued)
Ensure “Lane Alert” switch is in the on position and light on switch is illuminated.

## Slide 8
Pre/Post-Trip Inspections – In-Cab Displays (Continued)
Once Engine Starts, ensure “SPD CNTL” switch is switched OFF and then returned to the ON position and light on switch is illuminated.

## Slide 9
Operation
Crash Mitigation System (CMS)
Adaptive Cruise Control (ACC)
Lane Alert

## Slide 10
Operation - Crash Mitigation System (CMS)
Should work automatically once vehicle is above 17 MPH; display changes from “NO CMS” to “CMS”
Info on display is color coded:
Blue = no vehicle detected ahead
Green = vehicle detected – safe distance
Yellow = vehicle detected – caution
Red = vehicle detected – system activated

## Slide 11
Operation – Adaptive Cruise Control (ACC)
Cruise Control Button must be in on position and speed set
ACC System functions automatically
Display shows the following information:
Cruise speed setting
Speed of acquired vehicle ahead
Distance of acquired vehicle ahead

## Slide 12
Operation – Lane Alert
Lane Alert button must be in the on position
System functions automatically; provides audible “rumble” in left or right speakers
icon on dash display (behind steering wheel) indicates system has not identified a marked lane and audible signal will not be provided
https://youtu.be/LVCArsoXhSg

## Slide 13
Operation – Lane Alert
https://youtu.be/LVCArsoXhSg

## Slide 14
Troubleshooting
Observe/follow on-screen prompts
Check for visible damage
Check for blocked sensors/camera
Restart truck
Check fuses
Contact company/repair facility

## Slide 15
Carl Borleis
Director of Program Excellence, TCOE
PI, ISA-TOPE
651-423-8577
carl.borleis@dctc.edu
Chris Hadfield, Ed.M.
Executive Director, TCOE
Co-PI, National Center for Autonomous Technologies (NCAT)
Co-PI, ISA-TOPE
651-423-8311
Chris.hadfield@dctc.edu
Get in touch.
Forrest Brownlee
Diesel Technology Instructor, M-State
MTTIA Board of Directors
SME, ISA-TOPE
218-xxxxxxxxxx
Shannon.mohn@minnesota.edu
ISA-TOPE.ORG
Shannon Mohn
Automotive Instructor, M-State
MTTIA Training Coordinator
Co-PI, ISA-TOPE
218-299-6563
Shannon.mohn@minnesota.edu