## Slide 1
Network systems
DUE #2054997

## Slide 2
Agenda​
​
Overview of networks.
Testing

## Slide 3
Network Systems
Network systems offer many advantages over “hard wiring” components together
Network systems substantially lower the amount of wiring in a vehicle, sometimes eliminating a harness of 50 wires and replacing it with 3 wires.

## Slide 4
Traditional wiring systems would have “hard wiring” connecting each module with each input and output.
A good example would be the speed signal. Traditionally, the speed signal would be wired independently to the Engine Module, Anti-lock Brake Module, Transmission Module, Body Module, Radio, and Instrument Cluster.
Network Systems

## Slide 5
With networking, the speed signal would first go to one module, the Engine Module, and then be sent out over a 2-wire network to be shared with every module.
Some systems may utilize a 1-wire network.
Networks eliminate the need for having several different wires carrying the same information.
Network Systems

## Slide 6
Network Systems
Single Wire Network
CAN BUS 2-Wire Network
Networks Can Be Either a Single Wire or 2-WIre Networks

## Slide 7
CAN BUS
Controller Area Network (CAN) Protocol first Invented by Bosch in 1986
Now used by cars, trucks, drones, heavy equipment, boats, motorcycles, and many other applications.
Allows many modules to be connected via the “Twisted Wires”.
Some vehicles can have more than 70 modules connected together talking to each other on 1 network.
Allows for super fast communications between modules
2- Wire High Speed Networks Used In Vehicles are Called CAN BUS Networks.

## Slide 8
Overview of How CAN BUS Works

## Slide 9
Binary Language
Modules communicate with each other using Binary Language
Binary language is very simple: It is full of 1’s and 0’s
A “1” means that the “Bit” of information has power turned on
A “0” means that the “bit” of information has the power turned off
A group of 1’s and 0’s creates a Byte of information
A 500kb/second means that 500,000 of these “bits” is moving through the network
The very first binary language was Morse Code with on and off signals that would be sent via telegraph.

## Slide 10
Binary Language
As one can see, the on/off binary language is how a module on a network communicates with other modules.
Most CAN BUS networks use a 5-volt reference with a 2.5-volt bias
CAN BUS uses a High and a Low. One always mirrors the other to produce a “fail safe” signal if one were to fail

## Slide 11
CAN BUS Wiring
CAN BUS wiring is “twisted and shielded to reduce the possibility of interference.
RFI (radio Frequency Interference) can cause noise if the wiring is not twisted and shielded.
Shielding protects the twisted wires against outside radio frequency waves (called RFI). Shielding needs to be grounded on both ends.
If the ground is damaged on the shielding, it will pick up RFI like a vehicle's antenna, so it is important that grounds on shield wiring are intact.

## Slide 12
CAN BUS Network
Trucks use the J1939 connector.
This is the standard CAN BUS protocol for the heavy truck and heavy equipment industry.
The diagnostic pins for network communication are all located in the same place for all makes and models.
Trucks and heavy equipment may have several other networks in addition to the J1939 network.
Pins C and D are used for the J1939 network. This is standardized.

## Slide 13
Networks with a 500kb/s transfer rate or higher are called "High Speed" Networks.
J1939 Network
Transfers data at 250kb/second on older models and at 500kb/second on newer models.
Packets of data travel over the network and can be read by all modules.
Modules are connected to the network via 2 wires in the network. Each module has its own power and ground but exchange information on the network.
On each end of the network are 2–120-ohm resisters. These resisters are referred to as Terminating Resisters

## Slide 14
Terminating Resisters
On each side of the CAN BUS Network, connecting the high and low circuits are two 120-ohm terminating resisters. These resisters absorb any residual voltage allowing for a "clean" signal. These resisters can be located independently in the circuit, or in a module. The sum of these two resisters should give you 60 ohms of resistance. Any other reading you get will indicate a problem in the circuit. It is important to know where these resisters are to service the system. Service information should give you these locations.

## Slide 15
Terminating Resisters

## Slide 16
Data Packets
CAN BUS uses both a high voltage line and a low voltage Line.
The high voltage line toggles between a low of 2.5 volts and a high of 3.5 volts.
The low voltage line toggles between 1.5 volts and a high of 2.5 volts.

## Slide 17
Data Packets
The high side should ALWAYS be an exact opposite mirror image of the low side.
Both the high and low sides of the CAN BUS network should have a voltage right around 2.5 volts measured with a multi-meter with no traffic on the line.

## Slide 18
Data Packets
Because every module sees every message that is traveling on the BUS line, the first part of the message “identifies” which module(s) the message is intended for.
That is the 29 bit identifier
Every message contains this identifier and if it does not match what the module is looking for, it will disregard the message.
Breaking Down the Data Packet

## Slide 19
Data Packets
The second part of the message is the 64-bit data field.
This tells the modules what is the important data i.e., “Engine Speed”, “Transmission Temperature”, etc.
Breaking Down the Data Packet

## Slide 20
Data Packets
The next part repeats and rechecks the information
The last part of the message tells the modules that the message is ending.
Breaking Down the Data Packet

## Slide 21
Network Testing
Testing the network is actually done quite easily
Several quick diagnostic tests will help determine if the problem is network Related or just related to that module.
Every module needs power, ground, and network connections to talk on the CAN Bus Network.
Relax!

## Slide 22
Network Testing
The first step is to do a network test using the scan tool
When hooking up Cat ET it will search for equipment ECMs if the tool cannot hook up you will have to test the J1939 network manually at the diagnostic connector 9pin in cab
2 terminating resisters at 120 Ohms should equal 60 Ohms at the Diagnostic Data Link Connector Pins C and D

## Slide 23
Next if you power up the machine and Hit Menu and OK simultaneously
You should be able to see the networks on the Trimble system
Access by pressing menu and enter keys simultaneously
You will be able to view which components are communication with the CB450
And see what CAN port they are received on

## Slide 25
Network Testing
Trimble uses 3 CAN Bus networks
CAN 0
Communication between all devices
CAN 1
Communication between machine ecm and the system ecm
Can 2
Communication for recevers

## Slide 26
CAN Line Communication
Cat Machines

## Slide 27: Trimble
Disconnect all components and reconnect at one time to see if networks come down. A bad component will pull the can system off-line. See slide 29#
Each individual terminator should be 120 Ohms
At this time, we will:
Check resistance between the CAN high and CAN low pins Check with power off and components connected looking to see 60 Ohms of resistance Check voltage between CAN wires and ground. Check with power on Should be around 2.5v on each CAN wire

## Slide 28
Network Testing​
Once you have performed a network test and tested the integrity of the network, all that is left is to hook up a scope. Set scope to 50 us/div on the 5-volt scale and use both channels A and B.
This is a great tool if you have 1 module taking down the network.
You can unplug each module and see which module is bad.

## Slide 29
Network Testing​
If the network "comes back to life" after a module is disconnected, that is the module that is shorted.
You can also use this same method if the terminating resistance is above or below specifications. You will just need to have information on which modules contain the resisters.

## Slide 30
References Used:​
Slide #3​ - (https://rennlist.com/forums/944-turbo-and-turbo-s-forum/309056-how-to-read-wiring-diagrams-no-start-post-42-a-3.html) accessed 06/01/2023
Slide #6 - (https://www.mdpi.com/1424-8220/22/18/6901) accessed 06/01/2023
Slide #6 - (https://www.robotsforroboticists.com/can-bus/) accessed 06/01/2023
Slide #8 - (https://www.youtube.com/watch?v=FqLDpHsxvf8) accessed 06/01/2023
Slide #11 - (https://www.pngegg.com/en/search?q=shielded+Twisted+Pair) accessed 06/01/2023
Slide #12 - (https://static.nhtsa.gov/odi/tsbs/2018/MC-10161073-9999.pdf) accessed 06/01/2023
Slide #15 - (https://www.csselectronics.com/products/terminal-resistor-can-bus) accessed 06/01/2023
Slide #17-19 - (https://www.electriciansjournal.com/home/can-bus-j1939)
Slide #21 - (http://www.clipartbest.com/panic-gif)
Slide #23#24#25 https://learn.trimble.com/learn/course/1046/play/6773/mch-220-can-and-harness-troubleshooting ( accessed 6/16/23)

## Slide 31
Carl Borleis
Director of Program Excellence, TCOE
PI, ISA-TOPE
651-423-8577
carl.borleis@dctc.edu
Chris Hadfield, Ed.M.
Executive Director, TCOE
Co-PI, National Center for Autonomous Technologies (NCAT)
Co-PI, ISA-TOPE
651-423-8311
Chris.hadfield@dctc.edu
Get
Forrest Brownlee
Diesel Technology Instructor, Minnesota North - Hibbing
MTTIA Board of Directors
SME, ISA-TOPE
218-293-6862
forrest.brownlee@minnesotanorth.edu
ISA-TOPE.ORG
Shannon Mohn
Automotive Instructor, M-State
MTTIA Training Coordinator
Co-PI, ISA-TOPE
218-299-6563
Shannon.mohn@minnesota.edu
in
touch.