## Slide 1
Overview of System Components
DUE #2054997

## Slide 2
Agenda​
​
WAVS overview
2D system component overview

## Slide 3: Work Area Vision System (WAVS)
The Cat Work Area Vision System (WAVS) is designed to improve the operators view around a piece of equipment. The system consists of a dedicated 20.3 cm (8.00 inch) display and up to four cameras. The WAVS enhances an operator's awareness of the site surroundings, work tool activities, and changes in work area conditions increasing safety and productivity. The customer can select precisely the WAVS options the customer needs, based on equipment size, work site environment, and application.

## Slide 4: Work Area Vision System (WAVS) - Continued
Direct vision (from cab to ground)
Mirrors
Spotters
Warning horns
The operator still needs to use other means of safe operation. Use the following examples to verify that the area is clear or provide warning before the machine is moved:

## Slide 5
The WAVS can be set up for one to four cameras. These options are selected prior to installation and configured during installation process via Cat Electronic Technician (ET).
Our system relies on 1 camera located on the back of the machine to assist with work area vision
Work Area Vision System (WAVS) - Continued

## Slide 6
Location of camera

## Slide 7: For the operator to adjust back up lines to preference first locate the operator's main display

## Slide 8: Then Click on the Service Icon

## Slide 9: Then using the buttons scroll to the appropriate function

## Slide 10: From there the operator can adjust the witness lines to their preference

## Slide 11
2D system component overview

## Slide 12
Laser has four strips of red photodiodes for 360-degree reception
Diodes can detect laser "strike" from transmitter (at 600rpm strikes coming 10x per second)
Length of diode strip is 231mm / 9.1" (this impacts the amount of attachment travel after benching)
You do need a compatible laser transmitter
LR410
Receiver

## Slide 13: CB450
Control box!
Compatible with all GCS systems, 2D, and CAT Grade Control 3D systems
The control box is responsible for all operations of the system

## Slide 14: GL622N
Rotates at very fast speeds
  3 speed settings 300, 600, 750
  600rpm is optimal for machine control (10 rotations per second)
Rotation is so fast that light seems dispersed as a plane of light
  Spinning prism directs a vertical laser beam into a horizontal plane
  Based on rotation speed, discrete laser strikes are detected by laser receiver,
Self levelling for easy setup
Recommended maximum range for machine control
  Approximately 300m/1000 ft radius

## Slide 15: Laser Transmitter Reminders
Laser transmitter creates a reference plane that is parallel to the desired surface
Three options for laser planes
  Level (no slope)
  Single sloping plane (along an axis)
  Dual sloping plane (adds slope along the other axis)
Note these are all "flat" surfaces-but only one is level (zero slope)

## Slide 16
References Used:
https://learn.trimble.com/pages/189/home

## Slide 17
Carl Borleis
Director of Program Excellence, TCOE
PI, ISA-TOPE
651-423-8577
carl.borleis@dctc.edu
Chris Hadfield, Ed.M.
Executive Director, TCOE
Co-PI, National Center for Autonomous Technologies (NCAT)
Co-PI, ISA-TOPE
651-423-8311
Chris.hadfield@dctc.edu
Get
Forrest Brownlee
Diesel Technology Instructor, Minnesota North - Hibbing
MTTIA Board of Directors
SME, ISA-TOPE
218-293-6862
forrest.brownlee@minnesotanorth.edu
ISA-TOPE.ORG
Shannon Mohn
Automotive Instructor, M-State
MTTIA Training Coordinator
Co-PI, ISA-TOPE
218-299-6563
Shannon.mohn@minnesota.edu
in
touch.