## Slide 1
Machine start
2d system set up
DUE #2054997

## Slide 2
Agenda​
​
Machine start overview
2d set up and operation

## Slide 3: Machine Start up
After pre-operating inspection and review of machine controls. Proceed to turn on the machine power in engine compartment.
Sit in machine and buckle seat belt and pull-down arm rests
Turn the key in to run position check to see if the glow plug icon is illuminated if it's not, go ahead and turn the key to start and start machine

## Slide 4
2D setup

## Slide 5: Laser system
Machine components
  Laser receivers
  Machine display
  Cables
Off machine
  Laser transmitter
  Tripod

## Slide 6
Clear any accumulated debris from around the radiator and other engine components.
The engine is made of moving parts and belts that generate heat and friction – and systems designed to
cool the engine compartment require room to breathe. It’s important to check and remove any clutter or
material from the jobsite that may have found its way into the engine compartment.
Machine Components

## Slide 7: Laser Receiver
Needs to be installed so the Laser strikes can be detected ( preferably above cab )
Lach on the back of receiver is attached to the support poles on box blade Hand tight !
Facing forward
Attach harness between laser receiver and quick connect on box blade

## Slide 8
Harness
Hook up

## Slide 9: CB450 and Connector

## Slide 10: Machine Display (CB450)
Needs to be attached in the cab on the door or easily visible to operator
Carefully attach the Trimble control harness

## Slide 11: Guidance screens
Optional text information area
Guidance view area
Guidance settings bar

## Slide 12: CB450 controls
Power key: press once to start, hold 3 seconds to power down
Soft keys Row of vertical buttons F1 – F6 correspond to labels that appear on right side of screen
Zoom in
Zoom out
Next key – cycles through available views
Escape key use to escape out of one screen at a time
Ok/enter key use to select items or apply entered values or changes in editable fields
Menu key used to enter configuration and installation menus
Arrow keys move around menus

## Slide 13: Lazer Transmitter
Rotates at verry fast speeds
  600 RPM is optimal for machine control (10 rotations per second
Rotation is so fast that light seems dispersed as a plane of light
  Spinning prism directs a vertical laser beam into a horizontal plane
  Based on rotation speed, discrete laser strikes are detected by laser receiver
Self leveling for easy set up
Recommended maximum range for machine control:
  Approximately 300m / 1000ft radius
  Coverage is then roughly 600m / 2000 ft from one setup

## Slide 14
To set up the laser install on the tripod and press the red power button to turn on
For our set up we can set the rotation for 600 and then hit enter to turn on the laser then we can crank the laser to our desired Hight, and it will self-level when the eye starts spinning
Remember the foundation of the laser needs to be a stable area vibrations from other machines or infrastructure can affect the laser

## Slide 15: Running the 2D system
After installing the receivers and CB450 controller.
Find a suitable spot for the laser and tripod.
Start the laser adjust and let the laser self-level usually take a few seconds for the laser to start spinning up to speed
Power up the machine and find you bench location and set the cutting edge of the blade on it left side adjust the receivers so the laser is hitting them center then bench the left receiver on the CB450 then repeat for right side ( solid red light if you're too low it will be a slow flash if to high it will be fast )
Now you have Benched the machine !

## Slide 16: Benching
Process where we Fix the laser plane, machine receivers and blade relative to grade.
Requires two things
  A starting point at ground zero
  Laser transmitter ( laser plane )
We use this to determine the actual elevation of the laser plane or the relative height of the laser plane above a known point
  Result the machine blade is calibrated to the laser plane
Remember we only have 9.1 inches of receiver for the laser

## Slide 18
Press F6 to bench from right receiver
Press F5 to bench from left receiver

## Slide 19
Now pushing F4 you can set your setbacks into the system above or below your bench is set.

## Slide 20: Now you can tun on the auxiliary switch and hold the right joystick trigger down and thumb wheel up until beacon on the machine screen stops flashing
If you don’t hold your thumb wheel in the up position, you will not activate the correct aux hydraulics

## Slide 21: Auxiliary power switch

## Slide 22: Now make sure that the Aux 7 switch is on
This will allow the Left joystick to control the axillary to the box blade now the trigger on the left should toggle the CB450 controller from manual to auto if you have your of sets programed the box blade should move by itself then if you toggle the switch to manual, you can use the thumb buttons on the controllers to manually toggle the blade

## Slide 23
https://www.youtube.com/watch?v=voIJm3iV3iM

## Slide 25
References Used:
https://learn.trimble.com

## Slide 26
Carl Borleis
Director of Program Excellence, TCOE
PI, ISA-TOPE
651-423-8577
carl.borleis@dctc.edu
Chris Hadfield, Ed.M.
Executive Director, TCOE
Co-PI, National Center for Autonomous Technologies (NCAT)
Co-PI, ISA-TOPE
651-423-8311
Chris.hadfield@dctc.edu
Get
Forrest Brownlee
Diesel Technology Instructor, Minnesota North - Hibbing
MTTIA Board of Directors
SME, ISA-TOPE
218-293-6862
forrest.brownlee@minnesotanorth.edu
ISA-TOPE.ORG
Shannon Mohn
Automotive Instructor, M-State
MTTIA Training Coordinator
Co-PI, ISA-TOPE
218-299-6563
Shannon.mohn@minnesota.edu
in
touch.