## Slide 1
Systems Diagnostics and Repair
DUE #2054997

## Slide 2
Agenda​
​
2D System Diagnosis and Repair

## Slide 3: Terms to understand
Machine Calibration (valves, operator controls)
GCS - Grade Control System
GNSS – Global Navigation Satellite System
Function Instance - used to address having the multiple of the same device in the can-bus loop / different locations for the same devices using wiring harness pins to denote device locations
CAN – Controller Area Network
Communication Protocall, Primary SAE J1939 protocol
Others to be aware of
  ISO Bus protocol
  CAN open protocol
  Plain CAN protocol
  Propriety CAN protocol

## Slide 4: Terms to understand
2D sensors – relating to elevation and slope
LR 410 – laser receiver detects laser plane for height reference
CB450 – control box may be used with 2D or 3D systems with correct harnesses
Note : for detailed product information, access to the following is required:
Cat Sis Web 2.0
Trimble Learn

## Slide 5
Most Current Harness Design
GCS
CAN0 – Machine control CAN devices traffic for all sensors, control box, GNSS receiver configuration and position reporting.
CAN1 handles the Machine ECM and the display communication separate CAN-BUS that allows communication will all the rest of the traffic.
CAN2 left to right GNSS receivers

## Slide 7: To get good performance out of the system machine needs to be in good working condition
Worn or improperly adjusted undercarriage
Machine calibrations falling out of spec or improper calibrations
Might not see the problems as much with the machine in manual because an operator will be able to correct the machine better than the auto grade system.
Possible Problems

## Slide 8: BB124 box blade
Electrical connector locations
Implement control ECM (area A)
Valve body (area A)

## Slide 9: BB124 Box Blade
Implement valve
ECM location

## Slide 10: Most common problems
  Power supply
  Function Instance
  CAN

## Slide 11: Power supply
Check power to receivers and control modules
Are the auxiliary switches working correctly
Bad harness ?

## Slide 12: Function Instance
Instance is defined in wiring harness not in the devices
Pins B and E on 6 pin and 10 pin connectors
Designated in different variations of grounded or open wires or both
normally show up as conflicting sensors in controller diagnostics
Bad pins or harness normally

## Slide 14: CAN
Terminators / resistance through harness
Resistance between high and low
Connectivity
Hi and Low correct
Voltage correct CAN0 or CAN1

## Slide 15
References Used:
https://learn.trimble.com
https://sis2.cat.com/#/

## Slide 16
Carl Borleis
Director of Program Excellence, TCOE
PI, ISA-TOPE
651-423-8577
carl.borleis@dctc.edu
Chris Hadfield, Ed.M.
Executive Director, TCOE
Co-PI, National Center for Autonomous Technologies (NCAT)
Co-PI, ISA-TOPE
651-423-8311
Chris.hadfield@dctc.edu
Get
Forrest Brownlee
Diesel Technology Instructor, Minnesota North - Hibbing
MTTIA Board of Directors
SME, ISA-TOPE
218-293-6862
forrest.brownlee@minnesotanorth.edu
ISA-TOPE.ORG
Shannon Mohn
Automotive Instructor, M-State
MTTIA Training Coordinator
Co-PI, ISA-TOPE
218-299-6563
Shannon.mohn@minnesota.edu
in
touch.